## Slide 1: Lecture 0: Introduction
E85 Digital Design & Computer Engineering

## Slide 2
Course Overview
  Learning Objectives
  Schedule
  Assignments
The Game Plan
The Art of Managing Complexity
The Digital Abstraction
Number Systems
Lecture 0

## Slide 3
Build digital systems at all levels of abstraction from transistors through circuits, logic, microarchitecture, architecture, and C culminating with implementing and programming a microprocessor soft core on a field programable gate array.
Manage complexity using the digital abstraction, data types, static and dynamic disciplines, and hierarchical design.
Design and implement combinational and sequential digital circuits using schematics and hardware description languages.
Learning Objectives

## Slide 4
Program a commercial microcontroller in C and assembly language and use it in a physical system.
Begin the practice of implementing and debugging digital systems with appropriate lab techniques including breadboarding, interpreting datasheets, and using field-programmable gate arrays and microcontroller boards, simulators, debuggers, and test-and-measurement equipment.
Learning Objectives Cont.

## Slide 5
Start from the fundamentals so you understand why, not just how.
  What makes the system tick on the inside?
Some of you will become computer engineers.
  This material is the foundation of your career.
Most of you will pursue other paths.
  Digital systems are a tremendously valuable tool in your toolbox.
  This course will get you to the point you can be dangerous!
  Skills about managing complexity, designing nontrivial systems, debugging carry over to other fields.
  Programmable microprocessors are one of humanities great ideas.
  Computing has fundamentally changed the world we live in.
If you like this course, take E155 next Fall.
Big Picture

## Slide 6
Schedule
Lecture | Date | Topics | Readings | Assignment
0 | 1/22 | Introduction: digital abstraction, numbers | 1.1-1.5 | 
1 | 1/27 | Logic gates, Static discipline, transistors | 1.6-1.9, A1-A7 | 
10 | 1/29 | Combinational logic design | 2.1-2.8 | PS 1 due
11 | 2/3 | Timing, sequential circuits | 2.9-2.10, 3.1-3.2 | Lab 1 due Digital Circuits
100 | 2/5 | Finite state machines | 3.3-3.4 | PS 2 due
101 | 2/10 | Dynamic discipline, metastability | 3.5-3.7 | Lab 2 due Comb Logic
110 | 2/12 | Hardware description languages: Verilog | 4.1-4.3 | PS 3 due
111 | 2/17 | Verilog, Part II | 4.4-4.10 | Lab 3 due Structural FSM
1000 | 2/19 | Arithmetic circuits | 5.1-5.2 | PS 4 due
1001 | 2/24 | Fixed and floating-point number systems | 5.3 | Lab 4 due Behavioral FSM
1010 | 2/26 | Sequential building blocks, arrays | 5.4-5.7 | PS 5 due
1011 | 3/2 | Catchup / Midterm Review |  | Lab 5 due Building blocks
 | 3/4 | Midterm |  | 
1100 | 3/9 | C Programming | C.1-C.7 | 
1101 | 3/11 | C Programming | C.8-C.11 | 
 | 3/16 | Spring Break! |  | 
 | 3/18 | Spring Break! |  | 
1110 | 3/23 | Microcontrollers: Memory-mapped I/O | 9.1-9.3.3 | Lab 6 due C Programming
1111 | 3/25 | Parallel & serial interfacing, ADCs | 9.3-9.4 | PS 6 due
10000 | 3/30 | I/O libraries and examples |  | Lab 7 due C I/O
10001 | 4/1 | Assembly language | 6.1-6.3.6 | PS 7 due
10010 | 4/6 | Function calls, machine language | 6.3.7-6.9 | Lab 8 due C Peripherals
10011 | 4/8 | Single-cycle processor datapath | 7.1-7.3.1 | PS 8 due
10100 | 4/13 | Single-cycle processor control, Verilog | 7.3, 7.6 | Lab 9 due Assembly
10101 | 4/15 | Multicycle processor | 7.4 | 
10110 | 4/20 | Pipelining | 7.5.1-2 | PS 9 due
10111 | 4/22 | Advanced architecture: a sampler | 7.7 | Lab 10 due Multicycle Control
11000 | 4/27 | Case study: Processors | 6.7, 8.7, 8.5 | PS 10 due
11001 | 4/29 | Class summary and review |  | Lab 11 due Multicycle CPU

## Slide 7
Mondays: Labs (30%)
  Must complete Lab 11 to pass the class
  Digital Lab Tutoring Sat 12-2, Sun 12-6
Wednesdays: Problem Sets (20%)
  TBP TBD
Midterm & Final (50%)
You can have a 1-week extension on one assignment
  Just turn it in with your assignment next week
Your lowest lab and problem set score will be dropped
Assignments

## Slide 8
Speak with other students, instructor, tutors AFTER you have made an effort by yourself.
  Ask about tool issues in the lab!
Turn in your own work. Not identical to others.
  Don’t sit at adjacent computers and work in lockstep.
  Pair programming prohibited.
Credit classmates with whom you discussed ideas.
Don’t refer to old solutions!
Collaboration Policy

## Slide 9
Many students have found it enjoyable and useful
  Suggest reading before class, come with questions
  Reread key parts as you are doing the assignments
Not everything in the assignments is covered in lecture.
Copies available in the Eng. Lounge and Digital Lab.
Textbook

## Slide 10
Microprocessors have revolutionized our world
  Cell phones, Internet, rapid advances in medicine, etc.
The semiconductor industry has grown from $21 billion in 1985 to $412 billion in 2017
Background

## Slide 11
Abstraction
Discipline
The Three –y’s
  Hierarchy
  Modularity
  Regularity
The Art of Managing Complexity

## Slide 12
Hiding details when they aren’t important
Abstraction

## Slide 13
Intentionally restrict design choices
Example: Digital discipline
  Discrete voltages instead of continuous
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors: i.e., digital cameras, digital television, cell phones, CDs
Discipline

## Slide 14
Hierarchy
  A system divided into modules and submodules
Modularity
  Having well-defined functions and interfaces
Regularity
  Encouraging uniformity, so modules can be easily reused
The Three -y’s

## Slide 15
Hierarchy
  Three main modules: lock, stock, and barrel
  Submodules of lock: hammer, flint, frizzen, etc.
Example: The Flintlock Rifle

## Slide 16
Modularity
  Function of stock: mount barrel and lock
  Interface of stock: length and location of mounting pins
Regularity
  Interchangeable parts
Example: The Flintlock Rifle

## Slide 17
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
  Position of a mass
Digital abstraction considers discrete subset of values
The Digital Abstraction

## Slide 18
Designed by Charles Babbage from 1834 – 1871
Considered to be the first digital computer
Built from mechanical gears, where each gear represented a discrete value (0-9)
Babbage died before it was finished
The Analytical Engine

## Slide 19
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit
Digital Discipline: Binary Values

## Slide 20
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT
George Boole, 1815-1864

## Slide 21
Decimal numbers
Binary numbers
Number Systems

## Slide 22
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two
Handy to memorize

## Slide 23
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 24
Two methods:
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
Decimal to Binary Conversion

## Slide 25
  5310
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  5310 32×1
  53-32 = 21 16×1
  21-16 = 5 4×1
  5-4 = 1 1×1 = 1101012
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
  5310 = 53/2 = 26 R1
  26/2 = 13 R0
  13/2 = 6 R1
  6/2 = 3 R0
  3/2 = 1 R1
  1/2 = 0 R1 = 1101012
Decimal to Binary Conversion

## Slide 26
  Another example: Convert 7510 to binary.
  7510= 64 + 8 + 2 + 1 = 10010112
or
75/2 = 37 R1
37/2 = 18 R1
18/2 = 9 R0
9/2 = 4 R1
4/2 = 2 R0
2/2 = 1 R0
1/2 = 0 R1
Decimal to Binary Conversion

## Slide 27
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 28
Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 29
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 30
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 31
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 32
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
240 = 1 tera ≈ 1 trillion
250 = 1 peta ≈ 1 quadrillion
260 = 1 exa ≈ 1 quintillion
Large Powers of Two

## Slide 33
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 34
Decimal
Binary
Addition

## Slide 35
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 36
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 37
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 38
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 39
Problems:
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 40
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 41
msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s complement number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers
+

## Slide 42
“Taking the Two’s complement” flips the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 43
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 44
Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 45
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 46
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 47
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 48
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 49
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison