## Slide 1: Lecture 16: RISC-V Assembly Language
E85
Digital Electronics & Computer Architecture

## Slide 2
Lecture 16
Introduction
  Instruction Set Architecture (ISA)
  RISC-V History
RISC-V Assembly Language
  Instructions
  Register Set
  Memory
  Programming constructs

## Slide 3
Lecture 16
Introduction
  Instruction Set Architecture (ISA)
  RISC-V History
RISC-V Assembly Language
  Instructions
  Register Set
  Memory
  Programming constructs

## Slide 4
Jumping up a few levels of abstraction
Architecture: programmer’s view of computer
  Defined by instructions & operand locations
Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)
Introduction

## Slide 5
Instructions: commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
RISC-V architecture:
  Developed by Krste Asanovic, David Patterson and their colleagues at UC Berkeley in 2010.
  First open-source computer architecture
Once you’ve learned one architecture, it’s easier to learn others
Assembly Language

## Slide 6: Instruction Set Architecture Manual
RISC-V ISA Manual available at: https://riscv.org/specifications/isa-spec-pdf/
Details base integer ISA along with optional extensions
Gives not only the specs but also some helpful rationale and reasoning behind the decisions

## Slide 7
Professor of Computer Science at the University of California, Berkeley
Developed RISC-V during one summer
Chairman of the Board of the RISC-V Foundation
Co-Founder of SiFive, a company that commercializes and develops supporting tools for RISC-V
Krste Asanovic

## Slide 8
Professor of Computer Science at the University of California, Berkeley since 1976
Coinvented the Reduced Instruction Set Computer (RISC) with John Hennessy in the 1980’s
Developed the RISC architecture at Berkeley in 1984, which was later commercialized as SPARC architecture
David Patterson

## Slide 9
Underlying design principles, as articulated by Hennessy and Patterson:
    Simplicity favors regularity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises
Architecture Design Principles

## Slide 10
Lecture 16
Introduction
  Instruction Set Architecture (ISA)
  RISC-V History
RISC-V Assembly Language
  Instructions
  Register Set
  Memory
  Programming constructs

## Slide 11
add: mnemonic indicates operation to perform
b, c: source operands (on which the operation is performed)
a: destination operand (to which the result is written)
C Code
a = b + c;
RISC-V assembly code
add a, b, c
Instructions: Addition

## Slide 12
Similar to addition - only mnemonic changes
sub: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
RISC-V assembly code
sub a, b, c
Instructions: Subtraction

## Slide 13
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
Easier to encode and handle in hardware
Design Principle 1

## Slide 14
More complex code is handled by multiple RISC-V instructions.
C Code
a = b + c - d;
RISC-V assembly code
add t, b, c # t = b + c
sub a, t, d # a = t - d
Multiple Instructions

## Slide 15
Make the common case fast
RISC-V includes only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
RISC-V is a reduced instruction set computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)
Design Principle 2

## Slide 16
Operand location: physical location in computer
  Registers
  Memory
  Constants (also called immediates)
Operands

## Slide 17
RISC-V has 32 32-bit registers
Registers are faster than memory
RISC-V called “32-bit architecture” because it operates on 32-bit data
Operands: Registers

## Slide 18
Smaller is Faster
RISC-V includes only a small number of registers
Design Principle 3

## Slide 19
Name | Register Number | Usage
zero | x0 | Constant value 0
ra | x1 | Return address
sp | x2 | Stack pointer
gp | x3 | Global pointer
tp | x4 | Thread pointer
t0-2 | x5-7 | Temporaries
s0/fp | x8 | Saved register / Frame pointer
s1 | x9 | Saved register
a0-1 | x10-11 | Function arguments / return values
a2-7 | x12-17 | Function arguments
s2-11 | x18-27 | Saved registers
t3-6 | x28-31 | Temporaries
RISC-V Register Set

## Slide 20
Registers:
  Can use either name (i.e., ra, zero) or x0, x1, etc.
  Using name is preferred
Registers used for specific purposes:
    zero always holds the constant value 0.
    the saved registers, s0-s11, used to hold variables
    the temporary registers, t0-t6, used to hold intermediate values during a larger computation
    Discuss others later
Operands: Registers

## Slide 21
Revisit add instruction
C Code
a = b + c
RISC-V assembly code
# s0 = a, s1 = b, s2 = c
add s0, s1, s2
Instructions with Registers
# indicates a single-line comment

## Slide 22: Operands: Memory
Too much data to fit in only 32 registers
Store more data in memory
Memory is large, but slow
Commonly used variables kept in registers

## Slide 23
First, we’ll discuss word-addressable memory
Then we’ll discuss byte-addressable memory
Memory
RISC-V is byte-addressable

## Slide 24
Each 32-bit data word has a unique address
Word-Addressable Memory
Note: RISC-V uses byte-addressable memory, which we’ll talk about next.

## Slide 25
Memory read called load
Mnemonic: load word (lw)
Format:
lw <rd>, <offset>(<base register>)
lw t1, 5(s0)
Address calculation:
  add offset (5) to the base address (s0)
  address = (s0 + 5)
Destination register (rd):
  t1 holds the value at address (s0 + 5)
Any register may be used as base address
Reading Word-Addressable Memory

## Slide 26
Example: read a word of data at memory address 1 into s3
  address = (0 + 1) = 1
  s3 = 0xF2F1AC07 after load
Assembly code
lw s3, 1(zero) # read memory word 1 into s3
Reading Word-Addressable Memory

## Slide 27
Memory write are called store
Mnemonic: store word (sw)
Format similar to load
sw <src1>, <offset>(<base register>)
Writing Word-Addressable Memory

## Slide 28
Example: Write (store) the value in t4 into memory address 7
  add the base address (zero) to the offset (0x7)
  address: (0 + 0x7) = 7
  Offset can be written in decimal (default) or hexadecimal
Assembly code
sw t4, 0x7(zero) # write the value in t4
# to memory word 7
Writing Word-Addressable Memory

## Slide 29
Each data byte has unique address
Load/store words or single bytes: load byte (lb) and store byte (sb)
32-bit word = 4 bytes, so word address increments by 4
Byte-Addressable Memory

## Slide 30
The address of a memory word must now be multiplied by 4. For example,
  the address of memory word 2 is 2 × 4 = 8
  the address of memory word 10 is 10 × 4 = 40 (0x28)
RISC-V is byte-addressed, not word-addressed
Reading Byte-Addressable Memory

## Slide 31
Example: Load a word of data at memory address 4 into s3.
s3 holds the value 0xF2F1AC07 after load
RISC-V assembly code
lw s3, 4(zero) # read word at address 4 into s3
Reading Byte-Addressable Memory

## Slide 32
Example: stores the value held in t7 into memory address 0x2C (44)
RISC-V assembly code
sw t7, 44(zero) # write t7 into address 44
Writing Byte-Addressable Memory

## Slide 33
How to number bytes within a word?
Little-endian: byte numbers start at the little (least significant) end
Big-endian: byte numbers start at the big (most significant) end
Word address is the same for big- or little-endian
Big-Endian & Little-Endian Memory

## Slide 34
Jonathan Swift’s Gulliver’s Travels: the Little-Endians broke their eggs on the little end of the egg and the Big-Endians broke their eggs on the big end
It doesn’t really matter which addressing type used – except when the two systems need to share data!
Big-Endian & Little-Endian Memory

## Slide 35
Suppose t0 initially contains 0x23456789
After following code runs on big-endian system, what value is s0?
In a little-endian system?
sw t0, 0(zero)
lb s0, 1(zero)
Big-Endian & Little-Endian Example

## Slide 36
Big-Endian & Little-Endian Example
Suppose t0 initially contains 0x23456789
After following code runs on big-endian system, what value is s0?
In a little-endian system?
sw t0, 0(zero)
lb s0, 1(zero)
Big-endian: s0 = 0x00000045
Little-endian: s0 = 0x00000067

## Slide 37
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Common high-level software constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming

## Slide 38
Wrote the first computer program
Her program calculated the Bernoulli numbers on Charles Babbage’s Analytical Engine
She was the daughter of the poet Lord Byron
Ada Lovelace, 1815-1852

## Slide 39
Execute instructions out of sequence
Types of branches:
  Conditional
    branch if equal (beq)
    branch if not equal (bne)
    branch if less than (blt/bltu)
    branch if greater than or equal to (bge/bgeu)
  Unconditional
    jump (j)
    jump register (jr)
    jump and link (jal)
    jump and link register (jalr)
Branching
Will talk about these when we discuss function calls

## Slide 40
# RISC-V assembly
addi s0, zero, 4 # s0 = 0 + 4 = 4
addi s1, zero, 1 # s1 = 0 + 1 = 1
slli s1, s1, 2 # s1 = 1 << 2 = 4
beq s0, s1, target # branch is taken
addi s1, s1, 1 # not executed
sub s1, s1, s0 # not executed
target: # label
add s1, s1, s0 # s1 = 4 + 4 = 8
Labels indicate instruction location. They can’t be reserved words and must be followed by colon (:)
Conditional Branching (beq)

## Slide 41
# RISC-V assembly
addi s0, zero, 4 # s0 = 0 + 4 = 4
addi s1, zero, 1 # s1 = 0 + 1 = 1
slli s1, s1, 2 # s1 = 1 << 2 = 4
bne s0, s1, target # branch not taken
addi s1, s1, 1 # s1 = 4 + 1 = 5
sub s1, s1, s0 # s1 = 5 – 4 = 1
target:
add s1, s1, s0 # s1 = 1 + 4 = 5
The Branch Not Taken (bne)

## Slide 42: Other Conditional Branches
Branch if less than (blt/bltu)
  blt s0, s1, target # branches if s0 < s1 (signed)
  bltu s0, s1, target # same as blt but interprets # s0 and s1 as unsigned
Branch if less than (bge/bgeu)
  bge s0, s1, target # branches if s0 > s1 (signed)
  bgeu s0, s1, target # branches if s0 > s1 (unsigned)

## Slide 43
# RISC-V assembly
j target # jump to target
srai s1, s1, 2 # not executed
addi s1, s1, 1 # not executed
sub s1, s1, s0 # not executed
target:
add s1, s1, s0 # s1 = 1 + 4 = 5
Unconditional Branching (j)

## Slide 44
High-level constructs: loops, conditional statements
First, introduce:
  Logical operations
  Shifty instructions
  Generating constants
  Multiplication
Programming

## Slide 45
and, or, xor
  and: useful for masking bits
    Masking all but the least significant byte of a value:
    0xF234012F AND 0x000000FF = 0x0000002F
  or: useful for combining bit fields
    Combine 0xF2340000 with 0x000012BC:
    0xF2340000 OR 0x000012BC = 0xF23412BC
  xor: useful for inverting bits:
    A xor -1 = NOT A (remember that -1 = 0xFFFFFFFF)
Logical Instructions

## Slide 46
Logical Instructions Example 1

## Slide 47
Logical Instructions Example 2
-1484 = 0xA34 in 12-bit 2’s complement representation.

## Slide 48
Shift amount is in (lowest 5 bits of) a register
sll: shift left logical
  Example: sll t0, t1, t2 # t0 = t1 << t2
srl: shift right logical
  Example: srl t0, t1, t2 # t0 = t1 >> t2
sra: shift right arithmetic
  Example: sra t0, t1, t2 # t0 = t1 >>> t2
Shift Instructions

## Slide 49
Shift amount is an immediate between 0 to 31
slli: shift left logical immediate
  Example: slli t0, t1, 23 # t0 = t1 << 23
srli: shift right logical immediate
  Example: srli t0, t1, 18 # t0 = t1 >> 18
srai: shift right arithmetic imeediate
  Example: srai t0, t1, 5 # t0 = t1 >>> 5
Immediate Shift Instructions

## Slide 50
12-bit signed constants using addi:
Any immediate that needs more than 12 bits cannot use this method.
C Code
// int is a 32-bit signed word
int a = -372;
RISC-V assembly code
# s0 = a
addi s0, 0, -372
Generating Constants

## Slide 51
Use load upper immediate (lui) and addi:
lui: puts an immediate in the upper 20 bits of destination register, 0’s in lower 12 bits
C Code
int a = 0xFEDC8765;
RISC-V assembly code
# s0 = a
lui s0, 0xFEDC8
addi s0, s0, 0x765
Generating 32-bit Constants
Remember that addi sign-extends its 12-bit immediate

## Slide 52
If bit 11 of 32-bit constant is 1, increment upper 20 bits by 1 in lui
C Code
int a = 0xFEDC8EAB;
RISC-V assembly code
# s0 = a
lui s0, 0xFEDC9 # s0 = 0xFEDC9000
addi s0, s0, -341 # s0 = 0xFEDC9000 + 0xFFFFFEAB
# = 0xFEDC8EAB
Generating 32-bit Constants
Note: -341 = 0xEAB

## Slide 53
32 × 32 multiplication, 64-bit result
  mul s0, s1, s2
  s0 = lower 32 bits of result
  mulh s0, s1, s2
  s0 = upper 32 bits of result, treats operands as signed
  mulhu s0, s1, s2
  s0 = upper 32 bits of result, treats operands as
  unsigned
  mulhsu s0, s1, s2
  s0 = upper 32 bits of result, treats s1 as signed, s3
  as unsigned
Multiplication

## Slide 54
32 × 32 multiplication, 64-bit result
For full 64-bit result:
    mulh s4, s1, s2
    mul s3, s1, s2
    {s4, s3} = s1 x s2
Could also use mulhu or mulhsu instead of mulh
Multiplication

## Slide 55
32-bit division, 32-bit quotient, remainder
  div s1, s2, s3 # s1 = s2/s3
  divu s1, s2, s3 # unsigned division
Division

## Slide 56
if statements
if/else statements
while loops
for loops
High-Level Code Constructs

## Slide 57
C Code
if (i == j)
f = g + h;
f = f – i;
RISC-V assembly code
# s0 = f, s1 = g, s2 = h
# s3 = i, s4 = j
bne s3, s4, L1
add s0, s1, s2
L1:
sub s0, s0, s3
Assembly tests opposite case (i != j) of high-level code (i == j)
If Statement

## Slide 58
C Code
if (i == j)
f = g + h;
else
f = f – i;
RISC-V assembly code
# s0 = f, s1 = g, s2 = h
# s3 = i, s4 = j
bne s3, s4, L1
add s0, s1, s2
j done
L1:
sub s0, s0, s3
done:
If/Else Statement

## Slide 59
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
RISC-V assembly code
# s0 = pow, s1 = x
addi s0, zero, 1
add s1, zero, zero
addi t0, zero, 128
while:
beq s0, t0, done
slli s0, s0, 1
addi s1, s1, 1
j while
done:
While Loops
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).

## Slide 60
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met
For Loops

## Slide 61
C Code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
add s0, zero, zero
addi t0, zero, 10
for:
beq s0, t0, done
add s1, s1, s0
addi s0, s0, 1
j for
done:
For Loops

## Slide 62
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
addi s0, zero, 1
addi t0, zero, 101
loop:
bge s0, t0, done
add s1, s1, s0
slli s0, s0, 1
j loop
done:
Less Than Comparison

## Slide 63
Access large amounts of similar data
Index: access each element
Size: number of elements
Arrays

## Slide 64
5-element array
Base address = 0x12348000 (address of first element, array[0])
First step in accessing an array: load base address into a register
Arrays

## Slide 65
// C Code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# RISC-V assembly code
# s0 = array base address
lui s0, 0x12348 # 0x12348 in upper 20 bits of s0
lw t1, 0(s0) # t1 = array[0]
slli t1, t1, 1 # t1 = t1 * 2
sw t1, 0(s0) # array[0] = t1
lw t1, 4(s0) # t1 = array[1]
slli t1, t1, 1 # t1 = t1 * 2
sw t1, 4(s0) # array[1] = t1
Accessing Arrays

## Slide 66
// C Code
int array[1000];
int i;
for (i=0; i < 1000; i = i + 1)
array[i] = array[i] * 8;
# RISC-V assembly code
# s0 = array base address, s1 = i
Arrays Using For Loops

## Slide 67
# RISC-V assembly code
# s0 = array base address, s1 = i
# initialization code
lui s0, 0x23B8F # s0 = 0x23B8F000
ori s0, s0, 0x400 # s0 = 0x23B8F400
addi s1, zero, 0 # i = 0
addi t2, zero, 1000 # t2 = 1000
loop:
bge s1, t2, done # if not then done
slli t0, s1, 2 # t0 = i * 4 (byte offset)
add t0, t0, s0 # address of array[i]
lw t1, 0(t0) # t1 = array[i]
slli t1, t1, 3 # t1 = array[i] * 8
sw t1, 0(t0) # array[i] = array[i] * 8
addi s1, s1, 1 # i = i + 1
j loop # repeat
done:
Arrays Using For Loops

## Slide 68
American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)
ASCII Code

## Slide 69
Cast of Characters

## Slide 70
# RISC-V assembly
0x00000200 addi s0, zero, 0x210
0x00000204 jr s0
0x00000208 addi s1, zero, 1 # not executed
0x0000020C sra s1, s1, 2 # not executed
0x00000210 lw s3, 44(s1)
Unconditional Branching (jr)

## Slide 71
Lecture 16
Introduction
  Instruction Set Architecture (ISA)
  RISC-V History
RISC-V Assembly Language
  Instructions
  Register Set
  Memory
  Programming constructs