## Slide 1: Lecture 17: Function Calls
E85
Digital Electronics & Computer Architecture

## Slide 2
Caller: calling function (in this case, main)
Callee: called function (in this case, sum)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}
Function Calls

## Slide 3
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller
Function Conventions

## Slide 4
Call Function: jump and link (jal)
Return from function: jump register (jr ra)
Arguments: a0 – a7
Return value: a0
RISC-V Function Conventions
Name | Register Number | Usage
zero | x0 | Constant value 0
ra | x1 | Return address
sp | x2 | Stack pointer
gp | x3 | Global pointer
tp | x4 | Thread pointer
t0-2 | x5-7 | Temporaries
s0/fp | x8 | Saved register / Frame pointer
s1 | x9 | Saved register
a0-1 | x10-11 | Function arguments / return values
a2-7 | x12-17 | Function arguments
s2-11 | x18-27 | Saved registers
t3-6 | x28-31 | Temporaries

## Slide 5
void means that simple doesn’t return a value
Function Calls
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
RISC-V assembly code
0x00000300 main: jal ra, simple # call
0x00000304 add s0, s1, s1
... ...
0x0000051c simple: jr ra # return

## Slide 6
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
RISC-V assembly code
0x00000300 main: jal ra, simple # call
0x00000304 add s0, s1, s1
... ...
0x0000051c simple: jr ra # return
jal ra, simple:
ra = PC + 4 (0x00000304)
jumps to simple label (PC = 0x0000051c)
jr ra:
PC = ra (0x00000304)
Function Calls

## Slide 7
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
RISC-V assembly code
0x00000300 main: jal simple # call
0x00000304 add s0, s1, s1
... ...
0x0000051c simple: jr ra # return
Preferred instruction:
jal simple - a pseudoinstruction for jal ra, simple
Pseudoinstructions are not actual RISC-V instructions but they are often simpler for the programmer.
They are converted to real RISC-V instructions by the assembler
Function Calls

## Slide 8
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller
Function Conventions

## Slide 9
Call Function: jump and link (jal)
Return from function: jump and link register (jr ra)
Arguments: a0 – a7
Return value: a0
RISC-V Function Conventions

## Slide 10
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}
Input Arguments & Return Value

## Slide 11
RISC-V assembly code
# s7 = y
main:
. . .
addi a0, zero, 2 # argument 0 = 2
addi a1, zero, 3 # argument 1 = 3
addi a2, zero, 4 # argument 2 = 4
addi a3, zero, 5 # argument 3 = 5
jal diffofsums # call function
add s7, a0, zero # y = returned value
. . .
# s3 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
jr ra # return to caller
Input Arguments & Return Value
jal diffofsums
is pseudocode for
jal ra, diffofsums

## Slide 12
RISC-V assembly code
# s3 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
jr ra # return to caller
diffofsums overwrote 3 registers: t0, t1, s3
diffofsums can use the stack to temporarily store registers
Input Arguments & Return Value

## Slide 13
Memory used to temporarily save variables
Like stack of dishes, last-in-first-out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space is no longer needed
The Stack

## Slide 14
Grows down (from higher to lower memory addresses)
Stack pointer: sp points to top of the stack
The Stack

## Slide 15
# RISC-V assembly
# s3 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
jr ra # return to caller
Called functions must have no unintended side effects
But diffofsums overwrites 3 registers: t0, t1, s3
How Functions use the Stack

## Slide 16
# s3 = result
diffofsums:
addi sp, sp, -12 # make space on stack to
# store three registers
sw s3, 8(sp) # save s3 on stack
sw t0, 4(sp) # save t0 on stack
sw t1, 0(sp) # save t1 on stack
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
lw t1, 0(sp) # restore $t1 from stack
lw t0, 4(sp) # restore $t0 from stack
lw s3, 8(sp) # restore $s3 from stack
addi sp, sp, 12 # deallocate stack space
jr ra # return to caller
Storing Register Values on the Stack

## Slide 17
The Stack During diffofsums Call

## Slide 18
Preserved Callee-Saved | Nonpreserved Caller-Saved
s0-s11 | t0-t6
sp | ra
stack above sp | a0-a7
 | stack below sp
Register Saving Conventions

## Slide 19
Storing Saved Registers on the Stack
# s3 = result
diffofsums:
addi sp, sp, -4 # make space on stack to
# store one register
sw s3, 0(sp) # save s3 on stack
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
lw s3, 0(sp) # restore $s3 from stack
addi sp, sp, 4 # deallocate stack space
jr ra # return to caller

## Slide 20
Optimized diffofsums
# a0 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub a0, t0, t1 # result = (f + g) − (h + i)
jr ra # return to caller

## Slide 21
Non-leaf function:
a function that calls another function
func1:
addi sp, sp, -4 # make space on stack
sw ra, 0(sp) # save ra on stack
jal func2
...
lw ra, 0(sp) # restore ra from stack
addi sp, sp, 4 # deallocate stack space
jr ra # return to caller
Non-Leaf Function Calls

## Slide 22
Caller
  Put arguments in a0-a7
  Save any needed registers (ra, maybe t0-t6)
  Call function: jal callee
  (Possibly restore registers)
  Look for result in a0
Callee
  Save registers that might be disturbed (s0-s11)
  Perform function
  Put result in a0
  Restore registers
  Return: jr ra
Function Call Summary

## Slide 23
  int factorial(int n) {
  if (n <= 1)
  return 1;
  else
  return (n * factorial(n − 1));
  }
Recursive Functions

## Slide 24
  0x8500 factorial: addi sp, sp, -8 # make room for a0, ra
  0x8504 sw a0, 4(sp)
  0x8508 sw ra, 0(sp)
  0x850C addi t0, zero, 1 # temporary = 1
  0x8510 bgt a0, t0, else # if n>1, go to else
  0x8514 addi a0, zero, 1 # otherwise, return 1
  0x8518 addi sp, sp, 8 # restore sp
  0x851C jr ra # return
  0x8520 else: addi a0, a0, -1 # n = n − 1
  0x8524 jal factorial # recursive call
  0x8528 lw ra, 0(sp) # restore ra
  0x852C lw t1, 4(sp) # restore n into t1
  0x8530 addi sp, sp, 8 # restore sp
  0x8534 mul a0, t1, a0 # a0 = n*factorial(n−1)
  0x8538 jr ra # return
Recursive Functions

## Slide 25
Recursive Functions
What does the stack look like when executing factorial(3)?
  0x8500 factorial: addi sp, sp, -8
  0x8504 sw a0, 4(sp)
  0x8508 sw ra, 0(sp)
  0x850C addi t0, zero, 1
  0x8510 bgt a0, t0, else
  0x8514 addi a0, zero, 1
  0x8518 addi sp, sp, 8
  0x851C jr ra
  0x8520 else: addi a0, a0, -1
  0x8524 jal factorial
  0x8528 lw ra, 0(sp)
  0x852C lw t1, 4(sp)
  0x8530 addi sp, sp, 8
  0x8534 mul a0, t1, a0
  0x8538 jr ra

## Slide 26
Recursive Functions
Stack (a) before, (b) during, and (c) after recursive call.