## Slide 1: Lecture 18: RISC-V Machine Language
E85
Digital Electronics & Computer Architecture

## Slide 2
Lecture 18
Machine Language
  Instruction types and formats
  Interpreting machine code
  Addressing modes
  The stored program
  Odds & Ends
    Pseudoinstructions
    Signed and unsigned operations
    Floating point instructions

## Slide 3
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
4 Types of Instruction Formats
  R-Type
  I-Type
  S/B-Type
  U/J-Type
Machine Language

## Slide 4
Register-type
3 register operands:
  rs1, rs2: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode
  funct7,funct3:
  the function (7 bits and 3-bits, respectively)
  with opcode, tells computer what operation to perform
R-Type

## Slide 5
Note the order of registers in the assembly code:
add rd, rs1, rs2
R-Type Examples

## Slide 6
Note immediate shift instructions (like srai t1, t2, 29) are R-type instructions. They encode the shift amount in the rs2 field.
More R-Type Examples

## Slide 7
Immediate-type
3 operands:
  rs1: register source operand
  rd: register destination operand
  imm: 12-bit two’s complement immediate
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform
I-Type

## Slide 8
Note the differing order of operands in assembly and machine codes:
addi rd, rs1, imm
lw rd, imm(rs1)
I-Type Examples

## Slide 9
Store-Type
3 operands:
  rs1: base register
  rs2: value to be stored to memory
  imm: 12-bit two’s complement immediate
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform
S-Type

## Slide 10
Note the differing order of operands in assembly and machine codes:
sw rs2, imm(rs1)
S-Type Examples

## Slide 11
Branch-Type (similar format to S-Type)
3 operands:
  rs1: register source 1
  rs2: register source 2
  imm12:1: 12-bit two’s complement immediate – address offset
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform
B-Type

## Slide 12
The 13-bit immediate encodes where to branch (relative to the branch instruction)
Immediate encoding is strange
Example:
B-Type Example

## Slide 13
Note the differing order of operands in assembly and machine codes:
beq rs1, rs2, imm12:1
B-Type Example

## Slide 14
Upper-immediate-Type
Used for load upper immediate (lui)
2 operands:
  rd: destination register
  imm31:12:upper 20 bits of a 32-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform
U-Type

## Slide 15
U-Type Example

## Slide 16
Jump-Type
Used for jump-and-link instruction (jal)
2 operands:
  rd: destination register
  imm20,10:1,11,19:12: 20 bits (20:1) of a 21-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform
J-Type

## Slide 17
J-Type Example
Immediate encoding is strange
Example:

## Slide 18
J-Type Example
Immediate encoding is strange
Example:

## Slide 19
Unraveling the web of lies: jr
jr ra is not a real RISC-V instruction.
It is a pseudoinstruction for jalr x0, ra, 0
jalr is not a J-type instruction.

## Slide 20
jalr
jalr is an I-type instruction.
It writes PC+4 to rd and jumps to rs1+imm.
Example:
lui s7, 0x801FA # s7 = 0x801FA000
jalr s2, s7, 0x7BC # s2 = PC + 4
# PC = s7 + 0x7BC
# = 0x801FA7BC
In this case, rd = s2, rs1 = s7, imm = 0x7BC

## Slide 21
Review: Instruction Formats

## Slide 22
Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw, addi: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).
Design Principle 4

## Slide 23
lw and sw use constants or immediates
immediately available from instruction
12-bit two’s complement number
addi: add immediate
Subtract immediate (subi) necessary?
C Code
a = a + 4;
b = a – 12;
RISC-V assembly code
# s0 = a, s1 = b
addi s0, s0, 4
addi s1, s0, -12
Constants/Immediates

## Slide 24
Constants/Immediates

## Slide 25
Immediate Encodings
Immediate bits mostly occupy consistent instruction bits.
Sign bit of signed immediate is in msb of instruction.
Recall that rs2 of R-type can encode immediate shift amount.
Instruction Bits

## Slide 26
Instruction Fields & Formats
Instruction | op | funct3 | Funct7 | Type
add | 0110011 (51) | 000 (0) | 0000000 (0) | R-Type
sub | 0110011 (51) | 000 (0) | 0100000 (32) | R-Type
and | 0110011 (51) | 111 (7) | 0000000 (0) | R-Type
or | 0110011 (51) | 110 (6) | 0000000 (0) | R-Type
addi | 0010011 (19) | 000 (0) | - | I-Type
beq | 1100011 (99) | 000 (0) | - | B-Type
bne | 1100011 (99) | 001 (1) | - | B-Type
lw | 0000011 (3) | 010 (2) | - | I-Type
sw | 0100011 (35) | 010 (2) | - | S-Type
jal | 1101111 (111) | - | - | J-Type
jalr | 1100111 (103) | 000 (0) | - | I-Type
lui | 0110111 (55) | - | - | U-Type
See Appendix B, Table B.2 for other encodings

## Slide 27
Write in binary
Start with op (& funct3): tells how to parse rest
Extract fields
op, funct3, and funct7 fields to tell operation
Ex: 0x41FE83B3 and 0xFDA58393
0x41FE83B3: 0100 0001 1111 1110 1000 0011 1011 0011
op = 51: R-type
0xFDA48393: 1111 1101 1010 0100 1000 0011 1001 0011
op = 19, funct3 = 0: addi (I-type)
Interpreting Machine Code

## Slide 28
Write in binary
Start with op (& funct3): tells how to parse rest
Extract fields
op, funct3, and funct7 fields to tell operation
Ex: 0x41FE83B3 and 0xFDA58393
Interpreting Machine Code

## Slide 29
Write in binary
Start with op (& funct3): tells how to parse rest
Extract fields
op, funct3, and funct7 fields to tell operation
Ex: 0x41FE83B3 and 0xFDA58393
Interpreting Machine Code

## Slide 30
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation
Power of the Stored Program

## Slide 31
The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 32
How do we address the operands?
Register Only
Immediate
Base Addressing
PC-Relative
Pseudo Direct
Addressing Modes

## Slide 33
Register Only
Operands found in registers
  Example: add s0, t2, t3
  Example: sub t6, s1, s0
Immediate
12-bit signed immediate used as an operand
  Example: addi s4, t5, -73
  Example: ori t3, t7, 0xFF
Addressing Modes

## Slide 34
Base Addressing
Loads and Stores
Address of operand is:
  base address + immediate
  Example: lw s4, 72(zero)
    address = 0 + 72
  Example: sw t2, -25(t1)
    address = t1 - 25
Addressing Modes

## Slide 35
PC-Relative Addressing: branches and jal
Address Instruction
0x354 L1: addi s1, s1, 1
0x358 sub t0, t1, s7
... ...
0xEB0 bne s8, s9, L1
  The label is (0xEB0-0x354) = 0xB5C (2908) instructions before bne
Addressing Modes

## Slide 36
How to Compile & Run a Program

## Slide 37
Graduated from Yale University with a Ph.D. in mathematics
Developed first compiler
Helped develop the COBOL programming language
Highly awarded naval officer
Received World War II Victory Medal and National Defense Service Medal, among others
Grace Hopper, 1906-1992

## Slide 38
Instructions (also called text)
Data
  Global/static: allocated before program begins
  Dynamic: allocated within program
How big is memory?
  At most 232 = 4 gigabytes (4 GB)
  From address 0x00000000 to 0xFFFFFFFF
What is Stored in Memory?

## Slide 39
Example RISC-V Memory Map

## Slide 40
int f, g, y; // global
int main(void)
{
f = 2;
g = 3;
y = sum(f, g);
return y;
}
int sum(int a, int b) {
return (a + b);
}
.data
f:
g:
y:
.text
main:
addi sp, sp, -4 # stack frame
sw ra, 0(sp) # store $ra
addi a0, zero, 2 # a0 = 2
sw a0, f # f = 2
addi a1, zero, 3 # a1 = 3
sw a1, g # g = 3
jal sum # call sum
sw a0, y # y = sum()
lw ra, 0(sp) # restore ra
addi sp, sp, 4 # restore sp
jr ra # return to OS
sum:
add a0, a0, a1 # a0 = a + b
jr ra # return
Example Program: RISC-V Assembly

## Slide 41
Symbol | Address
f | 0x10000000
g | 0x10000004
y | 0x10000008
main | 0x00008000
sum | 0x0000802C
Example Program: Symbol Table

## Slide 42
Example Program: Executable

## Slide 43
Example Program: In Memory

## Slide 44
Pseudoinstructions
Signed and unsigned instructions
Floating point instructions
Odds & Ends

## Slide 45
Pseudoinstruction | RISC-V Instructions
j label | jal zero, label
mv t5, s3 | addi t5, s3, 0
not s7, t2 | xori s7, t2, -1
nop | addi zero, zero, 0
li s8, 0x56789DEF | lui s8, 0x5678A addi s8, s8, 0xDEF
Pseudoinstructions
See Appendix B, Table B.4 for more pseudoinstructions

## Slide 46
Multiplication and division
Set less than
Loads
Signed & Unsigned Instructions

## Slide 47
Signed: multh, div
Unsigned: multhu, multhsu, divu
Multiplication & Division

## Slide 48
Signed: slt, slti
Unsigned: sltu, sltiu
Note: sltiu sign-extends the immediate before comparing it to the register
Set Less Than

## Slide 49
Signed:
  Sign-extends to create 32-bit value to load into register
  Load halfword: lh
  Load byte: lb
Unsigned:
  Zero-extends to create 32-bit value
  Load halfword unsigned: lhu
  Load byte: lbu
Loads

## Slide 50
RISC-V does not provide unsigned addition or instructions for detecting overflow because it can be done with existing instructions:
Example: detecting unsigned overflow:
add t0, t1, t2
bltu t0, t1, overflow
Example: detecting signed overflow:
add t0, t1, t2
slti t3, t2, 0 # t3=1 if t2 neg.
slt t4, t0, t1 # t4=1 if result < t1
bne t3, t4, overflow # overflow if:
# t2 neg & result>=t1 or
# t2 pos & result<t1
Addition & Subtraction

## Slide 51
RISC-V offers three floating point extensions:
  RVF: single-precision (32-bit)
  RVD: double-precision (64-bit)
  RVQ: quad-precision (128-bit)
Floating Point Operations

## Slide 52
32 Floating point registers
Width is highest precision – for example, if RVQ is implemented, registers are 128 bits wide
When multiple floating point extensions are implemented, the lower-precision values occupy the lower bits of the register
Floating Point Registers

## Slide 53
Floating Point Registers
Name | Register Number | Usage
ft0-7 | f0-7 | Temporary variables
fs0-1 | f8-9 | Saved variables
fa0-1 | f10-11 | Function arguments/Return values
fa2-7 | f12-17 | Function arguments
fs2-11 | f18-27 | Saved variables
ft8-11 | f28-31 | Temporary variables

## Slide 54
Floating Point Instructions
Append .s (single), .d (double), .q (quad) for precision. I.e., add.s, add.d, and add.q
Arithmetic operations:
fadd, fsub, fdiv, fsqrt, fmin, fmax, multiply-add (fmadd, fmsub, fnmadd, fnmsub)
Other instructions:
move (fmv.x.w, fmv.w.x)
convert (fcvt.w.s, fcvt.s.w, etc.)
comparison (feq, flt, fle)
classify (fclass)
sign injection (fsgnj, fsgnjn, fsgnjx)

## Slide 55
Floating Point Instruction Formats
Use R-, I-, and S-type formats
Introduce another format for multiply-add instructions that have 4 register operands: R4-type