## Slide 1
Digital Design and Computer Architecture, RISC-V Edition
Chapter 6
David M. Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Microarchitecture
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Advanced Microarchitecture

## Slide 3
Single Cycle Processor

## Slide 4
Single Cycle Main Decoder
op | Instruct | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp | PCUpdate
3 | lw | 1 | 00 | 1 | 0 | 10 | 0 | 00 | 0
35 | sw | 0 | 01 | 1 | 1 | XX | 0 | 00 | 0
51 | R-type | 1 | XX | 0 | 0 | 01 | 0 | 10 | 0
99 | beq | 0 | 10 | 0 | 0 | XX | 1 | 01 | 0
19 | addi | 1 | 00 | 1 | 0 | 01 | 0 | 10 | 0
111 | jal | 1 | 11 | X | 0 | 00 | 0 | XX | 1

## Slide 5
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Processor Performance

## Slide 6
TC limited by critical path (lw)
Single-Cycle Performance

## Slide 7
Single-cycle critical path:
Tc1 = tpcq_PC + tmem + max[tRFread, tdec + text + tmux] + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc1 = tpcq_PC + 2tmem + tRFread + tALU + 2tmux + tRFsetup
Single-Cycle Performance

## Slide 8
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle processor addresses these issues by breaking instruction into shorter steps
  shorter instructions take fewer steps
  can re-use hardware
  cycle time is faster
Multicycle RISC-V Processor

## Slide 9
  Tc1 = ?
Single-Cycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
ALU | tALU | 120
Decoder (Control Unit) | tdec | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 10
  Tc1 = tpcq_PC + 2tmem + tRFread + tALU + tmux + tRFsetup
= [40 + 2(200) + 100 + 120 + 30 + 60] ps
= 750 ps
Single-Cycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
ALU | tALU | 120
Decoder (Control Unit) | tdec | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 11
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(750 × 10-12 s)
= 75 seconds
Single-Cycle Performance Example

## Slide 12
Review: Multicycle RISC-V Processor

## Slide 13
Review: Multicycle Main FSM

## Slide 14
Instructions take different number of cycles:
Multicycle Processor Performance

## Slide 15
Instructions take different number of cycles:
  3 cycles:
  4 cycles:
  5 cycles:
Multicycle Processor Performance

## Slide 16
Instructions take different number of cycles:
  3 cycles: beq
  4 cycles: R-type, addi, sw , jal
  5 cycles: lw
Multicycle Processor Performance

## Slide 17
Instructions take different number of cycles:
  3 cycles: beq
  4 cycles: R-type, addi, sw , jal
  5 cycles: lw
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% R-type
Multicycle Processor Performance

## Slide 18
Instructions take different number of cycles:
  3 cycles: beq
  4 cycles: R-type, addi, sw , jal
  5 cycles: lw
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% R-type
Average CPI = (0.13)(3) + (0.52 + 0.10)(4) + (0.25)(5) = 4.12
Multicycle Processor Performance

## Slide 19
Assumptions:
  RF is faster than memory
  writing memory is faster than reading memory
Two possibilities:
  Read memory (MemRead state)
  PC = PC + 4 path (Fetch state)
Multicycle Processor Critical Path

## Slide 20
Option 1: Read memory (MemRead state)
Multicycle Processor Critical Path
Tc2 = tpcq + tmux + tmux + tmem + tsetup

## Slide 21
Option 1: Read memory (MemRead state)
Multicycle Processor Critical Path
Tc2 = tpcq + tmux + tmux + tmem + tsetup
= tpcq + 2tmux + tmem + tsetup

## Slide 22
Option 2: PC = PC + 4 path (Fetch state)
Multicycle Processor Critical Path
Tc2 = tpcq + tmux + tALU + tmux + tsetup

## Slide 23
Option 2: PC = PC + 4 path (Fetch state)
Multicycle Processor Critical Path
Tc2 = tpcq + tmux + tALU + tmux + tsetup
= tpcq + 2tmux + tALU + tsetup

## Slide 24
Two possibilities:
  Read memory (MemRead state)
  PC = PC + 4 path (Fetch state)
Tc2 = tpcq + 2tmux + max[tALU, tmem] + tsetup
Multicycle Processor Critical Path

## Slide 25
Multi-Cycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
AND-OR gate | tAND-OR | 20
ALU | tALU | 120
Decoder (control unit) | tdec | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60
Tc2 = tpcq + 2tmux + max[tALU, tmem] + tsetup
= (40 + 2(30) + 200 + 50) ps = 350 ps

## Slide 26
For a program with 100 billion instructions executing on a multicycle RISC-V processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 350 ps
Execution Time = ?
Multicycle Performance Example

## Slide 27
For a program with 100 billion instructions executing on a multicycle RISC-V processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 350 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(350 × 10-12)
= 144 seconds
This is slower than the single-cycle processor (75 sec.)
Multicycle Performance Example

## Slide 28
Temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages
Pipelined RISC-V Processor

## Slide 29
Single-Cycle vs. Pipelined

## Slide 30
Pipelined Processor Abstraction

## Slide 31
Single-Cycle & Pipelined Datapath
Single-Cycle
Pipelined

## Slide 32
Rd must arrive at same time as Result
Register file written on falling edge of CLK
Corrected Pipelined Datapath

## Slide 33
Same control unit as single-cycle processor
Control signals travel with the instruction (drop off when used)
Pipelined Processor with Control

## Slide 34
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branch)
Pipeline Hazards

## Slide 35
Data Hazard

## Slide 36
How do we ensure that our programs run correctly?
Handling Data Hazards

## Slide 37
How do we ensure that our programs run correctly?
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time
Handling Data Hazards

## Slide 38
Insert enough nops for result to be ready
Or move independent useful instructions forward
Compile-Time Hazard Elimination

## Slide 39
Data Forwarding

## Slide 40
Data Forwarding
Check if register read in Execute stage matches register written in Memory or Writeback stage
If so, forward result

## Slide 41
Data Forwarding

## Slide 42
Data Forwarding
Case 1: Execute stage Rs1 or Rs2 matches Memory stage Rd?
Forward from Memory stage
Case 2: Execute stage Rs1 or Rs2 matches Writeback stage Rd?
Forward from Writeback stage
Case 3: Otherwise use value read from register file (as usual)
Equations for Rs1:
if ((Rs1E == RdM) & RegWriteM) // Case 1
ForwardAE = 10
else if ((Rs1E == RdW) & RegWriteW) // Case 2
ForwardAE = 01
else ForwardAE = 00 // Case 3

## Slide 43
Data Forwarding
Case 1: Execute stage Rs1 or Rs2 matches Memory stage Rd?
Forward from Memory stage
Case 2: Execute stage Rs1 or Rs2 matches Writeback stage Rd?
Forward from Writeback stage
Case 3: Otherwise use value read from register file (as usual)
Equations for Rs1:
if ((Rs1E == RdM) & RegWriteM) & (Rs1E != 0) // Case 1 ForwardAE = 10
else if ((Rs1E == RdW) & RegWriteW) & (Rs1E != 0) // Case 2 ForwardAE = 01
else ForwardAE = 00 // Case 3

## Slide 44
Data Forwarding
Case 1: Execute stage Rs1 or Rs2 matches Memory stage Rd?
Forward from Memory stage
Case 2: Execute stage Rs1 or Rs2 matches Writeback stage Rd?
Forward from Writeback stage
Case 3: Otherwise use value read from register file (as usual)
Equations for Rs1:
if ((Rs1E == RdM) & RegWriteM) & (Rs1E != 0) // Case 1 ForwardAE = 10
else if ((Rs1E == RdW) & RegWriteW) & (Rs1E != 0) // Case 2 ForwardAE = 01
else ForwardAE = 00 // Case 3
ForwardBE equation is similar (replace Rs1E with Rs2E)

## Slide 45
Stalling

## Slide 46
Stalling

## Slide 47
Stalling Hardware

## Slide 48
Is either source register in Decode stage the same as the one to be written by instruction in Execute stage? AND
Is the instruction in Execute stage a lw?
lwStall = ((Rs1D == RdE) | (Rs2D == RdE)) &
ResultSrcE0
StallF = StallD = FlushE = lwStall
Stalling Logic

## Slide 49
Is either source register in Decode stage the same as the one to be written by instruction in Execute stage? AND
Is the instruction in Execute stage a lw?
lwStall = ((Rs1D == RdE) | (Rs2D == RdE)) &
ResultSrcE0
StallF = StallD = FlushE = lwStall
Stalling Logic

## Slide 50
Is either source register in Decode stage the same as the one to be written by instruction in Execute stage? AND
Is the instruction in Execute stage a lw? AND
Is the lw’s destination register (RdE) not x0?
lwStall = ((Rs1D == RdE) | (Rs2D == RdE) & ~ALUSrcD) &
ResultSrcE0 &
(RdE != 0)
StallF = StallD = FlushE = lwStall
Stalling Logic

## Slide 51
Is either source register in Decode stage the same as the one to be written by instruction in Execute stage? AND
Is the instruction in Execute stage a lw? AND
Is the lw’s destination register (RdE) not x0? AND
Are the source registers (Rs1D and Rs2D) used?
lwStall = ((Rs1D == RdE) | (Rs2D == RdE) & ~ALUSrcD) &
ResultSrcE0 &
(RdE != 0) &
(~JumpD)
StallF = StallD = FlushE = lwStall
Stalling Logic

## Slide 52
Is either source register in Decode stage the same as the one to be written by instruction in Execute stage? AND
Is the instruction in Execute stage a lw? AND
Is the lw’s destination register (RdE) not x0? AND
Are the source registers (Rs1D and Rs2D) used?
lwStall = ((Rs1D == RdE) | (Rs2D == RdE) & ~ALUSrcD) &
ResultSrcE0 &
(RdE != 0) &
(~JumpD)
StallF = StallD = FlushE = lwStall
Stalling Logic
JAL doesn’t use rs1, rs2
I-type instructions don’t use rs2
(ALUSrcD = 1 selects ExtImm as SrcB of ALU)

## Slide 53
Is either source register in Decode stage the same as the one to be written by instruction in Execute stage? AND
Is the instruction in Execute stage a lw? AND
Is the lw’s destination register (RdE) not x0? AND
Are the source registers (Rs1D and Rs2D) used?
lwStall = ((Rs1D == RdE) | (Rs2D == RdE) & ~ALUSrcD) &
ResultSrcE0 &
(RdE != 0) &
(~JumpD)
StallF = StallD = FlushE = lwStall
Stalling Logic

## Slide 54
beq:
  branch not determined until the Execute stage of pipeline
  Instructions after branch fetched before branch occurs
  These 2 instructions must be flushed if branch happens
Control Hazards

## Slide 55
Control Hazards
Branch misprediction penalty
number of instruction flushed when branch is taken (2)

## Slide 56
Flushing Hardware for Control Hazards

## Slide 57
If branch is taken in execute stage, need to flush the instructions in the fetch and decode stages
  Do this by clearing Decode and Execute Pipeline registers using FlushD and FlushE
Equations:
FlushD = PCSrcE
FlushE = lwStall | PCSrcE
Control Flushing Logic

## Slide 58
Forward to solve data hazards when possible
if ((Rs1E == RdM) & RegWriteM) & (Rs1E != 0) then
ForwardAE = 10
else if ((Rs1E == RdW) & RegWriteW) & (Rs1E != 0) then
ForwardAE = 01
else ForwardAE = 00
Stall when a load hazard occurs
lwStall = ((Rs1D == RdE) | (Rs2D == RdE) & ~ALUSrcD) & ResultSrcE0 &
(RdE != 0) & ~JumpD
StallF = lwStall
StallD = lwStall
Flush when a branch is taken or a load introduces a bubble
FlushD = PCSrcE
FlushE = lwStall | PCSrcE
Pipeline Hazard Summary

## Slide 59
RISC-V Pipelined Processor with Hazard Unit

## Slide 60
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% R-type
Suppose:
  40% of loads used by next instruction
  50% of branches mispredicted
What is the average CPI?
Pipelined Performance Example

## Slide 61
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% R-type
Suppose:
  40% of loads used by next instruction
  50% of branches mispredicted
What is the average CPI?
  Load CPI = 1 when not stalling, 2 when stalling
    So, CPIlw = 1(0.6) + 2(0.4) = 1.4
  Branch CPI = 1 when not stalling, 3 when stalling
  So, CPIbeq = 1(0.5) + 3(0.5) = 2
  Average CPI = (0.25)(1.4) + (0.1)(1) + (0.13)(2) + (0.52)(1) = 1.23
Pipelined Performance Example

## Slide 62
Pipelined processor critical path:
Tc3 = max of
tpcq + tmem + tsetup Fetch
2(tRFread + tsetup ) Decode
tpcq + 4tmux + tALU + tAND-OR + tsetup Execute
tpcq + tmem + tsetup Memory
2(tpcq + tmux + tRFwrite) Writeback
Pipelined Performance

## Slide 63
Pipelined processor critical path:
Tc3 = max of
tpcq + tmem + tsetup Fetch
2(tRFread + tsetup ) Decode
tpcq + 4tmux + tALU + tAND-OR + tsetup Execute
tpcq + tmem + tsetup Memory
2(tpcq + tmux + tRFwrite) Writeback
Pipelined Performance
Decode and Writeback stages both use the register file in each cycle
So each stage gets half of the cycle time (Tc/2) to do their work
Or, stated a different way, 2x of their work must fit in a cycle (Tc)

## Slide 64
tpcq + 4tmux + tALU + tAND-OR + tsetup Execute
Pipelined Processor Critical Path
beq in Execute stage that requires forwarding

## Slide 65
Cycle time: Tc3 = tpcq + 4tmux + tALU + tAND-OR + tsetup = (40 + 4(30) + 120 + 20 + 50) ps = 350 ps
Pipelined Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 30
AND-OR gate | tAND-OR | 20
ALU | tALU | 120
Decoder (control unit) | tdec | 35
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 66
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(1.23)(350 × 10-12)
= 43 seconds
Pipelined Performance Example

## Slide 67
Processor | Execution Time (seconds) | Speedup (single-cycle as baseline)
Single-cycle | 75 | 1
Multicycle | 144 | 0.5
Pipelined | 43 | 1.7
Processor Performance Comparison