## Slide 1: Lecture 23: Advanced Microarchitecture
E85 Digital Design & Computer Engineering

## Slide 2
Deep Pipelining
Micro-operations
Branch Prediction
Superscalar Processors
Out of Order Processors
Register Renaming
SIMD
Multithreading
Multiprocessors
Advanced Microarchitecture

## Slide 3
10-20 stages typical
Number of stages limited by:
  Pipeline hazards
  Sequencing overhead
  Power
  Cost
Deep Pipelining

## Slide 4
Decompose more complex instructions into a series of simple instructions called micro-operations (micro-ops or µ-ops)
At run-time, complex instructions are decoded into one or more micro-ops
Used heavily in CISC (complex instruction set computer) architectures (e.g., x86)
Used for some ARM instructions, for example:
Complex Op Micro-op Sequence
LDR R1, [R2], #4 LDR R1, [R2]
ADD R2, R2, #4
Without u-ops, would need 2nd write port on the register file
Micro-operations

## Slide 5
Allow for dense code (fewer memory accesses)
Yet preserve simplicity of RISC hardware
ARM strikes balance by choosing instructions that:
  Give better code density than pure RISC instruction sets (such as MIPS)
  Enable more efficient decoding than CISC instruction sets (such as x86)
Micro-operations

## Slide 6
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history to improve guess
Good prediction reduces fraction of branches requiring a flush
Branch Prediction

## Slide 7
Ideal pipelined processor: CPI = 1
Branch misprediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last several hundred (or thousand) branches in branch target buffer, record:
    Branch destination
    Whether branch was taken
Branch Prediction

## Slide 8
MOV R1, #0 ; R1 = sum
MOV R0, #0 ; R0 = i
FOR ; for (i=0; i<10; i=i+1)
CMP R0, #10
BGE DONE
ADD R1, R1, R0 ; sum = sum + i
ADD R0, R0, #1
B FOR
DONE
Branch Prediction Example

## Slide 9
Remembers whether branch was taken the last time and does the same thing
Mispredicts first and last branch of loop
1-Bit Branch Predictor

## Slide 10
Only mispredicts last branch of loop
2-Bit Branch Predictor

## Slide 11
Multiple copies of datapath execute multiple instructions at once
Dependencies make it tricky to issue multiple instructions at once
Superscalar

## Slide 12
Ideal IPC: 2
Actual IPC: 2
Superscalar Example

## Slide 13
Superscalar with Dependencies
Ideal IPC: 2
Actual IPC: 6/5 = 1.2

## Slide 14
Looks ahead across multiple instructions
Issues as many instructions as possible at once
Issues instructions out of order (as long as no dependencies)
Dependencies:
  RAW (read after write): one instruction writes, later instruction reads a register
  WAR (write after read): one instruction reads, later instruction writes a register
  WAW (write after write): one instruction writes, later instruction writes a register
Out of Order Processor

## Slide 15
Instruction level parallelism (ILP): number of instruction that can be issued simultaneously (average < 3)
Scoreboard: table that keeps track of:
  Instructions waiting to issue
  Available functional units
  Dependencies
Out of Order Processor

## Slide 16
LDR R8, [R0, #40]
ADD R9, R8, R1
SUB R8, R2, R3 Ideal IPC: 2
AND R10, R4, R8 Actual IPC: 6/4 = 1.5
ORR R11, R5, R6
STR R7, [R11, #80]
Out of Order Processor Example

## Slide 17
LDR R8, [R0, #40]
ADD R9, R8, R1
SUB R8, R2, R3 Ideal IPC: 2
AND R10, R4, R8 Actual IPC: 6/3 = 2
ORR R11, R5, R6
STR R7, [R11, #80]
Register Renaming

## Slide 18
Single Instruction Multiple Data (SIMD)
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Perform short arithmetic operations (also called packed arithmetic)
For example, add eight 8-bit elements
SIMD

## Slide 19
Multithreading
  Word processor: thread for typing, spell checking, printing
Multiprocessors
  Multiple processors (cores) on a single chip
Advanced Architecture Techniques

## Slide 20
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing
Threading: Definitions

## Slide 21
One thread runs at at at a time
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously
Threads in Conventional Processor

## Slide 22
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”
Multithreading

## Slide 23
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared main memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system
Multiprocessors

## Slide 24
Multicycle Processor Test Bench

## Slide 25
Multicycle Processor Test Bench

## Slide 26
Multicycle Processor Test Program

## Slide 27
Multicycle Processor Memory
E04F000F E2802005 E280300C E2437009 E1874002 E0035004 E0855004 E255500A C2555002 E285500C E0558007 0A00000C E0538004 AA000000 E2805000 E0578002 B2857001 E0477002 E58370E0 E59020EC E08FF000 E280200E EA000001 E280200D E280200A E58020F8
initial
$readmemh("memfile.dat",RAM);