## Slide 1: Lecture 24: Evolution of ARM Processors
E85 Digital Design & Computer Engineering

## Slide 2
Evolution of ARM Processors
Architecture
Microarchitecture

## Slide 3
ARM v4 Architecture
16 32-bit registers
  R15 is the program counter
    Write to R15 causes a jump
    Read to R15 returns PC+8
  R14 is the link register for function calls
Typical RISC instruction set +
  Conditional execution
    Avoids need for some branches
  Shifter in datapath on second source
    Helpful for memory addressing
  Postincrement memory addressing mode

## Slide 4
ARM v4 Instruction Formats

## Slide 5
Data Processing Instructions

## Slide 6
Memory Instructions

## Slide 7
Branch Instructions

## Slide 8
Conditional Execution

## Slide 9
Single Cycle ARM Processor
Similar to RISC-V
PC/R15 input to register file
Source registers fields vary in location
ALU Flags

## Slide 10
Architecture Revisions
ARMv2: 1985 Acorn Computer
26-bit address bus, status in upper PC bits
ARMv3: 32-bit address bus, CPSR
ARMv4: 1993 Halfword loads & stores
Core ARM instruction set, described here
ARMv4T: Thumb instruction set (16-bit)
ARMv5TE: DSP, Floating point
ARMv6: multimedia, enhanced Thumb
ARMv7: advanced SIMD
ARMv8: 64-bit new instruction set

## Slide 11
Thumb
Pack common instructions into 16 bits.
Compete with 16-bit processors for code density.
Limitations:
R0-R7
Reuse register as source and dest
Shorter immediates
No conditional execution
Always write status flags

## Slide 12
Thumb Example Encodings

## Slide 13
Digital Signal Processing Instructions
Efficient DSP code, e.g. FFT and FIR
Especially support multiply-accumulate (MAC)
Z = Z + A * B
Needs extra source
Often run on shorter data types (e.g. 16 bits)
Need longer accumulator Z
Saturated arithmetic

## Slide 14
DSP Data Types

## Slide 15
Floating Point
16 64-bit double registers D0-D15
Also usable as 32 32-bit float registers S0-S31
Or 8 128-bit quad registers Q0-Q7 for SIMD
VADD.F32 S2, S0, S1
VADD.F64 D2,D0, D1

## Slide 16
Floating-Point Instructions

## Slide 17
SIMD Instructions
Packed operations on 8-64 bit data
in 64-128 bit registers D, Q
.I8, .I16, .I32, .I64
.F32, .F64
VADD.I8 D2, D1, D0
VADD.I32 Q2, Q1, Q0
VADD.F32 D2, D1, D0

## Slide 18
64-bit Instruction Set
32-bit addresses access 232 = 4GB of RAM
too little for PCs or phone nowadays
64-bit addresses access 264 bytes (huge)
ARMv8 uses 64-bit registers and addresses
Instructions still 32 bits

## Slide 19
ARMv8 Registers
Expands to 32 64-bit registers
X0-X30
PC and SP are no longer general purpose regs
X30 acts as the link regiser
No X31, but Zero Reg (ZR) instead
Hardwired to 0

## Slide 20
ARMv8 Instruction Encodings
Different instruction encoding in 64-bit mode
5 bit register addresses
Remove conditionals from all but branch instrs.
Expands SIMD registers
Cryptography instructions
Boot in 64-bit mode
Can change to 32-bit for compatibility

## Slide 21
Evolution of ARM Processors

## Slide 22
ARM1 die photo

## Slide 23
ARM7 Block Diagram (v4T)

## Slide 24
ARM9 Block Diagram (v5TE)

## Slide 25
Cortex A9 Block Diagram

## Slide 26
Cortex A7 Pipeline

## Slide 27
Cortex A15 Pipeline

## Slide 28
Recent Developments
64-bit ARMv8
Bit.LITTLE / DynamIQ
Cortex A73/A53
Cortex A75/A55
Cortex A76
Cortex A77

## Slide 29
2019 Benchmarks
Manufacturer | Chip | Product | Process | Big Core | Frequency (GHz) | SpecInt2006 Energy (kJ) | SpecInt2006 Speed | Core Size (mm2)
Apple | A12 | iPhone XS/XR | TSMC 7nm | Vortex | 2.49 | 9.5 | 45.3 | 2.07
Samsung | Exynos 9820 | Galaxy S10 | Samsung 8nm | M4 | 2.73 | 14.3 | 26.3 | 
Qualcomm | Snapdragon 855 | Galaxy S10+ | TSMC 7 nm | A76 | 2.84 | 9.7 | 26.7 | 
Huawei | Kirin 980 | Huawei P30 | TSMC 7nm | A76 | 2.6 | 9.5 | 25.7 | 
Apple | A11 | iPhone 8/X | TSCM 10 nm | Monsoon | 2.39 | 10.6 | 36.8 | 2.68
Samsung | Exynos 9810 | Galaxy S9 | Samsung 10 nm | M3 | 2.70 | 20.1 | 23.8 | 3.46
Qualcomm | Snapdragon 845 | Note S9 | Samsung 10 nm | A75 | 2.80 | 12.5 | 17.7 | 
Qualcomm | Snapdragon 835 | Galaxy S8 | 10 nm | A73 | 2.45 | 13.3 | 13.6 | 

## Slide 30
2019 Benchmarks
Manufacturer | Chip | Cores | Cache Size | Die Size (mm2) | Transistors (Billion)
Apple | A12 | 2 Vortex, 4 Tempest | 8 MB | 83 | 6.9B
Samsung | Exynos 9820 | 2 M4, 2 A75, 4 A55 | 2 MB | 127 | 
Qualcomm | Snapdragon 855 | 4 A76, 4 A55 | 5 MB | 73 | 
Huawei | Kirin 980 | 4 A76, 4 A55 | 4 MB | 74 | 6.9
Apple | A11 | 2 Monsoon, 4 Mistral | 8 MB | 88 | 4.3
Samsung | Exynos 9810 | 4 M3 | 4 MB | 119 | 
Qualcomm | Snapdragon 845 | 4 A75, 4 A55 | 2 MB | 95 | 5.3
Qualcomm | Snapdragon 835 | 4 A73, 4 A53 | 2 MB | 72 | 3

## Slide 31
Microarchitectures
Manufacturer | Core | Decode | Out-of-Order | Pipeline Stages
Apple | Vortex (A12) Monsoon (A11) | 7-Way | Yes | 
Samsung | M4 | 6-Way | Yes | 16
ARM | Cortex A76 | 4-Way | Yes | 11-13
ARM | Cortex A75 | 3-Way | Yes | 11-13
ARM | Cortex A55 | 2-Way | No | 8

## Slide 32
Apple A12
2018
TSMC 7 nm
83 mm2
2x Vortex
2.49 GHz
512 KB L2$
4x Tempest
1.8 GHz
128 KB L2$
4 MB L3$
Mali GPU
LTE Modem

## Slide 33
Samsung Exynos 9820
2018
TSMC 7 nm
74 mm2
2x M4 2.6 GHz
512 KB L2$
2x A75 1.92 GHz
4x A55 1.8 GHz
128 KB L2$
4 MB L3$
Mali GPU
LTE Modem

## Slide 34
Samsung Exynos 9820 M4 uArch
6-way decode
12 execution pipes
1 branch
2 alu
2 complex
4 ld/store
3 FP pipes

## Slide 35
Huawei Kirin 980
2018
TSMC 7 nm
74 mm2
2x A76 2.6 GHz
512 KB L2$
2x A76 1.92 GHz
4x A55 1.8 GHz
128 KB L2$
4 MB L3$
Mali GPU
LTE Modem

## Slide 36
ARM A76 uArch
4-way decode
8 execution pipes
1 branch
2 alu
1 complex
2 ld/store
2 FP pipes

## Slide 37
ARM A77 uArch
4-way decode
12 execution pipes
2 branch
3 alu
1 complex
4 ld/store
2 FP pipes