## Slide 1: Lecture 25: Final Review
E85 Digital Design & Computer Engineering

## Slide 2
1st Half Semester
Logic Levels
Number Systems
CMOS Transistors
Power Consumption
Combinational Logic Design
Finite State Machines
Timing
Verilog
Arithmetic Circuits
Course Overview
2nd Half Semester
Fixed & Floating Point
Building Blocks
C Programming
Assembly Language
Machine Language
Microarchitecture

## Slide 3
See midterm review
Make sure you can:
  Design a finite state machine
  Analyze its timing
  Express it in Verilog
  Estimate static and dynamic power
First Half Semester

## Slide 4
Express -5.625 as 4.4 fixed point and float
Fixed:
5.625 = 0101.1010
-5.625 = 1010.0101 + 1 lsb = 1010.0110
Float:
-5.625 = (-1)(1.01101)(22)
Sign = 1, biased exp = 127+2 = 129, fract = 01101
1 10000001 0110100.00000 = 0xC0B40000
Fixed and Floating Point

## Slide 5
Counters
Shift Registers
Memories
Building Blocks
Implementation:
Symbol:

## Slide 6
Each logic element has a 4-input LUT and one flop
Compute any function of up to 4 inputs
Ex:
y = a + b | (c ^ d) 1
7-input AND 2
4-bit shift register 4
3:8 decoder 8
FSM 3 bits state, 1 in, 2 out 5
FPGA Logic Elements

## Slide 7
Write basic programs in C
  Data types & sizes (char, short, int, long, float, double)
  If/else
  For, while
  Structures
  Arrays
  Pointers
C Programming

## Slide 8
typedef struct materialProps {
double youngModulus;
double hardness;
double density;
int color[3];
char name[36];
} materialProps; // size = 8 + 8 + 8 + 3*4 + 36*1 = 72
materialProps myMaterials[100]; // base address 2000
double *dp = &myMaterials[2].density; // 2000 + 2*72 + 8 + 8
Structure Example

## Slide 9
Architectural State:
32 registers (x0 is 0)
32-bit program counter (PC)
Up to 232 bytes of memory
32-bit instructions: 6 formats
RISC-V Assembly & Machine Language

## Slide 10
RISC-V Instructions
op | f3 | f7 | Type | Instruction | Description | Operation
3 | 0 | - | I | lb rd, imm(rs1) | load byte | rd = SignExt([Address]7:0)
3 | 1 | - | I | lh rd, imm(rs1) | load half | rd = SignExt([Address]15:0)
3 | 2 | - | I | lw rd, imm(rs1) | load word | rd = [Address]
3 | 4 | - | I | lbu rd, imm(rs1) | load byte unsigned | rd = ZeroExt([Address]7:0)
3 | 5 | - | I | lhu rd, imm(rs1) | load half unsigned | rd = ZeroExt([Address]15:0)
19 | 0 | - | I | addi rd, rs1, imm | add immediate | rd = rs1 + SignExt(imm)
19 | 1 | 0 | R | slli rd, rs1, shamt | shift left logical immediate | rd = rs1 << shamt
19 | 2 | - | I | slti rd, rs1, imm | set less than immediate | rd = (rs1 < SignExt(imm))
19 | 3 | - | I | sltiu rd, rs1, imm | set less than immediate unsigned | rd = (rs1 < SignExt(imm))
19 | 4 | - | I | xori rd, rs1, imm | xor immediate | rd = rs1 ^ SignExt(imm)
19 | 5 | 0 | R | srli rd, rs1, shamt | shift right logical immediate | rd = rs1 >> shamt
19 | 5 | 32 | R | srai rd, rs1, shamt | shift right arithmetic immediate | rd = rs1 >>> shamt
19 | 6 | - | I | ori rd, rs1, imm | or immediate | rd = rs1 ¦ SignExt(imm)
19 | 7 | - | I | andi rd, rs1, imm | and immediate | rd = rs1 & SignExt(imm)
23 | - | - | U | auipc rd, imm | add upper immediate to PC | rd = {imm31:12, 12’b0} + PC
35 | 0 | - | S | sb rs2, imm(rs1) | store byte | [Address]7:0 = rs27:0
35 | 1 | - | S | sh rs2, imm(rs1) | store half | [Address]15:0 = rs215:0
35 | 2 | - | S | sw rs2, imm(rs1) | store word | [Address] = rs2
51 | 0 | 0 | R | add rd, rs1, rs2 | add | rd = rs1 + rs2
51 | 0 | 32 | R | sub rd, rs1, rs2 | sub | rd = rs1 - rs2
51 | 1 | 0 | R | sll rd, rs1, rs2 | shift left logical | rd = rs1 << rs24:0
51 | 2 | 0 | R | slt rd, rs1, rs2 | set less than | rd = (rs1 < rs2)
51 | 3 | 0 | R | sltu rd, rs1, rs2 | set less than unsigned | rd = (rs1 < rs2)
51 | 4 | 0 | R | xor rd, rs1, rs2 | xor | rd = rs1 ^ rs2
51 | 5 | 0 | R | srl rd, rs1, rs2 | shift right logical | rd = rs1 >> rs2
51 | 5 | 32 | R | sra rd, rs1, rs2 | shift right arithmetic | rd = rs1 >>> rs2
51 | 6 | 0 | R | or rd, rs1, rs2 | or | rd = rs1 ¦ rs2
51 | 7 | 0 | R | and rd, rs1, rs2 | and | rd = rs1 & rs2
55 | - | - | U | lui rd, imm | load upper immediate | rd = {imm31:12, 12’b0}
99 | 0 | - | B | beq rs1, rs2, label | branch if = | if (rs1==rs2) PC = BTA
99 | 1 | - | B | bne rs1, rs2, label | branch if != | if (rs1!=rs2) PC = BTA
99 | 4 | - | B | blt rs1, rs2, label | branch if < | if (rs1< rs2) PC = BTA
99 | 5 | - | B | bge rs1, rs2, label | branch if ≥ | if (rs1>=rs2) PC = BTA
99 | 6 | - | B | bltu rs1, rs2, label | branch if < unsigned | if (rs1< rs2) PC = BTA
99 | 7 | - | B | bgeu rs1, rs2, label | branch if ≥ unsigned | if (rs1>=rs2) PC = BTA
103 | 0 | - | I | jalr rd, rs1, imm | jump and link register | rd = PC + 4, PC = rs1 + SignExt(imm)
111 | - | - | J | jal rd, label | jump and link | rd = PC + 4, PC = JTA

## Slide 11
void dotproduct (int v1[], int v2[], int len) {
int i, sum = 0;
for (i=0; i<len; i++)
sum += v1[i] * v2[i];
return sum;
}
void main(void) {
int a[3] = {1, 2, 3};
int b[3] = {4, 6, 6};
int d;
d = dotproduct(a, b, 3);
}
Assembly Language Programming

## Slide 12
// v1 in a0, v2 in a1, len in a2
// i in s0, sum in s1
dotproduct
addi sp, sp, -8 // room to save registers on stack
sw s0, 0(sp) // save s0
sw s1, 4(sp) // save s1
addi s1, zero, 0 // sum = 0
addi s0, zero, 0 // i = 0;
for
bge s0, a2, done // i < len?
slli t0, s0, 2 // i * 4
add t1, s0, t0 // address of v1[i]
lw t1, 0(t1) // v1[i]
add t2, s0, t0 // address of v2[i]
lw t2, 0(t2) // v2[i]
mul t3, t1, t2 // v1[i] * v2[i]
add s1, s1, t3 // sum += v1[i] * v2[i]
addi s0, s0, 1 // i++
j for // repeat for loop
done
mv a0, s1 // return sum
lw s0, 0(sp) // restore s0
lw s1, 4(sp) // restore s1
addi sp, sp, 8 // restore stack pointer
jr ra // and go back to caller
Assembly Language Programming

## Slide 13
xor x3, x8, x9
funct7 = 0
rs2 = 8
rs1 = 9
funct3 = 4
rd = 3
op = 51
0000000 01000 01001 100 00011 0110011
0x0084C1B3
Assembly to Machine Language

## Slide 14
0x00A5A823
Based on the bottom 7 bits, op = 35 (S-type)
Interpret the other bits according to S-type
0000000 01010 01011 010 10000 0100011
Imm11:5 = 0
rs2 = 10
rs1 = 11
funct3 = 2
Imm4:0 = 16
op = 35
sw x10, 16(x11)
Machine to Assembly Language

## Slide 15
Three Microarchitectures
  Single-cycle
  Multicycle
  Pipelined
Be able to add new features, such as new instructions
  Examples in the book/lecture and homework
Determine cycle time and performance
Don’t need to memorize diagrams or tables
Microarchitecture

## Slide 16
Single Cycle Processor

## Slide 17
Single Cycle Controller
Instruction | Opcode | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp | Jump
lw | 0000011 | 1 | 00 | 1 | 0 | 01 | 0 | 00 | 0
sw | 0100011 | 0 | 01 | 1 | 1 | xx | 0 | 00 | 0
R-type | 0110011 | 1 | xx | 0 | 0 | 00 | 0 | 10 | 0
beq | 1100011 | 0 | 10 | 0 | 0 | xx | 1 | 01 | 0
addi | 0010011 | 1 | 00 | 0 | 0 | 00 | 0 | 10 | 0
jal | 1101111 | 1 | 11 | x | 0 | 10 | 0 | xx | 1
ALUOp | funct3 | op5, funct75 | ALUControl | Instruction
00 | x | xx | 010 (add) | lw, sw
01 | x | xx | 110 (subtract) | beq
10 | 000 | 00, 01, 10 | 010 (add) | add
10 | 000 | 11 | 110 (subtract) | sub
10 | 010 | xx | 111 (set less than) | slt
10 | 110 | xx | 001 (or) | or
10 | 111 | xx | 000 (and) | and
ImmSrc | ImmExt | Type | Description
00 | {{20{Instr[31]}}, Instr[31:20]} | I | 12-bit signed immediate
01 | {{20{Instr[31]}}, Instr[31:25], Instr[11:7]} | S | 12-bit signed immediate
10 | {{20{Instr[31]}}, Instr[7], Instr[30:25], Instr[11:8], 1’b0} | B | 13-bit signed immediate
11 | {{12{Instr[31]}}, Instr[19:12], Instr[20], Instr[30:21], 1’b0} | J | 21-bit signed immediate

## Slide 18
Multicycle Processor

## Slide 19
Multicycle Controller

## Slide 20
Pipelined Processor

## Slide 21
Data hazards
  Instruction depends on result of previous instruction
  Handled by forwarding
  Most data hazards have zero latency
  1-cycle stall between load and use
Control hazards
  What instruction to fetch after branch
  Predict branch not taken, keep fetching from PC+4
  Flush two instructions if branch is actually taken
Pipeline Hazards

## Slide 22
Data Hazards

## Slide 23
Control Hazards