## Slide 1: little arduino microcontrollers
Meghan Jimenez
12 February 2014

## Slide 2
 | Arduino Uno | Arduino Micro | Teensy 3.1 | Trinket
Microcontroller | ATmega328 | ATmega32u4 | MK20DX256VLH7 Cortex M-4 | ATtiny85
Operating Voltage | 5 V | 5 V | 5 V | 3.3/5 V
Digital I/O Pins | 14 | 20 | 34 | 5
PWM Channels | 6 | 7 | 12 | 3
Analog Input Channels | 6 | 12 | 21 | 3
Flash Memory -Bootloader | 32 KB – 0.5 KB | 32 KB – 4 KB | 256 KB – 0.5KB? | 8 KB – 3 KB
SRAM | 2 KB | 2.5 KB | 64 KB | 512 bytes
EEPROM | 1 KB | 1 KB | 2 KB | 512 bytes
Clock Speed | 16 MHz | 16 MHz | 2-16 MHz | 8/8-16 MHz
Footprint | 6.26 in2 | 1.33 in2 | 0.98 in2 | 0.72 in2
Cost | $29.95 | $22.95 | $19.95 | $7.95

## Slide 3
Teensy 3.1
Trinket

## Slide 4: Trinket
For use in small, simple projects
Arduino IDE programmable over USB
I2C and SPI compatible
Not 100% Arduino compatible, needs some config changes to run at all
No serial port connection for debugging
Shares 2 GPIO pins with the USB interface
Recently release (Sept. 2013)

## Slide 5: Teensy 3.1

## Slide 6: Teensy 3.1
Programmable in the Arduino IDE with Teensyduino extension
  All standard Arduino functions and most programs written for Arduino work
  Many libraries have been tested and modified for use with Teensy and are available on the Teensy website
USB, UART, SPI, and I2C
I2S (high quality audio interface), IR modulator, 12-bit DAC, and touch sensor inputs
USB native - Emulates USB devices very easily – joystick, mouse, MIDI, etc.
Tons of memory and I/O pins
  Lots of memory makes it good for graphics applications

## Slide 7: Example Teensy Project

## Slide 8: Example Teensy Project

## Slide 9: References
http://learn.adafruit.com/usb-snes-gamepad?view=all
http://www.pjrc.com/
http://www.adafruit.com/

## Slide 10: Any Questions?