## Slide 1: Introduction to the Machine Shop
Harvey Mudd College
Johnson and Vincent
HMC Head Shop Proctors

## Slide 2: Outline
Logistics
Shop Safety
Advice
Preview of the Tours

## Slide 3: Logistics
Safety training – 4 parts
  This presentation
  In-Shop tours
  Shop videos
  Safety quiz (due by Feb 15th)
Some machines require additional training
  Table saw
  Miter saw
  and others
  Contact Paul or either of us to arrange training

## Slide 4: More on Logistics
Buddy System
  A shop proctor must be present for anyone to work in the shop.
  In extreme cases, Paul can substitute for a proctor.
ID-card checkout system
  All equipment in the main shop must be checked out
Check in with the proctor on duty if you are working in one of the other shops
Leave time to clean up before you leave
You can ask the shop proctor about anything
Notes: Stress cleaning up

## Slide 5: Shop Safety
Safety goggles
  Must be worn at all times when in the shop.
  Must have side guards.
  Must have safety rating of Z87.1-1989

## Slide 6: Proper Shop Attire
Roll up long sleeves
Remove loose jewelry, such as rings & watches
No dangling earphones
Don’t wear gloves when working with moving parts
Protective shoes
Long pants are preferable
Notes: Shoes that give protection, not just cloth keds/toe shoes

## Slide 7: Yale Incident
Tie back long hair
NEVER work alone (there should always be at least 1 other person there)

## Slide 8: More Shop Safety
Never:
  Get close to a moving part
  Reach where you can’t see
  Leave your machine unattended
  Distract someone who’s working on a machine
Always:
  Mind the point of operation
  Think ahead
  Pay attention to a machine when it’s turned on
  Work with a proctor on duty

## Slide 9: Working on a Machine is like Driving
You must be focused on the task at hand
The shop is full of powerful machines that can kill you if misused
Only machine when you are alert and focused
Set your phone to silent (do not call or text anyone while machining)
Do not come to the shop if you are under the influence
Shop proctors have the power to kick you out of the shop if you don’t follow the appropriate safety guidelines!

## Slide 10: How to Deal with Injuries
Report all injuries to the shop proctor on duty
  There are first aid kits in each shop, above the sink
In case of an emergency, dial campus safety
  The red phone in the shop is a direct line
  72000 on a school phone
  909-607-2000 on any phone
Notes: Red phone > bad shop signal

## Slide 11: Advice
Start early
Plan shop visits into your regular schedule
Come prepared to start machining
  Watch the videos and read your process router!
  http://www.eng.hmc.edu/E8/Videos.htm
You can always cut it smaller, but you can never cut it bigger!
Always clean up: pay it forward

## Slide 12: In-Shop Tours
  Mill
  Sheet Metal Shop
    Hole puncher
    Bender
    Band Saw
  Wood Shop
    Band Saw
    Belt Sander
    Drill Press
Specific safety information and tips for each machine

## Slide 13: Mill

## Slide 14: Band Saw & Belt Sander

## Slide 15: Bender & Drill Press

## Slide 16: Questions?