## Slide 1
Very High Radix Montgomery Multiplication
David Harris, Kyle Kelley and Ted Jiang
Harvey Mudd College
Claremont, CA
Supported by Intel Circuit Research Labs
Notes: Welcome to this presentation of a 64-state Viterbi Accelerator operating at 2GHz consuming 40mW in 90nm CMOS technology.

## Slide 2: Outline
RSA Encryption
Montgomery Multiplication
Radix 2 Implementations
  Tenca-Koç Radix 2
  Improved Radix 2
Very High Radix Implementations
  Very High Radix
  Parallel Very High Radix
  Quotient Pipelining
Results
Future Work
Notes: These circuits are key to achieving a low power energy efficient design.

## Slide 3: RSA Encryption
Most widely used public key system.
  Good for encryption and signatures.
  Invented by Rivest, Shamir, Adleman (1978)
Public e and private d keys are long #s
  n = 256-2048+ bits
  Satisfy xde mod M = x for all x
  Finding d from e is as hard as factoring M
Encryption: B = Ae mod M
Decryption: C = Bd mod M = Aed = A

## Slide 4: RSA Derivation
Choose two large random primes p, q
M = pq
Totient:  = (p-1)(q-1)
Public key e
  e is coprime to 
Private key d
  such that de = 1 mod 
Then xed mod M = x
  According to Fermat’s Little Theorem

## Slide 5: Cryptographic Algorithms
DES, AES
  Symmetric key algorithms
    Require exchange of secret key
  Computationally efficient
RSA, ECC
  Public key algorithms
    No key exchange needed (e.g. ecommerce)
  Computationally expensive
  Use public key to exchange symmetric key

## Slide 6: Modular Exponentiation
Critical operation in RSA and for
  Digital signature algorithm
  Diffie-Hellman key exchange
    SSL, IPSec, IPv6
  Elliptic curve cryptosystems
Done with modular multiplications
  Ex: A27 = ((((((A2) * A)2)2) * A)2) * A
  Division after each multiplication to compute modulo
  Maximum 2n, average 1.5n mults needed

## Slide 7: Binary Extension Fields
Building blocks are polynomials in x
  Operations performed modulo some irreducible polynomial f(x) of degree n
  Arithmetic done modulo 2
  Called GF(2n)
Example: GF(23)
  0, 1, x, x+1, x2, x2+1, x2+x, x2+x+1
Computation is the same as GF(p)
  Except that no carries are propagated

## Slide 8: Montgomery Multiplication
Faster way to do modular exponentation
  Operate on Montgomery residues
  Division becomes a simple shift
  Requires conversion to and from residues only once per exponentiation

## Slide 9: Montgomery Residues
Let the modulus M be an odd n-bit integer
  2n-1 < M < 2n
Define R = 2n
Define the M-residue of an integer A < M as
  A = AR mod M
There is a one-to-one correspondence between integers and M-residues for
0 < A < M-1

## Slide 10: Montgomery Multiplicaton
Define
  Z = MM(X, Y) = X Y R-1 mod M
Where R-1 is the inverse of R mod M:
  R-1R = 1 (mod M)
Montgomery Mult finds residue of Z = XY mod M
  Z = X Y R-1 mod M
  = (XR) (YR) R-1 mod M
  = XYR mod M
  = ZR mod M

## Slide 11: Montgomery Reduction
Precompute M’ satisfying RR-1 – MM’ = 1
Convert mult and mod to 3 mult and shift
Multiply: Z = X × Y
Reduce: reduce = Z × M’ mod R
Z = [Z + reduce × M] / R
Normalize: if Z ≥ M then Z = Z – M
Why is Z + Reduce × M divisible by R?
Mult
Mult
Mult
Shift for R-1
Drop bits

## Slide 12: Reduction Proof
[ Z + reduce × M ] mod R
= [ Z + (Z × M’ mod R) × M ] mod R
= [ Z + Z × M’M ] mod R
= [ Z + Z(RR-1 - 1) ] mod R
= ZRR-1 mod R
= 0 mod R
So Z + reduce × M is divisible by R

## Slide 13: More Comments on M’
RR-1 – MM’ = 1
  Implies M’  -M-1 mod R
  M’ is odd
M’ is precomputed from M using the extended Euclidian algorithm
  M is held constant over many mults
Only least significant v bits of M’ are needed when computing in radix 2v
  Dusse & Kaliski, Eurocrypt ’90s

## Slide 14: CPU Crypto Accelerators
VIA Esther Padlock Hardware Security
  Montgomery Multiplier < 0.5 mm2 die area
  Accessed by x86 instruction
  256b - 32Kb keys in 128 bit granularity
  Also supports AES
SmartMIPS Smart Card Extensions
  RSA, ECC, AES applications
  GF(2n) multiply, MAC instructions
  Carry propagation for multiword adds
  AES permutations and rotations
Intel LaGrande Technology
  Trusted computing

## Slide 15: Embedded Crypto Accelerators
3COM Router 5000 Series
Encryption Accelerator
IBM PCI SSL Cryptography Accelerator

## Slide 16: Radix 2 Algorithm
In radix 2, process one bit of X per step
  Reduction becomes trivial because M’ mod 2 = 1
  Two multiplies and one shift per step
    Z = 0
    for i = 0 to n-1
    Z = Z + Xi × Y
    reduce = Z0 trivial
    Z = Z + reduce × M make Z divisible by 2
    Z = Z/2
    if Z ≥ M then Z = Z – M final Mod M
Z = X × Y
reduce = Z × M’ mod R
Z = [Z + reduce × M] / R
if Z ≥ M then Z = Z – M

## Slide 17: Final Modulo
Result before last step in range
  0  Z < 2M
  Reducing Z-M at the end is a hassle
Allow 0  X, Y < 2M to avoid reduction
  Then if R > 4M, 0  Z < 2M
  Hence add two bits to R to avoid subtraction at end of each step
  Walter, Electronic Letters ’99

## Slide 18: Conversion
Conversion of integers to/from Montgomery residues takes one MM operation (if r2 mod M is precomputed and saved):
Modular exponentiation takes two conversion steps and ~2n multiplication steps.

## Slide 19: Reconfigurable Hardware
Building hardwired n-bit unit is limiting
  Slow for large n
  Not scalable to different n
Better to design for w-bit words
  Break n-bit operand into e w-bit words
    e = n/w
  This is called scalable
Also handle both GF(p) and GF(2n)
  Requires conditionally killing carries
  Called unified

## Slide 20: Tenca-Koç Montgomery Multiplier
Z = 0
for i = 0 to n-1
(Ca, Z0) = Z0 + Xi × Y0
reduce = Z0
(Cb, Z0) = Z0 + reduce × M0
for j = 1 to e
(Ca,Zj) = Zj + Ca + Xi × Yj
(Cb,Zj) = Zj + Cb + reduce × Mj
Zj-1 = (Zj0, Zj-1w-1:1)
M = (M(e-1), …, M1, M0),
Y = (Y(e-1), …, Y1, Y0),
Z = (Z(e-1), …, Z1, Z0),
X = (Xn-1, …, X1, X0)
Tenca, Koç, Trans. Computers, 2003

## Slide 21: Processing Elements
Keep Z in carry-save redundant form
  Tc = 2tAND + 2tCSA + tMUX + tBUF(w) + tREG

## Slide 22: Parallelism
Two dimensions of parallelism:
  Width of processing element w
  Number of pipelined PEs p
    Multiply takes k = n/p kernel cycles

## Slide 23: Pipeline Timing

## Slide 24: Queue
If full PEs cause stall, queue results
Convert back to nonredundant form
  Saves queue space
  CPA needed for final result anyway

## Slide 25: Improved Design
Don’t wait two cycles for MSB
Kick off dependent operation right away on the available bits
Take extra cycle(s) at the end to handle the extra bits
For p processing elements, cycle count reduces from 2p to p + (p/w)
Harris, Krishnamurthy, Anders, Mathew, Hsu, Arith 2005.

## Slide 26: Improved PE
Left-shift M and Y
  Rather than right-shift Z
Same amount of hardware

## Slide 27: Pipeline Timing

## Slide 28: Latency
Tenca-Koç
k(e+1) + 2(p-1) n > 2pw – w
k(2p+1) + e - 2 n  2pw – w
Improved Design
(k+1)(e+1) + p-2 n > pw
k(p+1) + 2e - 1 n  pw

## Slide 29: Break

## Slide 30: Break

## Slide 31: Break

## Slide 32: Very High Radix
Handle many bits of X at a time
  Radix 2v processes v bits of X
    Only f = n/v outer loop iterations needed
    k = n/pv kernel cycles with p PEs
  Hardware changes
    w bit AND  v  w bit multiplier
    Right shift by v bits after each step
      Use v  w so bits are available to shift
    Cycle time gets longer
  Reduce becomes more complicated
    Must drive v lsbs to 0

## Slide 33: Very High Radix Algorithm
Z = 0
for i = 0 to f-1
Z = Z + Xi × Y
reduce = (M’ × Z) mod 2v reduce bottom v bits
Z = Z + reduce × M
Z = Z / 2v
Z = X × Y
reduce = Z × M’ mod R
Z = [Z + reduce × M] / R

## Slide 34: Scalable Very High Radix MM
Z = 0
for i = 0 to f-1
(CA, Z0) = Z0 + X0 × Y0
reduce = (M’ × Z0) mod 2v only reduce bottom v bits
(CB, Z0) = Z0 + reduce × M0
for j = 1 to e + (v + 1) / w - 1
(CA, Zj) = Zj + CA + Xi × Yj
(CB, Zj) = Zj + CB + reduce × Mj
Zj-1 = (Zjv-1:0, Zj-1w-1:v)
2 mul, 1 shift
in inner loop

## Slide 35: Very High Radix PE
Kelley, Harris IWSOC 2005

## Slide 36: Pipeline Timing
Each MAC is given a full cycle
Tc = tMUL(v,w) + tCPA(v+w) + tmux + tREG
Two MAC columns for each PE
Four cycle latency between PEs:
1) Z0 = Xi × Y0
2) reduce = M’ × Z0 mod 2v
3) Z0 = Z0 + reduce × M0
4) Z1 = Z1 + reduce × M1, shift into Z0

## Slide 37: Very High Radix Latency
k(e + 3) + 4(p - 1) + 2 n > 4pw – 2w
k(4p + 1) + (e - 1) n  4pw – 2w
Design limited for small n by 4-cycle latency between PEs

## Slide 38: Parallel Very High Radix
Eliminate two of the cycles
  Multiplication to compute reduce
    By precomputing M = M’ × M mod R
  Dependency of Z0 on reduce
    By prescaling X by 2v so Z0 = 0
Math proposed by Orup Arith95
  But no scalable very high radix HW
~

## Slide 39: Improvement 1: Eliminate Multiply
Z = 0
for i = 0 to f-1
Z = Z + Xi × Y
Z = Z + Z0 × M M = (M’ mod 2v)M mod R
Z = Z / 2v
M = M’ × M mod R (precompute)
Z = X × Y
Z = [Z + Z × M] / R
Z = X × Y
reduce = Z × M’ mod R
Z = [Z + reduce × M] / R
~
~
~
~

## Slide 40: Improvement 2: Prescale X by 2v
Z = 0
for i = 0 to f
Z = Z + 2vXi × Y + Z0 × M
Z = Z / 2v
Z = 0
for i = 0 to f
Z = (Z + Z0 × M) / 2v + Xi × Y
Z = 0
for i = 0 to f-1
Z = Z + Xi × Y
Z = Z + Z0 × M
Z = Z / 2v
~
~
~
Because Z0 is independent of 2vXi
Final result in range 0  Z < 2n+v+1
- avoid final small mod in successive mults by using larger R
One more iteration

## Slide 41: Improvement 3: Avoid LSW add
Z = 0
for i = 0 to f
Z = (Z + Z0 × M) / 2v + Xi × Y
Z = 0
for i = 0 to f
reduce = Z0
Z = Z >> v + reduce × M + Xi × Y
~
M + 1
M =
~
2v
(Z + Z0 × M) / 2v
= Z >> v + (Z0 × M + Z mod 2v) / 2v
= Z >> v + (Z0 × (M+1)) / 2v
= Z >> v + Z0 × M
~
~
~
M  M’M  -1 mod 2v
So M + 1 is divisible
~
~

## Slide 42: Scalable Parallel Very High Radix
Z = 0
for i = 0 to f
C = 0
reduce = Z0
for j = 0 to e +  v/w 
(C, Zj) = Zj + C + reduce × Mj + Xi × Yj
Zj-1 = (Zjv-1:0, Zj-1w-1:v)

## Slide 43: Parallel Very High Radix PE
Kelley, Harris Asilomar 2005

## Slide 44: Pipeline Timing
Two cycle latency between PEs:
1) Z0 = Z0 + Xi × Y0 + reduce × M0
2) Z1 = Z1 + Xi × Y1 + reduce × M1,
shift into Z0
Tc = tMUL(v,w) + 2tCSA + tCPA(v+w) + tREG

## Slide 45: Parallel Very High Radix Latency
k(e+1) + e+1 + 2(f mod p) n > 2pw – v
k(2p+1) + e+1 + 2(f mod p) n  2pw – v

## Slide 46: Quotient Pipelining
Reduce depends on previous Z
  Pipeline reduce calculation to avoid reduce being on the critical path
  Parallel Very High Radix can be viewed as 0-stage Quotient Pipeline architecture

## Slide 47: 0-stage Quotient Pipelining
Parallel Very High Radix
  reduce × Mj and Xi × Yj occurs simultaneously
  Require reduce in non-redundant form
  Solution: Delay reduce × Mj calculation by d PE’s: d-stage delay Quotient Pipelining

## Slide 48: d-Stage Delay Quotient Pipelining
Parallel Design
  M = (M’ mod 2v) × M >> v
  reduce produced by PEi is used by PEi+1
Quotient Pipelining
  M = (M’ mod 2v(d+1)) × M >> v(d+1)
  Where d is the # of delay stages
  Reduce produced by PEi is used by PEi+1+d
Parallel: d = 0-Stage Quotient Pipelining

## Slide 49: 1-Stage Quotient Pipelined Algorithm
Z = 0
oldreduce = 0
for i = 0 to f
reduce = Z0
Z = Z >> v + oldreduce × M + Xi × Y
oldreduce = reduce
Z = Z << v + oldreduce

## Slide 50: 1-Stage Scalable Quotient Pipelining
Z = 0
oldreduce = 0
for i = 0 to f
C = 0
reduce = Z0
for j = 0 to e
(C, Zj) = (Zjv-1:0, Zj-1w- 1:v) +
oldreduce × Mj + Xj × Yj + C
oldreduce = reduce
Z = Z << v + oldreduce

## Slide 51: Quotient Pipelined PE

## Slide 52: Quotient Pipelined Performance
Tc = tMUL(v,w) + tCSA + tREG
k(e+1) + e+1 + 2(f mod p) for n > 2pw – v
k(2p+1) + e+1 + 2(f mod p) for n  2pw – v
k = n’/pv
e = n’/w
f = n’/v
n’ = n+2v
Differs from Parallel design:
  Parallel: n’ = n+v
  Extra v to account for the extra stage of delay

## Slide 53: Comparison of Latencies
Tenca-Koç Radix 2
n2/wp + n/p + 2p – 2 n > 2wp – w
2n + n/p + n/w – 2 n  2wp – w
Improved Radix 2
n2/wp + n/w + n/p + p – 1 n > wp
n + n/p + 2n/w – 1 n  wp
Very High Radix
n2/wpv + 3n/pv + 4p – 2 n > 4wp – 2w
4n/v + n/pv + n/w - 1 n  4wp – 2w
Parallel Very High Radix
n2/wpv + n/pv + n/w + 1 n > 2wp – v
2n/v + n/pv + n/w + 1 n  2wp – v

## Slide 54: Latency vs. # of PEs
Assume w = 16, v = 1 or 16
Let m = wvp be the amount of HW
For small m
  All similar
  Cycles  m
For large m
  Saturates
  High radix
  is better

## Slide 55: Comparison of Cycle Times
Tenca-Koç / Improved Radix 2
Tc = 2tAND + 2tCSA + tMUX + tBUF(w) + tREG
Very High Radix
Tc = tMUL(v,w) + tCPA(v+w) + tmux + tREG
Parallel Very High Radix
Tc = tMUL(v,w) + 2tCSA + tCPA(v+w) + tREG
Quotient Pipelining
Tc = tMUL(v,w) + tCSA + tREG

## Slide 56: Synthesis Results
Xilinx Virtex II Pro XC2V250-6
  ~5n RAM bits needed for X, Y, M, Z, FIFO
Arch | Freq (MHz) | LUTs/PE Regs/PE | 16 × 16 Mults/PE | RAM
Improved Radix 2 | 144 | 85 69 | 0 | 5n
Very High Radix | 107 | 178 218 | 2 | 5n
Parallel Very High Radix | 107 | 133 147 | 2 | 5n
Quotient Pipelined | 138 | 238 226 | 2 | 5n

## Slide 57: Exponentiation Times
On average, 1.5n + 2 Montgomery multiplies are needed for modular exponentiation
  Texp = Tc * latency(n, w, v, p) * (1.5n + 2)

## Slide 58: Hardware Results
Arch | Freq (MHz) | p | n | Latency (cycles) | Texp (ms)
Improved Radix 2 w = 16 | 144 | 16 | 256 | 303 | 0.81
 |  |  | 1024 | 4239 | 45.3
 |  | 64 | 256 | 291 | 0.78
 |  |  | 1024 | 1167 | 12.5
Very High Radix w = v = 16 | 107 | 4 | 256 | 90 | 0.32
 |  |  | 1024 | 1086 | 15.6
 |  | 16 | 256 | 80 | 0.28
 |  |  | 1024 | 330 | 4.74
Parallel Very High Radix w = v = 16 | 107 | 4 | 256 | 85 | 0.31
 |  |  | 1024 | 1105 | 15.9
 |  | 16 | 256 | 50 | 0.18
 |  |  | 1024 | 325 | 4.67
Quotient Pipelined w = v = 16 | 138 | 4 | 256 | 95 | 0.26
 |  |  | 1024 | 1139 | 12.7
 |  | 16 | 256 | 53 | 0.15
 |  |  | 1024 | 334 | 3.72

## Slide 59: Athena TeraFire 5008
5.5 ms 1024-bit exponentiation
95 Kgates IP block

## Slide 60: Software Results
1024 bit modular exponentiation
  2.4 GHz Pentium 4, FLINT/C library
    92 ms without Montgomery’s alg
    41 ms with Montgomery’s alg
  2.4 GHz Pentium 4, GMP library
    25 ms with Karatsuba’s algs
  80 MHz ARM
    876 ms with Montgomery’s alg

## Slide 61: Summary
Latency (cycles)
  Comparable per full adder for all designs when p small
  Saturates when p gets too big
    Improved radix 2 design 2x better than T-K
    Very high radix even better (by v/4 or v/2)
Cycle Time
  Worse for very high radix
  But only slightly so on FPGAs with efficient multiplier hardware
Total Time
  Radix 2 best when little HW is available
  Radix 216 attractive for FPGAs for minimum latency when plenty of HW is available

## Slide 62: Future Work
Better pipelining of parallel design
Radix 2 parallel design
Radix 4/8 with precomputed multiples
Karatsuba Algorithm
Side channel attack countermeasures
Reconfigurable Logic on CPUs

## Slide 63: Pipelining Parallel Design
Tc = tMUL(v,w) + 2tCSA + tREG

## Slide 64: Parallel Radix 2
Tc = tAND + 2tCSA + tREG
Z = 0
for i = 0 to n
C = 0
reduce = Z0
for j = 0 to e
(C, Zj) = Zj + C + reduce × Mj + Xi × Yj
Zj-1 = (Zj0, Zj-1w-1:1)

## Slide 65: Radix 4/8 with Precomputed Multiples
Todorov & Twalbeh extended T-K to radix 4/8
  Precompute multiples of Y, M
  Use mux instead of AND / MUL
Improve latency using right shifts
Does Booth encoding help?
Tc = tMUX + 2tCSA + tREG

## Slide 66: Karatsuba Algorithm
“The Karatsuba multiplication arouses our curiosity, since it seems simple, and one could pleasantly occupy a (preferably rainy) Sunday afternoon trying it out.”
  M. Welschenbach, Cryptography in C and C++
A = A12n + A0; B = B12n + B0
Regular Multiplication (O(n2))
  AB = 22nA1B1 + 2n(A0B1 + A1B0) + A0B0
Karatsuba Multiplication (O(n1.585))
  C0 = A0B0; C1 = A1B1; C2 = (A0 + A1)(B0 + B1) – C0 – C1
  AB = 22nC1 + 2nC2 + C0

## Slide 67: Side Channel Attacks
Monitor chip activity to try deducing private key
  Timing
  Current consumption
  Photon emissions
How vulnerable is very high radix MM to side channel attacks?
How can it be improved?
  CVSL, other differential logic families?
  Differential registers
  Inherent symmetry of addition & multiplication

## Slide 68: Reconfigurable Logic on CPU
Add FPGA for dynamically reconfigurable accelerators
  ~1000 transistors / 4-input LUT
Differentiates Intel from competition by unique reconfigurable logic fabric

## Slide 69: Applications
Montgomery Mult
  RSA, ECC, Diffie-Hellman Key Exchange
AES accelerator
  symmetric key crypto
Viterbi decoder
Pattern matching
  Genome BLAST, Google, network security
DSP accelerators
  photoshop filters, video encoding

## Slide 70: Example
Montecito
2 cores
28.5M Tran each
24MB L3$
1550M Transistors
Alternative
2 cores
20MB L3$
1300M Transistors
250 KLUT FPGA
250M Transistors
FPGA
FPGA

## Slide 71: Superblock Organization
Each contain substantial resources
  CLBs, memories, multipliers, etc.
Chip provides one or more superblock
  Accelerators are compiled for one or more Superblocks
  Easy reconfiguration without recompile
  “Memory manager” controls how many can be downloaded at a time

## Slide 72: Conclusions
High radix best when multipliers are cheap
  Is this a research direction of relevance to Intel?
Focus of future research
  Low radix improvements
  Side channel security
  FPGA coprocessor architectures
  Other Discussion ?