## Slide 1
David Harris
Harvey Mudd College
David_Harris@hmc.edu
Based on EE271 developed by Mark Horowitz, Stanford University

## Slide 2: Overview
Reading
    W&E Chapter 1 from 1.1 to 1.9
Background
  VLSI is pretty new; it has its beginning back in the early 60's with SSI, small scale integration, when a few bipolar transistors and resistors were fabricated on the same chip. Today chips are both simpler and more complex. They typically only contain two active elements (NMOS and PMOS transistors) and wires. But there might be millions of these transistors on the chip, and these chips can do amazing functions. You also find chips in everything. This lecture will look at why this has happened and what it hard about VLSI design. It will also take a quick look at the basic elements that make up VLSI chips: MOS transistors and wires.

## Slide 3: Big Picture
Want to go from this:

## Slide 4
To this:

## Slide 5: Magnified

## Slide 6: Why Integrated Circuits?
Break this question into two questions
  Why electronics
  Why use ICs to build electronics
Why use electronics
  Electons are easy to move / contol
    Easier to move/control electrons than real stuff
  If you don’t believe me look at a mechanical computer
    http://www.nmsi.ac.uk/on-line/treasure/objects/1862-89.html
  Move information, not things (phone, fax, WWW, etc.)
    Takes much less energy and $

## Slide 7: Electronics
Building electronics:
  Started with tubes, then miniature tubes
  Transistors, then miniature transistors
  Components were getting cheaper, more reliable but:
    There is a minimum cost of a component (storage, handling …)
    Total system cost was proportional to complexity
Integrated circuits changed that
  Printed a circuit, like you print a picture,
    Create components in parallel
    Cost no longer depended on # of devices
  What happens as resolution goes up?

## Slide 8: Moore’s Law
First stated by Intel’s Gordon Moore in the early 80’s. Saw that the resolution of the printing process was improving exponentially (0.7x feature size every 3 years) and predicted that it would continue into the future
Since the cost of the printing process (called wafer fabrication) was growing at a modest rate, it implied that the cost per function, was dropping exponentially. At each new generations, each gate cost about 1/2 what it did 3 years ago. Shrinking an existing chip makes it cheaper!
ln
(#dev)
year
good
y
ear
y
ear
die
cost
ln(cost/function)

## Slide 9: Bad News
Although the cost of manufacturing IC's remained approximately constant, the design cost did not. In fact, while designer productivity has improved with time, it has not increased a the same rate as the complexity of the chips.
So the cost of the chip design is growing exponentially with the complexity of the circuit. The integrating of a system on a piece of silicon has an attractive manufacturing cost but frightening design cost and risk. Need to build very complex stuff.
In addition, the number of custom IC designers was (and is) fairly limited. Even if you were willing to take the risk, where would you find the people to do the design?
y
ear
ln(design cost/function)
y
ear
ln(design cost)

## Slide 10: Sense of Scale
What fits on a VLSI Chip today?
State of the art logic chip
  18mm on a side (324mm2)
  0.25m drawn gate length
  1.0m wire pitch
  5-level metal
For comparison
  32b RISC processor
    8K  x 16K
  SRAM
    about 32x 32 per bit  1000 
    8K x 16K is 128Kb, 16KB
  DRAM
    8 x 16 per bit  100 
    8K x16K is 1Mb, 128KB
20 G
18mm
(18,000 wire pitches)
144,000 
0.25m (2 )
32b RISC
Processor
64b FP
Processor
1m
(8 

## Slide 11: Technology Scaling
Number of ‘grids’ per chip doubles every 3 years
  more functionality per chip
  harder to design
Two problems
  What do you do with all that space -- what function?
  How do you make sure it works
2010
2004
1998

## Slide 12: VLSI Design
Managing Complexity
Simplify the design problem
    Can’t understand 10M transistors, or 100M rectangles
    Need to make less complex (and less numerous) models
  Abstraction
    Simplified model for a thing, works well in some subset of the design space
  Constraints
    Needed to ensure that the abstractions are valid
    Might work if you violate constraints, but guarantees are off
Understand the underlying technology
  Provide a feeling for what abstractions and constraints are needed
  Determine efficient solutions (in design time, or implementation area, power, or performance)

## Slide 13: VLSI Design
Besides all that,
I think it is a blast!
I hope you agree.

## Slide 14: Abstractions and Disciplines How to Deal with 107 Transistors
Digital abstraction
  signals are 1 or 0
Switch abstraction
  MOSFETs as simple switches
Gate abstraction
  Unidirectional elements
  Separable timing
Synchronous abstraction
  Race free logic
  Function does not depend on timing
Constrain the design space to simplify the design process
  strike a balance between design complexity and absolute performance
Partition the problem
(Use hierarchy)
  Module is a box with pins
  apply recursively

## Slide 15: + Design Levels
Specification
  what the system (or component) is supposed to do
Architecture
  high-level design of component
    state defined
    logic partitioned into major blocks
Logic
  gates, flip-flops, and the connections between them
Circuit
  transistor circuits to realize logic elements
Device
  behavior of individual circuit elements
Layout
  geometry used to define and connect circuit elements
Process
  steps used to define circuit elements
Can describe design at many different levels of abstraction
High-lighted levels we will discuss in this class

## Slide 16: What is on an Integrated Circuit?
Actually only two types of things:
  Conducting layers which form the wires on the IC.
    There are many layers of wires (used to have 1 layer of metal, now advanced processes have 5-7 metal layers). Wires have electrical properties like resistance and capacitance.
    (Requires insulators and contacts between layers.)
  Transistors (the free things that fit under the wires).
    There are a few kinds of transistors. In this class we will study MOS ICs, so we will work with MOS transistors. These transistors can be thought of as a voltage controlled switch. The voltage on one terminal of the transistor determines whether the other two terminals are connected or not.

## Slide 17: Physical Topology of an Integrated Circuit
The transistors are built in the silicon, and then there are lots of wiring layers deposited on top. In cross-section it looks like (abstractly):
In the technology that we will use in the class (which can be scaled from 2 to 0.25) there are 4 primary layers. The top two layers are metal wires, and then there is a polysilicon layer and a diffusion layer (together poly and diff can form “active” devices – more on that later).
Silicon

## Slide 18: - Another View:
Chip consists of
  transistors: fabricated on the silicon surface and
  wires: that connect the transistors fabricated on layers of metal separated by insulators
Most of the area are the wires
Top View
Cross Section
poly
gate
metal
wire
contact
diffusion
n-well
n-well

## Slide 19: Layout: The Fabrication Specification
The end of the design process must create a set of drawings, one for each layer needed in the manufacturing process
  Layout drawing are complicated
    There are many rules about the geometry to make sure the circuits can be reliably manufactured
      Minimum width of wire, minimum spacing between wires, alignment rules
    The layers represent transistors and wires, and need to create the correct function
    Many rectangles for each transistor and wire, and there are millions of transistors and wires.
  Different layers are represented by different colors
    People used to draw the layout on mylar (10s of transistors)
    But not any more, now use CAD tools, and premade cells.

## Slide 20: Layout Example
Example from previous student project
Use hierarchy to hide complexity
Pads around chip
Major blocks are shown
Colored regions are really many wires

## Slide 21: Layout
This picture is an expanded view of a portion of the layout of the other page.
The next two slides will look at the controller layout and some layout in the datapath

## Slide 22: Controller Layout
Right half shows cells in the design
Left half has the cells expanded to show the layout layers
This design style has random wires

## Slide 23: Datapath Layout
Wires here are more regular
Again
  Cells on right
  Expanded cells on left
Transistor density is higher

## Slide 24: Stick Diagrams
Stick diagrams are a simplified version of layout
    Abstract the layout so wires are just lines
      Don’t worry about width or spacing
      Just draw the center line of the wire
    Spacing on different parts of the page need not be the same
      Sneak another wire in when needed, without needing to redraw the whole layout
      But try to keep spacing the same
      (since it will better estimate the real layout)
    Good starting point before doing layout
      But like most things, after you do some layout, you will have a better feeling for how to draw useful stick diagrams
We will use stick diagrams often to demo stuff …

## Slide 25: Wire Layers
We represent the different wiring layers with different colors
  metal2 - purple / orange
  metal1 - blue
  poly - red
  diff - green / yellow
Wires on the same layer that touch ALWAYS connect. There is no way to jumper a wire without changing layers.
Wires on different layers can cross without connections. To form connections between different layers you need to explicitly draw a contact.

## Slide 26: Transistors
Are formed when poly (red) crosses diffusion (green or yellow).
    (lots of fab steps to make it seem that simple)
no connection
connection
transistor
connected
red
green

## Slide 27: Transistors
The voltage on the gate (poly connection) controls the current that flows between the source and drain (diffusion terminals). The transistor model is often displayed by drawing its current-Voltage curve.
0
0
.
5
1
1
.
5
2
2
.
5
0
1
0
0
2
0
0
3
0
0
4
0
0
5
0
0
6
0
0
V
d
s
(
V
)
I
d
s
(
u
A
)

## Slide 28: Digital Abstraction
Rather than worrying about the precise voltages on the terminals of the transistor, guarantee that voltages will fall within two regions, one represents a logic ‘0’ and the other a ‘1’.
  Need to compute the output only for inputs in the allowable range
    Much simpler than before
    Model transistor as being either conducting, or off
  Need to ensure that the output is always in the allowable voltage range
    Need to make sure you produce valid digital outputs to the next stage
    Also want to have level restore. Allowable voltage range for output range should be smaller than allowable input range
      Attenuate noise on the signals

## Slide 29: The Digital Abstraction
Divide voltage into discrete regions
  logic 0
  logic 1
  X - between 0 and 1
  out of range
    may damage devices
Each logic gate restores the signal
  noise is not cumulative
  output voltage range is narrower than input range
  Noise margin (VOH-VIH)
X
0
1
Voltage
Noise
VIH
VIL
0
1
X
VOH
VOL

## Slide 30: Simple Model of a MOSFET
Three terminal device
  source, drain
    two ends of conductive path
  gate
    controls conductive path
  operation
    conducts when gate is high
    open circuit when gate is low
  caveat
    passes 0s well, not 1s
source
gate
drain

## Slide 31: Terminology
Note that the source and drain terminals are really the same, but by convention the source terminal is the one with the lower voltage on it. Thus, the maximum voltage between the gate and the {source, drain} is the voltage between the source and the gate. (This fact will be important later.)
The voltage on the gate controls the connection between the source and the drain. When the gate is high, the source and drain are connected together. When it is low, the terminals are disconnected.
CAUTION: do NOT use the words “open” and “closed” to describe switches. Is open an open electrical circuit (no flow), or an open fluid valve (flow)? You get opposite results, depending on which analogy you use.
This description is for NMOS transistors. For PMOS everything is reversed. The source is the higher voltage terminal, and the transistor is on when the gate is much lower than the source. More on PMOS later

## Slide 32: - Transistor Examples
The state of these transistors:
0
1
0
1
0
0
1
1
1
Complicated, it is really off. More on this next lecture. Assume it is on for now

## Slide 33: Switch Networks
Since transistors can be modeled as switches
  Look at what we can make out of switches
  Draw an abstract switch as
    Control (gate) terminal is on top
Can build switch networks
  Are not logic gates themselves!!!
  Are a collection of switches that still only has two non-control terminals
    Define function of a switch network as the inputs conditions that connect the two terminals of the network
Structure of switch network sets its logic functions:
    ‘OR’ functions are constructed by parallel switches
    ‘AND’ function are constructed by series switches

## Slide 34: - Switch Networks
The function of a switch network is true when the two terminals of the network are connected together. Since for parallel switches the terminals are connected if either switch is on, the function is OR. For series switches the network is conducting only if both switches are on, hence an AND.

## Slide 35: General Switch Networks
More complex connections are possible
Composition rules are simple. Use a recursive definition:
  Parallel combination of switch networks yields an OR of the component switch networks’ functions
  Series combination of switch networks yields on AND of the component switch networks’ functions.

## Slide 36: Switch Logic
Using switch-networks we can build up a simple kind of logic. The basic idea is to use switches to route one of several inputs to the output. There are two rules you must follow for switch logic to work:
  The primary output must always be connected to one of the inputs
    (the OR of all the switch-networks to output must be 1)
  Two (or more) inputs must not be connected together
    (the AND of any two of the switch-networks to output must be 0)
    (unless they are both constants and have the same value)
For now we will assume that both true and complement values of the inputs are available. A little later we will talk about how to make inverters to generate the complements.

## Slide 37: Multiplexer
A very useful switch network in an input multiplexer. It simply selects one of the inputs to the output. This structure can be used to easily map any logical function into switch logic -- all that needs to be done is present the right constant vector to the inputs of the multiplexer.
A
B
A
B
A
B
Z
0
0
0
1
0
1
0
1
1
1
1
0
Z
Constants
Output
Notice that the switch networks are exclusive of each other (AND is 0), and that the OR of all the terms is 1.
The layout shown is NOT a good way to build this function. It uses diffusion wires, which we will see later is not a good choice.

## Slide 38: Muxes
For some functions you can do better than just using constants and a multiplexor. You can implement an XOR gate in only two transistors (if you assume that both the inputs and their complements are available)
Notice also the change in floorplan with the inputs staying on poly.
    (which is a better layout)
A
A
Z
B
B

## Slide 39: Parity Function
A more complex switch logic function:
    A XOR B XOR C XOR D …
Try to minimize the work you need to do, so try for an iterating structure
    Parity of (…, An, An+1) = Parity (…, An) XOR An+1
    Looks promising but XOR switch logic needs both In and In_b
    Need to build both XOR XNOR

## Slide 40: Parity
Each stage looks like
Even
Odd
A_b
A
Even Out
Odd Out

## Slide 41: - Parity of Three Inputs
Can cascade them to form a larger structure
C_b
C
B_b
B
A_b
A
Even
Odd

## Slide 42: + Tally Function
This is a more complex function that can be implemented in switch logic. The function counts the number of ones in the input word:
Zn is 1 if there are n 1’s in the input word
For an n-bit number there are n+1 outputs
  Z0, Z1, … Zn
Example:
Input Z0 Z1 Z2 Z3 Z4 Z5
00000 1 0 0 0 0 0
11010 0 0 0 1 0 0
10111 0 0 0 0 1 0
00001 0 1 0 0 0 0

## Slide 43: + Tally Function Implementation
The easiest way to solve this is to solve iteratively (like parity):
Tn = f(Tn-1, Inputn)
Here each stage is a little different (since it must produce a different number of outputs)
How to build a stage?
If bit is one, increment count by shifting Zn by 1
Zn -> Zn+1
If bit is zero Zn remain the same
Zn -> Zn

## Slide 44: + Tally Function
Shown below is the tally function for one bit. It has two outputs, Z0 and Z1.
When the data is 0, the diagonal transistors are off, and the horizontal path (complementary switches) are on.
Output Z1 is set to 0
Output Z0 is set to 1
When the data is 1, the diagonal transistors are on, and the horizontal switches are off
Output Z1 is set to 1
Output Z0 is set to 0
Note: Each output is always driven by one and only one value. (Switch logic rule)
Z0
Z1

## Slide 45: + Two Input Tally
Simple generalization of the
one input case
Built by cascading 1 input
tally functions
Size of circuit is O(n
2
) where
n is the number of data
inputs
Simple cell (two transistors)
can be replicated to build
larger circuits
Z
2
Z
1
Z
0
Switches are set for 1, 1, so the
diagonal path is connected (Z2 = 1)

## Slide 46: + Two Input Tally
Circuit works by routing inputs either across or up

## Slide 47: Inverters
To build an inverter with switch networks, you want to connect the output to Gnd when the input is high (a simple switch) and connect the output to Vdd when the input is low (another simple switch). The problem is how to build the second switch -- NMOS transistors are on when the gate is high, and you can't use an inverter to build an inverter!

## Slide 48: CMOS inverters
In CMOS the solution is quite simple: use PMOS transistor. It connects its source/drain only when the gate is low.
In the next lecture we will discuss how to create NMOS and PMOS transistors.
in
out
1
0
switch ~
PMOS
CMOS