## Slide 1: Introduction to CMOS VLSI Design Lecture 1: Circuits & Layout
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
A Brief History
CMOS Gate Design
Pass Transistors
CMOS Latches & Flip-Flops
Standard Cell Layouts
Stick Diagrams

## Slide 3: A Brief History
1958: First integrated circuit
  Flip-flop using two transistors
  Built by Jack Kilby at Texas Instruments
2003
  Intel Pentium 4 processor (55 million transistors)
  512 Mbit DRAM (> 0.5 billion transistors)
53% compound annual growth rate over 45 years
  No other technology has grown so fast so long
Driven by miniaturization of transistors
  Smaller is cheaper, faster, lower in power!
  Revolutionary effects on society

## Slide 4: Annual Sales
1018 transistors manufactured in 2003
  100 million for every human on the planet

## Slide 5: Invention of the Transistor
Vacuum tubes ruled in first half of 20th century Large, expensive, power-hungry, unreliable
1947: first point contact transistor
  John Bardeen and Walter Brattain at Bell Labs
  See Crystal Fire
  by Riordan, Hoddeson

## Slide 6: Transistor Types
Bipolar transistors
  npn or pnp silicon structure
  Small current into very thin base layer controls large currents between emitter and collector
  Base currents limit integration density
Metal Oxide Semiconductor Field Effect Transistors
  nMOS and pMOS MOSFETS
  Voltage applied to insulated gate controls current between source and drain
  Low power allows very high integration

## Slide 7: MOS Integrated Circuits
1970’s processes usually had only nMOS transistors
  Inexpensive, but consume power while idle
1980s-present: CMOS processes for low idle power
Intel 1101 256-bit SRAM
Intel 4004 4-bit Proc

## Slide 8: Moore’s Law
1965: Gordon Moore plotted transistor on each chip
  Fit straight line on semilog scale
  Transistor counts have doubled every 26 months
Integration Levels
SSI: 10 gates
MSI: 1000 gates
LSI: 10,000 gates
VLSI: > 10k gates

## Slide 9: Corollaries
Many other factors grow exponentially
  Ex: clock frequency, processor performance

## Slide 10: CMOS Gate Design
Activity:
  Sketch a 4-input CMOS NOR gate

## Slide 11: CMOS Gate Design
Activity:
  Sketch a 4-input CMOS NOR gate

## Slide 12: Complementary CMOS
Complementary CMOS logic gates
  nMOS pull-down network
  pMOS pull-up network
  a.k.a. static CMOS
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Z (float) | 1
Pull-down ON | 0 | X (crowbar)

## Slide 13: Series and Parallel
nMOS: 1 = ON
pMOS: 0 = ON
Series: both must be ON
Parallel: either can be ON

## Slide 14: Conduction Complement
Complementary CMOS gates always produce 0 or 1
Ex: NAND gate
  Series nMOS: Y=0 when both inputs are 1
  Thus Y=1 when either input is 0
  Requires parallel pMOS
Rule of Conduction Complements
  Pull-up network is complement of pull-down
  Parallel -> series, series -> parallel

## Slide 15: Compound Gates
Compound gates can do any inverting function
Ex:

## Slide 16: Example: O3AI

## Slide 17: Example: O3AI

## Slide 18: Signal Strength
Strength of signal
  How close it approximates ideal voltage source
VDD and GND rails are strongest 1 and 0
nMOS pass strong 0
  But degraded or weak 1
pMOS pass strong 1
  But degraded or weak 0
Thus nMOS are best for pull-down network

## Slide 19: Pass Transistors
Transistors can be used as switches

## Slide 20: Pass Transistors
Transistors can be used as switches

## Slide 21: Transmission Gates
Pass transistors produce degraded outputs
Transmission gates pass both 0 and 1 well

## Slide 22: Transmission Gates
Pass transistors produce degraded outputs
Transmission gates pass both 0 and 1 well

## Slide 23: Tristates
Tristate buffer produces Z when not enabled
EN | A | Y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 24: Tristates
Tristate buffer produces Z when not enabled
EN | A | Y
0 | 0 | Z
0 | 1 | Z
1 | 0 | 0
1 | 1 | 1

## Slide 25: Nonrestoring Tristate
Transmission gate acts as tristate buffer
  Only two transistors
  But nonrestoring
    Noise on A is passed on to Y

## Slide 26: Tristate Inverter
Tristate inverter produces restored output
  Violates conduction complement rule
  Because we want a Z output

## Slide 27: Tristate Inverter
Tristate inverter produces restored output
  Violates conduction complement rule
  Because we want a Z output

## Slide 28: Multiplexers
2:1 multiplexer chooses between two inputs
S | D1 | D0 | Y
0 | X | 0 | 
0 | X | 1 | 
1 | 0 | X | 
1 | 1 | X | 

## Slide 29: Multiplexers
2:1 multiplexer chooses between two inputs
S | D1 | D0 | Y
0 | X | 0 | 0
0 | X | 1 | 1
1 | 0 | X | 0
1 | 1 | X | 1

## Slide 30: Gate-Level Mux Design
How many transistors are needed?

## Slide 31: Gate-Level Mux Design
How many transistors are needed? 20

## Slide 32: Transmission Gate Mux
Nonrestoring mux uses two transmission gates

## Slide 33: Transmission Gate Mux
Nonrestoring mux uses two transmission gates
  Only 4 transistors

## Slide 34: Inverting Mux
Inverting multiplexer
  Use compound AOI22
  Or pair of tristate inverters
  Essentially the same thing
Noninverting multiplexer adds an inverter

## Slide 35: 4:1 Multiplexer
4:1 mux chooses one of 4 inputs using two selects

## Slide 36: 4:1 Multiplexer
4:1 mux chooses one of 4 inputs using two selects
  Two levels of 2:1 muxes
  Or four tristates

## Slide 37: D Latch
When CLK = 1, latch is transparent
  D flows through to Q like a buffer
When CLK = 0, the latch is opaque
  Q holds its old value independent of D
a.k.a. transparent latch or level-sensitive latch

## Slide 38: D Latch Design
Multiplexer chooses D or old Q

## Slide 39: D Latch Operation

## Slide 40: D Flip-flop
When CLK rises, D is copied to Q
At all other times, Q holds its value
a.k.a. positive edge-triggered flip-flop, master-slave flip-flop

## Slide 41: D Flip-flop Design
Built from master and slave D latches

## Slide 42: D Flip-flop Operation

## Slide 43: Race Condition
Back-to-back flops can malfunction from clock skew
  Second flip-flop fires late
  Sees first flip-flop change and captures its result
  Called hold-time failure or race condition

## Slide 44: Nonoverlapping Clocks
Nonoverlapping clocks can prevent races
  As long as nonoverlap exceeds clock skew
We will use them in this class for safe design
  Industry manages skew more carefully instead

## Slide 45: Gate Layout
Layout can be very time consuming
  Design gates to fit together nicely
  Build a library of standard cells
Standard cell design methodology
  VDD and GND should abut (standard height)
  Adjacent gates should satisfy design rules
  nMOS at bottom and pMOS at top
  All gates include well and substrate contacts

## Slide 46: Example: Inverter

## Slide 47: Example: NAND3
Horizontal N-diffusion and p-diffusion strips
Vertical polysilicon gates
Metal1 VDD rail at top
Metal1 GND rail at bottom
32  by 40 

## Slide 48: Stick Diagrams
Stick diagrams help plan layout quickly
  Need not be to scale
  Draw with color pencils or dry-erase markers

## Slide 49: Wiring Tracks
A wiring track is the space required for a wire
  4  width, 4  spacing from neighbor = 8  pitch
Transistors also consume one wiring track

## Slide 50: Well spacing
Wells must surround transistors by 6 
  Implies 12  between opposite transistor flavors
  Leaves room for one wire track

## Slide 51: Area Estimation
Estimate area by counting wiring tracks
  Multiply by 8 to express in 

## Slide 52: Example: O3AI
Sketch a stick diagram for O3AI and estimate area

## Slide 53: Example: O3AI
Sketch a stick diagram for O3AI and estimate area

## Slide 54: Example: O3AI
Sketch a stick diagram for O3AI and estimate area