## Slide 1: Introduction to CMOS VLSI Design Lecture 11: Circuit Families
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Pseudo-nMOS Logic
Dynamic Logic
Pass Transistor Logic

## Slide 3: Introduction
What makes a circuit fast?
  I = C dV/dt -> tpd  (C/I) V
  low capacitance
  high current
  small swing
Logical effort is proportional to C/I
pMOS are the enemy!
  High capacitance for a given current
Can we take the pMOS capacitance off the input?
Various circuit families try to do this…

## Slide 4: Pseudo-nMOS
In the old days, nMOS processes had no pMOS
  Instead, use pull-up transistor that is always ON
In CMOS, use a pMOS that is always ON
  Ratio issue
  Make pMOS about ¼ effective strength of pulldown network

## Slide 5: Pseudo-nMOS Gates
Design for unit current on output
to compare with unit inverter.
pMOS fights nMOS

## Slide 6: Pseudo-nMOS Gates
Design for unit current on output
to compare with unit inverter.
pMOS fights nMOS

## Slide 7: Pseudo-nMOS Gates
Design for unit current on output
to compare with unit inverter.
pMOS fights nMOS

## Slide 8: Pseudo-nMOS Gates
Design for unit current on output
to compare with unit inverter.
pMOS fights nMOS

## Slide 9: Pseudo-nMOS Design
Ex: Design a k-input AND gate using pseudo-nMOS. Estimate the delay driving a fanout of H
G =
F =
P =
N =
D =

## Slide 10: Pseudo-nMOS Design
Ex: Design a k-input AND gate using pseudo-nMOS. Estimate the delay driving a fanout of H
G = 1 * 8/9 = 8/9
F = GBH = 8H/9
P = 1 + (4+8k)/9 = (8k+13)/9
N = 2
D = NF1/N + P =

## Slide 11: Pseudo-nMOS Power
Pseudo-nMOS draws power whenever Y = 0
  Called static power P = I•VDD
  A few mA / gate * 1M gates would be a problem
  This is why nMOS went extinct!
Use pseudo-nMOS sparingly for wide NORs
Turn off pMOS when not in use

## Slide 12: Dynamic Logic
Dynamic gates uses a clocked pMOS pullup
Two modes: precharge and evaluate

## Slide 13: The Foot
What if pulldown network is ON during precharge?
Use series evaluation transistor to prevent fight.

## Slide 14: Logical Effort

## Slide 15: Logical Effort

## Slide 16: Monotonicity
Dynamic gates require monotonically rising inputs during evaluation
  0 -> 0
  0 -> 1
  1 -> 1
  But not 1 -> 0

## Slide 17: Monotonicity Woes
But dynamic gates produce monotonically falling outputs during evaluation
Illegal for one dynamic gate to drive another!

## Slide 18: Monotonicity Woes
But dynamic gates produce monotonically falling outputs during evaluation
Illegal for one dynamic gate to drive another!

## Slide 19: Domino Gates
Follow dynamic stage with inverting static gate
  Dynamic / static pair is called domino gate
  Produces monotonic outputs

## Slide 20: Domino Optimizations
Each domino gate triggers next one, like a string of dominos toppling over
Gates evaluate sequentially but precharge in parallel
Thus evaluation is more critical than precharge
HI-skewed static stages can perform logic

## Slide 21: Dual-Rail Domino
Domino only performs noninverting functions:
  AND, OR but not NAND, NOR, or XOR
Dual-rail domino solves this problem
  Takes true and complementary inputs
  Produces true and complementary outputs
sig_h | sig_l | Meaning
0 | 0 | Precharged
0 | 1 | ‘0’
1 | 0 | ‘1’
1 | 1 | invalid

## Slide 22: Example: AND/NAND
Given A_h, A_l, B_h, B_l
Compute Y_h = A * B, Y_l = ~(A * B)

## Slide 23: Example: AND/NAND
Given A_h, A_l, B_h, B_l
Compute Y_h = A * B, Y_l = ~(A * B)
Pulldown networks are conduction complements

## Slide 24: Example: XOR/XNOR
Sometimes possible to share transistors

## Slide 25: Leakage
Dynamic node floats high during evaluation
  Transistors are leaky (IOFF  0)
  Dynamic value will leak away over time
  Formerly miliseconds, now nanoseconds!
Use keeper to hold dynamic node
  Must be weak enough not to fight evaluation

## Slide 26: Charge Sharing
Dynamic gates suffer from charge sharing

## Slide 27: Charge Sharing
Dynamic gates suffer from charge sharing

## Slide 28: Charge Sharing
Dynamic gates suffer from charge sharing

## Slide 29: Secondary Precharge
Solution: add secondary precharge transistors
  Typically need to precharge every other node
Big load capacitance CY helps as well

## Slide 30: Noise Sensitivity
Dynamic gates are very sensitive to noise
  Inputs: VIH  Vtn
  Outputs: floating output susceptible noise
Noise sources
  Capacitive crosstalk
  Charge sharing
  Power supply noise
  Feedthrough noise
  And more!

## Slide 31: Domino Summary
Domino logic is attractive for high-speed circuits
  1.5 – 2x faster than static CMOS
  But many challenges:
    Monotonicity
    Leakage
    Charge sharing
    Noise
Widely used in high-performance microprocessors

## Slide 32: Pass Transistor Circuits
Use pass transistors like switches to do logic
Inputs drive diffusion terminals as well as gates
CMOS + Transmission Gates:
  2-input multiplexer
  Gates should be restoring

## Slide 33: LEAP
LEAn integration with Pass transistors
Get rid of pMOS transistors
  Use weak pMOS feedback to pull fully high
  Ratio constraint

## Slide 34: CPL
Complementary Pass-transistor Logic
  Dual-rail form of pass transistor logic
  Avoids need for ratioed feedback
  Optional cross-coupling for rail-to-rail swing