## Slide 1: Introduction to CMOS VLSI Design Lecture 14: Wires
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Introduction
Wire Resistance
Wire Capacitance
Wire RC Delay
Crosstalk
Wire Engineering
Repeaters

## Slide 3: Introduction
Chips are mostly made of wires called interconnect
  In stick diagram, wires set size
  Transistors are little things under the wires
  Many layers of wires
Wires are as important as transistors
  Speed
  Power
  Noise
Alternating layers run orthogonally

## Slide 4: Wire Geometry
Pitch = w + s
Aspect ratio: AR = t/w
  Old processes had AR << 1
  Modern processes have AR  2
    Pack in many skinny wires

## Slide 5: Layer Stack
AMI 0.6 m process has 3 metal layers
Modern processes use 6-10+ metal layers
Example:
  Intel 180 nm process
M1: thin, narrow (< 3)
  High density cells
M2-M4: thicker
  For longer wires
M5-M6: thickest
  For VDD, GND, clk

## Slide 6: Wire Resistance
 = resistivity (*m)

## Slide 7: Wire Resistance
 = resistivity (*m)

## Slide 8: Wire Resistance
 = resistivity (*m)
R = sheet resistance (/)
   is a dimensionless unit(!)
Count number of squares
  R = R * (# of squares)

## Slide 9: Choice of Metals
Until 180 nm generation, most wires were aluminum
Modern processes often use copper
  Cu atoms diffuse into silicon and damage FETs
  Must be surrounded by a diffusion barrier
Metal | Bulk resistivity (*cm)
Silver (Ag) | 1.6
Copper (Cu) | 1.7
Gold (Au) | 2.2
Aluminum (Al) | 2.8
Tungsten (W) | 5.3
Molybdenum (Mo) | 5.3

## Slide 10: Sheet Resistance
Typical sheet resistances in 180 nm process
Layer | Sheet Resistance (/)
Diffusion (silicided) | 3-10
Diffusion (no silicide) | 50-200
Polysilicon (silicided) | 3-10
Polysilicon (no silicide) | 50-400
Metal1 | 0.08
Metal2 | 0.05
Metal3 | 0.05
Metal4 | 0.03
Metal5 | 0.02
Metal6 | 0.02

## Slide 11: Contacts Resistance
Contacts and vias also have 2-20 
Use many contacts for lower R
  Many small contacts for current crowding around periphery

## Slide 12: Wire Capacitance
Wire has capacitance per unit length
  To neighbors
  To layers above and below
Ctotal = Ctop + Cbot + 2Cadj

## Slide 13: Capacitance Trends
Parallel plate equation: C = A/d
  Wires are not parallel plates, but obey trends
  Increasing area (W, t) increases capacitance
  Increasing distance (s, h) decreases capacitance
Dielectric constant
  = k0
0 = 8.85 x 10-14 F/cm
k = 3.9 for SiO2
Processes are starting to use low-k dielectrics
  k  3 (or less) as dielectrics use air pockets

## Slide 14: M2 Capacitance Data
Typical wires have ~ 0.2 fF/m
  Compare to 2 fF/m for gate capacitance

## Slide 15: Diffusion & Polysilicon
Diffusion capacitance is very high (about 2 fF/m)
  Comparable to gate capacitance
  Diffusion also has high resistance
  Avoid using diffusion runners for wires!
Polysilicon has lower C but high R
  Use for transistor gates
  Occasionally for very short wires between gates

## Slide 16: Lumped Element Models
Wires are a distributed system
  Approximate with lumped element models
3-segment -model is accurate to 3% in simulation
L-model needs 100 segments for same accuracy!
Use single segment -model for Elmore delay

## Slide 17: Example
Metal2 wire in 180 nm process
  5 mm long
  0.32 m wide
Construct a 3-segment -model
  R =
  Cpermicron =

## Slide 18: Example
Metal2 wire in 180 nm process
  5 mm long
  0.32 m wide
Construct a 3-segment -model
  R = 0.05 / => R = 781 
  Cpermicron = 0.2 fF/m => C = 1 pF

## Slide 19: Wire RC Delay
Estimate the delay of a 10x inverter driving a 2x inverter at the end of the 5mm wire from the previous example.
  R = 2.5 k*m for gates
  Unit inverter: 0.36 m nMOS, 0.72 m pMOS
  tpd =

## Slide 20: Wire RC Delay
Estimate the delay of a 10x inverter driving a 2x inverter at the end of the 5mm wire from the previous example.
  R = 2.5 k*m for gates
  Unit inverter: 0.36 m nMOS, 0.72 m pMOS
  tpd = 1.1 ns

## Slide 21: Crosstalk
A capacitor does not like to change its voltage instantaneously.
A wire has high capacitance to its neighbor.
  When the neighbor switches from 1-> 0 or 0->1, the wire tends to switch too.
  Called capacitive coupling or crosstalk.
Crosstalk effects
  Noise on nonswitching wires
  Increased delay on switching wires

## Slide 22: Crosstalk Delay
Assume layers above and below on average are quiet
  Second terminal of capacitor can be ignored
  Model as Cgnd = Ctop + Cbot
Effective Cadj depends on behavior of neighbors
  Miller effect
B | V | Ceff(A) | MCF
Constant |  |  | 
Switching with A |  |  | 
Switching opposite A |  |  | 

## Slide 23: Crosstalk Delay
Assume layers above and below on average are quiet
  Second terminal of capacitor can be ignored
  Model as Cgnd = Ctop + Cbot
Effective Cadj depends on behavior of neighbors
  Miller effect
B | V | Ceff(A) | MCF
Constant | VDD | Cgnd + Cadj | 1
Switching with A | 0 | Cgnd | 0
Switching opposite A | 2VDD | Cgnd + 2 Cadj | 2

## Slide 24: Crosstalk Noise
Crosstalk causes noise on nonswitching wires
If victim is floating:
  model as capacitive voltage divider

## Slide 25: Driven Victims
Usually victim is driven by a gate that fights noise
  Noise depends on relative resistances
  Victim driver is in linear region, agg. in saturation
  If sizes are same, Raggressor = 2-4 x Rvictim

## Slide 26: Coupling Waveforms
Simulated coupling for Cadj = Cvictim

## Slide 27: Noise Implications
So what if we have noise?
If the noise is less than the noise margin, nothing happens
Static CMOS logic will eventually settle to correct output even if disturbed by large noise spikes
  But glitches cause extra delay
  Also cause extra power from false transitions
Dynamic logic never recovers from glitches
Memories and other sensitive circuits also can produce the wrong answer

## Slide 28: Wire Engineering
Goal: achieve delay, area, power goals with acceptable noise
Degrees of freedom:

## Slide 29: Wire Engineering
Goal: achieve delay, area, power goals with acceptable noise
Degrees of freedom:
  Width
  Spacing

## Slide 30: Wire Engineering
Goal: achieve delay, area, power goals with acceptable noise
Degrees of freedom:
  Width
  Spacing
  Layer

## Slide 31: Wire Engineering
Goal: achieve delay, area, power goals with acceptable noise
Degrees of freedom:
  Width
  Spacing
  Layer
  Shielding

## Slide 32: Repeaters
R and C are proportional to l
RC delay is proportional to l2
  Unacceptably great for long wires

## Slide 33: Repeaters
R and C are proportional to l
RC delay is proportional to l2
  Unacceptably great for long wires
Break long wires into N shorter segments
  Drive each one with an inverter or buffer

## Slide 34: Repeater Design
How many repeaters should we use?
How large should each one be?
Equivalent Circuit
  Wire length l/N
    Wire Capaitance Cw*l/N, Resistance Rw*l/N
  Inverter width W (nMOS = W, pMOS = 2W)
    Gate Capacitance C’*W, Resistance R/W

## Slide 35: Repeater Design
How many repeaters should we use?
How large should each one be?
Equivalent Circuit
  Wire length l
    Wire Capacitance Cw*l, Resistance Rw*l
  Inverter width W (nMOS = W, pMOS = 2W)
    Gate Capacitance C’*W, Resistance R/W

## Slide 36: Repeater Results
Write equation for Elmore Delay
  Differentiate with respect to W and N
  Set equal to 0, solve
~60-80 ps/mm
in 180 nm process