## Slide 1: Introduction to CMOS VLSI Design Lecture 15: Adders
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Single-bit Addition
Carry-Ripple Adder
Carry-Skip Adder
Carry-Lookahead Adder
Carry-Select Adder
Carry-Increment Adder
Tree Adder

## Slide 3: Single-Bit Addition
Half Adder Full Adder
A | B | Cout | S
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
A | B | C | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 4: Single-Bit Addition
Half Adder Full Adder
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | C | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 5: PGK
For a full adder, define what happens to carries
  Generate: Cout = 1 independent of C
    G =
  Propagate: Cout = C
    P =
  Kill: Cout = 0 independent of C
    K =

## Slide 6: PGK
For a full adder, define what happens to carries
  Generate: Cout = 1 independent of C
    G = A • B
  Propagate: Cout = C
    P = A  B
  Kill: Cout = 0 independent of C
    K = ~A • ~B

## Slide 7: Full Adder Design I
Brute force implementation from eqns

## Slide 8: Full Adder Design II
Factor S in terms of Cout
S = ABC + (A + B + C)(~Cout)
Critical path is usually C to Cout in ripple adder

## Slide 9: Layout
Clever layout circumvents usual line of diffusion
  Use wide transistors on critical path
  Eliminate output inverters

## Slide 10: Full Adder Design III
Complementary Pass Transistor Logic (CPL)
  Slightly faster, but more area

## Slide 11: Full Adder Design IV
Dual-rail domino
  Very fast, but large and power hungry
  Used in very fast multipliers

## Slide 12: Carry Propagate Adders
N-bit adder called CPA
  Each sum bit depends on all previous carries
  How do we compute all these carries quickly?

## Slide 13: Carry-Ripple Adder
Simplest design: cascade full adders
  Critical path goes from Cin to Cout
  Design full adder to have fast carry delay

## Slide 14: Inversions
Critical path passes through majority gate
  Built from minority + inverter
  Eliminate inverter and use inverting full adder

## Slide 15: Generate / Propagate
Equations often factored into G and P
Generate and propagate for groups spanning i:j
Base case
Sum:

## Slide 16: Generate / Propagate
Equations often factored into G and P
Generate and propagate for groups spanning i:j
Base case
Sum:

## Slide 17: PG Logic

## Slide 18: Carry-Ripple Revisited

## Slide 19: Carry-Ripple PG Diagram

## Slide 20: Carry-Ripple PG Diagram

## Slide 21: PG Diagram Notation

## Slide 22: Carry-Skip Adder
Carry-ripple is slow through all N stages
Carry-skip allows carry to skip over groups of n bits
  Decision based on n-bit propagate signal

## Slide 23: Carry-Skip PG Diagram
For k n-bit groups (N = nk)

## Slide 24: Carry-Skip PG Diagram
For k n-bit groups (N = nk)

## Slide 25: Variable Group Size
Delay grows as O(sqrt(N))

## Slide 26: Carry-Lookahead Adder
Carry-lookahead adder computes Gi:0 for many bits in parallel.
Uses higher-valency cells with more than two inputs.

## Slide 27: CLA PG Diagram

## Slide 28: Higher-Valency Cells

## Slide 29: Carry-Select Adder
Trick for critical paths dependent on late input X
  Precompute two possible outputs for X = 0, 1
  Select proper output when X arrives
Carry-select adder precomputes n-bit sums
  For both possible carries into n-bit group

## Slide 30: Carry-Increment Adder
Factor initial PG and final XOR out of carry-select

## Slide 31: Carry-Increment Adder
Factor initial PG and final XOR out of carry-select

## Slide 32: Variable Group Size
Also buffer
noncritical
signals

## Slide 33: Tree Adder
If lookahead is good, lookahead across lookahead!
  Recursive lookahead gives O(log N) delay
Many variations on tree adders

## Slide 34: Brent-Kung

## Slide 35: Sklansky

## Slide 36: Kogge-Stone

## Slide 37: Tree Adder Taxonomy
Ideal N-bit tree adder would have
  L = log N logic levels
  Fanout never exceeding 2
  No more than one wiring track between levels
Describe adder with 3-D taxonomy (l, f, t)
  Logic levels: L + l
  Fanout: 2f + 1
  Wiring tracks: 2t
Known tree adders sit on plane defined by
l + f + t = L-1

## Slide 38: Tree Adder Taxonomy

## Slide 39: Tree Adder Taxonomy

## Slide 40: Han-Carlson

## Slide 41: Knowles [2, 1, 1, 1]

## Slide 42: Ladner-Fischer

## Slide 43: Taxonomy Revisited

## Slide 44: Summary
Architecture | Classification | Logic Levels | Max Fanout | Tracks | Cells
Carry-Ripple |  | N-1 | 1 | 1 | N
Carry-Skip n=4 |  | N/4 + 5 | 2 | 1 | 1.25N
Carry-Inc. n=4 |  | N/4 + 2 | 4 | 1 | 2N
Brent-Kung | (L-1, 0, 0) | 2log2N – 1 | 2 | 1 | 2N
Sklansky | (0, L-1, 0) | log2N | N/2 + 1 | 1 | 0.5 Nlog2N
Kogge-Stone | (0, 0, L-1) | log2N | 2 | N/2 | Nlog2N
Adder architectures offer area / power / delay tradeoffs.
Choose the best one for your application.