## Slide 1: Introduction to CMOS VLSI Design Lecture 16: Datapath Functional Units
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Comparators
Shifters
Multi-input Adders
Multipliers

## Slide 3: Comparators
0’s detector: A = 00…000
1’s detector: A = 11…111
Equality comparator: A = B
Magnitude comparator: A < B

## Slide 4: 1’s & 0’s Detectors
1’s detector: N-input AND gate
0’s detector: NOTs + 1’s detector (N-input NOR)

## Slide 5: Equality Comparator
Check if each bit is equal (XNOR, aka equality gate)
1’s detect on bitwise equality

## Slide 6: Magnitude Comparator
Compute B-A and look at sign
B-A = B + ~A + 1
For unsigned numbers, carry out is sign bit

## Slide 7: Signed vs. Unsigned
For signed numbers, comparison is harder
  C: carry out
  Z: zero (all bits of A-B are 0)
  N: negative (MSB of result)
  V: overflow (inputs had different signs, output sign  B)

## Slide 8: Shifters
Logical Shift:
  Shifts number left or right and fills with 0’s
    1011 LSR 1 = ____ 1011 LSL1 = ____
Arithmetic Shift:
  Shifts number left or right. Rt shift sign extends
    1011 ASR1 = ____ 1011 ASL1 = ____
Rotate:
  Shifts number left or right and fills with lost bits
    1011 ROR1 = ____ 1011 ROL1 = ____

## Slide 9: Shifters
Logical Shift:
  Shifts number left or right and fills with 0’s
    1011 LSR 1 = 0101 1011 LSL1 = 0110
Arithmetic Shift:
  Shifts number left or right. Rt shift sign extends
    1011 ASR1 = 1101 1011 ASL1 = 0110
Rotate:
  Shifts number left or right and fills with lost bits
    1011 ROR1 = 1101 1011 ROL1 = 0111

## Slide 10: Funnel Shifter
A funnel shifter can do all six types of shifts
Selects N-bit field Y from 2N-bit input
  Shift by k bits (0  k < N)

## Slide 11: Funnel Shifter Operation
Computing N-k requires an adder

## Slide 12: Funnel Shifter Operation
Computing N-k requires an adder

## Slide 13: Funnel Shifter Operation
Computing N-k requires an adder

## Slide 14: Funnel Shifter Operation
Computing N-k requires an adder

## Slide 15: Funnel Shifter Operation
Computing N-k requires an adder

## Slide 16: Simplified Funnel Shifter
Optimize down to 2N-1 bit input

## Slide 17: Simplified Funnel Shifter
Optimize down to 2N-1 bit input

## Slide 18: Simplified Funnel Shifter
Optimize down to 2N-1 bit input

## Slide 19: Simplified Funnel Shifter
Optimize down to 2N-1 bit input

## Slide 20: Simplified Funnel Shifter
Optimize down to 2N-1 bit input

## Slide 21: Funnel Shifter Design 1
N N-input multiplexers
  Use 1-of-N hot select signals for shift amount
  nMOS pass transistor design (Vt drops!)

## Slide 22: Funnel Shifter Design 2
Log N stages of 2-input muxes
  No select decoding needed

## Slide 23: Multi-input Adders
Suppose we want to add k N-bit words
  Ex: 0001 + 0111 + 1101 + 0010 = _____

## Slide 24: Multi-input Adders
Suppose we want to add k N-bit words
  Ex: 0001 + 0111 + 1101 + 0010 = 10111

## Slide 25: Multi-input Adders
Suppose we want to add k N-bit words
  Ex: 0001 + 0111 + 1101 + 0010 = 10111
Straightforward solution: k-1 N-input CPAs
  Large and slow

## Slide 26: Carry Save Addition
A full adder sums 3 inputs and produces 2 outputs
  Carry output has twice weight of sum output
N full adders in parallel are called carry save adder
  Produce N sums and N carry outs

## Slide 27: CSA Application
Use k-2 stages of CSAs
  Keep result in carry-save redundant form
Final CPA computes actual result

## Slide 28: CSA Application
Use k-2 stages of CSAs
  Keep result in carry-save redundant form
Final CPA computes actual result

## Slide 29: CSA Application
Use k-2 stages of CSAs
  Keep result in carry-save redundant form
Final CPA computes actual result

## Slide 30: Multiplication
Example:

## Slide 31: Multiplication
Example:

## Slide 32: Multiplication
Example:

## Slide 33: Multiplication
Example:

## Slide 34: Multiplication
Example:

## Slide 35: Multiplication
Example:

## Slide 36: Multiplication
Example:
M x N-bit multiplication
  Produce N M-bit partial products
  Sum these to produce M+N-bit product

## Slide 37: General Form
Multiplicand: Y = (yM-1, yM-2, …, y1, y0)
Multiplier: X = (xN-1, xN-2, …, x1, x0)
Product:

## Slide 38: Dot Diagram
Each dot represents a bit

## Slide 39: Array Multiplier

## Slide 40: Rectangular Array
Squash array to fit rectangular floorplan

## Slide 41: Fewer Partial Products
Array multiplier requires N partial products
If we looked at groups of r bits, we could form N/r partial products.
  Faster and smaller?
  Called radix-2r encoding
Ex: r = 2: look at pairs of bits
  Form partial products of 0, Y, 2Y, 3Y
  First three are easy, but 3Y requires adder 

## Slide 42: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 43: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 44: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 45: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 46: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 47: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 48: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 49: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in next partial product

## Slide 50: Booth Hardware
Booth encoder generates control lines for each PP
  Booth selectors choose PP bits

## Slide 51: Sign Extension
Partial products can be negative
  Require sign extension, which is cumbersome
  High fanout on most significant bit

## Slide 52: Simplified Sign Ext.
Sign bits are either all 0’s or all 1’s
  Note that all 0’s is all 1’s + 1 in proper column
  Use this to reduce loading on MSB

## Slide 53: Even Simpler Sign Ext.
No need to add all the 1’s in hardware
  Precompute the answer!

## Slide 54: Advanced Multiplication
Signed vs. unsigned inputs
Higher radix Booth encoding
Array vs. tree CSA networks