## Slide 1: Introduction to CMOS VLSI Design Lecture 22: Circuit Pitfalls
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Circuit Pitfalls
  Detective puzzle
  Given circuit and symptom, diagnose cause and recommend solution
  All these pitfalls have caused failures in real chips
Noise Budgets
Reliability

## Slide 3: Bad Circuit 1
Circuit
  2:1 multiplexer
Symptom
  Mux works when selected D is 0 but not 1.
  Or fails at low VDD.
  Or fails in SFSF corner.
Principle:
Solution:

## Slide 4: Bad Circuit 1
Circuit
  2:1 multiplexer
Symptom
  Mux works when selected D is 0 but not 1.
  Or fails at low VDD.
  Or fails in SFSF corner.
Principle: Threshold drop
  X never rises above VDD-Vt
  Vt is raised by the body effect
  The threshold drop is most serious as Vt becomes a greater fraction of VDD.
Solution:

## Slide 5: Bad Circuit 1
Circuit
  2:1 multiplexer
Symptom
  Mux works when selected D is 0 but not 1.
  Or fails at low VDD.
  Or fails in SFSF corner.
Principle: Threshold drop
  X never rises above VDD-Vt
  Vt is raised by the body effect
  The threshold drop is most serious as Vt becomes a greater fraction of VDD.
Solution: Use transmission gates, not pass transistors

## Slide 6: Bad Circuit 2
Circuit
  Latch
Symptom
  Load a 0 into Q
  Set  = 0
  Eventually Q spontaneously flips to 1
Principle:
Solution:

## Slide 7: Bad Circuit 2
Circuit
  Latch
Symptom
  Load a 0 into Q
  Set  = 0
  Eventually Q spontaneously flips to 1
Principle: Leakage
  X is a dynamic node holding value as charge on the node
  Eventually subthreshold leakage may disturb charge
Solution:

## Slide 8: Bad Circuit 2
Circuit
  Latch
Symptom
  Load a 0 into Q
  Set  = 0
  Eventually Q spontaneously flips to 1
Principle: Leakage
  X is a dynamic node holding value as charge on the node
  Eventually subthreshold leakage may disturb charge
Solution: Staticize node with feedback
  Or periodically refresh node (requires fast clock,
  not practical processes with big leakage)

## Slide 9: Bad Circuit 3
Circuit
  Domino AND gate
Symptom
  Precharge gate (Y=0)
  Then evaluate
  Eventually Y spontaneously flips to 1
Principle:
Solution:

## Slide 10: Bad Circuit 3
Circuit
  Domino AND gate
Symptom
  Precharge gate (Y=0)
  Then evaluate
  Eventually Y spontaneously flips to 1
Principle: Leakage
  X is a dynamic node holding value as charge on the node
  Eventually subthreshold leakage may disturb charge
Solution:

## Slide 11: Bad Circuit 3
Circuit
  Domino AND gate
Symptom
  Precharge gate (Y=0)
  Then evaluate
  Eventually Y spontaneously flips to 1
Principle: Leakage
  X is a dynamic node holding value as charge on the node
  Eventually subthreshold leakage may disturb charge
Solution: Keeper

## Slide 12: Bad Circuit 4
Circuit
  Pseudo-nMOS OR
Symptom
  When only one input is true, Y = 0.
  Perhaps only happens in SF corner.
Principle:
Solution:

## Slide 13: Bad Circuit 4
Circuit
  Pseudo-nMOS OR
Symptom
  When only one input is true, Y = 0.
  Perhaps only happens in SF corner.
Principle: Ratio Failure
  nMOS and pMOS fight each other.
  If the pMOS is too strong, nMOS cannot pull X low enough.
Solution:

## Slide 14: Bad Circuit 4
Circuit
  Pseudo-nMOS OR
Symptom
  When only one input is true, Y = 0.
  Perhaps only happens in SF corner.
Principle: Ratio Failure
  nMOS and pMOS fight each other.
  If the pMOS is too strong, nMOS cannot pull X low enough.
Solution: Check that ratio is satisfied in all corners

## Slide 15: Bad Circuit 5
Circuit
  Latch
Symptom
  Q stuck at 1.
  May only happen for certain latches where input is driven by a small gate located far away.
Principle:
Solutions:

## Slide 16: Bad Circuit 5
Circuit
  Latch
Symptom
  Q stuck at 1.
  May only happen for certain latches where input is driven by a small gate located far away.
Principle: Ratio Failure (again)
  Series resistance of D driver, wire
  resistance, and tgate must be much
  less than weak feedback inverter.
Solutions:

## Slide 17: Bad Circuit 5
Circuit
  Latch
Symptom
  Q stuck at 1.
  May only happen for certain latches where input is driven by a small gate located far away.
Principle: Ratio Failure (again)
  Series resistance of D driver, wire
  resistance, and tgate must be much
  less than weak feedback inverter.
Solutions: Check relative strengths
  Avoid unbuffered diffusion inputs where driver is unknown

## Slide 18: Bad Circuit 6
Circuit
  Domino AND gate
Symptom
  Precharge gate while
  A = B = 0, so Z = 0
  Set  = 1
  A rises
  Z is observed to sometimes rise
Principle:
Solutions:

## Slide 19: Bad Circuit 6
Circuit
  Domino AND gate
Symptom
  Precharge gate while
  A = B = 0, so Z = 0
  Set  = 1
  A rises
  Z is observed to sometimes rise
Principle: Charge Sharing
  If X was low, it shares charge with Y
Solutions:

## Slide 20: Bad Circuit 6
Circuit
  Domino AND gate
Symptom
  Precharge gate while
  A = B = 0, so Z = 0
  Set  = 1
  A rises
  Z is observed to sometimes rise
Principle: Charge Sharing
  If X was low, it shares charge with Y
Solutions: Limit charge sharing
  Safe if CY >> CX
  Or precharge node X too

## Slide 21: Bad Circuit 7
Circuit
  Dynamic gate + latch
Symptom
  Precharge gate while transmission gate latch is opaque
  Evaluate
  When latch becomes transparent, X falls
Principle:
Solution:

## Slide 22: Bad Circuit 7
Circuit
  Dynamic gate + latch
Symptom
  Precharge gate while transmission gate latch is opaque
  Evaluate
  When latch becomes transparent, X falls
Principle: Charge Sharing
  If Y was low, it shares charge with X
Solution:

## Slide 23: Bad Circuit 7
Circuit
  Dynamic gate + latch
Symptom
  Precharge gate while transmission gate latch is opaque
  Evaluate
  When latch becomes transparent, X falls
Principle: Charge Sharing
  If Y was low, it shares charge with X
Solution: Buffer dynamic nodes before
  driving transmission gate

## Slide 24: Bad Circuit 8
Circuit
  Latch
Symptom
  Q changes while latch is opaque
  Especially if D comes from a far-away driver
Principle:
Solution:

## Slide 25: Bad Circuit 8
Circuit
  Latch
Symptom
  Q changes while latch is opaque
  Especially if D comes from a far-away driver
Principle: Diffusion Input Noise Sensitivity
  If D < -Vt, transmission gate turns on
  Most likely because of power supply noise or coupling on D
Solution:

## Slide 26: Bad Circuit 8
Circuit
  Latch
Symptom
  Q changes while latch is opaque
  Especially if D comes from a far-away driver
Principle: Diffusion Input Noise Sensitivity
  If D < -Vt, transmission gate turns on
  Most likely because of power supply noise or coupling on D
Solution: Buffer D locally

## Slide 27: Bad Circuit 9
Circuit
  Anything
Symptom
  Some gates are slower than expected
Principle:

## Slide 28: Bad Circuit 9
Circuit
  Anything
Symptom
  Some gates are slower than expected
Principle: Hot Spots and Power Supply Noise

## Slide 29: Noise
Sources
  Power supply noise / ground bounce
  Capacitive coupling
  Charge sharing
  Leakage
  Noise feedthrough
Consequences
  Increased delay (for noise to settle out)
  Or incorrect computations

## Slide 30: Reliability
Hard Errors
Soft Errors

## Slide 31: Electromigration
“Electron wind” causes movement of metal atoms along wires
Excessive electromigration leads to open circuits
Most significant for unidirectional (DC) current
  Depends on current density Jdc (current / area)
  Exponential dependence on temperature
  Black’s Equation:
  Typical limits: Jdc < 1 – 2 mA / m2
See videos

## Slide 32: Self-Heating
Current through wire resistance generates heat
  Oxide surrounding wires is a thermal insulator
  Heat tends to build up in wires
  Hotter wires are more resistive, slower
Self-heating limits AC current densities for reliability
  Typical limits: Jrms < 15 mA / m2

## Slide 33: Hot Carriers
Electric fields across channel impart high energies to some carriers
  These “hot” carriers may be blasted into the gate oxide where they become trapped
  Accumulation of charge in oxide causes shift in Vt over time
  Eventually Vt shifts too far for devices to operate correctly
Choose VDD to achieve reasonable product lifetime
  Worst problems for inverters and NORs with slow input risetime and long propagation delays

## Slide 34: Latchup
Latchup: positive feedback leading to VDD – GND short
  Major problem for 1970’s CMOS processes before
  it was well understood
Avoid by minimizing resistance of body to GND / VDD
  Use plenty of substrate and well taps

## Slide 35: Guard Rings
Latchup risk greatest when diffusion-to-substrate diodes could become forward-biased
Surround sensitive region with guard ring to collect injected charge

## Slide 36: Overvoltage
High voltages can damage transistors
  Electrostatic discharge
  Oxide arcing
  Punchthrough
  Time-dependent dielectric breakdown (TDDB)
    Accumulated wear from tunneling currents
Requires low VDD for thin oxides and short channels
Use ESD protection structures where chip meets real world

## Slide 37: Soft Errors
In 1970’s, DRAMs were observed to occasionally flip bits for no apparent reason
  Ultimately linked to alpha particles and cosmic rays
Collisions with particles create electron-hole pairs in substrate
  These carriers are collected on dynamic nodes, disturbing the voltage
Minimize soft errors by having plenty of charge on dynamic nodes
Tolerate errors through ECC, redundancy

## Slide 38: Summary
Static CMOS gates are very robust
  Will settle to correct value if you wait long enough
Other circuits suffer from a variety of pitfalls
  Tradeoff between performance & robustness
Very important to check circuits for pitfalls
  For large chips, you need an automatic checker.
  Design rules aren’t worth the paper they are printed on unless you back them up with a tool.