## Slide 1: Introduction to CMOS VLSI Design Lecture 23: Scaling and Economics
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Scaling
  Transistors
  Interconnect
  Future Challenges
VLSI Economics

## Slide 3: Moore’s Law
In 1965, Gordon Moore predicted the exponential growth of the number of transistors on an IC
Transistor count doubled
every year since invention
Predicted > 65,000
transistors by 1975!
Growth limited by power
[Moore65]

## Slide 4: More Moore
Transistor counts have doubled every 26 months for the past three decades.

## Slide 5: Speed Improvement
Clock frequencies have also increased exponentially
  A corollary of Moore’s Law

## Slide 6: Why?
Why more transistors per IC?
Why faster computers?

## Slide 7: Why?
Why more transistors per IC?
  Smaller transistors
  Larger dice
Why faster computers?

## Slide 8: Why?
Why more transistors per IC?
  Smaller transistors
  Larger dice
Why faster computers?
  Smaller, faster transistors
  Better microarchitecture (more IPC)
  Fewer gate delays per cycle

## Slide 9: Scaling
The only constant in VLSI is constant change
Feature size shrinks by 30% every 2-3 years
  Transistors become cheaper
  Transistors become faster
  Wires do not improve
  (and may get worse)
Scale factor S
  Typically
  Technology nodes

## Slide 10: Scaling Assumptions
What changes between technology nodes?
Constant Field Scaling
  All dimensions (x, y, z => W, L, tox)
  Voltage (VDD)
  Doping levels
Lateral Scaling
  Only gate length L
  Often done as a quick gate shrink (S = 1.05)

## Slide 11: Device Scaling

## Slide 12: Device Scaling

## Slide 13: Device Scaling

## Slide 14: Device Scaling

## Slide 15: Device Scaling

## Slide 16: Device Scaling

## Slide 17: Device Scaling

## Slide 18: Device Scaling

## Slide 19: Device Scaling

## Slide 20: Device Scaling

## Slide 21: Device Scaling

## Slide 22: Device Scaling

## Slide 23: Observations
Gate capacitance per micron is nearly independent of process
But ON resistance * micron improves with process
Gates get faster with scaling (good)
Dynamic power goes down with scaling (good)
Current density goes up with scaling (bad)
Velocity saturation makes lateral scaling unsustainable

## Slide 24: Example
Gate capacitance is typically about 2 fF/m
The FO4 inverter delay in the TT corner for a process of feature size f (in nm) is about 0.5f ps
Estimate the ON resistance of a unit (4/2 ) transistor.

## Slide 25: Solution
Gate capacitance is typically about 2 fF/m
The FO4 inverter delay in the TT corner for a process of feature size f (in nm) is about 0.5f ps
Estimate the ON resistance of a unit (4/2 ) transistor.
FO4 = 5  = 15 RC
RC = (0.5f) / 15 = (f/30) ps/nm
If W = 2f, R = 8.33 k
  Unit resistance is roughly independent of f

## Slide 26: Scaling Assumptions
Wire thickness
  Hold constant vs. reduce in thickness
Wire length
  Local / scaled interconnect
  Global interconnect
    Die size scaled by Dc  1.1

## Slide 27: Interconnect Scaling

## Slide 28: Interconnect Scaling

## Slide 29: Interconnect Scaling

## Slide 30: Interconnect Scaling

## Slide 31: Interconnect Scaling

## Slide 32: Interconnect Scaling

## Slide 33: Interconnect Scaling

## Slide 34: Interconnect Scaling

## Slide 35: Interconnect Scaling

## Slide 36: Interconnect Delay

## Slide 37: Interconnect Delay

## Slide 38: Interconnect Delay

## Slide 39: Interconnect Delay

## Slide 40: Interconnect Delay

## Slide 41: Interconnect Delay

## Slide 42: Interconnect Delay

## Slide 43: Observations
Capacitance per micron is remaining constant
  About 0.2 fF/m
  Roughly 1/10 of gate capacitance
Local wires are getting faster
  Not quite tracking transistor improvement
  But not a major problem
Global wires are getting slower
  No longer possible to cross chip in one cycle

## Slide 44: ITRS
Semiconductor Industry Association forecast
  Intl. Technology Roadmap for Semiconductors

## Slide 45: Scaling Implications
Improved Performance
Improved Cost
Interconnect Woes
Power Woes
Productivity Challenges
Physical Limits

## Slide 46: Cost Improvement
In 2003, $0.01 bought you 100,000 transistors
  Moore’s Law is still going strong
[Moore03]

## Slide 47: Interconnect Woes
SIA made a gloomy forecast in 1997
  Delay would reach minimum at 250 – 180 nm, then get worse because of wires
But…
[SIA97]

## Slide 48: Interconnect Woes
SIA made a gloomy forecast in 1997
  Delay would reach minimum at 250 – 180 nm, then get worse because of wires
But…
  Misleading scale
  Global wires
100 kgate blocks ok

## Slide 49: Reachable Radius
We can’t send a signal across a large fast chip in one cycle anymore
But the microarchitect can plan around this
  Just as off-chip memory latencies were tolerated

## Slide 50: Dynamic Power
Intel VP Patrick Gelsinger (ISSCC 2001)
  If scaling continues at present pace, by 2005, high speed processors would have power density of nuclear reactor, by 2010, a rocket nozzle, and by 2015, surface of sun.
  “Business as usual will not work in the future.”
Intel stock dropped 8%
on the next day
But attention to power is
increasing
[Moore03]

## Slide 51: Static Power
VDD decreases
  Save dynamic power
  Protect thin gate oxides and short channels
  No point in high value because of velocity sat.
Vt must decrease to
maintain device performance
But this causes exponential
increase in OFF leakage
Major future challenge
Static
Dynamic
[Moore03]

## Slide 52: Productivity
Transistor count is increasing faster than designer productivity (gates / week)
  Bigger design teams
    Up to 500 for a high-end microprocessor
  More expensive design cost
  Pressure to raise productivity
    Rely on synthesis, IP blocks
  Need for good engineering managers

## Slide 53: Physical Limits
Will Moore’s Law run out of steam?
  Can’t build transistors smaller than an atom…
Many reasons have been predicted for end of scaling
  Dynamic power
  Subthreshold leakage, tunneling
  Short channel effects
  Fabrication costs
  Electromigration
  Interconnect delay
Rumors of demise have been exaggerated

## Slide 54: VLSI Economics
Selling price Stotal
  Stotal = Ctotal / (1-m)
m = profit margin
Ctotal = total cost
  Nonrecurring engineering cost (NRE)
  Recurring cost
  Fixed cost

## Slide 55: NRE
Engineering cost
  Depends on size of design team
  Include benefits, training, computers
  CAD tools:
    Digital front end: $10K
    Analog front end: $100K
    Digital back end: $1M
Prototype manufacturing
  Mask costs: $500k – 1M in 130 nm process
  Test fixture and package tooling

## Slide 56: Recurring Costs
Fabrication
  Wafer cost / (Dice per wafer * Yield)
  Wafer cost: $500 - $3000
  Dice per wafer:
  Yield: Y = e-AD
    For small A, Y  1, cost proportional to area
    For large A, Y  0, cost increases exponentially
Packaging
Test

## Slide 57: Fixed Costs
Data sheets and application notes
Marketing and advertising
Yield analysis

## Slide 58: Example
You want to start a company to build a wireless communications chip. How much venture capital must you raise?
Because you are smarter than everyone else, you can get away with a small team in just two years:
  Seven digital designers
  Three analog designers
  Five support personnel

## Slide 59: Solution
Digital designers:
  salary
  overhead
  computer
  CAD tools
  Total:
Analog designers
  salary
  overhead
  computer
  CAD tools
  Total:
Support staff
  salary
  overhead
  computer
  Total:
Fabrication
  Back-end tools:
  Masks:
  Total:
Summary

## Slide 60: Solution
Digital designers:
  $70k salary
  $30k overhead
  $10k computer
  $10k CAD tools
  Total: $120k * 7 = $840k
Analog designers
  $100k salary
  $30k overhead
  $10k computer
  $100k CAD tools
  Total: $240k * 3 = $720k
Support staff
  $45k salary
  $20k overhead
  $5k computer
  Total: $70k * 5 = $350k
Fabrication
  Back-end tools: $1M
  Masks: $1M
  Total: $2M / year
Summary
  2 years @ $3.91M / year
  $8M design & prototype

## Slide 61: Cost Breakdown
New chip design is fairly capital-intensive
Maybe you can do it for less?