## Slide 1: Introduction to CMOS VLSI Design Lecture 25: Package, Power, Clock, and I/O
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
Packaging
Power Distribution
Clock Distribution
I/O

## Slide 3: Packages
Package functions
  Electrical connection of signals and power from chip to board
  Little delay or distortion
  Mechanical connection of chip to board
  Removes heat produced on chip
  Protects chip from mechanical damage
  Compatible with thermal expansion
  Inexpensive to manufacture and test

## Slide 4: Package Types
Through-hole vs. surface mount

## Slide 5: Multichip Modules
Pentium Pro MCM
  Fast connection of CPU to cache
  Expensive, requires known good dice

## Slide 6: Chip-to-Package Bonding
Traditionally, chip is surrounded by pad frame
  Metal pads on 100 – 200 m pitch
  Gold bond wires attach pads to package
  Lead frame distributes signals in package
  Metal heat spreader helps with cooling

## Slide 7: Advanced Packages
Bond wires contribute parasitic inductance
Fancy packages have many signal, power layers
  Like tiny printed circuit boards
Flip-chip places connections across surface of die rather than around periphery
  Top level metal pads covered with solder balls
  Chip flips upside down
  Carefully aligned to package (done blind!)
  Heated to melt balls
  Also called C4 (Controlled Collapse Chip Connection)

## Slide 8: Package Parasitics
Use many VDD, GND in parallel
  Inductance, IDD

## Slide 9: Heat Dissipation
60 W light bulb has surface area of 120 cm2
Itanium 2 die dissipates 130 W over 4 cm2
  Chips have enormous power densities
  Cooling is a serious challenge
Package spreads heat to larger surface area
  Heat sinks may increase surface area further
  Fans increase airflow rate over surface area
  Liquid cooling used in extreme cases ($$$)

## Slide 10: Thermal Resistance
T = jaP
  T: temperature rise on chip
  ja: thermal resistance of chip junction to ambient
  P: power dissipation on chip
Thermal resistances combine like resistors
  Series and parallel
ja = jp + pa
  Series combination

## Slide 11: Example
Your chip has a heat sink with a thermal resistance to the package of 4.0° C/W.
The resistance from chip to package is 1° C/W.
The system box ambient temperature may reach
55° C.
The chip temperature must not exceed 100° C.
What is the maximum chip power dissipation?

## Slide 12: Example
Your chip has a heat sink with a thermal resistance to the package of 4.0° C/W.
The resistance from chip to package is 1° C/W.
The system box ambient temperature may reach
55° C.
The chip temperature must not exceed 100° C.
What is the maximum chip power dissipation?
(100-55 C) / (4 + 1 C/W) = 9 W

## Slide 13: Power Distribution
Power Distribution Network functions
  Carry current from pads to transistors on chip
  Maintain stable voltage with low noise
  Provide average and peak power demands
  Provide current return paths for signals
  Avoid electromigration & self-heating wearout
  Consume little chip area and wire
  Easy to lay out

## Slide 14: Power Requirements
VDD = VDDnominal – Vdroop
Want Vdroop < +/- 10% of VDD
Sources of Vdroop
  IR drops
  L di/dt noise
IDD changes on many time scales

## Slide 15: Power System Model
Power comes from regulator on system board
  Board and package add parasitic R and L
  Bypass capacitors help stabilize supply voltage
  But capacitors also have parasitic R and L
Simulate system for time and frequency responses

## Slide 16: Bypass Capacitors
Need low supply impedance at all frequencies
Ideal capacitors have impedance decreasing with 
Real capacitors have parasitic R and L
  Leads to resonant frequency of capacitor

## Slide 17: Frequency Response
Use multiple capacitors in parallel
  Large capacitor near regulator has low impedance at low frequencies
  But also has a low self-resonant frequency
  Small capacitors near chip and on chip have low impedance at high frequencies
Choose caps to get low impedance at all frequencies

## Slide 18: Clock Distribution
On a small chip, the clock distribution network is just a wire
  And possibly an inverter for clkb
On practical chips, the RC delay of the wire resistance and gate load is very long
  Variations in this delay cause clock to get to different elements at different times
  This is called clock skew
Most chips use repeaters to buffer the clock and equalize the delay
  Reduces but doesn’t eliminate skew

## Slide 19: Example
Skew comes from differences in gate and wire delay
  With right buffer sizing, clk1 and clk2 could ideally arrive at the same time.
  But power supply noise changes buffer delays
  clk2 and clk3 will always see RC skew

## Slide 20: Review: Skew Impact
Ideally full cycle is
available for work
Skew adds sequencing
overhead
Increases hold time too

## Slide 21: Cycle Time Trends
Much of CPU performance comes from higher f
  f is improving faster than simple process shrinks
  Sequencing overhead is bigger part of cycle

## Slide 22: Solutions
Reduce clock skew
  Careful clock distribution network design
  Plenty of metal wiring resources
Analyze clock skew
  Only budget actual, not worst case skews
  Local vs. global skew budgets
Tolerate clock skew
  Choose circuit structures insensitive to skew

## Slide 23: Clock Dist. Networks
Ad hoc
Grids
H-tree
Hybrid

## Slide 24: Clock Grids
Use grid on two or more levels to carry clock
Make wires wide to reduce RC delay
Ensures low skew between nearby points
But possibly large skew across die

## Slide 25: Alpha Clock Grids

## Slide 26: H-Trees
Fractal structure
  Gets clock arbitrarily close to any point
  Matched delay along all paths
Delay variations cause skew
A and B might see big skew

## Slide 27: Itanium 2 H-Tree
Four levels of buffering:
  Primary driver
  Repeater
  Second-level
  clock buffer
  Gater
Route around
obstructions

## Slide 28: Hybrid Networks
Use H-tree to distribute clock to many points
Tie these points together with a grid
Ex: IBM Power4, PowerPC
  H-tree drives 16-64 sector buffers
  Buffers drive total of 1024 points
  All points shorted together with grid

## Slide 29: Input / Output
Input/Output System functions
  Communicate between chip and external world
  Drive large capacitance off chip
  Operate at compatible voltage levels
  Provide adequate bandwidth
  Limit slew rates to control di/dt noise
  Protect chip against electrostatic discharge
  Use small number of pins (low cost)

## Slide 30: I/O Pad Design
Pad types
  VDD / GND
  Output
  Input
  Bidirectional
  Analog

## Slide 31: Output Pads
Drive large off-chip loads (2 – 50 pF)
  With suitable rise/fall times
  Requires chain of successively larger buffers
Guard rings to protect against latchup
  Noise below GND injects charge into substrate
  Large nMOS output transistor
  p+ inner guard ring
  n+ outer guard ring
    In n-well

## Slide 32: Input Pads
Level conversion
  Higher or lower off-chip V
  May need thick oxide gates
Noise filtering
  Schmitt trigger
  Hysteresis changes VIH, VIL
Protection against electrostatic discharge

## Slide 33: ESD Protection
Static electricity builds up on your body
  Shock delivered to a chip can fry thin gates
  Must dissipate this energy in protection circuits before it reaches the gates
ESD protection circuits
  Current limiting resistor
  Diode clamps
ESD testing
  Human body model
  Views human as charged capacitor

## Slide 34: Bidirectional Pads
Combine input and output pad
Need tristate driver on output
  Use enable signal to set direction
  Optimized tristate avoids huge series transistors

## Slide 35: Analog Pads
Pass analog voltages directly in or out of chip
  No buffering
  Protection circuits must not distort voltages

## Slide 36: MOSIS I/O Pad
1.6 m two-metal process
  Protection resistors
  Protection diodes
  Guard rings
  Field oxide clamps