## Slide 1: Introduction to CMOS VLSI Design Lecture 6: Logical Effort
David Harris
Harvey Mudd College
Spring 2007

## Slide 2: Outline
RC Delay Estimation
Logical Effort
Delay in a Logic Gate
Multistage Logic Networks
Choosing the Best Number of Stages
Example
Summary

## Slide 3: RC Delay Model
Use equivalent circuits for MOS transistors
  Ideal switch + capacitance and ON resistance
  Unit nMOS has resistance R, capacitance C
  Unit pMOS has resistance 2R, capacitance C
Capacitance proportional to width
Resistance inversely proportional to width

## Slide 4: RC Values
Capacitance
  C = Cg = Cs = Cd = 2 fF/m of gate width
  Values similar across many processes
Resistance
  R  6 K*m in 0.6um process
  Improves with shorter channel lengths
Unit transistors
  May refer to minimum contacted device (4/2 )
  Or maybe 1 m wide device
  Doesn’t matter as long as you are consistent

## Slide 5: Inverter Delay Estimate
Estimate the delay of a fanout-of-1 inverter

## Slide 6: Inverter Delay Estimate
Estimate the delay of a fanout-of-1 inverter

## Slide 7: Inverter Delay Estimate
Estimate the delay of a fanout-of-1 inverter

## Slide 8: Inverter Delay Estimate
Estimate the delay of a fanout-of-1 inverter
d = 6RC

## Slide 9: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R).

## Slide 10: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R).

## Slide 11: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R).

## Slide 12: 3-input NAND Caps
Annotate the 3-input NAND gate with gate and diffusion capacitance.

## Slide 13: 3-input NAND Caps
Annotate the 3-input NAND gate with gate and diffusion capacitance.

## Slide 14: 3-input NAND Caps
Annotate the 3-input NAND gate with gate and diffusion capacitance.

## Slide 15: Elmore Delay
ON transistors look like resistors
Pullup or pulldown network modeled as RC ladder
Elmore delay of RC ladder

## Slide 16: Example: 2-input NAND
Estimate worst-case rising and falling delay of 2-input NAND driving h identical gates.

## Slide 17: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 18: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 19: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 20: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 21: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 22: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 23: Delay Components
Delay has two parts
  Parasitic delay
    6 or 7 RC
    Independent of load
  Effort delay
    4h RC
    Proportional to load capacitance

## Slide 24: Contamination Delay
Best-case (contamination) delay can be substantially less than propagation delay.
Ex: If both inputs fall simultaneously

## Slide 25: Diffusion Capacitance
We assumed contacted diffusion on every s / d.
Good layout minimizes diffusion area
Ex: NAND3 layout shares one diffusion contact
  Reduces output capacitance by 2C
  Merged uncontacted diffusion might help too

## Slide 26: Layout Comparison
Which layout is better?

## Slide 27: Introduction
Chip designers face a bewildering array of choices
  What is the best circuit topology for a function?
  How many stages of logic give least delay?
  How wide should the transistors be?
Logical effort is a method to make these decisions
  Uses a simple model of delay
  Allows back-of-the-envelope calculations
  Helps make rapid comparisons between alternatives
  Emphasizes remarkable symmetries

## Slide 28: Example
Ben Bitdiddle is the memory designer for the Motoroil 68W86, an embedded automotive processor. Help Ben design the decoder for a register file.
Decoder specifications:
  16 word register file
  Each word is 32 bits wide
  Each bit presents load of 3 unit-sized transistors
  True and complementary address inputs A[3:0]
  Each input may drive 10 unit-sized transistors
Ben needs to decide:
  How many stages to use?
  How large should each gate be?
  How fast can decoder operate?

## Slide 29: Delay in a Logic Gate
Express delays in process-independent unit
3RC
 12 ps in 180 nm process
40 ps in 0.6 m process

## Slide 30: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components

## Slide 31: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Effort delay f = gh (a.k.a. stage effort)
  Again has two components

## Slide 32: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Effort delay f = gh (a.k.a. stage effort)
  Again has two components
g: logical effort
  Measures relative ability of gate to deliver current
  g  1 for inverter

## Slide 33: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Effort delay f = gh (a.k.a. stage effort)
  Again has two components
h: electrical effort = Cout / Cin
  Ratio of output to input capacitance
  Sometimes called fanout

## Slide 34: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Parasitic delay p
  Represents delay of gate driving no load
  Set by internal parasitic capacitance

## Slide 35: Delay Plots
d = f + p
  = gh + p

## Slide 36: Delay Plots
d = f + p
  = gh + p
What about
NOR2?

## Slide 37: Computing Logical Effort
DEF: Logical effort is the ratio of the input capacitance of a gate to the input capacitance of an inverter delivering the same output current.
Measure from delay vs. fanout plots
Or estimate by counting transistor widths

## Slide 38: Catalog of Gates
Gate type | Number of inputs |  |  |  | 
 | 1 | 2 | 3 | 4 | n
Inverter | 1 |  |  |  | 
NAND |  | 4/3 | 5/3 | 6/3 | (n+2)/3
NOR |  | 5/3 | 7/3 | 9/3 | (2n+1)/3
Tristate / mux | 2 | 2 | 2 | 2 | 2
XOR, XNOR |  | 4, 4 | 6, 12, 6 | 8, 16, 16, 8 | 
Logical effort of common gates

## Slide 39: Catalog of Gates
Gate type | Number of inputs |  |  |  | 
 | 1 | 2 | 3 | 4 | n
Inverter | 1 |  |  |  | 
NAND |  | 2 | 3 | 4 | n
NOR |  | 2 | 3 | 4 | n
Tristate / mux | 2 | 4 | 6 | 8 | 2n
XOR, XNOR |  | 4 | 6 | 8 | 
Parasitic delay of common gates
  In multiples of pinv (1)

## Slide 40: Example: Ring Oscillator
Estimate the frequency of an N-stage ring oscillator
Logical Effort: g =
Electrical Effort: h =
Parasitic Delay: p =
Stage Delay: d =
Frequency: fosc =

## Slide 41: Example: Ring Oscillator
Estimate the frequency of an N-stage ring oscillator
Logical Effort: g = 1
Electrical Effort: h = 1
Parasitic Delay: p = 1
Stage Delay: d = 2
Frequency: fosc = 1/(2*N*d) = 1/4N
31 stage ring oscillator in 0.6 m process has frequency of ~ 200 MHz

## Slide 42: Example: FO4 Inverter
Estimate the delay of a fanout-of-4 (FO4) inverter
Logical Effort: g =
Electrical Effort: h =
Parasitic Delay: p =
Stage Delay: d =

## Slide 43: Example: FO4 Inverter
Estimate the delay of a fanout-of-4 (FO4) inverter
Logical Effort: g = 1
Electrical Effort: h = 4
Parasitic Delay: p = 1
Stage Delay: d = 5
The FO4 delay is about
200 ps in 0.6 m process
60 ps in a 180 nm process
f/3 ns in an f m process

## Slide 44: Multistage Logic Networks
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort

## Slide 45: Multistage Logic Networks
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort
Can we write F = GH?

## Slide 46: Paths that Branch
No! Consider paths that branch:
G =
H =
GH =
h1 =
h2 =
F = GH?

## Slide 47: Paths that Branch
No! Consider paths that branch:
G = 1
H = 90 / 5 = 18
GH = 18
h1 = (15 +15) / 5 = 6
h2 = 90 / 15 = 6
F = g1g2h1h2 = 36 = 2GH

## Slide 48: Branching Effort
Introduce branching effort
  Accounts for branching between stages in path
Now we compute the path effort
  F = GBH
Note:

## Slide 49: Multistage Delays
Path Effort Delay
Path Parasitic Delay
Path Delay

## Slide 50: Designing Fast Circuits
Delay is smallest when each stage bears same effort
Thus minimum delay of N stage path is
This is a key result of logical effort
  Find fastest possible delay
  Doesn’t require calculating gate sizes

## Slide 51: Gate Sizes
How wide should the gates be for least delay?
Working backward, apply capacitance transformation to find input capacitance of each gate given load it drives.
Check work by verifying input cap spec is met.

## Slide 52: Example: 3-stage path
Select gate sizes x and y for least delay from A to B

## Slide 53: Example: 3-stage path
Logical Effort G =
Electrical Effort H =
Branching Effort B =
Path Effort F =
Best Stage Effort
Parasitic Delay P =
Delay D =

## Slide 54: Example: 3-stage path
Logical Effort G = (4/3)*(5/3)*(5/3) = 100/27
Electrical Effort H = 45/8
Branching Effort B = 3 * 2 = 6
Path Effort F = GBH = 125
Best Stage Effort
Parasitic Delay P = 2 + 3 + 2 = 7
Delay D = 3*5 + 7 = 22 = 4.4 FO4

## Slide 55: Example: 3-stage path
Work backward for sizes
y =
x =

## Slide 56: Example: 3-stage path
Work backward for sizes
y = 45 * (5/3) / 5 = 15
x = (15*2) * (5/3) / 5 = 10

## Slide 57: Best Number of Stages
How many stages should a path use?
  Minimizing number of stages is not always fastest
Example: drive 64-bit datapath with unit inverter
D =

## Slide 58: Best Number of Stages
How many stages should a path use?
  Minimizing number of stages is not always fastest
Example: drive 64-bit datapath with unit inverter
D = NF1/N + P
= N(64)1/N + N

## Slide 59: Derivation
Consider adding inverters to end of path
  How many give least delay?
Define best stage effort

## Slide 60: Best Stage Effort
has no closed-form solution
Neglecting parasitics (pinv = 0), we find  = 2.718 (e)
For pinv = 1, solve numerically for  = 3.59

## Slide 61: Sensitivity Analysis
How sensitive is delay to using exactly the best number of stages?
2.4 <  < 6 gives delay within 15% of optimal
  We can be sloppy!
  I like  = 4

## Slide 62: Example, Revisited
Ben Bitdiddle is the memory designer for the Motoroil 68W86, an embedded automotive processor. Help Ben design the decoder for a register file.
Decoder specifications:
  16 word register file
  Each word is 32 bits wide
  Each bit presents load of 3 unit-sized transistors
  True and complementary address inputs A[3:0]
  Each input may drive 10 unit-sized transistors
Ben needs to decide:
  How many stages to use?
  How large should each gate be?
  How fast can decoder operate?

## Slide 63: Number of Stages
Decoder effort is mainly electrical and branching
Electrical Effort: H =
Branching Effort: B =
If we neglect logical effort (assume G = 1)
Path Effort: F =
Number of Stages: N =

## Slide 64: Number of Stages
Decoder effort is mainly electrical and branching
Electrical Effort: H = (32*3) / 10 = 9.6
Branching Effort: B = 8
If we neglect logical effort (assume G = 1)
Path Effort: F = GBH = 76.8
Number of Stages: N = log4F = 3.1
Try a 3-stage design

## Slide 65: Gate Sizes & Delay
Logical Effort: G =
Path Effort: F =
Stage Effort:
Path Delay:
Gate sizes: z = y =

## Slide 66: Gate Sizes & Delay
Logical Effort: G = 1 * 6/3 * 1 = 2
Path Effort: F = GBH = 154
Stage Effort:
Path Delay:
Gate sizes: z = 96*1/5.36 = 18 y = 18*2/5.36 = 6.7

## Slide 67: Comparison
Compare many alternatives with a spreadsheet
Design | N | G | P | D
NAND4-INV | 2 | 2 | 5 | 29.8
NAND2-NOR2 | 2 | 20/9 | 4 | 30.1
INV-NAND4-INV | 3 | 2 | 6 | 22.1
NAND4-INV-INV-INV | 4 | 2 | 7 | 21.1
NAND2-NOR2-INV-INV | 4 | 20/9 | 6 | 20.5
NAND2-INV-NAND2-INV | 4 | 16/9 | 6 | 19.7
INV-NAND2-INV-NAND2-INV | 5 | 16/9 | 7 | 20.4
NAND2-INV-NAND2-INV-INV-INV | 6 | 16/9 | 8 | 21.6

## Slide 68: Review of Definitions
Term | Stage | Path
number of stages |  | 
logical effort |  | 
electrical effort |  | 
branching effort |  | 
effort |  | 
effort delay |  | 
parasitic delay |  | 
delay |  | 

## Slide 69: Method of Logical Effort
Compute path effort
Estimate best number of stages
Sketch path with N stages
Estimate least delay
Determine best stage effort
Find gate sizes

## Slide 70: Limits of Logical Effort
Chicken and egg problem
  Need path to compute G
  But don’t know number of stages without G
Simplistic delay model
  Neglects input rise time effects
Interconnect
  Iteration required in designs with wire
Maximum speed only
  Not minimum area/power for constrained delay

## Slide 71: Summary
Logical effort is useful for thinking of delay in circuits
  Numeric logical effort characterizes gates
  NANDs are faster than NORs in CMOS
  Paths are fastest when effort delays are ~4
  Path delay is weakly sensitive to stages, sizes
  But using fewer stages doesn’t mean faster paths
  Delay of path is about log4F FO4 inverter delays
  Inverters and NAND2 best for driving large caps
Provides language for discussing fast circuits
  But requires practice to master