## Slide 1: The Mudd ][: A 6502 Microprocessor Implementation
E158 Introduction to CMOS VLSI Design
May 7, 2008

## Slide 2: Very Large Scale Integration
How do you…
design a chip with millions of transistors?
verify that the chip is correct?
make it fast?
make it consume minimal power?

## Slide 3: Apple ][ 6502 Microprocessor
8-bit microprocessor
First truly low-cost microprocessor
  Sold for ~$25 each
CISC (Complex Instruction Set Computer)
Clock speed: 1 MHz
Our goal: Minimize power
http://www.solarnavigator.net/computers.htm

## Slide 4: Team Dynamics
Instructor
Professor David Harris
Chief Circuit Designer
Nathaniel Pinckney
Chief Microarchitect
Thomas Barr
Microarchitecture
Heather Justice
Kyle Marsh
Schematics
Eric Burkhart
Trevin Murakami
Jason Squiers
Razor Latch
Sam Gordon
Tony Evans
Layout
Michael Braly
Nisha George
Corey Hebert
ROM Generation
Matt Jeffryes
I/O
Steve Huntzicker

## Slide 5: Microarchitecture
MOS Technology 6502 Architecture
  Architecture is the programmer’s view of the processor
Microarchitecture defines implementation:
  Controller
    Fully specifies datapath operation
  Datapath
    Register file and processor flags
    Program counter
    ALU (Arithmetic Logic Unit)

## Slide 6: Microarchitecture Design
CISC requires complex controlling logic
Mudd ][ datapath is very simple
  All controlling logic pushed into automatically synthesized ROMs
    Break down CISC instructions into “micro-ops”
  Datapath is extremely flexible
    Different architectures can be implemented by changing the ROMs

## Slide 7: Microcode
Controller broken into two ROMs
  State ROM groups commonly used operations
  Opcode ROM contains control signals specific to individual instructions

## Slide 8: Schematics
RTL (Verilog)
module regfile(input clk,
input write_enable,
input [1:0] read_addr_a, read_addr_b, write_addr,
input [7:0] write_data,
output [7:0] read_data_a, read_data_b);
reg [7:0] reg_file [3:0];
logic gated_clk;
assign gated_clk = clk & write_enable;
// three ported register file
// read two ports combinationally
// write third port as latch
always_latch
if (gated_clk) reg_file[write_addr] <= write_data;
assign read_data_a = reg_file[read_addr_a];
assign read_data_b = reg_file[read_addr_b];
endmodule
Schematic

## Slide 9: Schematics
Transistor level schematic
  Regbit

## Slide 10: Schematics
Designing for Layout

## Slide 11: Schematics
Layout in mind at abstract level
  Logical linear flow
Modular hierarchy
  For debugging

## Slide 12: Design Decisions
Power and Delay
  Transistor sizing
Synchronous Reset
Gated clock

## Slide 13: Clocking
Original 6502 used two-phase clocking system
Ours implements two-phase non-overlapping clocks
  Prevent race conditions
Input ph0 used to create ph1 & ph2

## Slide 14: Clock Generator

## Slide 15: Mudd ][ Critical Path

## Slide 16: Razor Latch

## Slide 17: Placement

## Slide 18: Layout
Generated by following schematics that followed the Register Transfer Level (RTL) description in the microcode
Tradeoffs between optimizing for min size, min power consumption, min area and max speed

## Slide 19: ALU and Ripple Carry Adder
ALU
  One of the largest components in the floorplan
  Ripple carry adder chosen to reduce amount of hardware needed for a comparable speed

## Slide 20: ALU

## Slide 21: Datapath

## Slide 22: ROM
Pseudo-nMOS NOR ROM layout
  Large number of states in controller FSM
  Significant power cost but without pMOS, saves space and delay without introducing timing challenges of dynamic logic

## Slide 23: ROM Example

## Slide 24: Generated Opcode ROM

## Slide 25: Controller

## Slide 26: Padframe
Structure that connects core to output pins
  One pad for each pinout
  Types of pads:
    Vdd • Gnd • Input • Output • In/Out
    External Vdd • Corner

## Slide 27: Level Converters

## Slide 28: Level Converters
  The lower 1.5 reference voltage will be seen as indeterminate in the pad
ERROR
ERROR

## Slide 29: Pad (Layout) with Level Converter
Level converter is long and narrow to fit

## Slide 30: Padframe (Layout)

## Slide 31: Complete Chip

## Slide 32: Verification
RTL behavioral verification (Modelsim)
  Test suites P and A
DRC, NCC, ERC
Behavioral of layout (Modelsim)
IRSIM switch-level simulations of Suite A
  Does not accurately model transistors
SPICE simulations of Suite P
  BSIM models of transistors
  Power estimates

## Slide 33: Ideal Testing Process

## Slide 34: Ideal Testing Process

## Slide 35: Additional Tests
Debugging
  Chip tester checks corner cases
  Ring oscillator checks padframe and level-converters
Analysis
  Plot power vs. core voltage
  Verify razor latches

## Slide 36: Lessons Learned / Conclusions
Good communication is essential
  Version control
  Understanding how parts fit into whole
The large group project has prepared us for team interactions in our future careers

## Slide 37: Questions?