## Slide 1: Lecture 14: Wires

## Slide 2: Outline
Introduction
Interconnect Modeling
  Wire Resistance
  Wire Capacitance
Wire RC Delay
Crosstalk
Wire Engineering
Repeaters

## Slide 3: Introduction
Chips are mostly made of wires called interconnect
  In stick diagram, wires set size
  Transistors are little things under the wires
  Many layers of wires
Wires are as important as transistors
  Speed
  Power
  Noise
Alternating layers run orthogonally

## Slide 4: Wire Geometry
Pitch = w + s
Aspect ratio: AR = t/w
  Old processes had AR << 1
  Modern processes have AR  2
    Pack in many skinny wires

## Slide 5: Layer Stack
AMI 0.6 m process has 3 metal layers
  M1 for within-cell routing
  M2 for vertical routing between cells
  M3 for horizontal routing between cells
Modern processes use 6-10+ metal layers
  M1: thin, narrow (< 3)
    High density cells
  Mid layers
    Thicker and wider, (density vs. speed)
  Top layers: thickest
    For VDD, GND, clk

## Slide 6: Example
Intel 90 nm Stack
Intel 45 nm Stack
[Thompson02]
[Moon08]

## Slide 7: Interconnect Modeling
Current in a wire is analogous to current in a pipe
  Resistance: narrow size impedes flow
  Capacitance: trough under the leaky pipe must fill first
  Inductance: paddle wheel inertia opposes changes in flow rate
    Negligible for most
    wires

## Slide 8: Lumped Element Models
Wires are a distributed system
  Approximate with lumped element models
3-segment -model is accurate to 3% in simulation
L-model needs 100 segments for same accuracy!
Use single segment -model for Elmore delay

## Slide 9: Wire Resistance
 = resistivity (*m)
R = sheet resistance (/)
   is a dimensionless unit(!)
Count number of squares
  R = R * (# of squares)

## Slide 10: Choice of Metals
Until 180 nm generation, most wires were aluminum
Contemporary processes normally use copper
  Cu atoms diffuse into silicon and damage FETs
  Must be surrounded by a diffusion barrier
Metal | Bulk resistivity (• cm)
Silver (Ag) | 1.6
Copper (Cu) | 1.7
Gold (Au) | 2.2
Aluminum (Al) | 2.8
Tungsten (W) | 5.3
Titanium (Ti) | 43.0

## Slide 11: Contacts Resistance
Contacts and vias also have 2-20 
Use many contacts for lower R
  Many small contacts for current crowding around periphery

## Slide 12: Copper Issues
Copper wires diffusion barrier has high resistance
Copper is also prone to dishing during polishing
Effective resistance is higher

## Slide 13: Example
Compute the sheet resistance of a 0.22 m thick Cu wire in a 65 nm process. Ignore dishing.
Find the total resistance if the wire is 0.125 m wide and 1 mm long. Ignore the barrier layer.

## Slide 14: Wire Capacitance
Wire has capacitance per unit length
  To neighbors
  To layers above and below
Ctotal = Ctop + Cbot + 2Cadj

## Slide 15: Capacitance Trends
Parallel plate equation: C = oxA/d
  Wires are not parallel plates, but obey trends
  Increasing area (W, t) increases capacitance
  Increasing distance (s, h) decreases capacitance
Dielectric constant
  ox= k0
    0 = 8.85 x 10-14 F/cm
    k = 3.9 for SiO2
Processes are starting to use low-k dielectrics
  k  3 (or less) as dielectrics use air pockets

## Slide 16: Capacitance Formula
Capacitance of a line without neighbors can be approximated as
This empirical formula is accurate to 6% for AR < 3.3

## Slide 17: M2 Capacitance Data
Typical dense wires have ~ 0.2 fF/m
  Compare to 1-2 fF/m for gate capacitance

## Slide 18: Diffusion & Polysilicon
Diffusion capacitance is very high (1-2 fF/m)
  Comparable to gate capacitance
  Diffusion also has high resistance
  Avoid using diffusion runners for wires!
Polysilicon has lower C but high R
  Use for transistor gates
  Occasionally for very short wires between gates

## Slide 19: Wire RC Delay
Estimate the delay of a 10x inverter driving a 2x inverter at the end of the 1 mm wire. Assume wire capacitance is 0.2 fF/m and that a unit-sized inverter has R = 10 K and C = 0.1 fF.
  tpd = (1000 )(100 fF) + (1000 + 800 )(100 + 0.6 fF) = 281 ps

## Slide 20: Wire Energy
Estimate the energy per unit length to send a bit of information (one rising and one falling transition) in a CMOS process.
E = (0.2 pF/mm)(1.0 V)2 = 0.2 pJ/bit/mm
  = 0.2 mW/Gbps

## Slide 21: Crosstalk
A capacitor does not like to change its voltage instantaneously.
A wire has high capacitance to its neighbor.
  When the neighbor switches from 1-> 0 or 0->1, the wire tends to switch too.
  Called capacitive coupling or crosstalk.
Crosstalk effects
  Noise on nonswitching wires
  Increased delay on switching wires

## Slide 22: Crosstalk Delay
Assume layers above and below on average are quiet
  Second terminal of capacitor can be ignored
  Model as Cgnd = Ctop + Cbot
Effective Cadj depends on behavior of neighbors
  Miller effect
B | V | Ceff(A) | MCF
Constant | VDD | Cgnd + Cadj | 1
Switching with A | 0 | Cgnd | 0
Switching opposite A | 2VDD | Cgnd + 2 Cadj | 2

## Slide 23: Crosstalk Noise
Crosstalk causes noise on nonswitching wires
If victim is floating:
  model as capacitive voltage divider

## Slide 24: Driven Victims
Usually victim is driven by a gate that fights noise
  Noise depends on relative resistances
  Victim driver is in linear region, agg. in saturation
  If sizes are same, Raggressor = 2-4 x Rvictim

## Slide 25: Coupling Waveforms
Simulated coupling for Cadj = Cvictim

## Slide 26: Noise Implications
So what if we have noise?
If the noise is less than the noise margin, nothing happens
Static CMOS logic will eventually settle to correct output even if disturbed by large noise spikes
  But glitches cause extra delay
  Also cause extra power from false transitions
Dynamic logic never recovers from glitches
Memories and other sensitive circuits also can produce the wrong answer

## Slide 27: Wire Engineering
Goal: achieve delay, area, power goals with acceptable noise
Degrees of freedom:
  Width
  Spacing
  Layer
  Shielding

## Slide 28: Repeaters
R and C are proportional to l
RC delay is proportional to l2
  Unacceptably great for long wires
Break long wires into N shorter segments
  Drive each one with an inverter or buffer

## Slide 29: Repeater Design
How many repeaters should we use?
How large should each one be?
Equivalent Circuit
  Wire length l/N
    Wire Capacitance Cw*l/N, Resistance Rw*l/N
  Inverter width W (nMOS = W, pMOS = 2W)
    Gate Capacitance C’*W, Resistance R/W

## Slide 30: Repeater Results
Write equation for Elmore Delay
  Differentiate with respect to W and N
  Set equal to 0, solve
~40 ps/mm
in 65 nm process

## Slide 31: Repeater Energy
Energy / length ≈ 1.87CwVDD2
  87% premium over unrepeated wires
  The extra power is consumed in the large repeaters
If the repeaters are downsized for minimum EDP:
  Energy premium is only 30%
  Delay increases by 14% from min delay