## Slide 1: Lecture 19: SRAM

## Slide 2: Outline
Memory Arrays
SRAM Architecture
  SRAM Cell
  Decoders
  Column Circuitry
  Multiple Ports
Serial Access Memories

## Slide 3: Memory Arrays

## Slide 4: Array Architecture
2n words of 2m bits each
If n >> m, fold by 2k into fewer rows of more columns
Good regularity – easy to design
Very high density if good cells are used

## Slide 5: 12T SRAM Cell
Basic building block: SRAM Cell
  Holds one bit of information, like a latch
  Must be read and written
12-transistor (12T) SRAM cell
  Use a simple latch connected to bitline
  46 x 75  unit cell

## Slide 6: 6T SRAM Cell
Cell size accounts for most of array size
  Reduce cell size at expense of complexity
6T SRAM Cell
  Used in most commercial chips
  Data stored in cross-coupled inverters
Read:
  Precharge bit, bit_b
  Raise wordline
Write:
  Drive data onto bit, bit_b
  Raise wordline

## Slide 7: SRAM Read
Precharge both bitlines high
Then turn on wordline
One of the two bitlines will be pulled down by the cell
Ex: A = 0, A_b = 1
  bit discharges, bit_b stays high
  But A bumps up slightly
Read stability
  A must not flip
  N1 >> N2

## Slide 8: SRAM Write
Drive one bitline high, the other low
Then turn on wordline
Bitlines overpower cell with new value
Ex: A = 0, A_b = 1, bit = 1, bit_b = 0
  Force A_b low, then A rises high
Writability
  Must overpower feedback inverter
  N2 >> P1

## Slide 9: SRAM Sizing
High bitlines must not overpower inverters during reads
But low bitlines must write new value into cell

## Slide 10: SRAM Column Example
Read Write

## Slide 11: SRAM Layout
Cell size is critical: 26 x 45  (even smaller in industry)
Tile cells sharing VDD, GND, bitline contacts

## Slide 12: Thin Cell
In nanometer CMOS
  Avoid bends in polysilicon and diffusion
  Orient all transistors in one direction
Lithographically friendly or thin cell layout fixes this
  Also reduces length and capacitance of bitlines

## Slide 13: Commercial SRAMs
Five generations of Intel SRAM cell micrographs
  Transition to thin cell at 65 nm
  Steady scaling of cell area

## Slide 14: Decoders
n:2n decoder consists of 2n n-input AND gates
  One needed for each row of memory
  Build AND from NAND or NOR gates
Static CMOS Pseudo-nMOS

## Slide 15: Decoder Layout
Decoders must be pitch-matched to SRAM cell
  Requires very skinny gates

## Slide 16: Large Decoders
For n > 4, NAND gates become slow
  Break large gates into multiple smaller gates

## Slide 17: Predecoding
Many of these gates are redundant
  Factor out common
  gates into predecoder
  Saves area
  Same path effort

## Slide 18: Column Circuitry
Some circuitry is required for each column
  Bitline conditioning
  Sense amplifiers
  Column multiplexing

## Slide 19: Bitline Conditioning
Precharge bitlines high before reads
Equalize bitlines to minimize voltage difference when using sense amplifiers

## Slide 20: Sense Amplifiers
Bitlines have many cells attached
  Ex: 32-kbit SRAM has 128 rows x 256 cols
  128 cells on each bitline
tpd  (C/I) V
  Even with shared diffusion contacts, 64C of diffusion capacitance (big C)
  Discharged slowly through small transistors (small I)
Sense amplifiers are triggered on small voltage swing (reduce V)

## Slide 21: Differential Pair Amp
Differential pair requires no clock
But always dissipates static power

## Slide 22: Clocked Sense Amp
Clocked sense amp saves power
Requires sense_clk after enough bitline swing
Isolation transistors cut off large bitline capacitance

## Slide 23: Twisted Bitlines
Sense amplifiers also amplify noise
  Coupling noise is severe in modern processes
  Try to couple equally onto bit and bit_b
  Done by twisting bitlines

## Slide 24: Column Multiplexing
Recall that array may be folded for good aspect ratio
Ex: 2 kword x 16 folded into 256 rows x 128 columns
  Must select 16 output bits from the 128 columns
  Requires 16 8:1 column multiplexers

## Slide 25: Tree Decoder Mux
Column mux can use pass transistors
  Use nMOS only, precharge outputs
One design is to use k series transistors for 2k:1 mux
  No external decoder logic needed

## Slide 26: Single Pass-Gate Mux
Or eliminate series transistors with separate decoder

## Slide 27: Ex: 2-way Muxed SRAM

## Slide 28: Multiple Ports
We have considered single-ported SRAM
  One read or one write on each cycle
Multiported SRAM are needed for register files
Examples:
  Multicycle MIPS must read two sources or write a result on some cycles
  Pipelined MIPS must read two sources and write a third result each cycle
  Superscalar MIPS must read and write many sources and results each cycle

## Slide 29: Dual-Ported SRAM
Simple dual-ported SRAM
  Two independent single-ended reads
  Or one differential write
Do two reads and one write by time multiplexing
  Read during ph1, write during ph2

## Slide 30: Multi-Ported SRAM
Adding more access transistors hurts read stability
Multiported SRAM isolates reads from state node
Single-ended bitlines save area

## Slide 31: Large SRAMs
Large SRAMs are split into subarrays for speed
Ex: UltraSparc 512KB cache
  4 128 KB subarrays
  Each have 16 8KB banks
  256 rows x 256 cols / bank
  60% subarray area efficiency
  Also space for tags & control
[Shin05]

## Slide 32: Serial Access Memories
Serial access memories do not use an address
  Shift Registers
  Tapped Delay Lines
  Serial In Parallel Out (SIPO)
  Parallel In Serial Out (PISO)
  Queues (FIFO, LIFO)

## Slide 33: Shift Register
Shift registers store and delay data
Simple design: cascade of registers
  Watch your hold times!

## Slide 34: Denser Shift Registers
Flip-flops aren’t very area-efficient
For large shift registers, keep data in SRAM instead
Move read/write pointers to RAM rather than data
  Initialize read address to first entry, write to last
  Increment address on each cycle

## Slide 35: Tapped Delay Line
A tapped delay line is a shift register with a programmable number of stages
Set number of stages with delay controls to mux
  Ex: 0 – 63 stages of delay

## Slide 36: Serial In Parallel Out
1-bit shift register reads in serial data
  After N steps, presents N-bit parallel output

## Slide 37: Parallel In Serial Out
Load all N bits in parallel when shift = 0
  Then shift one bit out per cycle

## Slide 38: Queues
Queues allow data to be read and written at different rates.
Read and write each use their own clock, data
Queue indicates whether it is full or empty
Build with SRAM and read/write counters (pointers)

## Slide 39: FIFO, LIFO Queues
First In First Out (FIFO)
  Initialize read and write pointers to first element
  Queue is EMPTY
  On write, increment write pointer
  If write almost catches read, Queue is FULL
  On read, increment read pointer
Last In First Out (LIFO)
  Also called a stack
  Use a single stack pointer for read and write