## Slide 1: Lecture 2: MIPS Processor Example

## Slide 2: Outline
Design Partitioning
MIPS Processor Example
  Architecture
  Microarchitecture
  Logic Design
  Circuit Design
  Physical Design
Fabrication, Packaging, Testing

## Slide 3: Activity 2
Sketch a stick diagram for a 4-input NOR gate

## Slide 4: Coping with Complexity
How to design System-on-Chip?
  Many millions (even billions!) of transistors
  Tens to hundreds of engineers
Structured Design
Design Partitioning

## Slide 5: Structured Design
Hierarchy: Divide and Conquer
  Recursively system into modules
Regularity
  Reuse modules wherever possible
  Ex: Standard cell library
Modularity: well-formed interfaces
  Allows modules to be treated as black boxes
Locality
  Physical and temporal

## Slide 6: Design Partitioning
Architecture: User’s perspective, what does it do?
  Instruction set, registers
  MIPS, x86, Alpha, PIC, ARM, …
Microarchitecture
  Single cycle, multcycle, pipelined, superscalar?
Logic: how are functional blocks constructed
  Ripple carry, carry lookahead, carry select adders
Circuit: how are transistors used
  Complementary CMOS, pass transistors, domino
Physical: chip layout
  Datapaths, memories, random logic

## Slide 7: Gajski Y-Chart

## Slide 8: MIPS Architecture
Example: subset of MIPS processor architecture
  Drawn from Patterson & Hennessy
MIPS is a 32-bit architecture with 32 registers
  Consider 8-bit subset using 8-bit datapath
  Only implement 8 registers ($0 - $7)
  $0 hardwired to 00000000
  8-bit program counter
You’ll build this processor in the labs
  Illustrate the key concepts in VLSI design

## Slide 9: Instruction Set

## Slide 10: Instruction Encoding
32-bit instruction encoding
  Requires four cycles to fetch on 8-bit datapath

## Slide 11: Fibonacci (C)
f0 = 1; f-1 = -1
fn = fn-1 + fn-2
f = 1, 1, 2, 3, 5, 8, 13, …

## Slide 12: Fibonacci (Assembly)
1st statement: n = 8
How do we translate this to assembly?

## Slide 13: Fibonacci (Binary)
1st statement: addi $3, $0, 8
How do we translate this to machine language?
  Hint: use instruction encodings below

## Slide 14: Fibonacci (Binary)
Machine language program

## Slide 15: MIPS Microarchitecture
Multicycle architecture ( [Paterson04], [Harris07] )

## Slide 16: Multicycle Controller

## Slide 17: Logic Design
Start at top level
  Hierarchically decompose MIPS into units
Top-level interface

## Slide 18: Block Diagram

## Slide 19: Hierarchical Design

## Slide 20: HDLs
Hardware Description Languages
  Widely used in logic design
  Verilog and VHDL
Describe hardware using code
  Document logic functions
  Simulate logic before building
  Synthesize code into gates and layout
    Requires a library of standard cells

## Slide 21: Verilog Example
module fulladder(input a, b, c,
output s, cout);
sum s1(a, b, c, s);
carry c1(a, b, c, cout);
endmodule
module carry(input a, b, c,
output cout)
assign cout = (a&b) | (a&c) | (b&c);
endmodule

## Slide 22: Circuit Design
How should logic be implemented?
  NANDs and NORs vs. ANDs and ORs?
  Fan-in and fan-out?
  How wide should transistors be?
These choices affect speed, area, power
Logic synthesis makes these choices for you
  Good enough for many applications
  Hand-crafted circuits are still better

## Slide 23: Example: Carry Logic
assign cout = (a&b) | (a&c) | (b&c);
Transistors? Gate Delays?

## Slide 24: Gate-level Netlist
module carry(input a, b, c,
output cout)
wire x, y, z;
and g1(x, a, b);
and g2(y, a, c);
and g3(z, b, c);
or g4(cout, x, y, z);
endmodule

## Slide 25: Transistor-Level Netlist
module carry(input a, b, c,
output cout)
wire i1, i2, i3, i4, cn;
tranif1 n1(i1, 0, a);
tranif1 n2(i1, 0, b);
tranif1 n3(cn, i1, c);
tranif1 n4(i2, 0, b);
tranif1 n5(cn, i2, a);
tranif0 p1(i3, 1, a);
tranif0 p2(i3, 1, b);
tranif0 p3(cn, i3, c);
tranif0 p4(i4, 1, b);
tranif0 p5(cn, i4, a);
tranif1 n6(cout, 0, cn);
tranif0 p6(cout, 1, cn);
endmodule

## Slide 26: SPICE Netlist
.SUBCKT CARRY A B C COUT VDD GND
MN1 I1 A GND GND NMOS W=1U L=0.18U AD=0.3P AS=0.5P
MN2 I1 B GND GND NMOS W=1U L=0.18U AD=0.3P AS=0.5P
MN3 CN C I1 GND NMOS W=1U L=0.18U AD=0.5P AS=0.5P
MN4 I2 B GND GND NMOS W=1U L=0.18U AD=0.15P AS=0.5P
MN5 CN A I2 GND NMOS W=1U L=0.18U AD=0.5P AS=0.15P
MP1 I3 A VDD VDD PMOS W=2U L=0.18U AD=0.6P AS=1 P
MP2 I3 B VDD VDD PMOS W=2U L=0.18U AD=0.6P AS=1P
MP3 CN C I3 VDD PMOS W=2U L=0.18U AD=1P AS=1P
MP4 I4 B VDD VDD PMOS W=2U L=0.18U AD=0.3P AS=1P
MP5 CN A I4 VDD PMOS W=2U L=0.18U AD=1P AS=0.3P
MN6 COUT CN GND GND NMOS W=2U L=0.18U AD=1P AS=1P
MP6 COUT CN VDD VDD PMOS W=4U L=0.18U AD=2P AS=2P
CI1 I1 GND 2FF
CI3 I3 GND 3FF
CA A GND 4FF
CB B GND 4FF
CC C GND 2FF
CCN CN GND 4FF
CCOUT COUT GND 2FF
.ENDS

## Slide 27: Physical Design
Floorplan
Standard cells
  Place & route
Datapaths
  Slice planning
Area estimation

## Slide 28: MIPS Floorplan

## Slide 29: MIPS Layout

## Slide 30: Standard Cells
Uniform cell height
Uniform well height
M1 VDD and GND rails
M2 Access to I/Os
Well / substrate taps
Exploits regularity

## Slide 31: Synthesized Controller
Synthesize HDL into gate-level netlist
Place & Route using standard cell library

## Slide 32: Pitch Matching
Synthesized controller area is mostly wires
  Design is smaller if wires run through/over cells
  Smaller = faster, lower power as well!
Design snap-together cells for datapaths and arrays
  Plan wires into cells
  Connect by abutment
    Exploits locality
    Takes lots of effort

## Slide 33: MIPS Datapath
8-bit datapath built from 8 bitslices (regularity)
Zipper at top drives control signals to datapath

## Slide 34: Slice Plans
Slice plan for bitslice
  Cell ordering, dimensions, wiring tracks
  Arrange cells for wiring locality

## Slide 35: Area Estimation
Need area estimates to make floorplan
  Compare to another block you already designed
  Or estimate from transistor counts
  Budget room for large wiring tracks
  Your mileage may vary; derate by 2x for class.

## Slide 36: Design Verification
Fabrication is slow & expensive
  MOSIS 0.6m: $1000, 3 months
  65 nm: $3M, 1 month
Debugging chips is very hard
  Limited visibility into operation
Prove design is right before building!
  Logic simulation
  Ckt. simulation / formal verification
  Layout vs. schematic comparison
  Design & electrical rule checks
Verification is > 50% of effort on most chips!

## Slide 37: Fabrication & Packaging
Tapeout final layout
Fabrication
  6, 8, 12” wafers
  Optimized for throughput,
  not latency (10 weeks!)
  Cut into individual dice
Packaging
  Bond gold wires from die I/O pads to package

## Slide 38: Testing
Test that chip operates
  Design errors
  Manufacturing errors
A single dust particle or wafer defect kills a die
  Yields from 90% to < 10%
  Depends on die size, maturity of process
  Test each part before shipping to customer

## Slide 39: Custom vs. Synthesis
8-bit Implementations

## Slide 40: MIPS R3000 Processor
32-bit 2nd generation commercial processor (1988)
Led by John Hennessy (Stanford, MIPS Founder)
32-64 KB Caches
1.2 m process
111K Transistor
Up to 12-40 MHz
66 mm2 die
145 I/O Pins
VDD = 5 V
4 Watts
SGI Workstations
http://gecko54000.free.fr/?documentations=1988_MIPS_R3000