## Slide 1: Lecture 20: CAMs, ROMs, PLAs

## Slide 2: Outline
Content-Addressable Memories
Read-Only Memories
Programmable Logic Arrays

## Slide 3: CAMs
Extension of ordinary memory (e.g. SRAM)
  Read and write memory as usual
  Also match to see which words contain a key

## Slide 4: 10T CAM Cell
Add four match transistors to 6T SRAM
  56 x 43  unit cell

## Slide 5: CAM Cell Operation
Read and write like ordinary SRAM
For matching:
  Leave wordline low
  Precharge matchlines
  Place key on bitlines
  Matchlines evaluate
Miss line
  Pseudo-nMOS NOR of match lines
  Goes high if no words match

## Slide 6: Read-Only Memories
Read-Only Memories are nonvolatile
  Retain their contents when power is removed
Mask-programmed ROMs use one transistor per bit
  Presence or absence determines 1 or 0

## Slide 7: ROM Example
4-word x 6-bit ROM
  Represented with dot diagram
  Dots indicate 1’s in ROM
Word 0: 010101
Word 1: 011001
Word 2: 100101
Word 3: 101010
Looks like 6 4-input pseudo-nMOS NORs

## Slide 8: ROM Array Layout
Unit cell is 12 x 8 (about 1/10 size of SRAM)

## Slide 9: Row Decoders
ROM row decoders must pitch-match with ROM
  Only a single track per word!

## Slide 10: Complete ROM Layout

## Slide 11: PROMs and EPROMs
Programmable ROMs
  Build array with transistors at every site
  Burn out fuses to disable unwanted transistors
Electrically Programmable ROMs
  Use floating gate to turn off unwanted transistors
  EPROM, EEPROM, Flash

## Slide 12: Flash Programming
Charge on floating gate determines Vt
Logic 1: negative Vt
Logic 0: positive Vt
Cells erased to 1 by applying a high body voltage so that electrons tunnel off floating gate into substrate
Programmed to 0 by applying high gate voltage

## Slide 13: NAND Flash
High density, low cost / bit
  Programmed one page at a time
  Erased one block at a time
Example:
  4096-bit pages
  16 pages / 8 KB block
  Many blocks / memory

## Slide 14: 64 Gb NAND Flash
64K cells / page
4 bits / cell (multiple Vt)
64 cells / string
  256 pages / block
2K blocks / plane
2 planes
[Trinh09]

## Slide 15: Building Logic with ROMs
Use ROM as lookup table containing truth table
  n inputs, k outputs requires 2n words x k bits
  Changing function is easy – reprogram ROM
Finite State Machine
  n inputs, k outputs, s bits of state
  Build with 2n+s x (k+s) bit ROM and (k+s) bit reg

## Slide 16: Example: RoboAnt
Let’s build an Ant
Sensors: Antennae
(L,R) – 1 when in contact
Actuators: Legs
Forward step F
Ten degree turns TL, TR
Goal: make our ant smart enough to
get out of a maze
Strategy: keep right antenna on wall
(RoboAnt adapted from MIT 6.004 2002 OpenCourseWare by Ward and Terman)
L
R

## Slide 17: Lost in space
Action: go forward until we hit something
  Initial state

## Slide 18: Bonk!!!
Action: turn left (rotate counterclockwise)
  Until we don’t touch anymore

## Slide 19: A little to the right
Action: step forward and turn right a little
  Looking for wall

## Slide 20: Then a little to the left
Action: step and turn left a little, until not touching

## Slide 21: Whoops – a corner!
Action: step and turn right until hitting next wall

## Slide 22: Simplification
Merge equivalent states where possible

## Slide 23: State Transition Table
S1:0 | L | R | S1:0’ | TR | TL | F
00 | 0 | 0 | 00 | 0 | 0 | 1
00 | 1 | X | 01 | 0 | 0 | 1
00 | 0 | 1 | 01 | 0 | 0 | 1
01 | 1 | X | 01 | 0 | 1 | 0
01 | 0 | 1 | 01 | 0 | 1 | 0
01 | 0 | 0 | 10 | 0 | 1 | 0
10 | X | 0 | 10 | 1 | 0 | 1
10 | X | 1 | 11 | 1 | 0 | 1
11 | 1 | X | 01 | 0 | 1 | 1
11 | 0 | 0 | 10 | 0 | 1 | 1
11 | 0 | 1 | 11 | 0 | 1 | 1
Lost
RCCW
Wall1
Wall2

## Slide 24: ROM Implementation
16-word x 5 bit ROM

## Slide 25: ROM Implementation
16-word x 5 bit ROM

## Slide 26: PLAs
A Programmable Logic Array performs any function in sum-of-products form.
Literals: inputs & complements
Products / Minterms: AND of literals
Outputs: OR of Minterms
Example: Full Adder

## Slide 27: NOR-NOR PLAs
ANDs and ORs are not very efficient in CMOS
Dynamic or Pseudo-nMOS NORs are very efficient
Use DeMorgan’s Law to convert to all NORs

## Slide 28: PLA Schematic & Layout

## Slide 29: PLAs vs. ROMs
The OR plane of the PLA is like the ROM array
The AND plane of the PLA is like the ROM decoder
PLAs are more flexible than ROMs
  No need to have 2n rows for n inputs
  Only generate the minterms that are needed
  Take advantage of logic simplification

## Slide 30: Example: RoboAnt PLA
Convert state transition table to logic equations
S1:0 | L | R | S1:0’ | TR | TL | F
00 | 0 | 0 | 00 | 0 | 0 | 1
00 | 1 | X | 01 | 0 | 0 | 1
00 | 0 | 1 | 01 | 0 | 0 | 1
01 | 1 | X | 01 | 0 | 1 | 0
01 | 0 | 1 | 01 | 0 | 1 | 0
01 | 0 | 0 | 10 | 0 | 1 | 0
10 | X | 0 | 10 | 1 | 0 | 1
10 | X | 1 | 11 | 1 | 0 | 1
11 | 1 | X | 01 | 0 | 1 | 1
11 | 0 | 0 | 10 | 0 | 1 | 1
11 | 0 | 1 | 11 | 0 | 1 | 1

## Slide 31: RoboAnt Dot Diagram