## Slide 1: Lecture 7: Power

## Slide 2: Outline
Power and Energy
Dynamic Power
Static Power

## Slide 3: Power and Energy
Power is drawn from a voltage source attached to the VDD pin(s) of a chip.
Instantaneous Power:
Energy:
Average Power:

## Slide 4: Power in Circuit Elements

## Slide 5: Charging a Capacitor
When the gate output rises
  Energy stored in capacitor is
  But energy drawn from the supply is
  Half the energy from VDD is dissipated in the pMOS transistor as heat, other half stored in capacitor
When the gate output falls
  Energy in capacitor is dumped to GND
  Dissipated as heat in the nMOS transistor

## Slide 6: Switching Waveforms
Example: VDD = 1.0 V, CL = 150 fF, f = 1 GHz

## Slide 7: Switching Power

## Slide 8: Activity Factor
Suppose the system clock frequency = f
Let fsw = f, where  = activity factor
  If the signal is a clock,  = 1
  If the signal switches once per cycle,  = ½
Dynamic power:

## Slide 9: Short Circuit Current
When transistors switch, both nMOS and pMOS networks may be momentarily ON at once
Leads to a blip of “short circuit” current.
< 10% of dynamic power if rise/fall times are comparable for input and output
We will generally ignore this component

## Slide 10: Power Dissipation Sources
Ptotal = Pdynamic + Pstatic
Dynamic power: Pdynamic = Pswitching + Pshortcircuit
  Switching load capacitances
  Short-circuit current
Static power: Pstatic = (Isub + Igate + Ijunct + Icontention)VDD
  Subthreshold leakage
  Gate leakage
  Junction leakage
  Contention current

## Slide 11: Dynamic Power Example
1 billion transistor chip
  50M logic transistors
    Average width: 12 
    Activity factor = 0.1
  950M memory transistors
    Average width: 4 
    Activity factor = 0.02
  1.0 V 65 nm process
  C = 1 fF/m (gate) + 0.8 fF/m (diffusion)
Estimate dynamic power consumption @ 1 GHz. Neglect wire capacitance and short-circuit current.

## Slide 12: Solution

## Slide 13: Dynamic Power Reduction
Try to minimize:
  Activity factor
  Capacitance
  Supply voltage
  Frequency

## Slide 14: Activity Factor Estimation
Let Pi = Prob(node i = 1)
  Pi = 1-Pi
i = Pi * Pi
Completely random data has P = 0.5 and  = 0.25
Data is often not completely random
  e.g. upper bits of 64-bit words representing bank account balances are usually 0
Data propagating through ANDs and ORs has lower activity factor
  Depends on design, but typically  ≈ 0.1

## Slide 15: Switching Probability

## Slide 16: Example
A 4-input AND is built out of two levels of gates
Estimate the activity factor at each node if the inputs have P = 0.5

## Slide 17: Clock Gating
The best way to reduce the activity is to turn off the clock to registers in unused blocks
  Saves clock activity ( = 1)
  Eliminates all switching activity in the block
  Requires determining if block will be used

## Slide 18: Capacitance
Gate capacitance
  Fewer stages of logic
  Small gate sizes
Wire capacitance
  Good floorplanning to keep communicating blocks close to each other
  Drive long wires with inverters or buffers rather than complex gates

## Slide 19: Voltage / Frequency
Run each block at the lowest possible voltage and frequency that meets performance requirements
Voltage Domains
  Provide separate supplies to different blocks
  Level converters required when crossing
  from low to high VDD domains
Dynamic Voltage Scaling
  Adjust VDD and f according to
  workload

## Slide 20: Static Power
Static power is consumed even when chip is quiescent.
  Leakage draws power from nominally OFF devices
  Ratioed circuits burn power in fight between ON transistors

## Slide 21: Static Power Example
Revisit power estimation for 1 billion transistor chip
Estimate static power consumption
  Subthreshold leakage
    Normal Vt: 100 nA/m
    High Vt: 10 nA/m
    High Vt used in all memories and in 95% of logic gates
  Gate leakage 5 nA/m
  Junction leakage negligible

## Slide 22: Solution

## Slide 23: Subthreshold Leakage
For Vds > 50 mV
Ioff = leakage at Vgs = 0, Vds = VDD
Typical values in 65 nm
Ioff = 100 nA/m @ Vt = 0.3 V
Ioff = 10 nA/m @ Vt = 0.4 V
Ioff = 1 nA/m @ Vt = 0.5 V
 = 0.1
k = 0.1
S = 100 mV/decade

## Slide 24: Stack Effect
Series OFF transistors have less leakage
  Vx > 0, so N2 has negative Vgs
  Leakage through 2-stack reduces ~10x
  Leakage through 3-stack reduces further

## Slide 25: Leakage Control
Leakage and delay trade off
  Aim for low leakage in sleep and low delay in active mode
To reduce leakage:
  Increase Vt: multiple Vt
    Use low Vt only in critical circuits
  Increase Vs: stack effect
    Input vector control in sleep
  Decrease Vb
    Reverse body bias in sleep
    Or forward body bias in active mode

## Slide 26: Gate Leakage
Extremely strong function of tox and Vgs
  Negligible for older processes
  Approaches subthreshold leakage at 65 nm and below in some processes
An order of magnitude less for pMOS than nMOS
Control leakage in the process using tox > 10.5 Å
  High-k gate dielectrics help
  Some processes provide multiple tox
    e.g. thicker oxide for 3.3 V I/O transistors
Control leakage in circuits by limiting VDD

## Slide 27: NAND3 Leakage Example
100 nm process
  Ign = 6.3 nA Igp = 0
  Ioffn = 5.63 nA Ioffp = 9.3 nA
Data from [Lee03]

## Slide 28: Junction Leakage
From reverse-biased p-n junctions
  Between diffusion and substrate or well
Ordinary diode leakage is negligible
Band-to-band tunneling (BTBT) can be significant
  Especially in high-Vt transistors where other leakage is small
  Worst at Vdb = VDD
Gate-induced drain leakage (GIDL) exacerbates
  Worst for Vgd = -VDD (or more negative)

## Slide 29: Power Gating
Turn OFF power to blocks when they are idle to save leakage
  Use virtual VDD (VDDV)
  Gate outputs to prevent
  invalid logic levels to next block
Voltage drop across sleep transistor degrades performance during normal operation
  Size the transistor wide enough to minimize impact
Switching wide sleep transistor costs dynamic power
  Only justified when circuit sleeps long enough