## Slide 1: Lecture 0: Introduction
Notes: <number>

## Slide 2: Learning Objectives
0: Introduction
<number>
At the end of this lecture, you should be able to
Define CMOS VLSI Design
Explain the behavior of CMOS transistors as digital switches
Design logic gates using transistors
Sketch cross-sections of transistors and logic gates
Describe the masks and steps used to fabricate a CMOS circuit
Notes: <number>

## Slide 3: Introduction
0: Introduction
<number>
Integrated circuits: many transistors on one chip.
Very Large Scale Integration (VLSI): bucketloads!
Complementary Metal Oxide Semiconductor
  Fast, cheap, low power transistors
Today: How to build your own simple CMOS chip
  CMOS transistors
  Building logic gates from transistors
  Transistor layout and fabrication
Rest of the course: How to build a good CMOS chip
Notes: <number>

## Slide 4: Silicon Lattice
0: Introduction
<number>
Transistors are built on a silicon substrate
Silicon is a Group IV material
Forms crystal lattice with bonds to four neighbors
Notes: <number>

## Slide 5: Dopants
0: Introduction
<number>
Silicon is a semiconductor
Pure silicon has no free carriers and conducts poorly
Adding dopants increases the conductivity
Group V: extra electron (n-type)
Group III: missing electron, called hole (p-type)
Notes: <number>

## Slide 6: p-n Junctions
0: Introduction
<number>
A junction between p-type and n-type semiconductor forms a diode.
Current flows only in one direction
Notes: <number>

## Slide 7: nMOS Transistor
0: Introduction
<number>
Four terminals: gate, source, drain, body
Symbol shows gate, source, drain
  Usually omits body
  Source and drain are logically indistinguishable
Notes: <number>

## Slide 8: nMOS Transistor
0: Introduction
<number>
Gate – oxide – body stack looks like a capacitor
  Gate and body are conductors
  Body is lightly doped p-type
  Gate is metal or polycrystalline silicon (polysilicon)
  SiO2 (oxide) is an excellent insulator
  Called metal – oxide – semiconductor (MOS) capacitor
Source and drain are
heavily doped (n+) silicon
Notes: <number>

## Slide 9: nMOS Operation
0: Introduction
<number>
Body is usually tied to ground (0 V)
When the gate is at a low voltage:
  P-type body is at low voltage
  Source-body and drain-body diodes are OFF
  No current flows, transistor is OFF
Notes: <number>

## Slide 10: nMOS Operation Cont.
0: Introduction
<number>
When the gate is at a high voltage:
  Positive charge on gate of MOS capacitor
  Negative charge attracted to body
  Inverts a channel under gate to n-type
  Now current can flow through n-type silicon from source through channel to drain, transistor is ON
Notes: <number>

## Slide 11: pMOS Transistor
0: Introduction
<number>
Similar, but doping and voltages reversed
  Body tied to high voltage (VDD)
  Gate low: transistor ON
  Gate high: transistor OFF
  Bubble indicates inverted behavior
Notes: <number>

## Slide 12: Power Supply Voltage
0: Introduction
<number>
GND = 0 V
In 1980’s, VDD = 5V
VDD has decreased in modern processes
  High VDD would damage modern tiny transistors
  Lower VDD saves power
VDD = 3.3, 2.5, 1.8, 1.5, 1.2, 1.0, 0.8, 0.7, …
  Gradually scaling down as transistors shrink
Notes: <number>

## Slide 13: Transistors as Switches
0: Introduction
<number>
We can view MOS transistors as electrically controlled switches
Voltage at gate controls path from source to drain
Notes: <number>

## Slide 14: CMOS Inverter
0: Introduction
<number>
0
A | Y
0 | 1
1 | 0
OFF
ON
1
ON
OFF
Notes: <number>

## Slide 15: CMOS NAND Gate
0: Introduction
<number>
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
OFF
OFF
ON
ON
1
1
OFF
ON
OFF
ON
0
1
ON
OFF
ON
OFF
1
0
ON
ON
OFF
OFF
0
0
Notes: <number>

## Slide 16: CMOS NOR Gate
0: Introduction
<number>
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Notes: <number>

## Slide 17: 3-input NAND Gate
0: Introduction
<number>
Y pulls low if ALL inputs are 1
Y pulls high if ANY input is 0
Notes: <number>

## Slide 18: CMOS Fabrication
0: Introduction
<number>
CMOS transistors are fabricated on silicon wafer
Lithography process similar to printing press
On each step, different materials are deposited or etched
Easiest to understand by viewing both top and cross-section of wafer in a simplified manufacturing process
Notes: <number>

## Slide 19: Inverter Cross-section
0: Introduction
<number>
Typically use p-type substrate for nMOS transistors
Requires n-well for body of pMOS transistors
  So pMOS p-type source/drain doesn’t short to p-type substrate
Notes: <number>

## Slide 20: Well and Substrate Taps
0: Introduction
<number>
Substrate must be tied to GND and n-well to VDD
Metal to lightly-doped semiconductor forms poor connection called Shottky Diode
Use heavily doped well and substrate contacts / taps
Notes: <number>

## Slide 21: Inverter Mask Set
0: Introduction
<number>
Transistors and wires are defined by masks
Cross-section taken along dashed line
Notes: <number>

## Slide 22: Detailed Mask Views
0: Introduction
<number>
Six masks
  n-well
  Polysilicon
  n+ diffusion
  p+ diffusion
  Contact
  Metal
Notes: <number>

## Slide 23: Fabrication
0: Introduction
<number>
Chips are built in huge factories called fabs
Contain clean rooms as large as football fields, costing billions of dollars
Courtesy of International
Business Machines Corporation.
Unauthorized use not permitted.
Notes: <number>

## Slide 24: Fabrication Steps
0: Introduction
<number>
Start with blank wafer
Build inverter from the bottom up
First step will be to form the n-well
  Cover wafer with protective layer of SiO2 (oxide)
  Remove layer where n-well should be built
  Implant or diffuse n dopants into exposed wafer
  Strip off SiO2
Notes: <number>

## Slide 25: Oxidation
0: Introduction
<number>
Grow SiO2 on top of Si wafer
  900 – 1200 C with H2O or O2 in oxidation furnace
Notes: <number>

## Slide 26: Photoresist
0: Introduction
<number>
Spin on photoresist
  Photoresist is a light-sensitive organic polymer
  Softens where exposed to light
Notes: <number>

## Slide 27: Lithography
0: Introduction
<number>
Expose photoresist through n-well mask
Strip off exposed photoresist
Notes: <number>

## Slide 28: Etch
0: Introduction
<number>
Etch oxide with hydrofluoric acid (HF)
  Seeps through skin and eats bone; nasty stuff!!!
Only attacks oxide where resist has been exposed
Notes: <number>

## Slide 29: Strip Photoresist
0: Introduction
<number>
Strip off remaining photoresist
  Use mixture of acids called piranah etch
Necessary so resist doesn’t melt in next step
Notes: <number>

## Slide 30: n-well
0: Introduction
<number>
n-well is formed with diffusion or ion implantation
Diffusion
  Place wafer in furnace with arsenic gas
  Heat until As atoms diffuse into exposed Si
Ion Implanatation
  Blast wafer with beam of As ions
  Ions blocked by SiO2, only enter exposed Si
Notes: <number>

## Slide 31: Strip Oxide
0: Introduction
<number>
Strip off the remaining oxide using HF
Back to bare wafer with n-well
Subsequent steps involve similar series of steps
Notes: <number>

## Slide 32: Polysilicon
0: Introduction
<number>
Deposit very thin layer of gate oxide
  < 20 Å (6-7 atomic layers)
Chemical Vapor Deposition (CVD) of silicon layer
  Place wafer in furnace with Silane gas (SiH4)
  Forms many small crystals called polysilicon
  Heavily doped to be good conductor
Notes: <number>

## Slide 33: Polysilicon Patterning
0: Introduction
<number>
Use same lithography process to pattern polysilicon
Notes: <number>

## Slide 34: Self-Aligned Process
0: Introduction
<number>
Use oxide and masking to expose where n+ dopants should be diffused or implanted
N-diffusion forms nMOS source, drain, and n-well contact
Notes: <number>

## Slide 35: N-diffusion
0: Introduction
<number>
Pattern oxide and form n+ regions
Self-aligned process where gate blocks diffusion
Polysilicon is better than metal for self-aligned gates because it doesn’t melt during later processing
Notes: <number>

## Slide 36: N-diffusion cont.
0: Introduction
<number>
Historically dopants were diffused
Usually ion implantation today
But regions are still called diffusion
Notes: <number>

## Slide 37: N-diffusion cont.
0: Introduction
<number>
Strip off oxide to complete patterning step
Notes: <number>

## Slide 38: P-Diffusion
0: Introduction
<number>
Similar set of steps form p+ diffusion regions for pMOS source and drain and substrate contact
Notes: <number>

## Slide 39: Contacts
0: Introduction
<number>
Now we need to wire together the devices
Cover chip with thick field oxide
Etch oxide where contact cuts are needed
Notes: <number>

## Slide 40: Metalization
0: Introduction
<number>
Sputter on aluminum over whole wafer
Pattern to remove excess metal, leaving wires
Notes: <number>

## Slide 41: Layout
0: Introduction
<number>
Chips are specified with set of masks
Minimum dimensions of masks determine transistor size (and hence speed, cost, and power)
Feature size f = distance between source and drain
  Set by minimum width of polysilicon
Feature size improves 30% every 3 years or so
Normalize for feature size when describing design rules
Express rules in terms of λ = f/2
  E.g.λ= 0.3 μm in 0.6 μm process
Notes: <number>

## Slide 42: Simplified Design Rules
0: Introduction
<number>
Conservative rules to get you started
Notes: <number>

## Slide 43: Inverter Layout
0: Introduction
<number>
Transistor dimensions specified as Width / Length
  Minimum size is 4λ / 2λsometimes called 1 unit
  In f = 0.6 μm process, this is 1.2 μm wide, 0.6 μm long
Notes: <number>

## Slide 44: Summary
0: Introduction
<number>
MOS transistors are stacks of gate, oxide, silicon
Act as electrically controlled switches
Build logic gates out of switches
Draw masks to specify layout of transistors
Now you know everything necessary to start designing schematics and layout for a simple chip!
Notes: <number>

## Slide 45: About these Notes
0: Introduction
<number>
Lecture notes © 2020 David Harris
These notes may be used and modified for educational and/or non-commercial purposes so long as the source is attributed.
Notes: <number>