## Slide 1: Lecture 10: Circuit Families
Notes: <number>

## Slide 2: Outline
10: Circuit Families
<number>
Pseudo-nMOS Logic
Dynamic Logic
Pass Transistor Logic
Notes: <number>

## Slide 3: Introduction
10: Circuit Families
<number>
What makes a circuit fast?
  I = C dV/dt -> tpd ≈ (C/I) ΔV
  low capacitance
  high current
  small swing
Logical effort is proportional to C/I
pMOS are the enemy!
  High capacitance for a given current
Can we take the pMOS capacitance off the input?
Various circuit families try to do this…
Notes: <number>

## Slide 4: Pseudo-nMOS
10: Circuit Families
<number>
In the old days, nMOS processes had no pMOS
  Instead, use pull-up transistor that is always ON
In CMOS, use a pMOS that is always ON
  Ratio issue
  Make pMOS about ¼ effective strength of pulldown network
Notes: <number>

## Slide 5: Pseudo-nMOS Gates
10: Circuit Families
<number>
Design for unit current on output
to compare with unit inverter.
pMOS fights nMOS
Notes: <number>

## Slide 6: Pseudo-nMOS Gates
10: Circuit Families
<number>
Design for unit current on output
to compare with unit inverter.
pMOS fights nMOS
Notes: <number>

## Slide 7: Pseudo-nMOS Design
10: Circuit Families
<number>
Ex: Design a k-input AND gate using pseudo-nMOS. Estimate the delay driving a fanout of H
G = 1 * 8/9 = 8/9
F = GBH = 8H/9
P = 1 + (4+8k)/9 = (8k+13)/9
N = 2
D = NF1/N + P =
Notes: <number>

## Slide 8: Pseudo-nMOS Power
10: Circuit Families
<number>
Pseudo-nMOS draws power whenever Y = 0
  Called static power P = IDDVDD
  A few mA / gate * 1M gates would be a problem
  Explains why nMOS went extinct
Use pseudo-nMOS sparingly for wide NORs
Turn off pMOS when not in use
Notes: <number>

## Slide 9: Ratio Example
10: Circuit Families
<number>
The chip contains a 32 word x 48 bit ROM
  Uses pseudo-nMOS decoder and bitline pullups
  On average, one wordline and 24 bitlines are high
Find static power drawn by the ROM
  Ion-p = 36 A, VDD = 1.0 V
Solution:
Notes: <number>

## Slide 10: Dynamic Logic
10: Circuit Families
<number>
Dynamic gates uses a clocked pMOS pullup
Two modes: precharge and evaluate
Notes: <number>

## Slide 11: The Foot
10: Circuit Families
<number>
What if pulldown network is ON during precharge?
Use series evaluation transistor to prevent fight.
Notes: <number>

## Slide 12: Logical Effort
10: Circuit Families
<number>
Notes: <number>

## Slide 13: Monotonicity
10: Circuit Families
<number>
Dynamic gates require monotonically rising inputs during evaluation
  0 -> 0
  0 -> 1
  1 -> 1
  But not 1 -> 0
Notes: <number>

## Slide 14: Monotonicity Woes
10: Circuit Families
<number>
But dynamic gates produce monotonically falling outputs during evaluation
Illegal for one dynamic gate to drive another!
Notes: <number>

## Slide 15: Domino Gates
10: Circuit Families
<number>
Follow dynamic stage with inverting static gate
  Dynamic / static pair is called domino gate
  Produces monotonic outputs
Notes: <number>

## Slide 16: Domino Optimizations
10: Circuit Families
<number>
Each domino gate triggers next one, like a string of dominos toppling over
Gates evaluate sequentially but precharge in parallel
Thus evaluation is more critical than precharge
HI-skewed static stages can perform logic
Notes: <number>

## Slide 17: Dual-Rail Domino
10: Circuit Families
<number>
Domino only performs noninverting functions:
  AND, OR but not NAND, NOR, or XOR
Dual-rail domino solves this problem
  Takes true and complementary inputs
  Produces true and complementary outputs
sig_h | sig_l | Meaning
0 | 0 | Precharged
0 | 1 | ‘0’
1 | 0 | ‘1’
1 | 1 | invalid
Notes: <number>

## Slide 18: Example: AND/NAND
10: Circuit Families
<number>
Given A_h, A_l, B_h, B_l
Compute Y_h = AB, Y_l = AB
Pulldown networks are conduction complements
Notes: <number>

## Slide 19: Example: XOR/XNOR
10: Circuit Families
<number>
Sometimes possible to share transistors
Notes: <number>

## Slide 20: Leakage
10: Circuit Families
<number>
Dynamic node floats high during evaluation
  Transistors are leaky (IOFF > 0)
  Dynamic value will leak away over time
  Formerly milliseconds, now nanoseconds
Use keeper to hold dynamic node
  Must be weak enough not to fight evaluation
Notes: <number>

## Slide 21: Charge Sharing
10: Circuit Families
<number>
Dynamic gates suffer from charge sharing
Notes: <number>

## Slide 22: Secondary Precharge
10: Circuit Families
<number>
Solution: add secondary precharge transistors
  Typically need to precharge every other node
Big load capacitance CY helps as well
Notes: <number>

## Slide 23: Noise Sensitivity
10: Circuit Families
<number>
Dynamic gates are very sensitive to noise
  Inputs: VIH ≈ Vtn
  Outputs: floating output susceptible noise
Noise sources
  Capacitive crosstalk
  Charge sharing
  Power supply noise
  Feedthrough noise
  And more!
Notes: <number>

## Slide 24: Power
10: Circuit Families
<number>
Domino gates have high activity factors
  Output evaluates and precharges
    If output probability = 0.5, α = 0.5
      Output rises and falls on half the cycles
  Clocked transistors have α = 1
Leads to very high power consumption
Notes: <number>

## Slide 25: Domino Summary
10: Circuit Families
<number>
Domino logic is attractive for high-speed circuits
  1.3 – 2x faster than static CMOS
  But many challenges:
    Monotonicity, leakage, charge sharing, noise
Widely used in high-performance microprocessors in 1990s when speed was king
Largely displaced by static CMOS now that power is the limiter
Still used in memories for area efficiency
Notes: <number>

## Slide 26: Pass Transistor Circuits
10: Circuit Families
<number>
Use pass transistors like switches to do logic
Inputs drive diffusion terminals as well as gates
CMOS + Transmission Gates:
  2-input multiplexer
  Gates should be restoring
Notes: <number>

## Slide 27: LEAP
10: Circuit Families
<number>
LEAn integration with Pass transistors
Get rid of pMOS transistors
  Use weak pMOS feedback to pull fully high
  Ratio constraint
Notes: <number>

## Slide 28: CPL
10: Circuit Families
<number>
Complementary Pass-transistor Logic
  Dual-rail form of pass transistor logic
  Avoids need for ratioed feedback
  Optional cross-coupling for rail-to-rail swing
Notes: <number>

## Slide 29: Pass Transistor Summary
10: Circuit Families
<number>
Researchers investigated pass transistor logic for general purpose applications in the 1990’s
  Benefits over static CMOS were small or negative
  No longer generally used
However, pass transistors still have a niche in special circuits such as memories where they offer small size and the threshold drops can be managed
Notes: <number>