## Slide 1: Lecture 16: CAMs, ROMs, PLAs
Notes: <number>

## Slide 2: Outline
20: CAMs, ROMs, and PLAs
<number>
Content-Addressable Memories
Read-Only Memories
Programmable Logic Arrays
Notes: <number>

## Slide 3: CAMs
20: CAMs, ROMs, and PLAs
<number>
Extension of ordinary memory (e.g. SRAM)
  Read and write memory as usual
  Also match to see which words contain a key
Notes: <number>

## Slide 4: 10T CAM Cell
20: CAMs, ROMs, and PLAs
<number>
Add four match transistors to 6T SRAM
  56 x 43 λ unit cell
Notes: <number>

## Slide 5: CAM Cell Operation
20: CAMs, ROMs, and PLAs
<number>
Read and write like ordinary SRAM
For matching:
  Leave wordline low
  Precharge matchlines
  Place key on bitlines
  Matchlines evaluate
Miss line
  Pseudo-nMOS NOR of match lines
  Goes high if no words match
Notes: <number>

## Slide 6: Read-Only Memories
20: CAMs, ROMs, and PLAs
<number>
Read-Only Memories are nonvolatile
  Retain their contents when power is removed
Mask-programmed ROMs use one transistor per bit
  Presence or absence determines 1 or 0
Notes: <number>

## Slide 7: ROM Example
20: CAMs, ROMs, and PLAs
<number>
4-word x 6-bit ROM
  Represented with dot diagram
  Dots indicate 1’s in ROM
Word 0: 010101
Word 1: 011001
Word 2: 100101
Word 3: 101010
Looks like 6 4-input pseudo-nMOS NORs
Notes: <number>

## Slide 8: ROM Array Layout
20: CAMs, ROMs, and PLAs
<number>
Unit cell is 12 x 8 λ(about 1/10 size of SRAM)
Notes: <number>

## Slide 9: Row Decoders
20: CAMs, ROMs, and PLAs
<number>
ROM row decoders must pitch-match with ROM
  Only a single track per word!
Notes: <number>

## Slide 10: Complete ROM Layout
20: CAMs, ROMs, and PLAs
<number>
Notes: <number>

## Slide 11: PROMs and EPROMs
20: CAMs, ROMs, and PLAs
<number>
Programmable ROMs
  Build array with transistors at every site
  Burn out fuses to disable unwanted transistors
Electrically Programmable ROMs
  Use floating gate to turn off unwanted transistors
  EPROM, EEPROM, Flash
Notes: <number>

## Slide 12: Flash Programming
20: CAMs, ROMs, and PLAs
<number>
Charge on floating gate determines Vt
Logic 1: negative Vt
Logic 0: positive Vt
Cells erased to 1 by applying a high body voltage so that electrons tunnel off floating gate into substrate
Programmed to 0 by applying high gate voltage
Notes: <number>

## Slide 13: NAND Flash
20: CAMs, ROMs, and PLAs
<number>
High density, low cost / bit
  Programmed one page at a time
  Erased one block at a time
Example:
  4096-bit pages
  16 pages / 8 KB block
  Many blocks / memory
Notes: <number>

## Slide 14: 64 Gb NAND Flash
20: CAMs, ROMs, and PLAs
<number>
64K cells / page
4 bits / cell (multiple Vt)
64 cells / string
  256 pages / block
2K blocks / plane
2 planes
[Trinh09]
Notes: <number>

## Slide 15: Building Logic with ROMs
20: CAMs, ROMs, and PLAs
<number>
Use ROM as lookup table containing truth table
  n inputs, k outputs requires 2n words x k bits
  Changing function is easy – reprogram ROM
Finite State Machine
  n inputs, k outputs, s bits of state
  Build with 2n+s x (k+s) bit ROM and (k+s) bit reg
Notes: <number>

## Slide 16: Example: RoboAnt
20: CAMs, ROMs, and PLAs
<number>
Let’s build an Ant
Sensors: Antennae
(L,R) – 1 when in contact
Actuators: Legs
Forward step F
Ten degree turns TL, TR
Goal: make our ant smart enough to
get out of a maze
Strategy: keep right antenna on wall
(RoboAnt adapted from MIT 6.004 2002 OpenCourseWare by Ward and Terman)
L
R
Notes: <number>

## Slide 17: Lost in space
20: CAMs, ROMs, and PLAs
<number>
Action: go forward until we hit something
  Initial state
Notes: <number>

## Slide 18: Bonk!!!
20: CAMs, ROMs, and PLAs
<number>
Action: turn left (rotate counterclockwise)
  Until we don’t touch anymore
Notes: <number>

## Slide 19: A little to the right
20: CAMs, ROMs, and PLAs
<number>
Action: step forward and turn right a little
  Looking for wall
Notes: <number>

## Slide 20: Then a little to the left
20: CAMs, ROMs, and PLAs
<number>
Action: step and turn left a little, until not touching
Notes: <number>

## Slide 21: Whoops – a corner!
20: CAMs, ROMs, and PLAs
<number>
Action: step and turn right until hitting next wall
Notes: <number>

## Slide 22: Simplification
20: CAMs, ROMs, and PLAs
<number>
Merge equivalent states where possible
Notes: <number>

## Slide 23: State Transition Table
20: CAMs, ROMs, and PLAs
<number>
S1:0 | L | R | S1:0’ | TR | TL | F
00 | 0 | 0 | 00 | 0 | 0 | 1
00 | 1 | X | 01 | 0 | 0 | 1
00 | 0 | 1 | 01 | 0 | 0 | 1
01 | 1 | X | 01 | 0 | 1 | 0
01 | 0 | 1 | 01 | 0 | 1 | 0
01 | 0 | 0 | 10 | 0 | 1 | 0
10 | X | 0 | 10 | 1 | 0 | 1
10 | X | 1 | 11 | 1 | 0 | 1
11 | 1 | X | 01 | 0 | 1 | 1
11 | 0 | 0 | 10 | 0 | 1 | 1
11 | 0 | 1 | 11 | 0 | 1 | 1
Lost
RCCW
Wall1
Wall2
Notes: <number>

## Slide 24: ROM Implementation
20: CAMs, ROMs, and PLAs
<number>
16-word x 5 bit ROM
Notes: <number>

## Slide 25: ROM Implementation
20: CAMs, ROMs, and PLAs
<number>
16-word x 5 bit ROM
Notes: <number>

## Slide 26: PLAs
20: CAMs, ROMs, and PLAs
<number>
A Programmable Logic Array performs any function in sum-of-products form.
Literals: inputs & complements
Products / Minterms: AND of literals
Outputs: OR of Minterms
Example: Full Adder
Notes: <number>

## Slide 27: NOR-NOR PLAs
20: CAMs, ROMs, and PLAs
<number>
ANDs and ORs are not very efficient in CMOS
Dynamic or Pseudo-nMOS NORs are very efficient
Use DeMorgan’s Law to convert to all NORs
Notes: <number>

## Slide 28: PLA Schematic & Layout
20: CAMs, ROMs, and PLAs
<number>
Notes: <number>

## Slide 29: PLAs vs. ROMs
20: CAMs, ROMs, and PLAs
<number>
The OR plane of the PLA is like the ROM array
The AND plane of the PLA is like the ROM decoder
PLAs are more flexible than ROMs
  No need to have 2n rows for n inputs
  Only generate the minterms that are needed
  Take advantage of logic simplification
Notes: <number>

## Slide 30: Example: RoboAnt PLA
20: CAMs, ROMs, and PLAs
<number>
Convert state transition table to logic equations
S1:0 | L | R | S1:0’ | TR | TL | F
00 | 0 | 0 | 00 | 0 | 0 | 1
00 | 1 | X | 01 | 0 | 0 | 1
00 | 0 | 1 | 01 | 0 | 0 | 1
01 | 1 | X | 01 | 0 | 1 | 0
01 | 0 | 1 | 01 | 0 | 1 | 0
01 | 0 | 0 | 10 | 0 | 1 | 0
10 | X | 0 | 10 | 1 | 0 | 1
10 | X | 1 | 11 | 1 | 0 | 1
11 | 1 | X | 01 | 0 | 1 | 1
11 | 0 | 0 | 10 | 0 | 1 | 1
11 | 0 | 1 | 11 | 0 | 1 | 1
Notes: <number>

## Slide 31: RoboAnt Dot Diagram
20: CAMs, ROMs, and PLAs
<number>
Notes: <number>