## Slide 1: Lecture 17: Scaling & Economics
Notes: <number>

## Slide 2: Outline
15: Scaling and Economics
<number>
Scaling
  Transistors
  Interconnect
  Future Challenges
Economics
Notes: <number>

## Slide 3: Moore’s Law
15: Scaling and Economics
<number>
Recall that Moore’s Law has been driving CMOS
[Moore65]
Moore’s Law today
Corollary: clock speeds have improved
Notes: <number>

## Slide 4: Why?
15: Scaling and Economics
<number>
Why more transistors per IC?
  Smaller transistors
  Larger dice
Why faster computers?
  Smaller, faster transistors
  Better microarchitecture (more IPC)
  Fewer gate delays per cycle
Notes: <number>

## Slide 5: Scaling
15: Scaling and Economics
<number>
The only constant in VLSI is constant change
Feature size shrinks by 30% every 2-3 years
  Transistors become cheaper
  Transistors become faster and lower power
  Wires do not improve
  (and may get worse)
Scale factor S
  Typically
  Technology nodes
Notes: <number>

## Slide 6: Dennard Scaling
15: Scaling and Economics
<number>
Proposed by Dennard in 1974
Also known as constant field scaling
  Electric fields remain the same as features scale
Scaling assumptions
  All dimensions (x, y, z => W, L, tox)
  Voltage (VDD)
  Doping levels
Notes: <number>

## Slide 7: Device Scaling
15: Scaling and Economics
<number>
Parameter | Sensitivity | Dennard Scaling
L: Length |  | 1/S
W: Width |  | 1/S
tox: gate oxide thickness |  | 1/S
VDD: supply voltage |  | 1/S
Vt: threshold voltage |  | 1/S
NA: substrate doping |  | S
β | W/(Ltox) | S
Ion: ON current | β(VDD-Vt)2 | 1/S
R: effective resistance | VDD/Ion | 1
C: gate capacitance | WL/tox | 1/S
τ: gate delay | RC | 1/S
f: clock frequency | 1/τ | S
E: switching energy / gate | CVDD2 | 1/S3
P: switching power / gate | Ef | 1/S2
A: area per gate | WL | 1/S2
Switching power density | P/A | 1
Switching current density | Ion/A | S
Notes: <number>

## Slide 8: Observations
15: Scaling and Economics
<number>
Gate capacitance per micron is nearly independent of process
But ON resistance * micron improves with process
Gates get faster with scaling (good)
Dynamic power goes down with scaling (good)
Current density goes up with scaling (bad)
Notes: <number>

## Slide 9: Example
15: Scaling and Economics
<number>
Gate capacitance is typically about 1 fF/m
The typical FO4 inverter delay for a process of feature size f (in nm) is about 0.5f ps
Estimate the ON resistance of a unit (4/2 λ) transistor.
FO4 = 5 τ = 15 RC
RC = (0.5f) / 15 = (f/30) ps/nm
If W = 2f, R = 16.6 k
  Unit resistance is roughly independent of f
Notes: <number>

## Slide 10: Real Scaling
15: Scaling and Economics
<number>
tox scaling has slowed since 65 nm
  Limited by gate tunneling current
  Gates are only about 4 atomic layers thick!
  High-k dielectrics have helped continued scaling of effective oxide thickness
VDD scaling has slowed since 65 nm
  SRAM cell stability at low voltage is challenging
Dennard scaling predicts cost, speed, power all improve
  Below 65 nm, some designers find they must choose just two of the three
Notes: <number>

## Slide 11: Wire Scaling
15: Scaling and Economics
<number>
Wire cross-section
  w, s, t all scale
Wire length
  Local / scaled interconnect
  Global interconnect
    Die size scaled by Dc ≈ 1.1
Notes: <number>

## Slide 12: Interconnect Scaling
15: Scaling and Economics
<number>
Parameter | Sensitivity | Scale Factor
w: width |  | 1/S
s: spacing |  | 1/S
t: thickness |  | 1/S
h: height |  | 1/S
Dc: die size |  | Dc
Rw: wire resistance/unit length | 1/wt | S2
Cwf: fringing capacitance / unit length | t/s | 1
Cwp: parallel plate capacitance / unit length | w/h | 1
Cw: total wire capacitance / unit length | Cwf + Cwp | 1
twu: unrepeated RC delay / unit length | RwCw | S2
twr: repeated RC delay / unit length | sqrt(RCRwCw) | sqrt(S)
Crosstalk noise | w/h | 1
Ew: energy per bit / unit length | CwVDD2 | 1/S2
Notes: <number>

## Slide 13: Interconnect Delay
15: Scaling and Economics
<number>
Parameter | Sensitivity | Local / Semiglobal | Global
l: length |  | 1/S | Dc
Unrepeated wire RC delay | l2twu | 1 | S2Dc2
Repeated wire delay | ltwr | sqrt(1/S) | Dcsqrt(S)
Energy per bit | lEw | 1/S3 | Dc/S2
Notes: <number>

## Slide 14: Observations
15: Scaling and Economics
<number>
Capacitance per micron is remaining constant
  About 0.2 fF/m
  Roughly 1/5 of gate capacitance
Local wires are getting faster
  Not quite tracking transistor improvement
  But not a major problem
Global wires are getting slower
  No longer possible to cross chip in one cycle
Notes: <number>

## Slide 15: ITRS
15: Scaling and Economics
<number>
Semiconductor Industry Association forecast
  Intl. Technology Roadmap for Semiconductors
Notes: <number>

## Slide 16: Scaling Implications
15: Scaling and Economics
<number>
Improved Performance
Improved Cost
Interconnect Woes
Power Woes
Productivity Challenges
Physical Limits
Notes: <number>

## Slide 17: Cost Improvement
15: Scaling and Economics
<number>
In 2003, $0.01 bought you 100,000 transistors
  Moore’s Law is still going strong
[Moore03]
Notes: <number>

## Slide 18: Interconnect Woes
15: Scaling and Economics
<number>
SIA made a gloomy forecast in 1997
  Delay would reach minimum at 250 – 180 nm, then get worse because of wires
But…
  Misleading scale
  Global wires
100 kgate blocks ok
[SIA97]
Notes: <number>

## Slide 19: Reachable Radius
15: Scaling and Economics
<number>
We can’t send a signal across a large fast chip in one cycle anymore
But the microarchitect can plan around this
  Just as off-chip memory latencies were tolerated
Notes: <number>

## Slide 20: Dynamic Power
15: Scaling and Economics
<number>
Intel VP Patrick Gelsinger (ISSCC 2001)
  If scaling continues at present pace, by 2005, high speed processors would have power density of nuclear reactor, by 2010, a rocket nozzle, and by 2015, surface of sun.
  “Business as usual will not work in the future.”
Attention to power is
increasing
[Intel]
Notes: <number>

## Slide 21: Static Power
15: Scaling and Economics
<number>
VDD decreases
  Save dynamic power
  Protect thin gate oxides and short channels
  No point in high value because of velocity sat.
Vt must decrease to
maintain device performance
But this causes exponential
increase in OFF leakage
Major future challenge
Static
Dynamic
[Moore03]
Notes: <number>

## Slide 22: Productivity
15: Scaling and Economics
<number>
Transistor count is increasing faster than designer productivity (gates / week)
  Bigger design teams
    Up to 500 for a high-end microprocessor
  More expensive design cost
  Pressure to raise productivity
    Rely on synthesis, IP blocks
  Need for good engineering managers
Notes: <number>

## Slide 23: Physical Limits
15: Scaling and Economics
<number>
Will Moore’s Law run out of steam?
  Can’t build transistors smaller than an atom…
Many reasons have been predicted for end of scaling
  Dynamic power
  Subthreshold leakage, tunneling
  Short channel effects
  Fabrication costs
  Electromigration
  Interconnect delay
Rumors of demise have been exaggerated
Notes: <number>

## Slide 24: VLSI Economics
15: Scaling and Economics
<number>
Selling price Stotal
  Stotal = Ctotal / (1-m)
m = profit margin
Ctotal = total cost
  Nonrecurring engineering cost (NRE)
  Recurring cost
  Fixed cost
Notes: <number>

## Slide 25: NRE
15: Scaling and Economics
<number>
Engineering cost
  Depends on size of design team
  Include benefits, training, computers
  CAD tools:
    Digital front end: $10K
    Analog front end: $100K
    Digital back end: $1M
Prototype manufacturing
  Mask costs: $5M in 45 nm process
  Test fixture and package tooling
Notes: <number>

## Slide 26: Recurring Costs
15: Scaling and Economics
<number>
Fabrication
  Wafer cost / (Dice per wafer * Yield)
  Wafer cost: $500 - $3000
  Dice per wafer:
  Yield: Y = e-AD
    For small A, Y ≈ 1, cost proportional to area
    For large A, Y ≈ 0, cost increases exponentially
Packaging
Test
Notes: <number>

## Slide 27: Fixed Costs
15: Scaling and Economics
<number>
Data sheets and application notes
Marketing and advertising
Yield analysis
Notes: <number>

## Slide 28: Example
15: Scaling and Economics
<number>
You want to start a company to build a wireless communications chip. How much venture capital must you raise?
Because you are smarter than everyone else, you can get away with a small team in just two years:
  Seven digital designers
  Three analog designers
  Five support personnel
Notes: <number>

## Slide 29: Solution
15: Scaling and Economics
<number>
Digital designers:
  $70k salary
  $30k overhead
  $10k computer
  $10k CAD tools
  Total: $120k * 7 = $840k
Analog designers
  $100k salary
  $30k overhead
  $10k computer
  $100k CAD tools
  Total: $240k * 3 = $720k
Support staff
  $45k salary
  $20k overhead
  $5k computer
  Total: $70k * 5 = $350k
Fabrication
  Back-end tools: $1M
  Masks: $5M
  Total: $6M / year
Summary
  2 years @ $7.91M / year
  $16M design & prototype
Notes: <number>