## Slide 1: Lecture 22: I/O
Notes: <number>

## Slide 2: Outline
23: I/O
<number>
Basic I/O Pads
I/O Channels
  Transmission Lines
  Noise and Interference
High-Speed I/O
  Transmitters
  Receivers
Clock Recovery
  Source-Synchronous
  Mesochronous
Notes: <number>

## Slide 3: Input / Output
23: I/O
<number>
Input/Output System functions
  Communicate between chip and external world
  Drive large capacitance off chip
  Operate at compatible voltage levels
  Provide adequate bandwidth
  Limit slew rates to control di/dt noise
  Protect chip against electrostatic discharge
  Use small number of pins (low cost)
Notes: <number>

## Slide 4: I/O Pad Design
23: I/O
<number>
Pad types
  VDD / GND
  Output
  Input
  Bidirectional
  Analog
Notes: <number>

## Slide 5: Output Pads
23: I/O
<number>
Drive large off-chip loads (2 – 50 pF)
  With suitable rise/fall times
  Requires chain of successively larger buffers
Guard rings to protect against latchup
  Noise below GND injects charge into substrate
  Large nMOS output transistor
  p+ inner guard ring
  n+ outer guard ring
    In n-well
Notes: <number>

## Slide 6: Input Pads
23: I/O
<number>
Level conversion
  Higher or lower off-chip V
  May need thick oxide gates
Noise filtering
  Schmitt trigger
  Hysteresis changes VIH, VIL
Protection against electrostatic discharge
Notes: <number>

## Slide 7: ESD Protection
23: I/O
<number>
Static electricity builds up on your body
  Shock delivered to a chip can fry thin gates
  Must dissipate this energy in protection circuits before it reaches the gates
ESD protection circuits
  Current limiting resistor
  Diode clamps
ESD testing
  Human body model
  Views human as charged capacitor
Notes: <number>

## Slide 8: Bidirectional Pads
23: I/O
<number>
Combine input and output pad
Need tristate driver on output
  Use enable signal to set direction
  Optimized tristate avoids huge series transistors
Notes: <number>

## Slide 9: Analog Pads
23: I/O
<number>
Pass analog voltages directly in or out of chip
  No buffering
  Protection circuits must not distort voltages
Notes: <number>

## Slide 10: MOSIS I/O Pad
23: I/O
<number>
1.6 m two-metal process
  Protection resistors
  Protection diodes
  Guard rings
  Field oxide clamps
Notes: <number>

## Slide 11: UofU I/O Pad
23: I/O
<number>
0.6 m three-metal process
  Similar I/O drivers
  Big driver transistors provide ESD protection
  Guard rings around driver
Notes: <number>

## Slide 12: I/O Channels
23: I/O
<number>
I/O Channel: connection between chips
  Low frequency: ideal equipotential net
  High frequency: transmission line
Transmission lines model
  Finite velocity of signal along wire
  Characteristic impedance of wire
Notes: <number>

## Slide 13: When is a wire a T-Line?
23: I/O
<number>
When propagation delay along the wire is comparable to the edge rate of the signal propagating
Depends on
  Length
  Speed of light in the medium
  Edge rate
Notes: <number>

## Slide 14: Example
23: I/O
<number>
When must a 10 cm trace on a PCB be treated as a transmission line
  FR4 epoxy has k = 4.35 ( = k0)
  Assume rise/fall times are ¼ of cycle time
Signal propagation velocity
Wire flight time
Thus the wire should be treated as a transmission line when signals have a period < 2.8 ns (> 350 MHz)
Notes: <number>

## Slide 15: Characteristic Impedance
23: I/O
<number>
Z0: ratio of voltage to current of a signal along the line
Depends on the geometry of the line
Microstrip: Outer layer of PCB
Stripline: Inner layer of PCB
Notes: <number>

## Slide 16: Example
23: I/O
<number>
A 4-layer PCB contains power and ground planes on the inner layers and signals on the outer layers. The board uses 1 oz copper (1.4 mils thick) and the FR4 dielectric is 8.7 mils thick. How wide should the traces be to achieve 50  characteristic impedance?
This is a microstrip design. Solve for w with
  t = 1.4 mils
  h = 8.7 mils
  k = 4.35
  Z0 = 50 
w = 15 mils
Notes: <number>

## Slide 17: Reflections
23: I/O
<number>
When a wave hits the end of a transmission line, part of the energy will reflect if the load impedance does not match the characteristic impedance.
Reflection coefficient:
A wave with an amplitude of Vreflected = Vincident returns along the line.
Notes: <number>

## Slide 18: Example: Reflections
23: I/O
<number>
A strong driver with a Thevenin equivalent resistance of 10  drives an unterminated transmission line with Z0 = 50  and flight time T. Plot the voltage at the 1/3 point and end of the line.
Reflection coefficients:
Initial wave: 50/(10+50) = 5/6
Observe ringing at load
Notes: <number>

## Slide 19: Intersymbol Interference
23: I/O
<number>
Must wait until reflections damp out before sending next bit
Otherwise, intersymbol interference will occur
With an unterminated transmission line, minimum bit time is equal to several round trips along the line
Notes: <number>

## Slide 20: Example: Load Termination
23: I/O
<number>
Redo the previous example if the load is terminated with a 50  resistor.
Reflection coefficients:
Initial wave: 50/(10+50) = 5/6
No ringing
Power dissipation in load resistor
Notes: <number>

## Slide 21: Example: Source Termination
23: I/O
<number>
Redo the previous example if the source is terminated with an extra 40  resistor.
Reflection coefficients:
Initial wave: 50/(50+50) = 1/2
No ringing
No power dissipation in load
Taps along T-line momentarily see invalid levels
Notes: <number>

## Slide 22: Termination Summary
23: I/O
<number>
For point-to-point links, source terminate to save power
For multidrop busses, load terminate to ensure valid logic levels
For busses with multiple receivers and drivers, terminate at both ends of the line to prevent reflections from either end
Notes: <number>

## Slide 23: Noise and Interference
23: I/O
<number>
Other sources of intersymbol interference:
  Dispersion
    Caused by nonzero line resistance
  Crosstalk
    Capacitive or inductive coupling between channels
  Ground Bounce
    Nonzero return path impedance
  Simultaneous Switching Noise
Notes: <number>

## Slide 24: High-Speed I/O
23: I/O
<number>
Transmit data faster than the flight time along the line
Transmitters must generate very short pulses
Receivers must be accurately synchronized to detect the pulses
Notes: <number>

## Slide 25: High Speed Transmitters
23: I/O
<number>
How to handle termination?
  High impedance current-mode driver + load term?
  Or low-impedance driver + source termination
Single-ended vs. differential
  Single-ended uses half the wires
  Differential is Immune to common mode noise
Pull-only vs. Push-Pull
  Pull-only has half the transistors
  Push-pull uses less power for the same swing
Notes: <number>

## Slide 26: High-Speed Transmitters
23: I/O
<number>
 | Pull-Only | Push-Pull
Single-Ended |  | 
Differential |  | 
Gunning Transceiver
Logic (GTL)
Current Mode
Logic (CML)
Low-Voltage
Differential
Signalling
(LVDS)
Notes: <number>

## Slide 27: High-Speed Receivers
23: I/O
<number>
Sample data in the middle of the bit interval
How do we know when?
Notes: <number>

## Slide 28: Source-Synchronous Clocking
23: I/O
<number>
Send clock with the data
Flight times roughly match each other
  Transmit on falling edge of tclk
  Receive on rising edge of rclk
Notes: <number>

## Slide 29: Single vs. Double Data Rate
23: I/O
<number>
In ordinary single data rate (SDR) system, clock switches twice as often as the data
If the system can handle this speed clock, the data is running at half the available bandwidth
In double-data-rate (DDR) transmit and receive on both edges of the clock
Notes: <number>

## Slide 30: Phase Alignment
23: I/O
<number>
If the DDR clock is aligned to the transmitted clock, it must be shifted by 90º before sampling
Use PLL
Notes: <number>

## Slide 31: Mesochronous Clocking
23: I/O
<number>
As speeds increase, it is difficult to keep clock and data aligned
  Mismatches in trace lengths
  Mismatches in propagation speeds
  Different in clock vs. data drivers
Mesochronous: clock and data have same frequency but unknown phase
  Use PLL/DLL to realign clock to each data channel
Notes: <number>

## Slide 32: Phase Calibration Loop
23: I/O
<number>
Special phase detector compares clock & data phase
Notes: <number>