## Slide 1: Lecture 5: DC & Transient Response
Notes: <number>

## Slide 2: Outline
5: DC and Transient Response
<number>
Pass Transistors
DC Response
Logic Levels and Noise Margins
Transient Response
RC Delay Models
Delay Estimation
Notes: <number>

## Slide 3: Pass Transistors
5: DC and Transient Response
<number>
We have assumed source is grounded
What if source > 0?
  e.g. pass transistor passing VDD
Vg = VDD
  If Vs > VDD-Vt, then Vgs < Vt
  Hence transistor would turn itself off
nMOS pass transistors pull no higher than VDD-Vtn
  Called a degraded “1”
  Approach degraded value slowly (low Ids)
pMOS pass transistors pull no lower than Vtp
Transmission gates are needed to pass both 0 and 1
Notes: <number>

## Slide 4: Pass Transistor Ckts
5: DC and Transient Response
<number>
Notes: <number>

## Slide 5: DC Response
5: DC and Transient Response
<number>
DC Response: Vout vs. Vin for a gate
Ex: Inverter
  When Vin = 0 -> Vout = VDD
  When Vin = VDD -> Vout = 0
  In between, Vout depends on
  transistor size and current
  By KCL, must settle such that
  Idsn = |Idsp|
  We could solve equations
  But graphical solution gives more insight
Notes: <number>

## Slide 6: Transistor Operation
5: DC and Transient Response
<number>
Current depends on region of transistor behavior
For what Vin and Vout are nMOS and pMOS in
  Cutoff?
  Linear?
  Saturation?
Notes: <number>

## Slide 7: nMOS Operation
5: DC and Transient Response
<number>
Cutoff | Linear | Saturated
Vgsn < Vtn Vin < Vtn | Vgsn > Vtn Vin > Vtn Vdsn < Vgsn – Vtn Vout < Vin - Vtn | Vgsn > Vtn Vin > Vtn Vdsn > Vgsn – Vtn Vout > Vin - Vtn
Vgsn = Vin
Vdsn = Vout
Notes: <number>

## Slide 8: pMOS Operation
5: DC and Transient Response
<number>
Cutoff | Linear | Saturated
Vgsp > Vtp Vin > VDD + Vtp | Vgsp < Vtp Vin < VDD + Vtp Vdsp > Vgsp – Vtp Vout > Vin - Vtp | Vgsp < Vtp Vin < VDD + Vtp Vdsp < Vgsp – Vtp Vout < Vin - Vtp
Vgsp = Vin - VDD
Vdsp = Vout - VDD
Vtp < 0
Notes: <number>

## Slide 9: I-V Characteristics
5: DC and Transient Response
<number>
Make pMOS is wider than nMOS such that n = p
Notes: <number>

## Slide 10: Current vs. Vout, Vin
5: DC and Transient Response
<number>
Notes: <number>

## Slide 11: Load Line Analysis
5: DC and Transient Response
<number>
For a given Vin:
  Plot Idsn, Idsp vs. Vout
  Vout must be where |currents| are equal in
Notes: <number>

## Slide 12: Load Line Analysis
5: DC and Transient Response
<number>
Vin = 0
Vin = 0
0.2VDD
0.4VDD
0.6VDD
0.8VDD
VDD
Notes: <number>

## Slide 13: DC Transfer Curve
5: DC and Transient Response
<number>
Transcribe points onto Vin vs. Vout plot
Notes: <number>

## Slide 14: Operating Regions
5: DC and Transient Response
<number>
Revisit transistor operating regions
Region | nMOS | pMOS
A | Cutoff | Linear
B | Saturation | Linear
C | Saturation | Saturation
D | Linear | Saturation
E | Linear | Cutoff
Notes: <number>

## Slide 15: Beta Ratio
5: DC and Transient Response
<number>
If βp / βn ≈ 1, switching point will move from VDD/2
Called skewed gate
Other gates: collapse into equivalent inverter
Notes: <number>

## Slide 16: Noise Margins
5: DC and Transient Response
<number>
How much noise can a gate input see before it does not recognize the input?
Notes: <number>

## Slide 17: Logic Levels
5: DC and Transient Response
<number>
To maximize noise margins, select logic levels at
  unity gain point of DC transfer characteristic
Notes: <number>

## Slide 18: Transient Response
5: DC and Transient Response
<number>
DC analysis tells us Vout if Vin is constant
Transient analysis tells us Vout(t) if Vin(t) changes
  Requires solving differential equations
Input is usually considered to be a step or ramp
  From 0 to VDD or vice versa
Notes: <number>

## Slide 19: Inverter Step Response
5: DC and Transient Response
<number>
Ex: find step response of inverter driving load cap
Notes: <number>

## Slide 20: Delay Definitions
5: DC and Transient Response
<number>
tpdr: rising propagation delay
  From input to rising output crossing VDD/2
tpdf: falling propagation delay
  From input to falling output crossing VDD/2
tpd: average propagation delay
  tpd = (tpdr + tpdf)/2
tr: rise time
  From output crossing 0.2 VDD to 0.8 VDD
tf: fall time
  From output crossing 0.8 VDD to 0.2 VDD
Notes: <number>

## Slide 21: Delay Definitions
5: DC and Transient Response
<number>
tcdr: rising contamination delay
  From input to rising output crossing VDD/2
tcdf: falling contamination delay
  From input to falling output crossing VDD/2
tcd: average contamination delay
  tpd = (tcdr + tcdf)/2
Notes: <number>

## Slide 22: Simulated Inverter Delay
5: DC and Transient Response
<number>
Solving differential equations by hand is too hard
SPICE simulator solves the equations numerically
  Uses more accurate I-V models too!
But simulations take time to write, may hide insight
Notes: <number>

## Slide 23: Delay Estimation
5: DC and Transient Response
<number>
We would like to be able to easily estimate delay
  Not as accurate as simulation
  But easier to ask “What if?”
The step response usually looks like a 1st order RC response with a decaying exponential.
Use RC delay models to estimate delay
  C = total capacitance on output node
  Use effective resistance R
  So that tpd = RC
Characterize transistors by finding their effective R
  Depends on average current as gate switches
Notes: <number>

## Slide 24: Effective Resistance
5: DC and Transient Response
<number>
Shockley models have limited value
  Not accurate enough for modern transistors
  Too complicated for much hand analysis
Simplification: treat transistor as resistor
  Replace Ids(Vds, Vgs) with effective resistance R
    Ids = Vds/R
  R averaged across switching of digital gate
Too inaccurate to predict current at any given time
  But good enough to predict RC delay
Notes: <number>

## Slide 25: RC Delay Model
5: DC and Transient Response
<number>
Use equivalent circuits for MOS transistors
  Ideal switch + capacitance and ON resistance
  Unit nMOS has resistance R, capacitance C
  Unit pMOS has resistance 2R, capacitance C
Capacitance proportional to width
Resistance inversely proportional to width
Notes: <number>

## Slide 26: RC Values
5: DC and Transient Response
<number>
Capacitance
  C = Cg = Cs = Cd = 2 fF/μm of gate width in 0.6 μm
  Gradually decline to 1 fF/μm in nanometer techs.
Resistance
  R ≈ 6 kΩ*μm in 0.6 m process
  Reduces with shorter channel lengths
Unit transistors
  May refer to minimum contacted device (4/2 )
  Or maybe 1 m wide device
  Doesn’t matter as long as you are consistent
Notes: <number>

## Slide 27: Inverter Delay Estimate
5: DC and Transient Response
<number>
Estimate the delay of a fanout-of-1 inverter
d = 6RC
Notes: <number>

## Slide 28: Delay Model Comparison
5: DC and Transient Response
<number>
Notes: <number>

## Slide 29: Example: 3-input NAND
5: DC and Transient Response
<number>
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R).
3
3
3
2
2
2
Notes: <number>

## Slide 30: 3-input NAND Caps
5: DC and Transient Response
<number>
Annotate the 3-input NAND gate with gate and diffusion capacitance.
Notes: <number>

## Slide 31: Elmore Delay
5: DC and Transient Response
<number>
ON transistors look like resistors
Pullup or pulldown network modeled as RC ladder
Elmore delay of RC ladder
Notes: <number>

## Slide 32: Example: 3-input NAND
5: DC and Transient Response
<number>
Estimate worst-case rising and falling delay of 3-input NAND driving h identical gates.
Notes: <number>

## Slide 33: Delay Components
5: DC and Transient Response
<number>
Delay has two parts
  Parasitic delay
    9 or 11 RC
    Independent of load
  Effort delay
    5h RC
    Proportional to load capacitance
Notes: <number>

## Slide 34: Contamination Delay
5: DC and Transient Response
<number>
Best-case (contamination) delay can be substantially less than propagation delay.
Ex: If all three inputs fall simultaneously
Notes: <number>

## Slide 35: Diffusion Capacitance
5: DC and Transient Response
<number>
We assumed contacted diffusion on every s / d.
Good layout minimizes diffusion area
Ex: NAND3 layout shares one diffusion contact
  Reduces output capacitance by 2C
  Merged uncontacted diffusion might help too
Notes: <number>

## Slide 36: Layout Comparison
5: DC and Transient Response
<number>
Which layout is better?
Left has less diffusion capacitance on Y
Notes: <number>