## Slide 1: Lecture 6: Logical Effort
Notes: <number>

## Slide 2: Outline
6: Logical Effort
<number>
Logical Effort
Delay in a Logic Gate
Multistage Logic Networks
Choosing the Best Number of Stages
Example
Summary
Notes: <number>

## Slide 3: Introduction
6: Logical Effort
<number>
Chip designers face a bewildering array of choices
  What is the best circuit topology for a function?
  How many stages of logic give least delay?
  How wide should the transistors be?
Logical effort is a method to make these decisions
  Uses a simple model of delay
  Allows back-of-the-envelope calculations
  Helps make rapid comparisons between alternatives
  Emphasizes remarkable symmetries
Notes: <number>

## Slide 4: Example
6: Logical Effort
<number>
Help Ben Bitdiddle design the decoder for a register file.
Decoder specifications:
  16 word register file
  Each word is 32 bits wide
  Each bit presents load of 3 unit-sized transistors
  True and complementary address inputs A[3:0]
  Each input may drive 10 unit-sized transistors
Ben needs to decide:
  How many stages to use?
  How large should each gate be?
  How fast can decoder operate?
Notes: <number>

## Slide 5: Delay in a Logic Gate
6: Logical Effort
<number>
Express delays in process-independent unit
Delay has two components: d = f + p
f: effort delay = gh (a.k.a. stage effort)
  Again has two components
g: logical effort
  Measures relative ability of gate to deliver current
  g =1 for inverter
h: electrical effort = Cout / Cin
  Ratio of output to input capacitance
  Sometimes called fanout
p: parasitic delay
  Represents delay of gate driving no load
  Set by internal parasitic capacitance
τ3RC
≈ 3 ps in 65 nm process
60 ps in 0.6 μm process
Notes: <number>

## Slide 6: Delay Plots
6: Logical Effort
<number>
d = f + p
  = gh + p
What about
NOR2?
Notes: <number>

## Slide 7: Computing Logical Effort
6: Logical Effort
<number>
DEF: Logical effort is the ratio of the input capacitance of a gate to the input capacitance of an inverter delivering the same output current.
Measure from delay vs. fanout plots
Or estimate by counting transistor widths
Notes: <number>

## Slide 8: Catalog of Gates
6: Logical Effort
<number>
Gate type | Number of inputs |  |  |  | 
 | 1 | 2 | 3 | 4 | n
Inverter | 1 |  |  |  | 
NAND |  | 4/3 | 5/3 | 6/3 | (n+2)/3
NOR |  | 5/3 | 7/3 | 9/3 | (2n+1)/3
Tristate / mux | 2 | 2 | 2 | 2 | 2
XOR, XNOR |  | 4, 4 | 6, 12, 6 | 8, 16, 16, 8 | 
Logical effort of common gates
Notes: <number>

## Slide 9: Catalog of Gates
6: Logical Effort
<number>
Gate type | Number of inputs |  |  |  | 
 | 1 | 2 | 3 | 4 | n
Inverter | 1 |  |  |  | 
NAND |  | 2 | 3 | 4 | n
NOR |  | 2 | 3 | 4 | n
Tristate / mux | 2 | 4 | 6 | 8 | 2n
XOR, XNOR |  | 4 | 6 | 8 | 
Parasitic delay of common gates
  In multiples of pinv (≈1)
Notes: <number>

## Slide 10: Example: Ring Oscillator
6: Logical Effort
<number>
Estimate the frequency of an N-stage ring oscillator
Logical Effort: g = 1
Electrical Effort: h = 1
Parasitic Delay: p = 1
Stage Delay: d = 2
Frequency: fosc = 1/(2*N*d) = 1/4N
31 stage ring oscillator in 0.6 μm process has frequency of ~ 200 MHz
Notes: <number>

## Slide 11: Example: FO4 Inverter
6: Logical Effort
<number>
Estimate the delay of a fanout-of-4 (FO4) inverter
Logical Effort: g = 1
Electrical Effort: h = 4
Parasitic Delay: p = 1
Stage Delay: d = 5
The FO4 delay is about
300 ps in 0.6 μm process
15 ps in a 65 nm process
Notes: <number>

## Slide 12: Multistage Logic Networks
6: Logical Effort
<number>
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort
Notes: <number>

## Slide 13: Multistage Logic Networks
6: Logical Effort
<number>
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort
Can we write F = GH?
Notes: <number>

## Slide 14: Paths that Branch
6: Logical Effort
<number>
No! Consider paths that branch:
G = 1
H = 90 / 5 = 18
GH = 18
h1 = (15 +15) / 5 = 6
h2 = 90 / 15 = 6
F = g1g2h1h2 = 36 = 2GH
Notes: <number>

## Slide 15: Branching Effort
6: Logical Effort
<number>
Introduce branching effort
  Accounts for branching between stages in path
Now we compute the path effort
  F = GBH
Note:
Notes: <number>

## Slide 16: Multistage Delays
6: Logical Effort
<number>
Path Effort Delay
Path Parasitic Delay
Path Delay
Notes: <number>

## Slide 17: Designing Fast Circuits
6: Logical Effort
<number>
Delay is smallest when each stage bears same effort
Thus minimum delay of N stage path is
This is a key result of logical effort
  Find fastest possible delay
  Doesn’t require calculating gate sizes
Notes: <number>

## Slide 18: Gate Sizes
6: Logical Effort
<number>
How wide should the gates be for least delay?
Working backward, apply capacitance transformation to find input capacitance of each gate given load it drives.
Check work by verifying input cap spec is met.
Notes: <number>

## Slide 19: Example: 3-stage path
6: Logical Effort
<number>
Select gate sizes x and y for least delay from A to B
Notes: <number>

## Slide 20: Example: 3-stage path
6: Logical Effort
<number>
Logical Effort G = (4/3)*(5/3)*(5/3) = 100/27
Electrical Effort H = 45/8
Branching Effort B = 3 * 2 = 6
Path Effort F = GBH = 125
Best Stage Effort
Parasitic Delay P = 2 + 3 + 2 = 7
Delay D = 3*5 + 7 = 22 = 4.4 FO4
Notes: <number>

## Slide 21: Example: 3-stage path
6: Logical Effort
<number>
Work backward for sizes
y = 45 * (5/3) / 5 = 15
x = (15*2) * (5/3) / 5 = 10
Notes: <number>

## Slide 22: Best Number of Stages
6: Logical Effort
<number>
How many stages should a path use?
  Minimizing number of stages is not always fastest
Example: drive 64-bit datapath with unit inverter
D = NF1/N + P
= N(64)1/N + N
Notes: <number>

## Slide 23: Derivation
6: Logical Effort
<number>
Consider adding inverters to end of path
  How many give least delay?
Define best stage effort
Notes: <number>

## Slide 24: Best Stage Effort
6: Logical Effort
<number>
has no closed-form solution
Neglecting parasitics (pinv = 0), we find ρ = 2.718 (e)
For pinv = 1, solve numerically for ρ = 3.59
Notes: <number>

## Slide 25: Sensitivity Analysis
6: Logical Effort
<number>
How sensitive is delay to using exactly the best number of stages?
2.4 < ρ < 6 gives delay within 15% of optimal
  We can be sloppy!
  I like ρ = 4
Notes: <number>

## Slide 26: Example, Revisited
6: Logical Effort
<number>
Help Ben Bitdiddle design the decoder for a register file.
Decoder specifications:
  16 word register file
  Each word is 32 bits wide
  Each bit presents load of 3 unit-sized transistors
  True and complementary address inputs A[3:0]
  Each input may drive 10 unit-sized transistors
Ben needs to decide:
  How many stages to use?
  How large should each gate be?
  How fast can decoder operate?
Notes: <number>

## Slide 27: Number of Stages
6: Logical Effort
<number>
Decoder effort is mainly electrical and branching
Electrical Effort: H = (32*3) / 10 = 9.6
Branching Effort: B = 8
If we neglect logical effort (assume G = 1)
Path Effort: F = GBH = 76.8
Number of Stages: N = log4F = 3.1
Try a 3-stage design
Notes: <number>

## Slide 28: Gate Sizes & Delay
6: Logical Effort
<number>
Logical Effort: G = 1 * 6/3 * 1 = 2
Path Effort: F = GBH = 154
Stage Effort:
Path Delay:
Gate sizes: z = 96*1/5.36 = 18 y = 18*2/5.36 = 6.7
Notes: <number>

## Slide 29: Comparison
6: Logical Effort
<number>
Compare many alternatives with a spreadsheet
D = N(76.8 G)1/N + P
Design | N | G | P | D
NOR4 | 1 | 3 | 4 | 234
NAND4-INV | 2 | 2 | 5 | 29.8
NAND2-NOR2 | 2 | 20/9 | 4 | 30.1
INV-NAND4-INV | 3 | 2 | 6 | 22.1
NAND4-INV-INV-INV | 4 | 2 | 7 | 21.1
NAND2-NOR2-INV-INV | 4 | 20/9 | 6 | 20.5
NAND2-INV-NAND2-INV | 4 | 16/9 | 6 | 19.7
INV-NAND2-INV-NAND2-INV | 5 | 16/9 | 7 | 20.4
NAND2-INV-NAND2-INV-INV-INV | 6 | 16/9 | 8 | 21.6
Notes: <number>

## Slide 30: Review of Definitions
6: Logical Effort
<number>
Term | Stage | Path
number of stages |  | 
logical effort |  | 
electrical effort |  | 
branching effort |  | 
effort |  | 
effort delay |  | 
parasitic delay |  | 
delay |  | 
Notes: <number>

## Slide 31: Method of Logical Effort
6: Logical Effort
<number>
Compute path effort
Estimate best number of stages
Sketch path with N stages
Estimate least delay
Determine best stage effort
Find gate sizes
Notes: <number>

## Slide 32: Limits of Logical Effort
6: Logical Effort
<number>
Chicken and egg problem
  Need path to compute G
  But don’t know number of stages without G
Simplistic delay model
  Neglects input rise time effects
Interconnect
  Iteration required in designs with wire
Maximum speed only
  Not minimum area/power for constrained delay
Notes: <number>

## Slide 33: Summary
6: Logical Effort
<number>
Logical effort is useful for thinking of delay in circuits
  Numeric logical effort characterizes gates
  NANDs are faster than NORs in CMOS
  Paths are fastest when effort delays are ~4
  Path delay is weakly sensitive to stages, sizes
  But using fewer stages doesn’t mean faster paths
  Delay of path is about log4F FO4 inverter delays
  Inverters and NAND2 best for driving large caps
Provides language for discussing fast circuits
  But requires practice to master
Notes: <number>