## Slide 1: Lecture 9: Combinational Circuit Design
Notes: <number>

## Slide 2: Outline
10: Combinational Circuits
<number>
Bubble Pushing
Compound Gates
Logical Effort Example
Input Ordering
Asymmetric Gates
Skewed Gates
Best P/N ratio
Notes: <number>

## Slide 3: Example 1
10: Combinational Circuits
<number>
module mux(input s, d0, d1,
output y);
assign y = s ? d1 : d0;
endmodule
1) Sketch a design using AND, OR, and NOT gates.
Notes: <number>

## Slide 4: Example 2
10: Combinational Circuits
<number>
2) Sketch a design using NAND, NOR, and NOT gates. Assume ~S is available.
Notes: <number>

## Slide 5: Bubble Pushing
10: Combinational Circuits
<number>
Start with network of AND / OR gates
Convert to NAND / NOR + inverters
Push bubbles around to simplify logic
  Remember DeMorgan’s Law
Notes: <number>

## Slide 6: Example 3
10: Combinational Circuits
<number>
3) Sketch a design using one compound gate and one NOT gate. Assume ~S is available.
Notes: <number>

## Slide 7: Compound Gates
10: Combinational Circuits
<number>
Logical Effort of compound gates
Notes: <number>

## Slide 8: Example 4
10: Combinational Circuits
<number>
The multiplexer has a maximum input capacitance of 16 units on each input. It must drive a load of 160 units. Estimate the delay of the two designs.
H = 160 / 16 = 10 B = 1 N = 2
Notes: <number>

## Slide 9: Example 5
10: Combinational Circuits
<number>
Annotate your designs with transistor sizes that achieve this delay.
Notes: <number>

## Slide 10: Input Order
10: Combinational Circuits
<number>
Our parasitic delay model was too simple
  Calculate parasitic delay for Y falling
    If A arrives latest? 2τ
    If B arrives latest? 2.33τ
Notes: <number>

## Slide 11: Inner & Outer Inputs
10: Combinational Circuits
<number>
Inner input is closest to output (A)
Outer input is closest to rail (B)
If input arrival time is known
  Connect latest input to inner terminal
Notes: <number>

## Slide 12: Asymmetric Gates
10: Combinational Circuits
<number>
Asymmetric gates favor one input over another
Ex: suppose input A of a NAND gate is most critical
  Use smaller transistor on A (less capacitance)
  Boost size of noncritical input
  So total resistance is same
gA = 10/9
gB = 2
gtotal = gA + gB = 28/9
Asymmetric gate approaches g = 1 on critical input
But total logical effort goes up
Notes: <number>

## Slide 13: Symmetric Gates
10: Combinational Circuits
<number>
Inputs can be made perfectly symmetric
Notes: <number>

## Slide 14: Skewed Gates
10: Combinational Circuits
<number>
Skewed gates favor one edge over another
Ex: suppose rising output of inverter is most critical
  Downsize noncritical nMOS transistor
Calculate logical effort by comparing to unskewed inverter with same effective resistance on that edge.
  gu = 2.5 / 3 = 5/6
  gd = 2.5 / 1.5 = 5/3
Notes: <number>

## Slide 15: HI- and LO-Skew
10: Combinational Circuits
<number>
Def: Logical effort of a skewed gate for a particular transition is the ratio of the input capacitance of that gate to the input capacitance of an unskewed inverter delivering the same output current for the same transition.
Skewed gates reduce size of noncritical transistors
  HI-skew gates favor rising output (small nMOS)
  LO-skew gates favor falling output (small pMOS)
Logical effort is smaller for favored direction
But larger for the other direction
Notes: <number>

## Slide 16: Catalog of Skewed Gates
10: Combinational Circuits
<number>
Notes: <number>

## Slide 17: Asymmetric Skew
10: Combinational Circuits
<number>
Combine asymmetric and skewed gates
  Downsize noncritical transistor on unimportant input
  Reduces parasitic delay for critical input
Notes: <number>

## Slide 18: Best P/N Ratio
10: Combinational Circuits
<number>
We have selected P/N ratio for unit rise and fall resistance (μ = 2-3 for an inverter).
Alternative: choose ratio for least average delay
Ex: inverter
  Delay driving identical inverter
  tpdf = (P+1)
  tpdr = (P+1)(μ/P)
  tpd = (P+1)(1+μ/P)/2 = (P + 1 + μ + μ/P)/2
  dtpd / dP = (1- μ/P2)/2 = 0
  Least delay for P =
Notes: <number>

## Slide 19: P/N Ratios
10: Combinational Circuits
<number>
In general, best P/N ratio is sqrt of equal delay ratio.
  Only improves average delay slightly for inverters
  But significantly decreases area and power
Notes: <number>

## Slide 20: Observations
10: Combinational Circuits
<number>
For speed:
  NAND vs. NOR
  Many simple stages vs. fewer high fan-in stages
  Latest-arriving input
For area and power:
  Many simple stages vs. fewer high fan-in stages
Notes: <number>