## Slide 1: Lecture 1: Circuits & Layout
Notes: <number>

## Slide 2: Outline
1: Circuits & Layout
<number>
A Brief History
CMOS Gate Design
Pass Transistors
CMOS Latches & Flip-Flops
Standard Cell Layouts
Stick Diagrams
Notes: <number>

## Slide 3: A Brief History
1: Circuits & Layout
<number>
1958: First integrated circuit
  Flip-flop using two transistors
  Built by Jack Kilby at Texas Instruments
2010
  Intel Core i7 processor
    2.3 billion transistors
  64 Gb Flash memory
    > 16 billion transistors
Courtesy Texas Instruments
[Trinh09]
© 2009 IEEE.
Notes: <number>

## Slide 4: Growth Rate
1: Circuits & Layout
<number>
53% compound annual growth rate over 50 years
  No other technology has grown so fast so long
Driven by miniaturization of transistors
  Smaller is cheaper, faster, lower in power!
  Revolutionary effects on society
[Moore65]
Electronics Magazine
Notes: <number>

## Slide 5: Annual Sales
1: Circuits & Layout
<number>
>1019 transistors manufactured in 2008
  1 billion for every human on the planet
Notes: <number>

## Slide 6: Invention of the Transistor
1: Circuits & Layout
<number>
Vacuum tubes ruled in first half of 20th century Large, expensive, power-hungry, unreliable
1947: first point contact transistor
  John Bardeen and Walter Brattain at Bell Labs
  See Crystal Fire
  by Riordan, Hoddeson
AT&T Archives. Reprinted with permission.
Notes: <number>

## Slide 7: Transistor Types
1: Circuits & Layout
<number>
Bipolar transistors
  npn or pnp silicon structure
  Small current into very thin base layer controls large currents between emitter and collector
  Base currents limit integration density
Metal Oxide Semiconductor Field Effect Transistors
  nMOS and pMOS MOSFETS
  Voltage applied to insulated gate controls current between source and drain
  Low power allows very high integration
Notes: <number>

## Slide 8: MOS Integrated Circuits
1: Circuits & Layout
<number>
1970’s processes usually had only nMOS transistors
  Inexpensive, but consume power while idle
1980s-present: CMOS processes for low idle power
Intel 1101 256-bit SRAM
Intel 4004 4-bit Proc
[Vadasz69]
© 1969 IEEE.
Intel Museum.
Reprinted with permission.
Notes: <number>

## Slide 9: Moore’s Law: Then
1: Circuits & Layout
<number>
1965: Gordon Moore plotted transistor on each chip
  Fit straight line on semilog scale
  Transistor counts have doubled every 26 months
Integration Levels
SSI: 10 gates
MSI: 1000 gates
LSI: 10,000 gates
VLSI: > 10k gates
[Moore65]
Electronics Magazine
Notes: <number>

## Slide 10: And Now…
1: Circuits & Layout
<number>
Notes: <number>

## Slide 11: Feature Size
1: Circuits & Layout
<number>
Minimum feature size shrinking 30% every 2-3 years
Notes: <number>

## Slide 12: Corollaries
1: Circuits & Layout
<number>
Many other factors grow exponentially
  Ex: clock frequency, processor performance
Notes: <number>

## Slide 13: CMOS Gate Design
1: Circuits & Layout
<number>
Activity:
  Sketch a 4-input CMOS NOR gate
Notes: <number>

## Slide 14: Complementary CMOS
1: Circuits & Layout
<number>
Complementary CMOS logic gates
  nMOS pull-down network
  pMOS pull-up network
  a.k.a. static CMOS
 | Pull-up OFF | Pull-up ON
Pull-down OFF | Z (float) | 1
Pull-down ON | 0 | X (crowbar)
Notes: <number>

## Slide 15: Series and Parallel
1: Circuits & Layout
<number>
nMOS: 1 = ON
pMOS: 0 = ON
Series: both must be ON
Parallel: either can be ON
Notes: <number>

## Slide 16: Conduction Complement
1: Circuits & Layout
<number>
Complementary CMOS gates always produce 0 or 1
Ex: NAND gate
  Series nMOS: Y=0 when both inputs are 1
  Thus Y=1 when either input is 0
  Requires parallel pMOS
Rule of Conduction Complements
  Pull-up network is complement of pull-down
  Parallel -> series, series -> parallel
Notes: <number>

## Slide 17: Compound Gates
1: Circuits & Layout
<number>
Compound gates can do any inverting function
Ex:
Notes: <number>

## Slide 18: Example: O3AI
1: Circuits & Layout
<number>
Notes: <number>

## Slide 19: Signal Strength
1: Circuits & Layout
<number>
Strength of signal
  How close it approximates ideal voltage source
VDD and GND rails are strongest 1 and 0
nMOS pass strong 0
  But degraded or weak 1
pMOS pass strong 1
  But degraded or weak 0
Thus nMOS are best for pull-down network
Notes: <number>

## Slide 20: Pass Transistors
1: Circuits & Layout
<number>
Transistors can be used as switches
Notes: <number>

## Slide 21: Transmission Gates
1: Circuits & Layout
<number>
Pass transistors produce degraded outputs
Transmission gates pass both 0 and 1 well
Notes: <number>

## Slide 22: Tristates
1: Circuits & Layout
<number>
Tristate buffer produces Z when not enabled
EN | A | Y
0 | 0 | Z
0 | 1 | Z
1 | 0 | 0
1 | 1 | 1
Notes: <number>

## Slide 23: Nonrestoring Tristate
1: Circuits & Layout
<number>
Transmission gate acts as tristate buffer
  Only two transistors
  But nonrestoring
    Noise on A is passed on to Y
Notes: <number>

## Slide 24: Tristate Inverter
1: Circuits & Layout
<number>
Tristate inverter produces restored output
  Violates conduction complement rule
  Because we want a Z output
Notes: <number>

## Slide 25: Multiplexers
1: Circuits & Layout
<number>
2:1 multiplexer chooses between two inputs
S | D1 | D0 | Y
0 | X | 0 | 0
0 | X | 1 | 1
1 | 0 | X | 0
1 | 1 | X | 1
Notes: <number>

## Slide 26: Gate-Level Mux Design
1: Circuits & Layout
<number>
How many transistors are needed? 20
Notes: <number>

## Slide 27: Transmission Gate Mux
1: Circuits & Layout
<number>
Nonrestoring mux uses two transmission gates
  Only 4 transistors
Notes: <number>

## Slide 28: Inverting Mux
1: Circuits & Layout
<number>
Inverting multiplexer
  Use compound AOI22
  Or pair of tristate inverters
  Essentially the same thing
Noninverting multiplexer adds an inverter
Notes: <number>

## Slide 29: 4:1 Multiplexer
1: Circuits & Layout
<number>
4:1 mux chooses one of 4 inputs using two selects
  Two levels of 2:1 muxes
  Or four tristates
Notes: <number>

## Slide 30: D Latch
1: Circuits & Layout
<number>
When CLK = 1, latch is transparent
  D flows through to Q like a buffer
When CLK = 0, the latch is opaque
  Q holds its old value independent of D
a.k.a. transparent latch or level-sensitive latch
Notes: <number>

## Slide 31: D Latch Design
1: Circuits & Layout
<number>
Multiplexer chooses D or old Q
Notes: <number>

## Slide 32: D Latch Operation
1: Circuits & Layout
<number>
Notes: <number>

## Slide 33: D Flip-flop
1: Circuits & Layout
<number>
When CLK rises, D is copied to Q
At all other times, Q holds its value
a.k.a. positive edge-triggered flip-flop, master-slave flip-flop
Notes: <number>

## Slide 34: D Flip-flop Design
1: Circuits & Layout
<number>
Built from master and slave D latches
Notes: <number>

## Slide 35: D Flip-flop Operation
1: Circuits & Layout
<number>
Notes: <number>

## Slide 36: Race Condition
1: Circuits & Layout
<number>
Back-to-back flops can malfunction from clock skew
  Second flip-flop fires late
  Sees first flip-flop change and captures its result
  Called hold-time failure or race condition
Notes: <number>

## Slide 37: Nonoverlapping Clocks
1: Circuits & Layout
<number>
Nonoverlapping clocks can prevent races
  As long as nonoverlap exceeds clock skew
We will use them in this class for safe design
  Industry manages skew more carefully instead
Notes: <number>

## Slide 38: Gate Layout
1: Circuits & Layout
<number>
Layout can be very time consuming
  Design gates to fit together nicely
  Build a library of standard cells
Standard cell design methodology
  VDD and GND should abut (standard height)
  Adjacent gates should satisfy design rules
  nMOS at bottom and pMOS at top
  All gates include well and substrate contacts
Notes: <number>

## Slide 39: Example: Inverter
1: Circuits & Layout
<number>
Notes: <number>

## Slide 40: Example: NAND3
1: Circuits & Layout
<number>
Horizontal N-diffusion and p-diffusion strips
Vertical polysilicon gates
Metal1 VDD rail at top
Metal1 GND rail at bottom
32  by 40 
Notes: <number>

## Slide 41: Stick Diagrams
1: Circuits & Layout
<number>
Stick diagrams help plan layout quickly
  Need not be to scale
  Draw with color pencils or dry-erase markers
Notes: <number>

## Slide 42: Wiring Tracks
1: Circuits & Layout
<number>
A wiring track is the space required for a wire
  4  width, 4  spacing from neighbor = 8  pitch
Transistors also consume one wiring track
Notes: <number>

## Slide 43: Well spacing
1: Circuits & Layout
<number>
Wells must surround transistors by 6 
  Implies 12  between opposite transistor flavors
  Leaves room for one wire track
Notes: <number>

## Slide 44: Area Estimation
1: Circuits & Layout
<number>
Estimate area by counting wiring tracks
  Multiply by 8 to express in 
Notes: <number>

## Slide 45: Example: O3AI
1: Circuits & Layout
<number>
Sketch a stick diagram for O3AI and estimate area
Notes: <number>