## Slide 1: Lecture 3: CMOS Transistor Theory
Notes: <number>

## Slide 2: Outline
3: CMOS Transistor Theory
<number>
Introduction
MOS Capacitor
nMOS I-V Characteristics
pMOS I-V Characteristics
Gate and Diffusion Capacitance
Notes: <number>

## Slide 3: Introduction
3: CMOS Transistor Theory
<number>
So far, we have treated transistors as ideal switches
An ON transistor passes a finite amount of current
  Depends on terminal voltages
  Derive current-voltage (I-V) relationships
Transistor gate, source, drain all have capacitance
  I = C (ΔV/Δt) -> Δt = (C/I) ΔV
  Capacitance and current determine speed
Notes: <number>

## Slide 4: MOS Capacitor
3: CMOS Transistor Theory
<number>
Gate and body form MOS capacitor
Operating modes
  Accumulation
  Depletion
  Inversion
Notes: <number>

## Slide 5: Terminal Voltages
3: CMOS Transistor Theory
<number>
Mode of operation depends on Vg, Vd, Vs
  Vgs = Vg – Vs
  Vgd = Vg – Vd
  Vds = Vd – Vs = Vgs - Vgd
Source and drain are symmetric diffusion terminals
  By convention, source is terminal at lower voltage
  Hence Vds ≥ 0
nMOS body is grounded. First assume source is 0 too.
Three regions of operation
  Cutoff
  Linear
  Saturation
Notes: <number>

## Slide 6: nMOS Cutoff
3: CMOS Transistor Theory
<number>
No channel
Ids ≈ 0
Notes: <number>

## Slide 7: nMOS Linear
3: CMOS Transistor Theory
<number>
Channel forms
Current flows from d to s
  e- from s to d
Ids increases with Vds
Similar to linear resistor
Notes: <number>

## Slide 8: nMOS Saturation
3: CMOS Transistor Theory
<number>
Channel pinches off
Ids independent of Vds
We say current saturates
Similar to current source
Notes: <number>

## Slide 9: I-V Characteristics
3: CMOS Transistor Theory
<number>
In Linear region, Ids depends on
  How much charge is in the channel?
  How fast is the charge moving?
Notes: <number>

## Slide 10: Channel Charge
3: CMOS Transistor Theory
<number>
MOS structure looks like parallel plate capacitor while operating in inversions
  Gate – oxide – channel
Qchannel = CV
C = Cg = εoxWL/tox = CoxWL
V = Vgc – Vt = (Vgs – Vds/2) – Vt
Cox = εox / tox
Notes: <number>

## Slide 11: Carrier velocity
3: CMOS Transistor Theory
<number>
Charge is carried by e-
Electrons are propelled by the lateral electric field between source and drain
  E = Vds/L
Carrier velocity v proportional to lateral E-field
  v = μE μ called mobility
Time for carrier to cross channel:
  t = L / v
Notes: <number>

## Slide 12: nMOS Linear I-V
3: CMOS Transistor Theory
<number>
Now we know
  How much charge Qchannel is in the channel
  How much time t each carrier takes to cross
Notes: <number>

## Slide 13: nMOS Saturation I-V
3: CMOS Transistor Theory
<number>
If Vgd < Vt, channel pinches off near drain
  When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current
Notes: <number>

## Slide 14: nMOS I-V Summary
3: CMOS Transistor Theory
<number>
Shockley 1st order transistor models
Notes: <number>

## Slide 15: Example
3: CMOS Transistor Theory
<number>
We will be using a 0.6 μm process for your project
  From AMI Semiconductor
  tox = 100 Å
  μ = 350 cm2/V*s
  Vt = 0.7 V
Plot Ids vs. Vds
  Vgs = 0, 1, 2, 3, 4, 5
  Use W/L = 4/2 λ
Notes: <number>

## Slide 16: pMOS I-V
3: CMOS Transistor Theory
<number>
All dopings and voltages are inverted for pMOS
  Source is the more positive terminal
Mobility μp is determined by holes
  Typically 2-3x lower than that of electrons μn
  120 cm2/V•s in AMI 0.6 μm process
Thus pMOS must be wider to
provide same current
  In this class, assume
  μn / μp = 2
Notes: <number>

## Slide 17: Capacitance
3: CMOS Transistor Theory
<number>
Any two conductors separated by an insulator have capacitance
Gate to channel capacitor is very important
  Creates channel charge necessary for operation
Source and drain have capacitance to body
  Across reverse-biased diodes
  Called diffusion capacitance because it is associated with source/drain diffusion
Notes: <number>

## Slide 18: Gate Capacitance
3: CMOS Transistor Theory
<number>
Approximate channel as connected to source
Cgs = εoxWL/tox = CoxWL = CpermicronW
Cpermicron is typically about 2 fF/m
Notes: <number>

## Slide 19: Diffusion Capacitance
3: CMOS Transistor Theory
<number>
Csb, Cdb
Undesirable, called parasitic capacitance
Capacitance depends on area and perimeter
  Use small diffusion nodes
  Comparable to Cg
  for contacted diff
  ½ Cg for uncontacted
  Varies with process
Notes: <number>