## Slide 1: Lecture 1: Logic Gates & Analog Behavior of Digital Systems
E85 Digital Design & Computer Engineering

## Slide 2
Logic Gates
Verilog
Logic Levels
CMOS Transistors
Power Consumption
Datasheets
Lecture 1

## Slide 3
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 4
Single-Input Logic Gates

## Slide 5
Two-Input Logic Gates

## Slide 6
More Two-Input Logic Gates

## Slide 7
Multi-input XOR: Odd parity (true if odd number of inputs are true)
Multiple-Input Logic Gates

## Slide 8
Multi-input XOR: Odd parity
SystemVerilog Description
module gates(input logic a, b, c,
output logic y1, y2, y3, y4, y5);
not g1(y1, a);
and g2(y2, a, b);
or g3(y3, a, b, c);
nand g4(y4, b, c);
xor g5(y5, a, c);
endmodule

## Slide 9
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 10
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 11
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 12
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 13
Noise Margins

## Slide 14
High Noise Margin: NMH = VOH – VIH
Low Noise Margin: NML = VIL – VOL
Noise Margins

## Slide 15
Ideal Buffer: Real Buffer:
NMH = NML = VDD/2
DC Transfer Characteristics
NMH, NML < VDD/2

## Slide 16
DC Transfer Characteristics

## Slide 17
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
VDD Scaling

## Slide 18
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
Chips operate because they contain magic smoke
Proof: if the magic smoke is let out, the chip stops working
VDD Scaling

## Slide 19
Logic Family | VDD | VIL | VIH | VOL | VOH
TTL | 5 (4.75 - 5.25) | 0.8 | 2.0 | 0.4 | 2.4
CMOS | 5 (4.5 - 6) | 1.35 | 3.15 | 0.33 | 3.84
LVTTL | 3.3 (3 - 3.6) | 0.8 | 2.0 | 0.4 | 2.4
LVCMOS | 3.3 (3 - 3.6) | 0.9 | 1.8 | 0.36 | 2.7
Logic Family Examples

## Slide 20
Logic gates built from transistors
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd
  d and s are connected (ON) when g is 1
Transistors

## Slide 21
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit
Robert Noyce, 1927-1990

## Slide 22
Transistors built from silicon, a semiconductor
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (free positive charges, holes)
Silicon

## Slide 23
Metal oxide silicon (MOS) transistors:
  Polysilicon (used to be metal) gate
  Oxide (silicon dioxide) insulator
  Doped silicon
MOS Transistors

## Slide 24
Gate = 0
OFF (no connection between source and drain)
Gate = 1
ON (channel between source and drain)
Transistors: nMOS

## Slide 25
pMOS transistor is opposite
  ON when Gate = 0
  OFF when Gate = 1
Transistors: pMOS

## Slide 26
Transistor Function

## Slide 27
nMOS: pass good 0’s, so connect source to GND
pMOS: pass good 1’s, so connect source to VDD
Transistor Function

## Slide 28
CMOS Gates: NOT Gate
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0

## Slide 29
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
CMOS Gates: NAND Gate

## Slide 30
CMOS Gate Structure

## Slide 31
NOR3 Gate
How do you build a three-input NOR gate?

## Slide 32
AND2 Gate
How do you build a two-input AND gate?

## Slide 33
nMOS pass 1’s poorly
pMOS pass 0’s poorly
Transmission gate is a better switch
  passes both 0 and 1 well
When EN = 1, the switch is ON:
  EN = 0 and A is connected to B
When EN = 0, the switch is OFF:
  A is not connected to B
Transmission Gates

## Slide 34
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Since 1975, transistor counts have doubled every two years.
Gordon Moore, 1929-

## Slide 35
“If the automobile had followed the same development cycle as the computer, a Rolls-Royce would today cost $100, get one million miles to the gallon, and explode once a year . . .” (Robert Cringely, Infoworld)
– Robert Cringley
Moore’s Law

## Slide 36
Power = Energy consumed per unit time
Dynamic power consumption
Static power consumption
Power Consumption

## Slide 37
Power to charge transistor gate capacitances
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f: transistors switch (from 1 to 0 or vice versa) at that frequency
  Capacitor is charged f/2 times per second (discharging from 1 to 0 is free)
Dynamic power consumption:
Pdynamic = ½CVDD2f
Dynamic Power Consumption

## Slide 38
Power consumed when no gates are switching
Caused by the quiescent supply current, IDD (also called the leakage current)
Static power consumption:
Pstatic = IDDVDD
Static Power Consumption

## Slide 39
Estimate the power consumption of a mobile phone running Angry Birds
  VDD = 0.8 V
  C = 5 nF
  f = 2 GHz
  IDD = 10 mA
P = ½CVDD2f + IDDVDD
= ½(5 nF)(0.8 V)2(2 GHz) + (10 mA)(0.8 V)
= (3.2 + 0.008) W ≈ 3.2 W
Power Consumption Example

## Slide 40
Datasheets are a contract between the manufactuer and the user.
74LS04 has six NOT gates
Pinout
  Input A, output Y
  Also hook up VCC and GND
74-series are logic gates
LS: Low power Shottky
HC: High speed CMOS
04: six NOT gates
Datasheets

## Slide 41
Chips are available in plastic or ceramic packages with different temperature ratings.
Dual Inline Package (DIP)
Small Outline IC (SOIC)
Small Outline Package (SOP)
Leadless Chip Carrier (LCC)
Datasheets

## Slide 42
Six NOT gates
Input A, output Y
Datasheets

## Slide 43
Internal structure
  Not too important for you.
  NPN transistor at middle and resistors above and below comprise the inverter
  NPN transistors on right form an output stage for driving more current
Datasheets

## Slide 44
Absolute Maximums specify when the chip will catch on fire or suffer permanent damage. It is not guaranteed to function correctly near these levels. Don’t use for design purposes.
Recommended Operating Conditions say how it should be used.
Different vendors have different names for conditions
  Use some common sense to interpret
Datasheets

## Slide 45
Note 74LS vs. 74
Supply voltage (VCC)
Logic levels (VIH, VIL, VOH, VOL)
Currents
  Output (IOH, IOL, IOS)
  Input (II, IH, IL)
  Supply (ICCH, ICCL)
Propagation Delay (tPLH, tPHL)
Datasheets

## Slide 46
Mechanical data important when you are designing a printed circuit board.
Make sure the pins fit your board!
Datasheets

## Slide 47
What is the maximum fanout for a 74LS04 NOT gate?
Solution:
Maximum current into a 74LS04 is IIL = 0.4 mA. Output voltage VOL is guaranteed at IOL = 8 mA
Hence, maximum fanout is IOL / IIL = 20.
Example: Fanout

## Slide 48
One 74LS04 NOT gate drives 20 identical gates. VCC = 5V. What is the power consumption of the entire system if the input to the first gate switches at 1 MHz?
Static Power:
  Each gate draws ICC = (ICCL + ICCH)/2 = (6.6 + 2.4 mA)/2 = 4.5 mA
  Istatic = (21 gates)(4.5 mA/gate) = 94.5 mA
  Pstatic = 94.5 mA * 5 V = 472.5 mW
Dynamic Power
  Cin is not specified. Assume 15 pF/gate * 20 gates = 300 pF.
  P = CVDD2f = (300x10-12)(52)(1x106) = 7.5 mW
Ptotal = Pstatic + Pdynamic = 480 mW
  TTL power is primarily static
Example: Power Consumption