## Slide 1: Lecture 11: Midterm Review
E85 Digital Design & Computer Engineering

## Slide 2
Logic Levels
Number Systems
CMOS Transistors
Power Consumption
Combinational Logic Design
Finite State Machines
Timing
Verilog
Arithmetic Circuits
Lecture 11

## Slide 3
Assign VIH, VIL, VOH, VOL to maximize noise margins |VOH – VIH|, |VOL – VIL|
Normally at the unity gain points
If the curve has many bends, pick the ones to maximize noise margins
Logic Levels

## Slide 4
What is the logic function?
  OR
What are the logic levels?
VIL = 2 VIH = 2.7
VOL = 0.2 VOH = 2.8
What are the noise margins?
  NML = 1.8 NMH = 0.1
Logic Levels: Example

## Slide 5
Consider two logic families
A: VIL = 1, VIH = 2.3, VOL = 0.4, VOH = 2.9
B: VIL = 2, VIH = 3, VOL = 1.1, VOH = 3.2
Can A drive itself? YES
Can B drive itself? YES
Can A drive B? NO: VOH of 2.9 < VIH of 3
Can B drive A? NO: VOL of 1.1 > VIL of 1
Logic Levels: Compatibility

## Slide 6
Find decimal value of 1012 interpreted as:
Unsigned: 1x4 + 0x2 + 1x1 = 5
Sign/Magnitude: (-1)1 x (0x2+1x1) = -1
Two’s Complement: 1x-4 + 0x2 + 1x1 = -3
Number Systems: Signed and Unsigned

## Slide 7
Write 19 as a 6-bit binary number:
19 = 0100112
Write -19 as a 6-bit binary number
Two’s complement
Invert the bits and add 1
101100+1 = 1011012
Sign/Magnitude
1100112
Number Systems: Negative Numbers

## Slide 8
Write 3710 in other bases
Hexadecimal: 2516
Binary: 1001012
Number Systems: Bases

## Slide 9
Design nMOS pull-down network
  Series for AND, parallel for OR
pMOS pull-up network is complement
CMOS gates are inherently inverting
Add another stage to get non-inverting
CMOS Transistors

## Slide 10
Sketch a 3-input OR gate
  Use NOR3 + inverter
  NOR3: nMOS in parallel, hence pMOS in series
CMOS Transistors: OR3

## Slide 11
Sketch an AND-OR-INVERT gate Y = ~(AB+C)
  nMOS network
    A and B in series. This stack in parallel with C
  pMOS network is complement
    A and B in parallel. This stack in series with C
CMOS Transistors: AOI

## Slide 12
Switch:
  Choose R big enough to limit power, small enough to keep a good logic level if Iload is leakage current.
  P = VDD2/R
  Vout = Iload * R < VIL
Light Emitting Diode
  Choose R small enough to make the LED bright, large enough to not overstress IOH of the gate driving Vin.
  ID ~ (Vin-2) / R
  5 mA is visible in room lighting and near max IOH of many gates
Switches and LEDs

## Slide 13
P = Pdynamic + Pstatic = aCVDD2f + IstaticVDD
  a = activity factor:
    1 for clocks rising and falling each cycle
    0.5 for data signal switching once per cycle
    0.5p for data signal switching with probability p
Know your units
  K = 103, M = 106, G = 109, T=1012
  m = 10-3, m = 10-6, n = 10-9, p = 10-12, f=10-15
Power Consumption

## Slide 14
VDD = 0.707 V
1000 flip-flops clocked at 1 GHz. For each:
  100 nA leakage
  5 fF of clock capacitance
  20 fF capacitance on Q
  10% of inputs change on any given cycle
Idle power = Pstatic =
  100 nA/flop * 1000 flops * 0.707 = 70.7 mW
Running power = Pstatic + Pdynamic = 70.7 uW +
1000 * (5 + 0.1 * 20 * 0.5) fF * (0.707)2 * 1 GHz = 3.07 mW
Power Consumption: Example

## Slide 15
Output depends on current inputs
Write truth table
Circle 1’s to find sum of products
Simplify with Boolean algebra or inspection
Combinational Logic Design

## Slide 16
Write a truth table & eqn for
Combinational Logic: Example
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 17
Write inputs in Gray code order 00 01 11 10
Populate grid
Circle 1’s in boxes 1, 2, or 4 on a side
Optionally circle Xs if it simplifies
Combinational Logic: K-Map
 |  | AB |  |  | 
 |  | 00 | 01 | 11 | 10
CD | 00 | 0 | 1 | X | 1
 | 01 | 0 | 1 | 1 | 0
 | 11 | 0 | 0 | 0 | 0
 | 10 | X | 0 | 0 | 1

## Slide 18
Sequential circuits: output depends on previous as well as current inputs
Flip-flops
  On the rising edge of CLK, Q gets D.
  Enables
  Reset: synchronous or asynchronous
Synchronous sequential design: every element is combinational or a flip-flop, and all flops share the same clock. Easy to analyze.
Sequential Circuits

## Slide 19
State transition diagram
State encodings
Next state and output tables
Derive and simplify Boolean equations
Sketch circuit
Inverse problems: derive diagram from circuit
Finite State Machines

## Slide 20
Timing
Tc ≥ tpcq + tpd + tsetup + tskew
tccq + tcd > thold + tske

## Slide 21
Think of the logic you want first
Use Verilog as shorthand for logic
Pick the appropriate idiom for each element
Verilog

## Slide 22
Combinational Logic with Boolean Eqns.
assign y = (a & b) ^ (c | ~d);
Multipliexers
assign y = s ? d1 : d0;
Comb logic with truth tables
always_comb
casez(in)
3’b1xx: y <= 2’b11;
3’b01x: y <= 2’b10;
3’b001: y <= 2’b01;
default: y <= 2’b00;
endcase
Verilog Idioms: Combinational Logic

## Slide 23
Verilog Idioms: FSMs
module fsmWithInputs(input logic clk,
input logic reset,
input logic a,
output logic q);
typedef enum logic [1:0] {S0, S1, S2} statetype;
statetype state, nextstate;
// state register
always_ff @(posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always_comb
case (state)
S0: if (a) nextstate = S1;
else nextstate = S0;
S1: nextstate = S2;
S2: if (a) nextstate = S2;
else nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign q = (state == S2);
endmodule

## Slide 24
Verilog Idioms: Structural
module mux2(input logic [3:0] d0, d1,
input logic s,
output logic [3:0] y);
assign y = s ? d1 : d0;
endmodule
module mux2_8(input logic [7:0] d0, d1,
input logic s,
output logic [7:0] y);
mux2 lsbmux(d0[3:0], d1[3:0], s, y[3:0]);
mux2 msbmux(d0[7:4], d1[7:4], s, y[7:4]);
endmodule

## Slide 25
Adders
Ripple Carry
Carry Lookahead Parallel Prefix
0:-1
-1
2:1
1:-1
2:-1
0
1
2
4:3
3
6:5
5:3
6:3
4
5
6
5:-1
6:-1
3:-1
4:-1
8:7
7
10:9
9:7
10:7
8
9
10
12:11
11
14:13
13:11
14:11
12
13
14
13:7
14:7
11:7
12:7
9:-1
10:-1
7:-1
8:-1
13:-1
14:-1
11:-1
12:-1
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 26
ALU
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR