## Slide 1: Lecture 17: ARM Assembly Language
E85 Digital Design & Computer Engineering

## Slide 2
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes
Lecture 17

## Slide 3
Jumping up a few levels of abstraction
  Architecture: programmer’s view of computer
    Defined by instructions & operand locations
  Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)
Introduction

## Slide 4
Commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
Instructions

## Slide 5
Developed in the 1980’s by Advanced RISC Machines – now called ARM Holdings
Nearly 10 billion ARM processors sold/year
Almost all cell phones and tablets have multiple ARM processors
Over 75% of humans use products with an ARM processor
Used in servers, cameras, robots, cars, pinball machines, etc.
ARM Architecture

## Slide 6
Developed in the 1980’s by Advanced RISC Machines – now called ARM Holdings
Nearly 10 billion ARM processors sold/year
Almost all cell phones and tablets have multiple ARM processors
Over 75% of humans use products with an ARM processor
Used in servers, cameras, robots, cars, pinball machines,, etc.
ARM Architecture
Once you’ve learned one architecture, it’s easier to learn others

## Slide 7
Underlying design principles, as articulated by Hennessy and Patterson:
    Regularity supports design simplicity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises
Architecture Design Principles

## Slide 8
ADD: mnemonic – indicates operation to perform
b, c: source operands
a: destination operand
C Code
a = b + c;
ARM Assembly Code
ADD a, b, c
Instruction: Addition

## Slide 9
Similar to addition - only mnemonic changes
SUB: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
ARM assembly code
SUB a, b, c
Instruction: Subtraction

## Slide 10
Regularity supports design simplicity
Consistent instruction format
Same number of operands (two sources and one destination)
Ease of encoding and handling in hardware
Design Principle 1

## Slide 11
More complex code handled by multiple ARM instructions
C Code
a = b + c - d;
ARM assembly code
ADD t, b, c ; t = b + c
SUB a, t, d ; a = t - d
Multiple Instructions

## Slide 12
Make the common case fast
ARM includes only simple, commonly used instructions
Hardware to decode and execute instructions kept simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
Design Principle 2

## Slide 13
Make the common case fast
ARM is a Reduced Instruction Set Computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are Complex Instruction Set Computers (CISC)
Design Principle 2

## Slide 14
Physical location in computer
  Registers
  Constants (also called immediates)
  Memory
Operand Location

## Slide 15
ARM has 16 registers
Registers are faster than memory
Each register is 32 bits
ARM is called a “32-bit architecture” because it operates on 32-bit data
Operands: Registers

## Slide 16
Smaller is Faster
ARM includes only a small number of registers
Design Principle 3

## Slide 17
Name | Use
R0 | Argument / return value / temporary variable
R1-R3 | Argument / temporary variables
R4-R11 | Saved variables
R12 | Temporary variable
R13 (SP) | Stack Pointer
R14 (LR) | Link Register
R15 (PC) | Program Counter
ARM Register Set

## Slide 18
Registers:
  R before number, all capitals
  Example: “R0” or “register zero” or “register R0”
Operands: Registers

## Slide 19
Registers used for specific purposes:
  Saved registers: R4-R11 hold variables
  Temporary registers: R0-R3 and R12, hold intermediate values
  Discuss others later
Operands: Registers

## Slide 20
Revisit ADD instruction
C Code
a = b + c;
ARM Assembly Code
; R0 = a, R1 = b, R2 = c
ADD R0, R1, R2
Instructions with Registers

## Slide 21
Many instructions can use constants or immediate operands
For example: ADD and SUB
value is immediately available from instruction
C Code
a = a + 4;
b = a – 12;
ARM Assembly Code
; R0 = a, R1 = b
ADD R0, R0, #4
SUB R1, R0, #12
Operands: Constants\Immediates

## Slide 22
Generating small constants using move (MOV):
C Code
//int: 32-bit signed word
int a = 23;
int b = 0x45;
ARM Assembly Code
; R0 = a, R1 = b
MOV R0, #23
MOV R1, #0x45
Generating Constants

## Slide 23
Generating small constants using move (MOV):
Constant must have < 8 bits of precision
Note: MOV can also use 2 registers: MOV R7, R9
C Code
//int: 32-bit signed word
int a = 23;
int b = 0x45;
ARM Assembly Code
; R0 = a, R1 = b
MOV R0, #23
MOV R1, #0x45
Generating Constants

## Slide 24
Generate larger constants using move (MOV) and or (ORR):
C Code
int a = 0x7EDC8765;
ARM Assembly Code
# R0 = a
MOV R0, #0x7E000000
ORR R0, R0, #0xDC0000
ORR R0, R0, #0x8700
ORR R0, R0, #0x65
Generating Constants

## Slide 25
Too much data to fit in only 16 registers
Store more data in memory
Memory is large, but slow
Commonly used variables still kept in registers
Operands: Memory

## Slide 26
Each data byte has unique address
32-bit word = 4 bytes, so word address increments by 4
Byte-Addressable Memory

## Slide 27
Memory read called load
Mnemonic: load register (LDR)
Format:
LDR R0, [R1, #12]
  Address calculation:
    add base address (R1) to the offset (12)
    address = (R1 + 12)
  Result:
    R0 holds the data at memory address (R1 + 12)
Any register may be used as base address
Reading Memory

## Slide 28
Example: Read a word of data at memory address 8 into R3
  Address = (R2 + 8) = 8
  R3 = 0x01EE2842 after load
ARM Assembly Code
MOV R2, #0
LDR R3, [R2, #8]
Reading Memory

## Slide 29
Memory write are called stores
Mnemonic: store register (STR)
Writing Memory

## Slide 30
Example: Store the value held in R7 into memory word 21.
Memory address = 4 x 21 = 84 = 0x54
ARM assembly code
MOV R5, #0
STR R7, [R5, #0x54]
Writing Memory
The offset can be written in decimal or hexadecimal

## Slide 31
Address of a memory word must be multiplied by 4
Examples:
  Address of memory word 2 = 2 × 4 = 8
  Address of memory word 10 = 10 × 4 = 40
Recap: Accessing Memory

## Slide 32
How to number bytes within a word?
  Little-endian: byte numbers start at the little (least significant) end
  Big-endian: byte numbers start at the big (most significant) end
Big-Endian & Little-Endian Memory

## Slide 33
Jonathan Swift’s Gulliver’s Travels: the Little-Endians broke their eggs on the little end of the egg and the Big-Endians broke their eggs on the big end
It doesn’t really matter which addressing type used – except when two systems share data
Big-Endian & Little-Endian Memory

## Slide 34
Suppose R2 and R5 hold the values 8 and 0x23456789
After following code runs on big-endian system, what value is in R7?
In a little-endian system?
      STR R5, [R2, #0]
      LDRB R7, [R2, #1]
Big-Endian & Little-Endian Example

## Slide 35
Suppose R2 and R5 hold the values 8 and 0x23456789
After following code runs on big-endian system, what value is in R7?
In a little-endian system?
      STR R5, [R2, #0]
      LDRB R7, [R2, #1]
Big-Endian & Little-Endian Example
      Big-endian: 0x00000045
      Little-endian: 0x00000067

## Slide 36
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Programming

## Slide 37
British mathematician
Wrote the first computer program
Her program calculated the Bernoulli numbers on Charles Babbage’s Analytical Engine
She was a child of the poet Lord Byron
Ada Lovelace, 1815-1852

## Slide 38
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 39
Logical operations
Shifts / rotate
Multiplication
Data-processing Instructions

## Slide 40
AND
ORR
EOR (XOR)
BIC (Bit Clear = A & ~B)
MVN (MoVe and NOT)
Logical Instructions

## Slide 41
Logical Instructions: Examples

## Slide 42
AND or BIC: useful for masking bits
  Example: Masking all but the least significant byte of a value
  0xF234012F AND 0x000000FF = 0x0000002F
  0xF234012F BIC 0xFFFFFF00 = 0x0000002F
ORR: useful for combining bit fields
  Example: Combine 0xF2340000 with 0x000012BC:
  0xF2340000 ORR 0x000012BC = 0xF23412BC
Logical Instructions: Uses

## Slide 43
LSL: logical shift left
  Example: LSL R0, R7, #5 ; R0 = R7 << 5
LSR: logical shift right
  Example: LSR R3, R2, #31 ; R3 = R2 >> 31
ASR: arithmetic shift right
  Example: ASR R9, R11, R4 ; R9 = R11 >>> R47:0
ROR: rotate right
  Example: ROR R8, R1, #3 ; R8 = R1 ROR 3
Shift Instructions

## Slide 44
Shift Instructions: Example 1
Immediate shift amount (5-bit immediate)
Shift amount: 0-31

## Slide 45
Shift Instructions: Example 2
Register shift amount (uses low 8 bits of register)
Shift amount: 0-255

## Slide 46
MUL: 32 × 32 multiplication, 32-bit result
  MUL R1, R2, R3
  Result: R1 = (R2 x R3)31:0 (signed doesn’t matter)
UMULL: Unsigned multiply long: 32 × 32 multiplication, 64-bit result
  UMULL R1, R2, R3, R4
  Result: {R1,R4} = R2 x R3 (R2, R3 unsigned)
SMULL: Signed multiply long: 32 × 32 multiplication, 64-bit result
  SMULL R1, R2, R3, R4
  Result: {R1,R4} = R2 x R3 (R2, R3 signed)
Multiplication

## Slide 47
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 48
Don’t always want to execute code sequentially
For example:
  if/else statements, while loops, etc.: only want to execute code if a condition is true
  branching: jump to another portion of code if a condition is true
Conditional Execution

## Slide 49
Don’t always want to execute code sequentially
For example:
  if/else statements, while loops, etc.: only want to execute code if a condition is true
  branching: jump to another portion of code if a condition is true
ARM includes condition flags that can be:
  set by an instruction
  used to conditionally execute an instruction
Conditional Execution

## Slide 50
Set by ALU (recall from Chapter 5)
Held in Current Program Status Register (CPSR)
ARM Condition Flags
Flag | Name | Description
N | Negative | Instruction result is negative
Z | Zero | Instruction results in zero
C | Carry | Instruction causes an unsigned carry out
V | oVerflow | Instruction causes an overflow

## Slide 51
Review: ARM ALU

## Slide 52
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Does not save result
    Sets flags. If result:
      Is 0, Z=1
      Is negative, N=1
      Causes a carry out, C=1
      Causes a signed overflow, V=1
Setting the Condition Flags: NZCV

## Slide 53
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Does not save result
Method 2: Append instruction mnemonic with S
  Example: ADDS R1, R2, R3
    Performs: R2 + R3
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Saves result in R1
Setting the Condition Flags: NZCV

## Slide 54
Instruction may be conditionally executed based on the condition flags
Condition of execution is encoded as a condition mnemonic appended to the instruction mnemonic
  Example: CMP R1, R2
  SUBNE R3, R5, R8
        NE: not equal condition mnemonic
        SUB will only execute if R1 ≠ R2
        (i.e., Z = 0)
Condition Mnemonics

## Slide 55
Condition Mnemonics

## Slide 56
Example:
  CMP R5, R9 ; performs R5-R9
  ; sets condition flags
  SUBEQ R1, R2, R3 ; executes if R5==R9 (Z=1)
  ORRMI R4, R0, R9 ; executes if R5-R9 is
  ; negative (N=1)
  Suppose R5 = 17, R9 = 23:
    CMP performs: 17 – 23 = -6 (Sets flags: N=1, Z=0, C=0, V=0)
    SUBEQ doesn’t execute (they aren’t equal: Z=0)
    ORRMI executes because the result was negative (N=1)
Conditional Execution

## Slide 57
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 58
Branches enable out of sequence instruction execution
Types of branches:
  Branch (B)
    branches to another instruction
  Branch and link (BL)
    discussed later
Both can be conditional or unconditional
Branching

## Slide 59
The Stored Program

## Slide 60
ARM assembly
MOV R2, #17 ; R2 = 17
B TARGET ; branch to target
ORR R1, R1, #0x4 ; not executed
TARGET
SUB R1, R1, #78 ; R1 = R1 + 78
Labels (like TARGET) indicate instruction location. Labels can’t be reserved words (like ADD, ORR, etc.)
Unconditional Branching (B)

## Slide 61
ARM Assembly
MOV R0, #4 ; R0 = 4
ADD R1, R0, R0 ; R1 = R0+R0 = 8
CMP R0, R1 ; sets flags with R0-R1
BEQ THERE ; branch not taken (Z=0)
ORR R1, R1, #1 ; R1 = R1 OR R1 = 9
THERE
ADD R1, R1, 78 ; R1 = R1 + 78 = 87
The Branch Not Taken

## Slide 62
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 63
C Code
if (i == j)
f = g + h;
f = f – i;
if Statement

## Slide 64
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
L1
SUB R0, R0, R2 ; f = f - i
if Statement

## Slide 65
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
L1
SUB R0, R0, R2 ; f = f - i
if Statement
Assembly tests opposite case (i != j) of high-level code (i == j)

## Slide 66
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code

## Slide 67
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
L1
SUB R0, R0, R2

## Slide 68
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
L1
SUB R0, R0, R2
Useful for short conditional blocks of code

## Slide 69
C Code
if (i == j)
f = g + h;
else
f = f – i;
if/else Statement
ARM Assembly Code

## Slide 70
C Code
if (i == j)
f = g + h;
else
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
B L2 ; branch past else block
L1
SUB R0, R0, R2 ; f = f – i
L2
if/else Statement

## Slide 71
C Code
if (i == j)
f = g + h;
else
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUBNE R0, R0, R2 ; else f = f - i
if/else Statement: Alternate Code

## Slide 72
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUBNE R0, R0, R2 ; else f = f - i
if/else Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
B L2
L1
SUB R0, R0, R2
L2

## Slide 73
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
while Loops

## Slide 74
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
; R0 = pow, R1 = x
MOV R0, #1 ; pow = 1
MOV R1, #0 ; x = 0
WHILE
CMP R0, #128 ; R0-128
BEQ DONE ; if (pow==128) ; exit loop
LSL R0, R0, #1 ; pow=pow*2
ADD R1, R1, #1 ; x=x+1
B WHILE ; repeat loop
DONE
while Loops

## Slide 75
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
; R0 = pow, R1 = x
MOV R0, #1 ; pow = 1
MOV R1, #0 ; x = 0
WHILE
CMP R0, #128 ; R0-128
BEQ DONE ; if (pow==128) ; exit loop
LSL R0, R0, #1 ; pow=pow*2
ADD R1, R1, #1 ; x=x+1
B WHILE ; repeat loop
DONE
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).
while Loops

## Slide 76
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met
for Loops

## Slide 77
C Code
// adds numbers from 1-9
int sum = 0;
int i;
for (i=1; i!=10; i=i+1)
sum = sum + i;
ARM Assembly Code
for Loops

## Slide 78
C Code
// adds numbers from 1-9
int sum = 0
for (i=1; i!=10; i=i+1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #1 ; i = 1
MOV R1, #0 ; sum = 0
FOR
CMP R0, #10 ; R0-10
BEQ DONE ; if (i==10) ; exit loop
ADD R1, R1, R0 ; sum=sum + i
ADD R0, R0, #1 ; i = i + 1
B FOR ; repeat loop
DONE
for Loops

## Slide 79
In ARM, decremented loop variables are more efficient
for Loops: Decremented Loops

## Slide 80
C Code
// adds numbers from 1-9
int sum = 0
for (i=9; i!=0; i=i-1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #9 ; i = 9
MOV R1, #0 ; sum = 0
FOR
ADD R1, R1, R0 ; sum=sum + i
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BNE FOR ; if (i!=0) ; repeat loop
In ARM, decremented loop variables are more efficient
for Loops: Decremented Loops

## Slide 81
C Code
// adds numbers from 1-9
int sum = 0
for (i=9; i!=0; i=i-1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #9 ; i = 9
MOV R1, #0 ; sum = 0
FOR
ADD R1, R1, R0 ; sum=sum + i
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BNE FOR ; if (i!=0) ; repeat loop
In ARM, decremented loop variables are more efficient
Saves 2 instructions per iteration:
Decrement loop variable & compare: SUBS R0, R0, #1
Only 1 branch – instead of 2
for Loops: Decremented Loops

## Slide 82
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 83
Access large amounts of similar data
  Index: access to each element
  Size: number of elements
Arrays

## Slide 84
200-element array
  Base address = 0x14000000 (address of first element, scores[0])
  Array elements accessed relative to base address
Arrays

## Slide 85
C Code
int array[200];
array[0] = array[0] * 8;
array[1] = array[1] * 8;
ARM Assembly Code
; R0 = array base address
Accessing Arrays

## Slide 86
C Code
int array[5];
array[0] = array[0] * 8;
array[1] = array[1] * 8;
ARM Assembly Code
; R0 = array base address
MOV R0, #0x60000000 ; R0 = 0x60000000
LDR R1, [R0] ; R1 = array[0]
LSL R1, R1, 3 ; R1 = R1 << 3 = R1*8
STR R1, [R0] ; array[0] = R1
LDR R1, [R0, #4] ; R1 = array[1]
LSL R1, R1, 3 ; R1 = R1 << 3 = R1*8
STR R1, [R0, #4] ; array[1] = R1
Accessing Arrays

## Slide 87
C Code
int array[200];
int i;
for (i=199; i >= 0; i = i - 1)
array[i] = array[i] * 8;
ARM Assembly Code
; R0 = array base address, R1 = i
Arrays using for Loops

## Slide 88
C Code
int array[200];
int i;
for (i=199; i >= 0; i = i - 1)
array[i] = array[i] * 8;
ARM Assembly Code
; R0 = array base address, R1 = i
MOV R0, 0x60000000
MOV R1, #199
FOR
LDR R2, [R0, R1, LSL #2] ; R2 = array(i)
LSL R2, R2, #3 ; R2 = R2<<3 = R3*8
STR R2, [R0, R1, LSL #2] ; array(i) = R2
SUBS R1, R1, #1 ; i = i – 1
; and set flags
BPL FOR ; if (i>=0) repeat loop
Arrays using for Loops

## Slide 89
American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)
ASCII Code

## Slide 90
Cast of Characters