## Slide 1: Lecture 18: Function Calls & Machine Language
E85 Digital Design & Computer Engineering

## Slide 2
Function Calls
Machine Language
Lecture 18

## Slide 3
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 4
Caller: calling function (in this case, main)
Callee: called function (in this case, sum)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}
Function Calls

## Slide 5
Caller:
  passes arguments to callee
  jumps to callee
Function Conventions

## Slide 6
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller
Function Conventions

## Slide 7
Call Function: branch and link
BL
Return from function: move the link register to PC: MOV PC, LR
Arguments: R0-R3
Return value: R0
ARM Function Conventions

## Slide 8
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls
void means that simple doesn’t return a value

## Slide 9
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
BL branches to SIMPLE
LR = PC + 4 = 0x00000204
MOV PC, LR makes PC = LR
(the next instruction executed is at 0x00000200)
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls

## Slide 10
ARM conventions:
Argument values: R0 - R3
Return value: R0
Input Arguments and Return Value

## Slide 11
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}
Input Arguments and Return Value

## Slide 12
ARM Assembly Code
; R4 = y
MAIN
...
MOV R0, #2 ; argument 0 = 2
MOV R1, #3 ; argument 1 = 3
MOV R2, #4 ; argument 2 = 4
MOV R3, #5 ; argument 3 = 5
BL DIFFOFSUMS ; call function
MOV R4, R0 ; y = returned value
...
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
Input Arguments and Return Value

## Slide 13
ARM Assembly Code
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
diffofsums overwrote 3 registers: R4, R8, R9
diffofsums can use stack to temporarily store registers
Input Arguments and Return Value

## Slide 14
Memory used to temporarily save variables
Like stack of dishes, last-in-first-out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space no longer needed
The Stack

## Slide 15
Grows down (from higher to lower memory addresses)
Stack pointer: SP points to top of the stack
The Stack
Stack expands by 2 words

## Slide 16
Called functions must have no unintended side effects
But diffofsums overwrites 3 registers: R4, R8, R9
ARM Assembly Code
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
How Functions use the Stack

## Slide 17
ARM Assembly Code
; R2 = result
DIFFOFSUMS
SUB SP, SP, #12 ; make space on stack for 3 registers
STR R4, [SP, 8] ; save R4 on stack
STR R8, [SP, #4] ; save R8 on stack
STR R9, [SP] ; save R9 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R9, [SP] ; restore R9 from stack
LDR R8, [SP, #4] ; restore R8 from stack
LDR R4, [SP, #8] ; restore R4 from stack
ADD SP, SP, #12 ; deallocate stack space
MOV PC, LR ; return to caller
Storing Register Values on the Stack

## Slide 18
Before call
During call
After call
The Stack during diffofsums Call

## Slide 19
Preserved Callee-Saved | Nonpreserved Caller-Saved
R4-R11 | R12
R14 (LR) | R0-R3
R13 (SP) | CPSR
stack above SP | stack below SP
Registers

## Slide 20
ARM Assembly Code
; R2 = result
DIFFOFSUMS
STR R4, [SP, #-4]! ; save R4 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R4, [SP], #4 ; restore R4 from stack
MOV PC, LR ; return to caller
Storing Saved Registers only on Stack

## Slide 21
ARM Assembly Code
; R2 = result
DIFFOFSUMS
STR R4, [SP, #-4]! ; save R4 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R4, [SP], #4 ; restore R4 from stack
MOV PC, LR ; return to caller
Notice code optimization for expanding/contracting stack
Storing Saved Registers only on Stack

## Slide 22
ARM Assembly Code
STR LR, [SP, #-4]! ; store LR on stack
BL PROC2 ; call another function
...
LDR LR, [SP], #4 ; restore LR from stack
MOV PC, LR ; return to caller
Nonleaf Function

## Slide 23
C Code
int f1(int a, int b) {
int i, x;
x = (a + b)*(a − b);
for (i=0; i<a; i++)
x = x + f2(b+i);
return x;
}
int f2(int p) {
int r;
r = p + 5;
return r + p;
}
Nonleaf Function Example

## Slide 24
C Code
int f1(int a, int b) {
int i, x;
x = (a + b)*(a − b);
for (i=0; i<a; i++)
x = x + f2(b+i);
return x;
}
int f2(int p) {
int r;
r = p + 5;
return r + p;
}
Nonleaf Function Example
ARM Assembly Code
; R0=a, R1=b, R4=i, R5=x
F1
PUSH {R4, R5, LR}
ADD R5, R0, R1
SUB R12, R0, R1
MUL R5, R5, R12
MOV R4, #0
FOR
CMP R4, R0
BGE RETURN
PUSH {R0, R1}
ADD R0, R1, R4
BL F2
ADD R5, R5, R0
POP {R0, R1}
ADD R4, R4, #1
B FOR
RETURN
MOV R0, R5
POP {R4, R5, LR}
MOV PC, LR
; R0=p, R4=r
F2
PUSH {R4}
ADD R4, R0, 5
ADD R0, R4, R0
POP {R4}
MOV PC, LR

## Slide 25
Nonleaf Function Example
ARM Assembly Code
; R0=a, R1=b, R4=i, R5=x
F1
PUSH {R4, R5, LR} ; save regs
ADD R5, R0, R1 ; x = (a+b)
SUB R12, R0, R1 ; temp = (a-b)
MUL R5, R5, R12 ; x = x*temp
MOV R4, #0 ; i = 0
FOR
CMP R4, R0 ; i < a?
BGE RETURN ; no: exit loop
PUSH {R0, R1} ; save regs
ADD R0, R1, R4 ; arg is b+i
BL F2 ; call f2(b+i)
ADD R5, R5, R0 ; x = x+f2(b+i)
POP {R0, R1} ; restore regs
ADD R4, R4, #1 ; i++
B FOR ; repeat loop
RETURN
MOV R0, R5 ; return x
POP {R4, R5, LR} ; restore regs
MOV PC, LR ; return
; R0=p, R4=r
F2
PUSH {R4} ; save regs
ADD R4, R0, 5 ; r = p+5
ADD R0, R4, R0 ; return r+p
POP {R4} ; restore regs
MOV PC, LR ; return

## Slide 26
Stack during Nonleaf Function
At beginning of f1
Just before calling f2
After calling f2

## Slide 27
C Code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}
Recursive Function Call

## Slide 28
ARM Assembly Code
0x94 FACTORIAL STR R0, [SP, #-4]! ;store R0 on stack
0x98 STR LR, [SP, #-4]! ;store LR on stack
0x9C CMP R0, #2 ;set flags with R0-2
0xA0 BHS ELSE ;if (r0>=2) branch to else
0xA4 MOV R0, #1 ; otherwise return 1
0xA8 ADD SP, SP, #8 ; restore SP 1
0xAC MOV PC, LR ; return
0xB0 ELSE SUB R0, R0, #1 ; n = n - 1
0xB4 BL FACTORIAL ; recursive call
0xB8 LDR LR, [SP], #4 ; restore LR
0xBC LDR R1, [SP], #4 ; restore R0 (n) into R1
0xC0 MUL R0, R1, R0 ; R0 = n*factorial(n-1)
0xC4 MOV PC, LR ; return
Recursive Function Call

## Slide 29
ARM Assembly Code
0x94 FACTORIAL STR R0, [SP, #-4]!
0x98 STR LR, [SP, #-4]!
0x9C CMP R0, #2
0xA0 BHS ELSE
0xA4 MOV R0, #1
0xA8 ADD SP, SP, #8
0xAC MOV PC, LR
0xB0 ELSE SUB R0, R0, #1
0xB4 BL FACTORIAL
0xB8 LDR LR, [SP], #4
0xBC LDR R1, [SP], #4
0xC0 MUL R0, R1, R0
0xC4 MOV PC, LR
Recursive Function Call
C Code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}

## Slide 30
Before call
During call
After call
Stack during Recursive Call

## Slide 31
Caller
  Puts arguments in R0-R3
  Saves any needed registers (LR, maybe R0-R3, R8-R12)
  Calls function: BL CALLEE
  Restores registers
  Looks for result in R0
Callee
  Saves registers that might be disturbed (R4-R7)
  Performs function
  Puts result in R0
  Restores registers
  Returns: MOV PC, LR
Function Call Summary

## Slide 32
How to Encode Instructions?

## Slide 33
How to Encode Instructions?
Design Principle 1: Regularity supports design simplicity
  32-bit data, 32-bit instructions
  For design simplicity, would prefer a single instruction format but…

## Slide 34
How to Encode Instructions?
Design Principle 1: Regularity supports design simplicity
  32-bit data, 32-bit instructions
  For design simplicity, would prefer a single instruction format but…
  Instructions have different needs

## Slide 35
Good design demands good compromises
Multiple instruction formats allow flexibility
  ADD, SUB: use 3 register operands
  LDR, STR: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (regularity supports design simplicity and smaller is faster)
Design Principle 4

## Slide 36
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
3 instruction formats:
  Data-processing
  Memory
  Branch
Machine Language

## Slide 37
Data-processing
Memory
Branch
Instruction Formats

## Slide 38
Operands:
  Rn: first source register
  Src2: second source – register or immediate
  Rd: destination register
Control fields:
  cond: specifies conditional execution
  op: the operation code or opcode
  funct: the function/operation to perform
Data-processing Instruction Format

## Slide 39
op = 002 for data-processing (DP) instructions
funct is composed of cmd, I-bit, and S-bit
Data-processing Control Fields

## Slide 40
op = 002 for data-processing (DP) instructions
funct is composed of cmd, I-bit, and S-bit
  cmd: specifies the specific data-processing instruction. For example,
    cmd = 01002 for ADD
    cmd = 00102 for SUB
  I-bit
    I = 0: Src2 is a register
    I = 1: Src2 is an immediate
  S-bit: 1 if sets condition flags
    S = 0: SUB R0, R5, R7
    S = 1: ADDS R8, R2, R4 or CMP R3, #10
Data-processing Control Fields

## Slide 41
Src2 can be:
  Immediate
  Register
  Register-shifted register
Data-processing Src2 Variations

## Slide 42
Src2 can be:
  Immediate
  Register
  Register-shifted register
Data-processing Src2 Variations

## Slide 43
Immediate encoded as:
  imm8: 8-bit unsigned immediate
  rot: 4-bit rotation value
32-bit constant is: imm8 ROR (rot × 2)
Immediate Src2

## Slide 44
Immediate encoded as:
  imm8: 8-bit unsigned immediate
  rot: 4-bit rotation value
32-bit constant is: imm8 ROR (rot × 2)
Example: imm8 = abcdefgh
Immediate Src2
rot | 32-bit constant
0000 | 0000 0000 0000 0000 0000 0000 abcd efgh
0001 | gh00 0000 0000 0000 0000 0000 00ab cdef
… | …
1111 | 0000 0000 0000 0000 0000 00ab cdef gh00

## Slide 45
Immediate encoded as:
  imm8: 8-bit unsigned immediate
  rot: 4-bit rotation value
32-bit constant is: imm8 ROR (rot × 2)
Example: imm8 = abcdefgh
Immediate Src2
rot | 32-bit constant
0000 | 0000 0000 0000 0000 0000 0000 abcd efgh
0001 | gh00 0000 0000 0000 0000 0000 00ab cdef
… | …
1111 | 0000 0000 0000 0000 0000 00ab cdef gh00
ROR by X = ROL by (32-X)
Ex: ROR by 30 = ROL by 2

## Slide 46
  ADD R0, R1, #42
        cond = 11102 (14) for unconditional execution
        op = 002 (0) for data-processing instructions
        cmd = 01002 (4) for ADD
        Src2 is an immediate so I = 1
        Rd = 0, Rn = 1
        imm8 = 42, rot = 0
DP Instruction with Immediate Src2

## Slide 47
  ADD R0, R1, #42
        cond = 11102 (14) for unconditional execution
        op = 002 (0) for data-processing instructions
        cmd = 01002 (4) for ADD
        Src2 is an immediate so I = 1
        Rd = 0, Rn = 1
        imm8 = 42, rot = 0
DP Instruction with Immediate Src2
0xE281002A

## Slide 48
  SUB R2, R3, #0xFF0
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 00102 (2) for SUB
  Src2 is an immediate so I=1
  Rd = 2, Rn = 3
  imm8 = 0xFF
  imm8 must be rotated right by 28 to produce 0xFF0, so rot = 14
DP Instruction with Immediate Src2
0xE2432EFF
ROR by 28 =
ROL by (32-28) = 4

## Slide 49
DP Instruction with Register Src2
Src2 can be:
  Immediate
  Register
  Register-shifted register

## Slide 50
DP Instruction with Register Src2
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift (i.e., >>, <<, >>>, ROR)

## Slide 51
DP Instruction with Register Src2
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift (i.e., >>, <<, >>>, ROR)
  First, consider unshifted versions of Rm (shamt5=0, sh=0)

## Slide 52
  ADD R5, R6, R7
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 01002 (4) for ADD
  Src2 is a register so I=0
  Rd = 5, Rn = 6, Rm = 7
  shamt = 0, sh = 0
DP Instruction with Register Src2
0xE0865007

## Slide 53
DP Instruction with Register Src2
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift
Shift Type | sh
LSL | 002
LSR | 012
ASR | 102
ROR | 112
  Now, consider shifted versions.

## Slide 54
DP Instruction with Register Src2
  ORR R9, R5, R3, LSR #2
  Operation: R9 = R5 OR (R3 >> 2)
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11002 (12) for ORR
  Src2 is a register so I=0
  Rd = 9, Rn = 5, Rm = 3
  shamt5 = 2, sh = 012 (LSR)
  1110 00 0 1100 0 0101 1001 00010 01 0 0011
  0xE1859123

## Slide 55
DP with Register-shifted Reg. Src2
Src2 can be:
  Immediate
  Register
  Register-shifted register

## Slide 56
DP with Register-shifted Reg. Src2
  EOR R8, R9, R10, ROR R12
  Operation: R8 = R9 XOR (R10 ROR R12)
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 00012 (1) for EOR
  Src2 is a register so I=0
  Rd = 8, Rn = 9, Rm = 10, Rs = 12
  sh = 112 (ROR)
  1110 00 0 0001 0 1001 1000 1100 0 11 1 1010
  0xE0298C7A

## Slide 57
Shift Instructions Encoding
Shift Type | sh
LSL | 002
LSR | 012
ASR | 102
ROR | 112

## Slide 58
Shift Instructions: Immediate shamt
  ROR R1, R2, #23
  Operation: R1 = R2 ROR 23
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is an immediate-shifted register so I=0
  Rd = 1, Rn = 0, Rm = 2
  shamt5 = 23, sh = 112 (ROR)
  1110 00 0 1101 0 0000 0001 10111 11 0 0010
  0xE1A01BE2

## Slide 59
Shift Instructions: Immediate shamt
  ROR R1, R2, #23
  Operation: R1 = R2 ROR 23
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is an immediate-shifted register so I=0
  Rd = 1, Rn = 0, Rm = 2
  shamt5 = 23, sh = 112 (ROR)
Uses (immediate-shifted) register Src2 encoding
  1110 00 0 1101 0 0000 0001 10111 11 0 0010
  0xE1A01BE2

## Slide 60
Shift Instructions: Register shamt
  ASR R5, R6, R10
  Operation: R5 = R6 >>> R107:0
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is a register so I=0
  Rd = 5, Rn = 0, Rm = 6, Rs = 10
  sh = 102 (ASR)
  1110 00 0 1101 0 0000 0101 1010 0 10 1 0110
  0xE1A05A56

## Slide 61
Shift Instructions: Register shamt
  ASR R5, R6, R10
  Operation: R5 = R6 >>> R107:0
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is a register so I=0
  Rd = 5, Rn = 0, Rm = 6, Rs = 10
  sh = 102 (ASR)
  1110 00 0 1101 0 0000 0101 1010 0 10 1 0110
  0xE1A05A56
Uses register-shifted register Src2 encoding

## Slide 62
Src2 can be:
  Immediate
  Register
  Register-shifted register
Review: Data-processing Format

## Slide 63
Data-processing
Memory
Branch
Instruction Formats

## Slide 64
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset
funct = 6 control bits
Memory Instruction Format

## Slide 65
Recall: Address = Base Address + Offset
  Example: LDR R1, [R2, #4]
  Base Address = R2, Offset = 4
  Address = (R2 + 4)
Base address always in a register
The offset can be:
  an immediate
  a register
  or a scaled (shifted) register
Offset Options

## Slide 66
ARM Assembly | Memory Address
LDR R0, [R3, #4] | R3 + 4
LDR R0, [R5, #-16] | R5 – 16
LDR R1, [R6, R7] | R6 + R7
LDR R2, [R8, -R9] | R8 – R9
LDR R3, [R10, R11, LSL #2] | R10 + (R11 << 2)
LDR R4, [R1, -R12, ASR #4] | R1 – (R12 >>> 4)
LDR R0, [R9] | R9
Offset Examples

## Slide 67
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: register (optionally shifted) or immediate
funct = 6 control bits
Memory Instruction Format

## Slide 68
Mode | Address | Base Reg. Update
Offset | Base register ± Offset | No change
Preindex | Base register ± Offset | Base register ± Offset
Postindex | Base register | Base register ± Offset
Examples
Offset: LDR R1, [R2, #4] ; R1 = mem[R2+4]
Preindex: LDR R3, [R5, #16]! ; R3 = mem[R5+16]
; R5 = R5 + 16
Postindex: LDR R8, [R1], #8 ; R8 = mem[R1]
    ; R1 = R1 + 8
Indexing Modes

## Slide 69
funct:
  I: Immediate bar
  P: Preindex
  U: Add
  B: Byte
  W: Writeback
  L: Load
Memory Instruction Format

## Slide 70
Memory Format funct Encodings
Type of Operation
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 71
P | W | Indexing Mode
0 | 1 | Not supported
0 | 0 | Postindex
1 | 0 | Offset
1 | 1 | Preindex
Memory Format funct Encodings
Type of Operation
Indexing Mode
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 72
P | W | Indexing Mode
0 | 1 | Not supported
0 | 0 | Postindex
1 | 0 | Offset
1 | 1 | Preindex
Memory Format funct Encodings
Type of Operation
Value | I | U
0 | Immediate offset in Src2 | Subtract offset from base
1 | Register offset in Src2 | Add offset to base
Add/Subtract Immediate/Register Offset
Indexing Mode
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 73
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: immediate or register (optionally shifted)
funct = I (immediate bar), P (preindex), U (add),
B (byte), W (writeback), L (load)
Memory Instruction Format

## Slide 74
Memory Instr. with Immediate Src2
  STR R11, [R5], #-26
  Operation: mem[R5] <= R11; R5 = R5 - 26
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 00000002 (0)
  I = 0 (immediate offset), P = 0 (postindex),
  U = 0 (subtract), B = 0 (store word), W = 0 (postindex),
  L = 0 (store)
  Rd = 11, Rn = 5, imm12 = 26

## Slide 75
Memory Instr. with Register Src2
  LDR R3, [R4, R5]
  Operation: R3 <= mem[R4 + R5]
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 1110012 (57)
  I = 1 (register offset), P = 1 (offset indexing),
  U = 1 (add), B = 0 (load word), W = 0 (offset indexing),
  L = 1 (load)
  Rd = 3, Rn = 4, Rm = 5 (shamt5 = 0, sh = 0)
  1110 01 111001 0100 0011 00000 00 0 0101 = 0xE7943005

## Slide 76
Memory Instr. with Scaled Reg. Src2
  STR R9, [R1, R3, LSL #2]
  Operation: mem[R1 + (R3 << 2)] <= R9
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 1110002 (0)
  I = 1 (register offset), P = 1 (offset indexing),
  U = 1 (add), B = 0 (store word), W = 0 (offset indexing),
  L = 0 (store)
  Rd = 9, Rn = 1, Rm = 3, shamt = 2, sh = 002 (LSL)
  1110 01 111000 0001 1001 00010 00 0 0011 = 0xE7819103

## Slide 77
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: register (optionally shifted) or immediate
funct = I (immediate bar), P (preindex), U (add),
B (byte), W (writeback), L (load)
Review: Memory Instruction Format

## Slide 78
Data-processing
Memory
Branch
Instruction Formats

## Slide 79
Encodes B and BL
op = 102
imm24: 24-bit immediate
funct = 1L2: L = 1 for BL, L = 0 for B
Branch Instruction Format

## Slide 80
Branch Target Address (BTA): Next PC when branch taken
BTA is relative to current PC + 8
imm24 encodes BTA
imm24 = # of words BTA is away from PC+8
Encoding Branch Target Address

## Slide 81
ARM assembly code
0xA0 BLT THERE
0xA4 ADD R0, R1, R2
0xA8 SUB R0, R0, R9
0xAC ADD SP, SP, #8
0xB0 MOV PC, LR
0xB4 THERE SUB R0, R0, #1
0xB8 BL TEST
PC = 0xA0
PC + 8 = 0xA8
THERE label is 3 instructions past PC+8
So, imm24 = 3
PC
PC+8
BTA
Branch Instruction: Example 1
0xBA000003

## Slide 82
ARM assembly code
0x8040 TEST LDRB R5, [R0, R3]
0x8044 STRB R5, [R1, R3]
0x8048 ADD R3, R3, #1
0x8044 MOV PC, LR
0x8050 BL TEST
0x8054 LDR R3, [R1], #4
0x8058 SUB R4, R3, #9
PC = 0x8050
PC + 8 = 0x8058
TEST label is 6 instructions before PC+8
So, imm24 = -6
Branch Instruction: Example 2
PC
PC+8
BTA
0xEBFFFFFA

## Slide 83
Review: Instruction Formats

## Slide 84
Encode in cond bits of machine instruction
  For example,
  ANDEQ R1, R2, R3 (cond = 0000)
  ORRMI R4, R5, #0xF (cond = 0100)
  SUBLT R9, R3, R8 (cond = 1011)
Conditional Execution

## Slide 85
Review: Condition Mnemonics

## Slide 86
Conditional Execution: Machine Code

## Slide 87
Start with op: tells how to parse rest
    op = 00 (Data-processing)
    op = 01 (Memory)
    op = 10 (Branch)
I-bit: tells how to parse Src2
Data-processing instructions:
    If I-bit is 0, bit 4 determines if Src2 is a register (bit 4 = 0) or a register-shifted register (bit 4 = 1)
Memory instructions:
    Examine funct bits for indexing mode, instruction, and add or subtract offset
Interpreting Machine Code

## Slide 88
0xE0475001
Interpreting Machine Code: Example 1

## Slide 89
0xE0475001
  Start with op: 002, so data-processing instruction
Interpreting Machine Code: Example 1

## Slide 90
0xE0475001
  Start with op: 002, so data-processing instruction
  I-bit: 0, so Src2 is a register
  bit 4: 0, so Src2 is a register (optionally shifted by shamt5)
Interpreting Machine Code: Example 1

## Slide 91
0xE0475001
  Start with op: 002, so data-processing instruction
  I-bit: 0, so Src2 is a register
  bit 4: 0, so Src2 is a register (optionally shifted by shamt5)
  cmd: 00102 (2), so SUB
  Rn=7, Rd=5, Rm=1, shamt5 = 0, sh = 0
  So, instruction is: SUB R5,R7,R1
Interpreting Machine Code: Example 1

## Slide 92
0xE5949010
Interpreting Machine Code: Example 2

## Slide 93
0xE5949010
  Start with op: 012, so memory instruction
  funct: B=0, L=1, so LDR; P=1, W=0, so offset indexing;
  I=0, so immediate offset, U=1, so add offset
  Rn=4, Rd=9, imm12 = 16
  So, instruction is: LDR R9,[R4,#16]
Interpreting Machine Code: Example 2

## Slide 94
How do we address operands?
Register
Immediate
Base
PC-Relative
Addressing Modes

## Slide 95
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 96
Source and destination operands found in registers
Used by data-processing instructions
Three submodes:
  Register-only
  Immediate-shifted register
  Register-shifted register
Register Addressing

## Slide 97
Register-only
  Example: ADD R0, R2, R7
Immediate-shifted register
  Example: ORR R5, R1, R3, LSL #1
Register-shifted register
  Example: SUB R12, R9, R0, ASR R1
Register Addressing Examples

## Slide 98
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 99
Operands found in registers and immediates
  Example: ADD R9, R1, #14
Uses data-processing format with I=1
  Immediate is encoded as
    8-bit immediate (imm8)
    4-bit rotation (rot)
  32-bit immediate = imm8 ROR (rot x 2)
Immediate Addressing

## Slide 100
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 101
Address of operand is:
base register + offset
Offset can be a:
  12-bit Immediate
  Register
  Immediate-shifted Register
Base Addressing

## Slide 102
Immediate offset
  Example: LDR R0, [R8, #-11]
  (R0 = mem[R8 - 11] )
Register offset
  Example: LDR R1, [R7, R9]
  (R1 = mem[R7 + R9] )
Immediate-shifted register offset
  Example: STR R5, [R3, R2, LSL #4]
  (R5 = mem[R3 + (R2 << 4)] )
Base Addressing Examples

## Slide 103
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 104
Used for branches
Branch instruction format:
  Operands are PC and a signed 24-bit immediate (imm24)
  Changes the PC
  New PC is relative to the old PC
  imm24 indicates the number of words away from PC+8
PC = (PC+8) + (SignExtended(imm24) x 4)
PC-Relative Addressing

## Slide 105
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation
Power of the Stored Program

## Slide 106
Program Counter (PC): keeps track of current instruction
The Stored Program

## Slide 107
How to implement the ARM Instruction Set
Architecture in Hardware
  Microarchitecture
Up Next