## Slide 1: Lecture 21: Multicycle Processor
E85 Digital Design & Computer Engineering

## Slide 2
Multicycle Processor
Lecture 21

## Slide 3
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle processor addresses these issues by breaking instruction into shorter steps
  shorter instructions take fewer steps
  can re-use hardware
  cycle time is faster
Multicycle ARM Processor

## Slide 4
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Multicycle ARM Processor

## Slide 5
Single-cycle:
  + simple
  cycle time limited by longest instruction (LDR)
  separate memories for instruction and data
  3 adders/ALUs
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Multicycle ARM Processor
Same design steps as single-cycle:
first datapath
then control

## Slide 6
Replace Instruction and Data memories with a single unified memory – more realistic
Multicycle State Elements

## Slide 7
STEP 1: Fetch instruction
Multicycle Datapath: Instruction Fetch
LDR Rd, [Rn, imm12]

## Slide 8
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Register Read
STEP 2: Read source operands from RF

## Slide 9
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Address
STEP 3: Compute the memory address

## Slide 10
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Memory Read
STEP 4: Read data from memory

## Slide 11
LDR Rd, [Rn, imm12]
Multicycle Datapath: LDR Write Register
STEP 5: Write data back to register file

## Slide 12
Multicycle Datapath: Increment PC
Meanwhile: Increment PC
Concurrent with fetching instruction

## Slide 13
Multicycle Datapath: Access to PC
PC can be read/written by instruction

## Slide 14
Multicycle Datapath: Access to PC
PC can be read/written by instruction
Read: R15 (PC+8) available in Register File

## Slide 15
Multicycle Datapath: Read to PC (R15)
Example: ADD R1, R15, R2

## Slide 16
Multicycle Datapath: Read to PC (R15)
Example: ADD R1, R15, R2
R15 needs to be read as PC+8 from Register File (RF) in 2nd step
PC+4 was computed in 1st step
So (also in 2nd step) ALU computes (PC+4) + 4 for R15 input

## Slide 17
Multicycle Datapath: Read to PC (R15)
Example: ADD R1, R15, R2
R15 needs to be read as PC+8 from Register File (RF) in 2nd step
PC+4 was computed in 1st step
So (also in 2nd step) ALU computes (PC+4) + 4 for R15 input
  SrcA = PC (which was already updated in step 1 to PC+4)
  SrcB = 4
  ALUResult = PC + 8
ALUResult is fed to R15 input port of RF in 2nd step (which is then routed to RD1 output of RF)

## Slide 18
Multicycle Datapath: Access to PC
PC can be read/written by instruction
Read: R15 (PC+8) available in Register File
Write: Be able to write result of instruction to PC

## Slide 19
Multicycle Datapath: Write to PC (R15)
Example: SUB R15, R8, R3

## Slide 20
Multicycle Datapath: Write to PC (R15)
Example: SUB R15, R8, R3
Result of instruction needs to be written to the PC register
ALUResult already routed to the PC register, just assert PCWrite

## Slide 21
Multicycle Datapath: Write to PC (R15)
Example: SUB R15, R8, R3
Result of instruction needs to be written to the PC register
ALUResult already routed to the PC register, just assert PCWrite

## Slide 22
Write data in Rn to memory
Multicycle Datapath: STR

## Slide 23
With immediate addressing (i.e., an immediate Src2), no additional changes needed for datapath
Multicycle Datapath: Data-processing

## Slide 24
With register addressing (register Src2):
Read from Rn and Rm
Multicycle Datapath: Data-processing

## Slide 25
Calculate branch target address:
BTA = (ExtImm) + (PC+8)
ExtImm = Imm24 << 2 and sign-extended
Multicycle Datapath: B

## Slide 26
Multicycle ARM Processor

## Slide 27
Multicycle Control
First, discuss Decoder
Then, Conditional Logic

## Slide 28
Multicycle Control: Decoder

## Slide 29
Multicycle Control: Decoder
Decoder

## Slide 30
Multicycle Control: Decoder
ALU Decoder and PC Logic same as single-cycle

## Slide 31
Multicycle Control: Instr Decoder
RegSrc0 = (Op == 102)
RegSrc1 = (Op == 012)
ImmSrc1:0 = Op
Instruction | Op | Funct5 | Funct0 | RegSrc0 | RegSrc1 | ImmSrc1:0
LDR | 01 | X | 1 | 0 | X | 01
STR | 01 | X | 0 | 0 | 1 | 01
DP immediate | 00 | 1 | X | 0 | X | 00
DP register | 00 | 0 | X | 0 | 0 | 00
B | 10 | X | X | 1 | X | 10

## Slide 32
Multicycle ARM Processor

## Slide 33
Multicycle Control: Main FSM
Decoder

## Slide 34
Main Controller FSM: Fetch

## Slide 35
Main Controller FSM: Decode

## Slide 36
Main Controller FSM: Address

## Slide 37
Main Controller FSM: Read Memory

## Slide 38
Multicycle ARM Processor

## Slide 39
Main Controller FSM: LDR

## Slide 40
Main Controller FSM: STR

## Slide 41
Main Controller FSM: Data-processing

## Slide 42
Main Controller FSM: Data-processing

## Slide 43
Multicycle Controller FSM

## Slide 44
Multicycle Control
First, discuss Decoder
Then, Conditional Logic

## Slide 45
Multicycle Control: Cond. Logic

## Slide 46
Single-Cycle Conditional Logic

## Slide 47
Multicycle Conditional Logic
PCWrite asserted in Fetch state
ExecuteI/ExecuteR state:
CondEx asserts
ALUFlags generated
ALUWB state:
Flags updated
CondEx changes
PCWrite, RegWrite, and
MemWrite don’t see
change till new
instruction (Fetch state)

## Slide 48
Instructions take different number of cycles.
Multicycle Processor Performance

## Slide 49
Multicycle Controller FSM

## Slide 50
Instructions take different number of cycles:
  3 cycles:
  4 cycles:
  5 cycles:
Multicycle Processor Performance

## Slide 51
Instructions take different number of cycles:
  3 cycles: B
  4 cycles: DP, STR
  5 cycles: LDR
Multicycle Processor Performance

## Slide 52
Instructions take different number of cycles:
  3 cycles: B
  4 cycles: DP, STR
  5 cycles: LDR
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% data processing
Multicycle Processor Performance

## Slide 53
Instructions take different number of cycles:
  3 cycles: B
  4 cycles: DP, STR
  5 cycles: LDR
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  13% branches
  52% data processing
Average CPI = (0.13)(3) + (0.52 + 0.10)(4) + (0.25)(5) = 4.12
Multicycle Processor Performance

## Slide 54
Multicycle critical path:
Assumptions:
  RF is faster than memory
  writing memory is faster than reading memory
Tc2 = tpcq + 2tmux + max(tALU + tmux, tmem) + tsetup
Multicycle Processor Performance

## Slide 55
Tc2 = ?
Multicycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 56
Tc2 = tpcq + 2tmux + max[tALU + tmux, tmem] + tsetup
= [40 + 2(25) + 200 + 50] ps = 340 ps
Multicycle Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 40
Register setup | tsetup | 50
Multiplexer | tmux | 25
ALU | tALU | 120
Decoder | tdec | 70
Memory read | tmem | 200
Register file read | tRFread | 100
Register file setup | tRFsetup | 60

## Slide 57
For a program with 100 billion instructions executing on a multicycle ARM processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 340 ps
Execution Time = ?
Multicycle Performance Example

## Slide 58
For a program with 100 billion instructions executing on a multicycle ARM processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 340 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(340 × 10-12)
= 140 seconds
Multicycle Performance Example

## Slide 59
For a program with 100 billion instructions executing on a multicycle ARM processor
  CPI = 4.12 cycles/instruction
  Clock cycle time: Tc2 = 340 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(340 × 10-12)
= 140 seconds
This is slower than the single-cycle processor (84 sec.)
Multicycle Performance Example

## Slide 60
Processor Comparisons
Single Cycle Multicycle
One cycle/instruction 3-5 cycles/instruction
Long clock period Shorter clock period
Separate I and D Mem Unified Memory
Combinational controller FSM controller
Architectural State Only Extra state