## Slide 1: Lecture 3: Timing & Sequential Circuits
E85 Digital Design & Computer Engineering

## Slide 2
Timing
Sequential Circuits
Latches and Flip-Flops
Synchronous Logic Design
Lecture 3

## Slide 3
A logic circuit is composed of:
Inputs
Outputs
Functional specification
Timing specification
Introduction

## Slide 4
Delay: time between input change and output changing
How to build fast circuits?
Timing

## Slide 5
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output
Propagation & Contamination Delay

## Slide 6
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others
  Circuits slow down when hot and speed up when cold
Propagation & Contamination Delay

## Slide 7
Critical (Long) Path: tpd = 2tpd_AND + tpd_OR
Short Path: tcd = tcd_AND
Critical (Long) & Short Paths

## Slide 8
Example: 8-input OR Delay
Find the minimum and maximum delay of this 8-input OR
Cell | Propagation Delay (ps) | Contamination Delay (ps)
OR2 | 20 | 15
OR3 | 25 | 19
OR4 | 35 | 28

## Slide 9
Solution: 8-input OR Delay
Find the minimum and maximum delay of this 8-input OR
Annotate each node with earliest and latest arrivals
Min = 15 ps from A7 to Y.
Max = 140 ps from A0 to Y.
Cell | Propagation Delay (ps) | Contamination Delay (ps)
OR2 | 20 | 15
OR3 | 25 | 19
OR4 | 35 | 28

## Slide 10
Example: Optimized 8-input OR
Redesign the 8-input OR to be as fast as possible.
Cell | Propagation Delay (ps) | Contamination Delay (ps)
OR2 | 20 | 15
OR3 | 25 | 19
OR4 | 35 | 28

## Slide 11
Example: Optimized 8-input OR
Redesign the 8-input OR to be as fast as possible.
Try various possibilities:
Cell | Propagation Delay (ps) | Contamination Delay (ps)
OR2 | 20 | 15
OR3 | 25 | 19
OR4 | 35 | 28

## Slide 12
Solution: Optimized 8-input OR
Redesign the 8-input OR to be as fast as possible.
Annotate delays. OR3+OR3 is fastest (50 ps).
Cell | Propagation Delay (ps) | Contamination Delay (ps)
OR2 | 20 | 15
OR3 | 25 | 19
OR4 | 35 | 28

## Slide 13
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about past inputs necessary to explain its future behavior
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: combinational logic followed by a bank of flip-flops
Sequential Logic Introduction

## Slide 14
Give sequence to events
Have memory (short-term)
Use feedback from output to input to store information
Sequential Circuits

## Slide 15
The state of a circuit influences its future behavior
State elements store state
  Bistable circuit
  SR Latch
  D Latch
  D Flip-flop
State Elements

## Slide 16
Fundamental building block of other state elements
Two outputs: Q, Q
No inputs
Bistable Circuit

## Slide 17
Consider the two possible cases:
  Q = 0:
  then Q = 0, Q = 1 (consistent)
  Q = 1:
  then Q = 1, Q = 0 (consistent)
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state
Bistable Circuit Analysis

## Slide 18
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1
SR (Set/Reset) Latch

## Slide 19
  S = 1, R = 0:
  then Q = 1 and Q = 0
  Set the output
  S = 0, R = 1:
  then Q = 0 and Q = 1
  Reset the output
SR Latch Analysis
1
1

## Slide 20
  S = 0, R = 0:
  then Q = Qprev
  Memory!
  S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid State
  Q ≠ NOT Q
SR Latch Analysis
1

## Slide 21
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1
  (S = 1, R = 0, Q = 1)
  Reset: Make the output 0
  (S = 0, R = 1, Q = 0)
Avoid invalid state
(when S = R = 1)
SR Latch Symbol

## Slide 22
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1,
  D passes through to Q (transparent)
  When CLK = 0,
  Q holds its previous value (opaque)
Avoids invalid case when
Q ≠ NOT Q
D Latch

## Slide 23
D Latch Internal Circuit

## Slide 24
Inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered
Activated on the clock edge
D Flip-Flop

## Slide 25
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q
D Flip-Flop Internal Circuit

## Slide 26
D Latch vs. D Flip-Flop

## Slide 27
Registers: Multi-bit Flip-Flop

## Slide 28
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
Enabled Flip-Flops

## Slide 29
Inputs: CLK, D, Reset
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Resettable Flip-Flops

## Slide 30
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 31
Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop

## Slide 32
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves as ordinary D flip-flop
Settable Flip-Flops

## Slide 33
Sequential circuits: all circuits that aren’t combinational
A problematic circuit:
No inputs and 1-3 outputs
Astable circuit, oscillates
Period depends on inverter delay
It has a cyclic path: output fed back to input
Sequential Logic

## Slide 34
Multi-input XOR: Odd parity
SystemVerilog Description
module flop(input logic clk, d,
output logic q);
always_ff @(posedge clk)
q <= d;
endmodule

## Slide 35
Multi-input XOR: Odd parity
SystemVerilog Description
module flopenr(input logic clk, en, reset, d,
output logic q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (en) q <= d;
endmodule

## Slide 36
Multi-input XOR: Odd parity
SystemVerilog Description
module flopenr #(parameter WIDTH = 4)
(input logic clk, reset, en,
input logic [WIDTH-1:0] d,
output logic [WIDTH-1:0] q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (en) q <= d;
endmodule

## Slide 37
Breaks cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge: system synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock signal
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines
Synchronous Sequential Logic Design