## Slide 1: Lecture 5: Sequential Timing
E85 Digital Design & Computer Engineering

## Slide 2
Timing of Sequential Logic
Metastability
Parallelism
Lecture 5

## Slide 3
Flip-flop samples D at clock edge
D must be stable when sampled
Similar to a photograph, D must be stable around clock edge
If not, metastability can occur
Timing

## Slide 4
Setup time: tsetup = time before clock edge data must be stable (i.e. not changing)
Hold time: thold = time after clock edge data must be stable
Aperture time: ta = time around clock edge data must be stable (ta = tsetup + thold)
Input Timing Constraints

## Slide 5
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)
Output Timing Parameters

## Slide 6
Synchronous sequential circuit inputs must be stable during aperture (setup and hold) time around clock edge
Specifically, inputs must be stable
  at least tsetup before the clock edge
  at least until thold after the clock edge
Dynamic Discipline

## Slide 7
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements
Dynamic Discipline

## Slide 8
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)
Setup Time Constraint
(tpcq + tsetup): sequencing overhead

## Slide 9
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold < tccq + tcd
tcd > thold - tccq
Hold Time Constraint

## Slide 10
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!
Timing Analysis

## Slide 11
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Timing Analysis
Add buffers to the short paths:

## Slide 12
The clock doesn’t arrive at all registers at same time
Skew: difference between two clock edges
Perform worst case analysis to guarantee dynamic discipline is not violated for any register – many registers in a system!
Clock Skew

## Slide 13
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)
Setup Time Constraint with Skew

## Slide 14
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq
Hold Time Constraint with Skew

## Slide 15
Asynchronous (for example, user) inputs might violate the dynamic discipline
Violating the Dynamic Discipline

## Slide 16
Bistable devices: two stable states, and a metastable state between them
Flip-flop: two stable states (1 and 0) and one metastable state
If flip-flop lands in metastable state, could stay there for an undetermined amount of time
Metastability

## Slide 17
Flip-flop has feedback: if Q is somewhere between 1 and 0, cross-coupled gates drive output to either rail (1 or 0)
Metastable signal: if it hasn’t resolved to 1 or 0
If flip-flop input changes at random time, probability that output Q is metastable after waiting some time, t:
P(tres > t) = (T0/Tc ) e-t/τ
tres : time to resolve to 1 or 0
T0, τ : properties of the circuit
Flip-Flop Internals

## Slide 18
Intuitively:
  T0/Tc: probability input changes at a bad time (during aperture)
P(tres > t) = (T0/Tc ) e-t/τ
  τ: time constant for how fast flip-flop moves away from metastability
P(tres > t) = (T0/Tc ) e-t/τ
If flip-flop samples metastable input, if you wait long enough (t), the output will have resolved to 1 or 0 with high probability.
Metastability

## Slide 19
Asynchronous inputs are inevitable (user interfaces, systems with different clocks interacting, etc.)
Synchronizer goal: make the probability of failure (the output Q still being metastable) low
Synchronizer cannot make the probability of failure 0
Synchronizers

## Slide 20
Synchronizer: built with two back-to-back flip-flops
Suppose D is transitioning when sampled by F1
Internal signal D2 has (Tc - tsetup) time to resolve to 1 or 0
Synchronizer Internals

## Slide 21
For each sample, probability of failure is:
P(failure) = (T0/Tc ) e-(Tc - tsetup)/τ
Synchronizer Probability of Failure

## Slide 22
If asynchronous input changes once per second, probability of failure per second is P(failure).
If input changes N times per second, probability of failure per second is:
P(failure)/second = (NT0/Tc) e-(Tc - tsetup)/τ
Synchronizer fails, on average, 1/[P(failure)/second]
Called mean time between failures, MTBF:
MTBF = 1/[P(failure)/second] = (Tc/NT0) e(Tc - tsetup)/τ
Synchronizer Mean Time Between Failures

## Slide 23
Suppose: Tc = 1/500 MHz = 2 ns τ = 200 ps
T0 = 150 ps tsetup = 100 ps
N = 10 events per second
What is the probability of failure? MTBF?
P(failure) = (150 ps/2 ns) e-(1.9 ns)/200 ps
= 5.6 × 10-6
P(failure)/second = 10 × (5.6 × 10-6 )
= 5.6 × 10-5 / second
MTBF = 1/[P(failure)/second] ≈ 5 hours
Example Synchronizer

## Slide 24
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line
Parallelism

## Slide 25
Token: Group of inputs processed to produce group of outputs
Latency: Time for one token to pass from start to end
Throughput: Number of tokens produced per unit time
Parallelism increases throughput
Parallelism Definitions

## Slide 26
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour
Parallelism Example

## Slide 27
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa P. Hacker to help, using her own oven
  Temporal parallelism:
    two stages: rolling and baking
    He uses two trays
    While first batch is baking, he rolls the second batch, etc.
Parallelism Example

## Slide 28
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 2 trays/ 1/3 hour = 6 trays/hour
Spatial Parallelism

## Slide 29
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour
Temporal Parallelism