## Slide 1: Lecture 7: Verilog Part II
E85 Digital Design & Computer Engineering

## Slide 2
Lecture 7
More Combinational Logic
Finite State Machines
Parameterized Modules
Testbenches

## Slide 3
Statements that must be inside always statements:
  if / else
  case, casez
Other Behavioral Statements

## Slide 4
// combinational logic using an always statement
module gates(input logic [3:0] a, b,
output logic [3:0] y1, y2, y3, y4, y5);
always_comb // need begin/end because there is
begin // more than one statement in always
y1 = a & b; // AND
y2 = a | b; // OR
y3 = a ^ b; // XOR
y4 = ~(a & b); // NAND
y5 = ~(a | b); // NOR
end
endmodule
This hardware could be described with assign statements using fewer lines of code, so it’s better to use assign statements in this case.
Combinational Logic using always

## Slide 5
module sevenseg(input logic [3:0] data,
output logic [6:0] segments);
always_comb
case (data)
// abc_defg
0: segments = 7'b111_1110;
1: segments = 7'b011_0000;
2: segments = 7'b110_1101;
3: segments = 7'b111_1001;
4: segments = 7'b011_0011;
5: segments = 7'b101_1011;
6: segments = 7'b101_1111;
7: segments = 7'b111_0000;
8: segments = 7'b111_1111;
9: segments = 7'b111_0011;
default: segments = 7'b000_0000; // required
endcase
endmodule
Combinational Logic using case

## Slide 6
case statement implies combinational logic only if all possible input combinations described
Remember to use default statement
Combinational Logic using case

## Slide 7
module priority_casez(input logic [3:0] a,
output logic [3:0] y);
always_comb
casez(a)
4'b1???: y = 4'b1000; // ?=don’t care
4'b01??: y = 4'b0100;
4'b001?: y = 4'b0010;
4'b0001: y = 4'b0001;
default: y = 4'b0000;
endcase
endmodule
Combinational Logic using casez
Synthesis:

## Slide 8
<= is nonblocking assignment
  Occurs simultaneously with others
= is blocking assignment
  Occurs in order it appears in file
// Good synchronizer using
// nonblocking assignments
module syncgood(input logic clk,
input logic d,
output logic q);
logic n1;
always_ff @(posedge clk)
begin
n1 <= d; // nonblocking
q <= n1; // nonblocking
end
endmodule
// Bad synchronizer using
// blocking assignments
module syncbad(input logic clk,
input logic d,
output logic q);
logic n1;
always_ff @(posedge clk)
begin
n1 = d; // blocking
q = n1; // blocking
end
endmodule
Blocking vs. Nonblocking Assignment

## Slide 9
Synchronous sequential logic: use always_ff @(posedge clk)and nonblocking assignments (<=)
always_ff @(posedge clk)
q <= d; // nonblocking
Simple combinational logic: use continuous assignments (assign…)
assign y = a & b;
More complicated combinational logic: use always_comb and blocking assignments (=)
Assign a signal in only one always statement or continuous assignment statement.
Rules for Signal Assignment

## Slide 10
Three blocks:
  next state logic
  state register
  output logic
Finite State Machines (FSMs)

## Slide 11
The double circle indicates the reset state
FSM Example: Divide by 3

## Slide 12
module divideby3FSM(input logic clk,
input logic reset,
output logic q);
typedef enum logic [1:0] {S0, S1, S2} statetype;
statetype state, nextstate;
// state register
always_ff @(posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always_comb
case (state)
S0: nextstate = S1;
S1: nextstate = S2;
S2: nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign q = (state == S0);
endmodule
FSM in SystemVerilog

## Slide 13
module fsmWithInputs(input logic clk,
input logic reset,
input logic a,
output logic q);
typedef enum logic [1:0] {S0, S1, S2} statetype;
statetype state, nextstate;
// state register
always_ff @(posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always_comb
case (state)
S0: if (a) nextstate = S1;
else nextstate = S0;
S1: nextstate = S2;
S2: if (a) nextstate = S2;
else nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign q = (state == S2);
endmodule
FSM with Inputs

## Slide 14
2:1 mux:
module mux2
#(parameter width = 8) // name and default value
(input logic [width-1:0] d0, d1,
input logic s,
output logic [width-1:0] y);
assign y = s ? d1 : d0;
endmodule
Instance with 8-bit bus width (uses default):
mux2 myMux(d0, d1, s, out);
Instance with 12-bit bus width:
mux2 #(12) lowmux(d0, d1, s, out);
Parameterized Modules

## Slide 15
HDL that tests another module: device under test (dut)
Not synthesizeable
Uses different features of SystemVerilog
Types:
  Simple
  Self-checking
  Self-checking with testvectors
Testbenches

## Slide 16
Write SystemVerilog code to implement the following function in hardware:
y = bc + ab
Name the module sillyfunction
Testbench Example

## Slide 17
Write SystemVerilog code to implement the following function in hardware:
y = bc + ab
module sillyfunction(input logic a, b, c,
output logic y);
assign y = ~b & ~c | a & ~b;
endmodule
Testbench Example

## Slide 18
module testbench1();
logic a, b, c;
logic y;
// instantiate device under test
sillyfunction dut(a, b, c, y);
// apply inputs one at a time
initial begin
a = 0; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
a = 1; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
end
endmodule
Simple Testbench

## Slide 19
module testbench2();
logic a, b, c;
logic y;
sillyfunction dut(a, b, c, y); // instantiate dut
initial begin // apply inputs, check results one at a time
a = 0; b = 0; c = 0; #10;
if (y !== 1) $display("000 failed.");
c = 1; #10;
if (y !== 0) $display("001 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("010 failed.");
c = 1; #10;
if (y !== 0) $display("011 failed.");
a = 1; b = 0; c = 0; #10;
if (y !== 1) $display("100 failed.");
c = 1; #10;
if (y !== 1) $display("101 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("110 failed.");
c = 1; #10;
if (y !== 0) $display("111 failed.");
end
endmodule
Self-checking Testbench

## Slide 20
Testvector file: inputs and expected outputs
Testbench:
  Generate clock for assigning inputs, reading outputs
  Read testvectors file into array
  Assign inputs, expected outputs
  Compare outputs with expected outputs and report errors
Testbench with Testvectors

## Slide 21
Testbench clock:
  assign inputs (on rising edge)
  compare outputs with expected outputs (on falling edge).
Testbench clock also used as clock for synchronous sequential circuits
Testbench with Testvectors

## Slide 22
File: example.tv
contains vectors of abc_yexpected
000_1
001_0
010_0
011_0
100_1
101_1
110_0
111_0
Testvectors File

## Slide 23
module testbench3();
logic clk, reset;
logic a, b, c, yexpected;
logic y;
logic [31:0] vectornum, errors; // bookkeeping variables
logic [3:0] testvectors[10000:0]; // array of testvectors
// instantiate device under test
sillyfunction dut(a, b, c, y);
// generate clock
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5;
end
1. Generate Clock

## Slide 24
// at start of test, load vectors and pulse reset
initial
begin
$readmemb("example.tv", testvectors);
vectornum = 0; errors = 0;
reset = 1; #27; reset = 0;
end
// Note: $readmemh reads testvector files written in
// hexadecimal
2. Read Testvectors into Array

## Slide 25
// apply test vectors on rising edge of clk
always @(posedge clk)
begin
#1; {a, b, c, yexpected} = testvectors[vectornum];
end
3. Assign Inputs & Expected Outputs

## Slide 26
// check results on falling edge of clk
always @(negedge clk)
if (~reset) begin // skip during reset
if (y !== yexpected) begin
$display("Error: inputs = %b", {a, b, c});
$display(" outputs = %b (%b expected)",y,yexpected);
errors = errors + 1;
end
// Note: to print in hexadecimal, use %h. For example,
// $display(“Error: inputs = %h”, {a, b, c});
4. Compare with Expected Outputs

## Slide 27
// increment array index and read next testvector
vectornum = vectornum + 1;
if (testvectors[vectornum] === 4'bx) begin
$display("%d tests completed with %d errors",
vectornum, errors);
$stop;
end
end
endmodule
// === and !== can compare values that are 1, 0, x, or z.
4. Compare with Expected Outputs