## Slide 1: Lecture 9: Shift, Mult, Div Fixed & Floating Point
E85 Digital Design & Computer Engineering

## Slide 2
Lecture 9
Shifters
Multipliers
Dividers
Fixed Point Numbers
Floating Point Numbers

## Slide 3
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb)
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 4
Shifter Design

## Slide 5
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 6
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers

## Slide 7
4 x 4 Multiplier

## Slide 8
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Dividers

## Slide 9
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Long-Hand:
Dividers

## Slide 10
A/B = Q + R/B
Decimal Example: 2584/15 = 172 R4
Long-Hand:
Dividers
Long-Hand Revisited:

## Slide 11
A/B = Q + R/B
Decimal: 2584/15 = 172 R4
Dividers
Binary: 1101/0010 = 0110 R1

## Slide 12
Divider Algorithm
A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi= 0; R’= R
else Qi= 1; R’= D
R=R’
Binary: 1101/10 = 0110 R1

## Slide 13
4 x 4 Divider
Division: A/B = Q + R/B
R’ = 0
for i = N-1 to 0
R = {R’ << 1, Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R=R’
Each row computes one iteration of the division algorithm.

## Slide 14
4 x 4 Divider
Each row computes one iteration of the division algorithm.

## Slide 15
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 16
Two common notations:
Fixed-point: binary point fixed
Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions

## Slide 17
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers

## Slide 18
Represent 7.510 using 4 integer bits and 4 fraction bits.
  01111000
Fixed-Point Number Example

## Slide 19
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers

## Slide 20
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Floating-Point Numbers

## Slide 21
Example: represent the value 22810 using a 32-bit floating point representation
We show three versions – final version is called the IEEE 754 floating-point standard
Floating-Point Numbers

## Slide 22
Convert decimal to binary
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Floating-Point Representation 1

## Slide 23
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Floating-Point Representation 2

## Slide 24
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Floating-Point Representation 3

## Slide 25
Write -58.2510 in floating point (IEEE 754)
Floating-Point Example

## Slide 26
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Floating-Point Example

## Slide 27
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
Floating-Point: Special Cases

## Slide 28
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
Floating-Point Precision

## Slide 29
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)
Floating-Point: Rounding

## Slide 30
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Floating-Point Addition

## Slide 31
Add the following floating-point numbers:
0x3FC00000
0x40500000
Floating-Point Addition Example

## Slide 32
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Floating-Point Addition Example

## Slide 33
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Floating-Point Addition Example

## Slide 34
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Floating Point Addition Example