## Slide 1: Chapter Six

## Slide 2: Pipelining
Improve perfomance by increasing instruction throughput
Ideal speedup is number of stages in the pipeline. Do we achieve this?

## Slide 3: Pipelining
What makes it easy
  all instructions are the same length
  just a few instruction formats
  memory operands appear only in loads and stores
What makes it hard?
  structural hazards: suppose we had only one memory
  control hazards: need to worry about branch instructions
  data hazards: an instruction depends on a previous instruction
We’ll build a simple pipeline and look at these issues
We’ll talk about modern processors and what really makes it hard:
  exception handling
  trying to improve performance with out-of-order execution, etc.

## Slide 4: Basic Idea
What do we need to add to actually split the datapath into stages?

## Slide 5: Pipelined Datapath
Can you find a problem even if there are no dependencies? What instructions can we execute to manifest the problem?

## Slide 6: Corrected Datapath

## Slide 7: Graphically Representing Pipelines
Can help with answering questions like:
  how many cycles does it take to execute this code?
  what is the ALU doing during cycle 4?
  use this representation to help understand datapaths

## Slide 8: Pipeline Control

## Slide 9: Pipeline control
We have 5 stages. What needs to be controlled in each stage?
  Instruction Fetch and PC Increment
  Instruction Decode / Register Fetch
  Execution
  Memory Stage
  Write Back
How would control be handled in an automobile plant?
  a fancy control center telling everyone what to do?
  should we use a finite state machine?

## Slide 10: Pipeline Control
Pass control signals along just like the data

## Slide 11: Datapath with Control

## Slide 12: Dependencies
Problem with starting next instruction before first is finished
  dependencies that “go backward in time” are data hazards

## Slide 13: Software Solution
Have compiler guarantee no hazards
Where do we insert the “nops” ? sub $2, $1, $3 and $12, $2, $5 or $13, $6, $2 add $14, $2, $2 sw $15, 100($2)
Problem: this really slows us down!

## Slide 14: Forwarding
Use temporary results, don’t wait for them to be written
  register file forwarding to handle read/write to same register
  ALU forwarding
what if this $2 was $13?

## Slide 15: Forwarding

## Slide 16: Can't always forward
Load word can still cause a hazard:
  an instruction tries to read a register following a load instruction that writes to the same register.
Thus, we need a hazard detection unit to “stall” the load instruction

## Slide 17: Stalling
We can stall the pipeline by keeping an instruction in the same stage

## Slide 18: Hazard Detection Unit
Stall by letting an instruction that won’t write anything go forward

## Slide 19: Branch Hazards
When we decide to branch, other instructions are in the pipeline!
We are predicting “branch not taken”
  need to add hardware for flushing instructions if we are wrong

## Slide 20: Flushing Instructions

## Slide 21: Improving Performance
Try and avoid stalls! E.g., reorder these instructions:
  lw $t0, 0($t1)
  lw $t2, 4($t1)
  sw $t2, 0($t1)
  sw $t0, 4($t1)
Add a “branch delay slot”
  the next instruction after a branch is always executed
  rely on compiler to “fill” the slot with something useful
Superscalar: start more than one instruction in the same cycle

## Slide 22: Dynamic Scheduling
The hardware performs the “scheduling”
  hardware tries to find instructions to execute
  out of order execution is possible
  speculative execution and dynamic branch prediction
All modern processors are very complicated
  DEC Alpha 21264: 9 stage pipeline, 6 instruction issue
  PowerPC and Pentium: branch history table
  Compiler technology important
This class has given you the background you need to learn more
Video: An Overview of Intel’s Pentium Processor (available from University Video Communications)