## Slide 1: Chapter Seven

## Slide 2: Memories: Review
SRAM:
  value is stored on a pair of inverting gates
  very fast but takes up more space than DRAM (4 to 6 transistors)
DRAM:
  value is stored as a charge on capacitor (must be refreshed)
  very small but slower than SRAM (factor of 5 to 10)

## Slide 3: Exploiting Memory Hierarchy
Users want large and fast memories! SRAM access times are 2 - 25ns at cost of $100 to $250 per Mbyte. DRAM access times are 60-120ns at cost of $5 to $10 per Mbyte. Disk access times are 10 to 20 million ns at cost of $.10 to $.20 per Mbyte.
Try and give it to them anyway
  build a memory hierarchy
1997

## Slide 4: Locality
A principle that makes having a memory hierarchy a good idea
If an item is referenced, temporal locality: it will tend to be referenced again soon
spatial locality: nearby items will tend to be referenced soon.
Why does code have locality?
Our initial focus: two levels (upper, lower)
  block: minimum unit of data
  hit: data requested is in the upper level
  miss: data requested is not in the upper level

## Slide 5: Cache
Two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?
Our first example:
  block size is one word of data
  "direct mapped"
For each item of data at the lower level,
there is exactly one location in the cache where it might be.
e.g., lots of items at the lower level share locations in the upper level

## Slide 6: Direct Mapped Cache
Mapping: address is modulo the number of blocks in the cache

## Slide 7: Direct Mapped Cache
For MIPS:
What kind of locality are we taking advantage of?

## Slide 8: Direct Mapped Cache
Taking advantage of spatial locality:

## Slide 9: Hits vs. Misses
Read hits
  this is what we want!
Read misses
  stall the CPU, fetch block from memory, deliver to cache, restart
Write hits:
  can replace data in cache and memory (write-through)
  write the data only into the cache (write-back the cache later)
Write misses:
  read the entire block into the cache, then write the word

## Slide 10: Hardware Issues
Make reading multiple words easier by using banks of memory
It can get a lot more complicated...

## Slide 11: Performance
Increasing the block size tends to decrease miss rate:
Use split caches because there is more spatial locality in code:

## Slide 12: Performance
Simplified model: execution time = (execution cycles + stall cycles)  cycle time stall cycles = # of instructions  miss ratio  miss penalty
Two ways of improving performance:
  decreasing the miss ratio
  decreasing the miss penalty
What happens if we increase block size?

## Slide 13: Decreasing miss ratio with associativity
Compared to direct mapped, give a series of references that:
  results in a lower miss ratio using a 2-way set associative cache
  results in a higher miss ratio using a 2-way set associative cache
assuming we use the “least recently used” replacement strategy

## Slide 14: An implementation

## Slide 15: Performance

## Slide 16: Decreasing miss penalty with multilevel caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  CPI of 1.0 on a 500Mhz machine with a 5% miss rate, 200ns DRAM access
  Adding 2nd level cache with 20ns access time decreases miss rate to 2%
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache

## Slide 17: Virtual Memory
Main memory can act as a cache for the secondary storage (disk)
Advantages:
  illusion of having more physical memory
  program relocation
  protection

## Slide 18: Pages: virtual memory blocks
Page faults: the data is not in memory, retrieve it from disk
  huge miss penalty, thus pages should be fairly large (e.g., 4KB)
  reducing page faults is important (LRU is worth the price)
  can handle the faults in software instead of hardware
  using write-through is too expensive so we use writeback

## Slide 19: Page Tables

## Slide 20: Page Tables

## Slide 21: Making Address Translation Fast
A cache for address translations: translation lookaside buffer

## Slide 22: TLBs and caches

## Slide 23: Modern Systems
Very complicated memory systems:

## Slide 24: Some Issues
Processor speeds continue to increase very fast — much faster than either DRAM or disk access times
Design challenge: dealing with this growing disparity
Trends:
  synchronous SRAMs (provide a burst of data)
  redesign DRAM chips to provide higher bandwidth or processing
  restructure code to increase locality
  use prefetching (make cache visible to ISA)