## Slide 1
Chapter 4
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 4 :: Topics
Introduction
Combinational Logic
Structural Modeling
Sequential Logic
More Combinational Logic
Finite State Machines
Parameterized Modules
Testbenches

## Slide 3
Hardware description language (HDL):
  specifies logic function only
  Computer-aided design (CAD) tool produces or synthesizes the optimized gates
Most commercial designs built using HDLs
Two leading HDLs:
  SystemVerilog
    developed in 1984 by Gateway Design Automation
    IEEE standard (1364) in 1995
    Extended in 2005 (IEEE STD 1800-2009)
  VHDL 2008
    Developed in 1981 by the Department of Defense
    IEEE standard (1076) in 1987
    Updated in 2008 (IEEE STD 1076-2008)
Introduction

## Slide 4
Simulation
  Inputs applied to circuit
  Outputs checked for correctness
  Millions of dollars saved by debugging in simulation instead of hardware
Synthesis
  Transforms HDL code into a netlist describing the hardware (i.e., a list of gates and the wires connecting them)
HDL to Gates

## Slide 5
Simulation
  Inputs applied to circuit
  Outputs checked for correctness
  Millions of dollars saved by debugging in simulation instead of hardware
Synthesis
  Transforms HDL code into a netlist describing the hardware (i.e., a list of gates and the wires connecting them)
IMPORTANT: When using an HDL, think of the hardware the HDL should implies
HDL to Gates

## Slide 6
Two types of Modules:
  Behavioral: describe what a module does
  Structural: describe how it is built from simpler modules
SystemVerilog Modules
SystemVerilog
Module

## Slide 7
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
SystemVerilog:
Behavioral SystemVerilog

## Slide 8
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
SystemVerilog:
Behavioral SystemVerilog
module/endmodule: required to begin/end module
example: name of the module
Operators:
  ~: NOT
  &: AND
  |: OR

## Slide 9
HDL Simulation
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
SystemVerilog:

## Slide 10
HDL Synthesis
module example(input logic a, b, c,
output logic y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
SystemVerilog:
Synthesis:

## Slide 11
Case sensitive
  Example: reset and Reset are not the same signal.
No names that start with numbers
  Example: 2mux is an invalid name
Whitespace ignored
Comments:
  // single line comment
  /* multiline
  comment */
SystemVerilog Syntax

## Slide 12
module and3(input logic a, b, c,
output logic y);
assign y = a & b & c;
endmodule
module inv(input logic a,
output logic y);
assign y = ~a;
endmodule
module nand3(input logic a, b, c
output logic y);
logic n1; // internal signal
and3 andgate(a, b, c, n1); // instance of and3
inv inverter(n1, y); // instance of inv
endmodule
Structural Modeling - Hierarchy

## Slide 13
module gates(input logic [3:0] a, b,
output logic [3:0] y1, y2, y3, y4, y5);
/* Five different two-input logic
gates acting on 4 bit busses */
assign y1 = a & b; // AND
assign y2 = a | b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a | b); // NOR
endmodule
// single line comment
/*…*/ multiline comment
Bitwise Operators
Synthesis:

## Slide 14
module and8(input logic [7:0] a,
output logic y);
assign y = &a;
// &a is much easier to write than
// assign y = a[7] & a[6] & a[5] & a[4] &
// a[3] & a[2] & a[1] & a[0];
endmodule
Reduction Operators
Synthesis:
SystemVerilog:

## Slide 15
module mux2(input logic [3:0] d0, d1,
input logic s,
output logic [3:0] y);
assign y = s ? d1 : d0;
endmodule
? : is also called a ternary operator because it
operates on 3 inputs: s, d1, and d0.
Conditional Assignment
Synthesis:
SystemVerilog:

## Slide 16
module fulladder(input logic a, b, cin,
output logic s, cout);
logic p, g; // internal nodes
assign p = a ^ b;
assign g = a & b;
assign s = p ^ cin;
assign cout = g | (p & cin);
endmodule
Internal Variables
SystemVerilog:
Synthesis:

## Slide 17
~ | NOT
*, /, % | mult, div, mod
+, - | add,sub
<<, >> | shift
<<<, >>> | arithmetic shift
<, <=, >, >= | comparison
==, != | equal, not equal
&, ~& | AND, NAND
^, ~^ | XOR, XNOR
¦, ~¦ | OR, NOR
?: | ternary operator
Highest
Lowest
Precedence

## Slide 18
Number | # Bits | Base | Decimal Equivalent | Stored
3'b101 | 3 | binary | 5 | 101
'b11 | unsized | binary | 3 | 00…0011
8'b11 | 8 | binary | 3 | 00000011
8'b1010_1011 | 8 | binary | 171 | 10101011
3'd6 | 3 | decimal | 6 | 110
6'o42 | 6 | octal | 34 | 100010
8'hAB | 8 | hexadecimal | 171 | 10101011
42 | Unsized | decimal | 42 | 00…0101010
Format: N'Bvalue
N = number of bits, B = base
N'B is optional but recommended (default is decimal)
Numbers

## Slide 19
assign y = {a[2:1], {3{b[0]}}, a[0], 6'b100_010};
// if y is a 12-bit signal, the above statement produces:
y = a[2] a[1] b[0] b[0] b[0] a[0] 1 0 0 0 1 0
// underscores (_) are used for formatting only to make
// it easier to read. SystemVerilog ignores them.
Bit Manipulations: Example 1

## Slide 20
module mux2_8(input logic [7:0] d0, d1,
input logic s,
output logic [7:0] y);
mux2 lsbmux(d0[3:0], d1[3:0], s, y[3:0]);
mux2 msbmux(d0[7:4], d1[7:4], s, y[7:4]);
endmodule
Bit Manipulations: Example 2
SystemVerilog:
Synthesis:

## Slide 21
module tristate(input logic [3:0] a,
input logic en,
output tri [3:0] y);
assign y = en ? a : 4'bz;
endmodule
Z: Floating Output
SystemVerilog:
Synthesis:

## Slide 22
module example(input logic a, b, c,
output logic y);
logic ab, bb, cb, n1, n2, n3;
assign #1 {ab, bb, cb} = ~{a, b, c};
assign #2 n1 = ab & bb & cb;
assign #2 n2 = a & bb & cb;
assign #2 n3 = a & bb & c;
assign #4 y = n1 | n2 | n3;
endmodule
Delays

## Slide 23
module example(input logic a, b, c,
output logic y);
logic ab, bb, cb, n1, n2, n3;
assign #1 {ab, bb, cb} =
~{a, b, c};
assign #2 n1 = ab & bb & cb;
assign #2 n2 = a & bb & cb;
assign #2 n3 = a & bb & c;
assign #4 y = n1 | n2 | n3;
endmodule
Delays

## Slide 24
module example(input logic a, b, c,
output logic y);
logic ab, bb, cb, n1, n2, n3;
assign #1 {ab, bb, cb} =
~{a, b, c};
assign #2 n1 = ab & bb & cb;
assign #2 n2 = a & bb & cb;
assign #2 n3 = a & bb & c;
assign #4 y = n1 | n2 | n3;
endmodule
Delays
1

## Slide 25
module example(input logic a, b, c,
output logic y);
logic ab, bb, cb, n1, n2, n3;
assign #1 {ab, bb, cb} =
~{a, b, c};
assign #2 n1 = ab & bb & cb;
assign #2 n2 = a & bb & cb;
assign #2 n3 = a & bb & c;
assign #4 y = n1 | n2 | n3;
endmodule
Delays
2

## Slide 26
module example(input logic a, b, c,
output logic y);
logic ab, bb, cb, n1, n2, n3;
assign #1 {ab, bb, cb} =
~{a, b, c};
assign #2 n1 = ab & bb & cb;
assign #2 n2 = a & bb & cb;
assign #2 n3 = a & bb & c;
assign #4 y = n1 | n2 | n3;
endmodule
Delays
2

## Slide 27
module example(input logic a, b, c,
output logic y);
logic ab, bb, cb, n1, n2, n3;
assign #1 {ab, bb, cb} =
~{a, b, c};
assign #2 n1 = ab & bb & cb;
assign #2 n2 = a & bb & cb;
assign #2 n3 = a & bb & c;
assign #4 y = n1 | n2 | n3;
endmodule
Delays
4

## Slide 28
SystemVerilog uses idioms to describe latches, flip-flops and FSMs
Other coding styles may simulate correctly but produce incorrect hardware
Sequential Logic

## Slide 29
General Structure:
always @(sensitivity list)
statement;
Whenever the event in sensitivity list occurs, statement is executed
always Statement

## Slide 30
module flop(input logic clk,
input logic [3:0] d,
output logic [3:0] q);
always_ff @(posedge clk)
q <= d; // pronounced “q gets d”
endmodule
D Flip-Flop
Synthesis:

## Slide 31
module flopr(input logic clk,
input logic reset,
input logic [3:0] d,
output logic [3:0] q);
// synchronous reset
always_ff @(posedge clk)
if (reset) q <= 4'b0;
else q <= d;
endmodule
Resettable D Flip-Flop
Synthesis:

## Slide 32
module flopr(input logic clk,
input logic reset,
input logic [3:0] d,
output logic [3:0] q);
// asynchronous reset
always_ff @(posedge clk, posedge reset)
if (reset) q <= 4'b0;
else q <= d;
endmodule
Resettable D Flip-Flop
Synthesis:

## Slide 33
module flopren(input logic clk,
input logic reset,
input logic en,
input logic [3:0] d,
output logic [3:0] q);
// enable and asynchronous reset
always_ff @(posedge clk, posedge reset)
if (reset) q <= 4'b0;
else if (en) q <= d;
endmodule
D Flip-Flop with Enable
Synthesis:

## Slide 34
module latch(input logic clk,
input logic [3:0] d,
output logic [3:0] q);
always_latch
if (clk) q <= d;
endmodule
Warning: We don’t use latches in this text. But you might write code that inadvertently implies a latch. Check synthesized hardware – if it has latches
in it, there’s an error.
Latch
Synthesis:

## Slide 35
Review
General Structure:
always @(sensitivity list)
statement;
Flip-flop: always_ff
Latch: always_latch (don’t use)

## Slide 36
Statements that must be inside always statements:
  if / else
  case, casez
Other Behavioral Statements

## Slide 37
// combinational logic using an always statement
module gates(input logic [3:0] a, b,
output logic [3:0] y1, y2, y3, y4, y5);
always_comb // need begin/end because there is
begin // more than one statement in always
y1 = a & b; // AND
y2 = a | b; // OR
y3 = a ^ b; // XOR
y4 = ~(a & b); // NAND
y5 = ~(a | b); // NOR
end
endmodule
This hardware could be described with assign statements using fewer lines of code, so it’s better to use assign statements in this case.
Combinational Logic using always

## Slide 38
module sevenseg(input logic [3:0] data,
output logic [6:0] segments);
always_comb
case (data)
// abc_defg
0: segments = 7'b111_1110;
1: segments = 7'b011_0000;
2: segments = 7'b110_1101;
3: segments = 7'b111_1001;
4: segments = 7'b011_0011;
5: segments = 7'b101_1011;
6: segments = 7'b101_1111;
7: segments = 7'b111_0000;
8: segments = 7'b111_1111;
9: segments = 7'b111_0011;
default: segments = 7'b000_0000; // required
endcase
endmodule
Combinational Logic using case

## Slide 39
case statement implies combinational logic only if all possible input combinations described
Remember to use default statement
Combinational Logic using case

## Slide 40
module priority_casez(input logic [3:0] a,
output logic [3:0] y);
always_comb
casez(a)
4'b1???: y = 4'b1000; // ?=don’t care
4'b01??: y = 4'b0100;
4'b001?: y = 4'b0010;
4'b0001: y = 4'b0001;
default: y = 4'b0000;
endcase
endmodule
Combinational Logic using casez
Synthesis:

## Slide 41
<= is nonblocking assignment
  Occurs simultaneously with others
= is blocking assignment
  Occurs in order it appears in file
// Good synchronizer using
// nonblocking assignments
module syncgood(input logic clk,
input logic d,
output logic q);
logic n1;
always_ff @(posedge clk)
begin
n1 <= d; // nonblocking
q <= n1; // nonblocking
end
endmodule
// Bad synchronizer using
// blocking assignments
module syncbad(input logic clk,
input logic d,
output logic q);
logic n1;
always_ff @(posedge clk)
begin
n1 = d; // blocking
q = n1; // blocking
end
endmodule
Blocking vs. Nonblocking Assignment

## Slide 42
Synchronous sequential logic: use always_ff @(posedge clk)and nonblocking assignments (<=)
always_ff @(posedge clk)
q <= d; // nonblocking
Simple combinational logic: use continuous assignments (assign…)
assign y = a & b;
More complicated combinational logic: use always_comb and blocking assignments (=)
Assign a signal in only one always statement or continuous assignment statement.
Rules for Signal Assignment

## Slide 43
Three blocks:
  next state logic
  state register
  output logic
Finite State Machines (FSMs)

## Slide 44
The double circle indicates the reset state
FSM Example: Divide by 3

## Slide 45
module divideby3FSM(input logic clk,
input logic reset,
output logic q);
typedef enum logic [1:0] {S0, S1, S2} statetype;
statetype state, nextstate;
// state register
always_ff @(posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always_comb
case (state)
S0: nextstate = S1;
S1: nextstate = S2;
S2: nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign q = (state == S0);
endmodule
FSM in SystemVerilog

## Slide 46
module fsmWithInputs(input logic clk,
input logic reset,
input logic a,
output logic q);
typedef enum logic [1:0] {S0, S1, S2} statetype;
statetype state, nextstate;
// state register
always_ff @(posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
// next state logic
always_comb
case (state)
S0: if (a) nextstate = S1;
else nextstate = S0;
S1: nextstate = S2;
S2: if (a) nextstate = S2;
else nextstate = S0;
default: nextstate = S0;
endcase
// output logic
assign q = (state == S2);
endmodule
FSM with Inputs

## Slide 47
2:1 mux:
module mux2
#(parameter width = 8) // name and default value
(input logic [width-1:0] d0, d1,
input logic s,
output logic [width-1:0] y);
assign y = s ? d1 : d0;
endmodule
Instance with 8-bit bus width (uses default):
mux2 myMux(d0, d1, s, out);
Instance with 12-bit bus width:
mux2 #(12) lowmux(d0, d1, s, out);
Parameterized Modules

## Slide 48
HDL that tests another module: device under test (dut)
Not synthesizeable
Uses different features of SystemVerilog
Types:
  Simple
  Self-checking
  Self-checking with testvectors
Testbenches

## Slide 49
Write SystemVerilog code to implement the following function in hardware:
y = bc + ab
Name the module sillyfunction
Testbench Example

## Slide 50
Write SystemVerilog code to implement the following function in hardware:
y = bc + ab
module sillyfunction(input logic a, b, c,
output logic y);
assign y = ~b & ~c | a & ~b;
endmodule
Testbench Example

## Slide 51
module testbench1();
logic a, b, c;
logic y;
// instantiate device under test
sillyfunction dut(a, b, c, y);
// apply inputs one at a time
initial begin
a = 0; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
a = 1; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
end
endmodule
Simple Testbench

## Slide 52
module testbench2();
logic a, b, c;
logic y;
sillyfunction dut(a, b, c, y); // instantiate dut
initial begin // apply inputs, check results one at a time
a = 0; b = 0; c = 0; #10;
if (y !== 1) $display("000 failed.");
c = 1; #10;
if (y !== 0) $display("001 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("010 failed.");
c = 1; #10;
if (y !== 0) $display("011 failed.");
a = 1; b = 0; c = 0; #10;
if (y !== 1) $display("100 failed.");
c = 1; #10;
if (y !== 1) $display("101 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("110 failed.");
c = 1; #10;
if (y !== 0) $display("111 failed.");
end
endmodule
Self-checking Testbench

## Slide 53
Testvector file: inputs and expected outputs
Testbench:
  Generate clock for assigning inputs, reading outputs
  Read testvectors file into array
  Assign inputs, expected outputs
  Compare outputs with expected outputs and report errors
Testbench with Testvectors

## Slide 54
Testbench clock:
  assign inputs (on rising edge)
  compare outputs with expected outputs (on falling edge).
Testbench clock also used as clock for synchronous sequential circuits
Testbench with Testvectors

## Slide 55
File: example.tv
contains vectors of abc_yexpected
000_1
001_0
010_0
011_0
100_1
101_1
110_0
111_0
Testvectors File

## Slide 56
module testbench3();
logic clk, reset;
logic a, b, c, yexpected;
logic y;
logic [31:0] vectornum, errors; // bookkeeping variables
logic [3:0] testvectors[10000:0]; // array of testvectors
// instantiate device under test
sillyfunction dut(a, b, c, y);
// generate clock
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5;
end
1. Generate Clock

## Slide 57
// at start of test, load vectors and pulse reset
initial
begin
$readmemb("example.tv", testvectors);
vectornum = 0; errors = 0;
reset = 1; #27; reset = 0;
end
// Note: $readmemh reads testvector files written in
// hexadecimal
2. Read Testvectors into Array

## Slide 58
// apply test vectors on rising edge of clk
always @(posedge clk)
begin
#1; {a, b, c, yexpected} = testvectors[vectornum];
end
3. Assign Inputs & Expected Outputs

## Slide 59
// check results on falling edge of clk
always @(negedge clk)
if (~reset) begin // skip during reset
if (y !== yexpected) begin
$display("Error: inputs = %b", {a, b, c});
$display(" outputs = %b (%b expected)",y,yexpected);
errors = errors + 1;
end
// Note: to print in hexadecimal, use %h. For example,
// $display(“Error: inputs = %h”, {a, b, c});
4. Compare with Expected Outputs

## Slide 60
// increment array index and read next testvector
vectornum = vectornum + 1;
if (testvectors[vectornum] === 4'bx) begin
$display("%d tests completed with %d errors",
vectornum, errors);
$stop;
end
end
endmodule
// === and !== can compare values that are 1, 0, x, or z.
4. Compare with Expected Outputs