## Slide 1
Digital Design and Computer Architecture: ARM® Edition
Chapter 6
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 6 :: Topics
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes

## Slide 3
Jumping up a few levels of abstraction
  Architecture: programmer’s view of computer
    Defined by instructions & operand locations
  Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)
Introduction

## Slide 4
Commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
Instructions

## Slide 5
Developed in the 1980’s by Advanced RISC Machines – now called ARM Holdings
Nearly 10 billion ARM processors sold/year
Almost all cell phones and tablets have multiple ARM processors
Over 75% of humans use products with an ARM processor
Used in servers, cameras, robots, cars, pinball machines, etc.
ARM Architecture

## Slide 6
Developed in the 1980’s by Advanced RISC Machines – now called ARM Holdings
Nearly 10 billion ARM processors sold/year
Almost all cell phones and tablets have multiple ARM processors
Over 75% of humans use products with an ARM processor
Used in servers, cameras, robots, cars, pinball machines,, etc.
ARM Architecture
Once you’ve learned one architecture, it’s easier to learn others

## Slide 7
Underlying design principles, as articulated by Hennessy and Patterson:
    Regularity supports design simplicity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises
Architecture Design Principles

## Slide 8
ADD: mnemonic – indicates operation to perform
b, c: source operands
a: destination operand
C Code
a = b + c;
ARM Assembly Code
ADD a, b, c
Instruction: Addition

## Slide 9
Similar to addition - only mnemonic changes
SUB: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
ARM assembly code
SUB a, b, c
Instruction: Subtraction

## Slide 10
Regularity supports design simplicity
Consistent instruction format
Same number of operands (two sources and one destination)
Ease of encoding and handling in hardware
Design Principle 1

## Slide 11
More complex code handled by multiple ARM instructions
C Code
a = b + c - d;
ARM assembly code
ADD t, b, c ; t = b + c
SUB a, t, d ; a = t - d
Multiple Instructions

## Slide 12
Make the common case fast
ARM includes only simple, commonly used instructions
Hardware to decode and execute instructions kept simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
Design Principle 2

## Slide 13
Make the common case fast
ARM is a Reduced Instruction Set Computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are Complex Instruction Set Computers (CISC)
Design Principle 2

## Slide 14
Physical location in computer
  Registers
  Constants (also called immediates)
  Memory
Operand Location

## Slide 15
ARM has 16 registers
Registers are faster than memory
Each register is 32 bits
ARM is called a “32-bit architecture” because it operates on 32-bit data
Operands: Registers

## Slide 16
Smaller is Faster
ARM includes only a small number of registers
Design Principle 3

## Slide 17
Name | Use
R0 | Argument / return value / temporary variable
R1-R3 | Argument / temporary variables
R4-R11 | Saved variables
R12 | Temporary variable
R13 (SP) | Stack Pointer
R14 (LR) | Link Register
R15 (PC) | Program Counter
ARM Register Set

## Slide 18
Registers:
  R before number, all capitals
  Example: “R0” or “register zero” or “register R0”
Operands: Registers

## Slide 19
Registers used for specific purposes:
  Saved registers: R4-R11 hold variables
  Temporary registers: R0-R3 and R12, hold intermediate values
  Discuss others later
Operands: Registers

## Slide 20
Revisit ADD instruction
C Code
a = b + c;
ARM Assembly Code
; R0 = a, R1 = b, R2 = c
ADD R0, R1, R2
Instructions with Registers

## Slide 21
Many instructions can use constants or immediate operands
For example: ADD and SUB
value is immediately available from instruction
C Code
a = a + 4;
b = a – 12;
ARM Assembly Code
; R0 = a, R1 = b
ADD R0, R0, #4
SUB R1, R0, #12
Operands: Constants\Immediates

## Slide 22
Generating small constants using move (MOV):
C Code
//int: 32-bit signed word
int a = 23;
int b = 0x45;
ARM Assembly Code
; R0 = a, R1 = b
MOV R0, #23
MOV R1, #0x45
Generating Constants

## Slide 23
Generating small constants using move (MOV):
Constant must have < 8 bits of precision
Note: MOV can also use 2 registers: MOV R7, R9
C Code
//int: 32-bit signed word
int a = 23;
int b = 0x45;
ARM Assembly Code
; R0 = a, R1 = b
MOV R0, #23
MOV R1, #0x45
Generating Constants

## Slide 24
Generate larger constants using move (MOV) and or (ORR):
C Code
int a = 0x7EDC8765;
ARM Assembly Code
# R0 = a
MOV R0, #0x7E000000
ORR R0, R0, #0xDC0000
ORR R0, R0, #0x8700
ORR R0, R0, #0x65
Generating Constants

## Slide 25
Too much data to fit in only 16 registers
Store more data in memory
Memory is large, but slow
Commonly used variables still kept in registers
Operands: Memory

## Slide 26
Each data byte has unique address
32-bit word = 4 bytes, so word address increments by 4
Byte-Addressable Memory

## Slide 27
Memory read called load
Mnemonic: load register (LDR)
Format:
LDR R0, [R1, #12]
  Address calculation:
    add base address (R1) to the offset (12)
    address = (R1 + 12)
  Result:
    R0 holds the data at memory address (R1 + 12)
Any register may be used as base address
Reading Memory

## Slide 28
Example: Read a word of data at memory address 8 into R3
  Address = (R2 + 8) = 8
  R3 = 0x01EE2842 after load
ARM Assembly Code
MOV R2, #0
LDR R3, [R2, #8]
Reading Memory

## Slide 29
Memory write are called stores
Mnemonic: store register (STR)
Writing Memory

## Slide 30
Example: Store the value held in R7 into memory word 21.
Memory address = 4 x 21 = 84 = 0x54
ARM assembly code
MOV R5, #0
STR R7, [R5, #0x54]
Writing Memory
The offset can be written in decimal or hexadecimal

## Slide 31
Address of a memory word must be multiplied by 4
Examples:
  Address of memory word 2 = 2 × 4 = 8
  Address of memory word 10 = 10 × 4 = 40
Recap: Accessing Memory

## Slide 32
How to number bytes within a word?
  Little-endian: byte numbers start at the little (least significant) end
  Big-endian: byte numbers start at the big (most significant) end
Big-Endian & Little-Endian Memory

## Slide 33
Jonathan Swift’s Gulliver’s Travels: the Little-Endians broke their eggs on the little end of the egg and the Big-Endians broke their eggs on the big end
It doesn’t really matter which addressing type used – except when two systems share data
Big-Endian & Little-Endian Memory

## Slide 34
Suppose R2 and R5 hold the values 8 and 0x23456789
After following code runs on big-endian system, what value is in R7?
In a little-endian system?
      STR R5, [R2, #0]
      LDRB R7, [R2, #1]
Big-Endian & Little-Endian Example

## Slide 35
Suppose R2 and R5 hold the values 8 and 0x23456789
After following code runs on big-endian system, what value is in R7?
In a little-endian system?
      STR R5, [R2, #0]
      LDRB R7, [R2, #1]
Big-Endian & Little-Endian Example
      Big-endian: 0x00000045
      Little-endian: 0x00000067

## Slide 36
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Programming

## Slide 37
British mathematician
Wrote the first computer program
Her program calculated the Bernoulli numbers on Charles Babbage’s Analytical Engine
She was a child of the poet Lord Byron
Ada Lovelace, 1815-1852

## Slide 38
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 39
Logical operations
Shifts / rotate
Multiplication
Data-processing Instructions

## Slide 40
AND
ORR
EOR (XOR)
BIC (Bit Clear = A & ~B)
MVN (MoVe and NOT)
Logical Instructions

## Slide 41
Logical Instructions: Examples

## Slide 42
AND or BIC: useful for masking bits
  Example: Masking all but the least significant byte of a value
  0xF234012F AND 0x000000FF = 0x0000002F
  0xF234012F BIC 0xFFFFFF00 = 0x0000002F
ORR: useful for combining bit fields
  Example: Combine 0xF2340000 with 0x000012BC:
  0xF2340000 ORR 0x000012BC = 0xF23412BC
Logical Instructions: Uses

## Slide 43
LSL: logical shift left
  Example: LSL R0, R7, #5 ; R0 = R7 << 5
LSR: logical shift right
  Example: LSR R3, R2, #31 ; R3 = R2 >> 31
ASR: arithmetic shift right
  Example: ASR R9, R11, R4 ; R9 = R11 >>> R47:0
ROR: rotate right
  Example: ROR R8, R1, #3 ; R8 = R1 ROR 3
Shift Instructions

## Slide 44
Shift Instructions: Example 1
Immediate shift amount (5-bit immediate)
Shift amount: 0-31

## Slide 45
Shift Instructions: Example 2
Register shift amount (uses low 8 bits of register)
Shift amount: 0-255

## Slide 46
MUL: 32 × 32 multiplication, 32-bit result
  MUL R1, R2, R3
  Result: R1 = (R2 x R3)31:0 (signed doesn’t matter)
UMULL: Unsigned multiply long: 32 × 32 multiplication, 64-bit result
  UMULL R1, R2, R3, R4
  Result: {R1,R4} = R2 x R3 (R2, R3 unsigned)
SMULL: Signed multiply long: 32 × 32 multiplication, 64-bit result
  SMULL R1, R2, R3, R4
  Result: {R1,R4} = R2 x R3 (R2, R3 signed)
Multiplication

## Slide 47
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 48
Don’t always want to execute code sequentially
For example:
  if/else statements, while loops, etc.: only want to execute code if a condition is true
  branching: jump to another portion of code if a condition is true
Conditional Execution

## Slide 49
Don’t always want to execute code sequentially
For example:
  if/else statements, while loops, etc.: only want to execute code if a condition is true
  branching: jump to another portion of code if a condition is true
ARM includes condition flags that can be:
  set by an instruction
  used to conditionally execute an instruction
Conditional Execution

## Slide 50
Set by ALU (recall from Chapter 5)
Held in Current Program Status Register (CPSR)
ARM Condition Flags
Flag | Name | Description
N | Negative | Instruction result is negative
Z | Zero | Instruction results in zero
C | Carry | Instruction causes an unsigned carry out
V | oVerflow | Instruction causes an overflow

## Slide 51
Review: ARM ALU

## Slide 52
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Does not save result
    Sets flags. If result:
      Is 0, Z=1
      Is negative, N=1
      Causes a carry out, C=1
      Causes a signed overflow, V=1
Setting the Condition Flags: NZCV

## Slide 53
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Does not save result
Method 2: Append instruction mnemonic with S
  Example: ADDS R1, R2, R3
    Performs: R2 + R3
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Saves result in R1
Setting the Condition Flags: NZCV

## Slide 54
Instruction may be conditionally executed based on the condition flags
Condition of execution is encoded as a condition mnemonic appended to the instruction mnemonic
  Example: CMP R1, R2
  SUBNE R3, R5, R8
        NE: not equal condition mnemonic
        SUB will only execute if R1 ≠ R2
        (i.e., Z = 0)
Condition Mnemonics

## Slide 55
Condition Mnemonics

## Slide 56
Example:
  CMP R5, R9 ; performs R5-R9
  ; sets condition flags
  SUBEQ R1, R2, R3 ; executes if R5==R9 (Z=1)
  ORRMI R4, R0, R9 ; executes if R5-R9 is
  ; negative (N=1)
  Suppose R5 = 17, R9 = 23:
    CMP performs: 17 – 23 = -6 (Sets flags: N=1, Z=0, C=0, V=0)
    SUBEQ doesn’t execute (they aren’t equal: Z=0)
    ORRMI executes because the result was negative (N=1)
Conditional Execution

## Slide 57
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 58
Branches enable out of sequence instruction execution
Types of branches:
  Branch (B)
    branches to another instruction
  Branch and link (BL)
    discussed later
Both can be conditional or unconditional
Branching

## Slide 59
The Stored Program

## Slide 60
ARM assembly
MOV R2, #17 ; R2 = 17
B TARGET ; branch to target
ORR R1, R1, #0x4 ; not executed
TARGET
SUB R1, R1, #78 ; R1 = R1 + 78
Labels (like TARGET) indicate instruction location. Labels can’t be reserved words (like ADD, ORR, etc.)
Unconditional Branching (B)

## Slide 61
ARM Assembly
MOV R0, #4 ; R0 = 4
ADD R1, R0, R0 ; R1 = R0+R0 = 8
CMP R0, R1 ; sets flags with R0-R1
BEQ THERE ; branch not taken (Z=0)
ORR R1, R1, #1 ; R1 = R1 OR R1 = 9
THERE
ADD R1, R1, 78 ; R1 = R1 + 78 = 87
The Branch Not Taken

## Slide 62
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 63
C Code
if (i == j)
f = g + h;
f = f – i;
if Statement

## Slide 64
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
L1
SUB R0, R0, R2 ; f = f - i
if Statement

## Slide 65
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
L1
SUB R0, R0, R2 ; f = f - i
if Statement
Assembly tests opposite case (i != j) of high-level code (i == j)

## Slide 66
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code

## Slide 67
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
L1
SUB R0, R0, R2

## Slide 68
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
L1
SUB R0, R0, R2
Useful for short conditional blocks of code

## Slide 69
C Code
if (i == j)
f = g + h;
else
f = f – i;
if/else Statement
ARM Assembly Code

## Slide 70
C Code
if (i == j)
f = g + h;
else
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
B L2 ; branch past else block
L1
SUB R0, R0, R2 ; f = f – i
L2
if/else Statement

## Slide 71
C Code
if (i == j)
f = g + h;
else
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUBNE R0, R0, R2 ; else f = f - i
if/else Statement: Alternate Code

## Slide 72
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUBNE R0, R0, R2 ; else f = f - i
if/else Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
B L2
L1
SUB R0, R0, R2
L2

## Slide 73
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
while Loops

## Slide 74
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
; R0 = pow, R1 = x
MOV R0, #1 ; pow = 1
MOV R1, #0 ; x = 0
WHILE
CMP R0, #128 ; R0-128
BEQ DONE ; if (pow==128) ; exit loop
LSL R0, R0, #1 ; pow=pow*2
ADD R1, R1, #1 ; x=x+1
B WHILE ; repeat loop
DONE
while Loops

## Slide 75
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
; R0 = pow, R1 = x
MOV R0, #1 ; pow = 1
MOV R1, #0 ; x = 0
WHILE
CMP R0, #128 ; R0-128
BEQ DONE ; if (pow==128) ; exit loop
LSL R0, R0, #1 ; pow=pow*2
ADD R1, R1, #1 ; x=x+1
B WHILE ; repeat loop
DONE
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).
while Loops

## Slide 76
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met
for Loops

## Slide 77
C Code
// adds numbers from 1-9
int sum = 0;
int i;
for (i=1; i!=10; i=i+1)
sum = sum + i;
ARM Assembly Code
for Loops

## Slide 78
C Code
// adds numbers from 1-9
int sum = 0
for (i=1; i!=10; i=i+1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #1 ; i = 1
MOV R1, #0 ; sum = 0
FOR
CMP R0, #10 ; R0-10
BEQ DONE ; if (i==10) ; exit loop
ADD R1, R1, R0 ; sum=sum + i
ADD R0, R0, #1 ; i = i + 1
B FOR ; repeat loop
DONE
for Loops

## Slide 79
In ARM, decremented loop variables are more efficient
for Loops: Decremented Loops

## Slide 80
C Code
// adds numbers from 1-9
int sum = 0
for (i=9; i!=0; i=i-1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #9 ; i = 9
MOV R1, #0 ; sum = 0
FOR
ADD R1, R1, R0 ; sum=sum + i
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BNE FOR ; if (i!=0) ; repeat loop
In ARM, decremented loop variables are more efficient
for Loops: Decremented Loops

## Slide 81
C Code
// adds numbers from 1-9
int sum = 0
for (i=9; i!=0; i=i-1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #9 ; i = 9
MOV R1, #0 ; sum = 0
FOR
ADD R1, R1, R0 ; sum=sum + i
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BNE FOR ; if (i!=0) ; repeat loop
In ARM, decremented loop variables are more efficient
Saves 2 instructions per iteration:
Decrement loop variable & compare: SUBS R0, R0, #1
Only 1 branch – instead of 2
for Loops: Decremented Loops

## Slide 82
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 83
Access large amounts of similar data
  Index: access to each element
  Size: number of elements
Arrays

## Slide 84
200-element array
  Base address = 0x14000000 (address of first element, scores[0])
  Array elements accessed relative to base address
Arrays

## Slide 85
C Code
int array[200];
array[0] = array[0] * 8;
array[1] = array[1] * 8;
ARM Assembly Code
; R0 = array base address
Accessing Arrays

## Slide 86
C Code
int array[5];
array[0] = array[0] * 8;
array[1] = array[1] * 8;
ARM Assembly Code
; R0 = array base address
MOV R0, #0x60000000 ; R0 = 0x60000000
LDR R1, [R0] ; R1 = array[0]
LSL R1, R1, 3 ; R1 = R1 << 3 = R1*8
STR R1, [R0] ; array[0] = R1
LDR R1, [R0, #4] ; R1 = array[1]
LSL R1, R1, 3 ; R1 = R1 << 3 = R1*8
STR R1, [R0, #4] ; array[1] = R1
Accessing Arrays

## Slide 87
C Code
int array[200];
int i;
for (i=199; i >= 0; i = i - 1)
array[i] = array[i] * 8;
ARM Assembly Code
; R0 = array base address, R1 = i
Arrays using for Loops

## Slide 88
C Code
int array[200];
int i;
for (i=199; i >= 0; i = i - 1)
array[i] = array[i] * 8;
ARM Assembly Code
; R0 = array base address, R1 = i
MOV R0, 0x60000000
MOV R1, #199
FOR
LDR R2, [R0, R1, LSL #2] ; R2 = array(i)
LSL R2, R2, #3 ; R2 = R2<<3 = R3*8
STR R2, [R0, R1, LSL #2] ; array(i) = R2
SUBS R1, R1, #1 ; i = i – 1
; and set flags
BPL FOR ; if (i>=0) repeat loop
Arrays using for Loops

## Slide 89
American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)
ASCII Code

## Slide 90
Cast of Characters

## Slide 91
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 92
Caller: calling function (in this case, main)
Callee: called function (in this case, sum)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}
Function Calls

## Slide 93
Caller:
  passes arguments to callee
  jumps to callee
Function Conventions

## Slide 94
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller
Function Conventions

## Slide 95
Call Function: branch and link
BL
Return from function: move the link register to PC: MOV PC, LR
Arguments: R0-R3
Return value: R0
ARM Function Conventions

## Slide 96
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls
void means that simple doesn’t return a value

## Slide 97
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
BL branches to SIMPLE
LR = PC + 4 = 0x00000204
MOV PC, LR makes PC = LR
(the next instruction executed is at 0x00000200)
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls

## Slide 98
ARM conventions:
Argument values: R0 - R3
Return value: R0
Input Arguments and Return Value

## Slide 99
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}
Input Arguments and Return Value

## Slide 100
ARM Assembly Code
; R4 = y
MAIN
...
MOV R0, #2 ; argument 0 = 2
MOV R1, #3 ; argument 1 = 3
MOV R2, #4 ; argument 2 = 4
MOV R3, #5 ; argument 3 = 5
BL DIFFOFSUMS ; call function
MOV R4, R0 ; y = returned value
...
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
Input Arguments and Return Value

## Slide 101
ARM Assembly Code
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
diffofsums overwrote 3 registers: R4, R8, R9
diffofsums can use stack to temporarily store registers
Input Arguments and Return Value

## Slide 102
Memory used to temporarily save variables
Like stack of dishes, last-in-first-out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space no longer needed
The Stack

## Slide 103
Grows down (from higher to lower memory addresses)
Stack pointer: SP points to top of the stack
The Stack
Stack expands by 2 words

## Slide 104
Called functions must have no unintended side effects
But diffofsums overwrites 3 registers: R4, R8, R9
ARM Assembly Code
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
How Functions use the Stack

## Slide 105
ARM Assembly Code
; R2 = result
DIFFOFSUMS
SUB SP, SP, #12 ; make space on stack for 3 registers
STR R4, [SP, 8] ; save R4 on stack
STR R8, [SP, #4] ; save R8 on stack
STR R9, [SP] ; save R9 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R9, [SP] ; restore R9 from stack
LDR R8, [SP, #4] ; restore R8 from stack
LDR R4, [SP, #8] ; restore R4 from stack
ADD SP, SP, #12 ; deallocate stack space
MOV PC, LR ; return to caller
Storing Register Values on the Stack

## Slide 106
Before call
During call
After call
The Stack during diffofsums Call

## Slide 107
Preserved Callee-Saved | Nonpreserved Caller-Saved
R4-R11 | R12
R14 (LR) | R0-R3
R13 (SP) | CPSR
stack above SP | stack below SP
Registers

## Slide 108
ARM Assembly Code
; R2 = result
DIFFOFSUMS
STR R4, [SP, #-4]! ; save R4 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R4, [SP], #4 ; restore R4 from stack
MOV PC, LR ; return to caller
Storing Saved Registers only on Stack

## Slide 109
ARM Assembly Code
; R2 = result
DIFFOFSUMS
STR R4, [SP, #-4]! ; save R4 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R4, [SP], #4 ; restore R4 from stack
MOV PC, LR ; return to caller
Notice code optimization for expanding/contracting stack
Storing Saved Registers only on Stack

## Slide 110
ARM Assembly Code
STR LR, [SP, #-4]! ; store LR on stack
BL PROC2 ; call another function
...
LDR LR, [SP], #4 ; restore LR from stack
MOV PC, LR ; return to caller
Nonleaf Function

## Slide 111
C Code
int f1(int a, int b) {
int i, x;
x = (a + b)*(a − b);
for (i=0; i<a; i++)
x = x + f2(b+i);
return x;
}
int f2(int p) {
int r;
r = p + 5;
return r + p;
}
Nonleaf Function Example

## Slide 112
C Code
int f1(int a, int b) {
int i, x;
x = (a + b)*(a − b);
for (i=0; i<a; i++)
x = x + f2(b+i);
return x;
}
int f2(int p) {
int r;
r = p + 5;
return r + p;
}
Nonleaf Function Example
ARM Assembly Code
; R0=a, R1=b, R4=i, R5=x
F1
PUSH {R4, R5, LR}
ADD R5, R0, R1
SUB R12, R0, R1
MUL R5, R5, R12
MOV R4, #0
FOR
CMP R4, R0
BGE RETURN
PUSH {R0, R1}
ADD R0, R1, R4
BL F2
ADD R5, R5, R0
POP {R0, R1}
ADD R4, R4, #1
B FOR
RETURN
MOV R0, R5
POP {R4, R5, LR}
MOV PC, LR
; R0=p, R4=r
F2
PUSH {R4}
ADD R4, R0, 5
ADD R0, R4, R0
POP {R4}
MOV PC, LR

## Slide 113
Nonleaf Function Example
ARM Assembly Code
; R0=a, R1=b, R4=i, R5=x
F1
PUSH {R4, R5, LR} ; save regs
ADD R5, R0, R1 ; x = (a+b)
SUB R12, R0, R1 ; temp = (a-b)
MUL R5, R5, R12 ; x = x*temp
MOV R4, #0 ; i = 0
FOR
CMP R4, R0 ; i < a?
BGE RETURN ; no: exit loop
PUSH {R0, R1} ; save regs
ADD R0, R1, R4 ; arg is b+i
BL F2 ; call f2(b+i)
ADD R5, R5, R0 ; x = x+f2(b+i)
POP {R0, R1} ; restore regs
ADD R4, R4, #1 ; i++
B FOR ; repeat loop
RETURN
MOV R0, R5 ; return x
POP {R4, R5, LR} ; restore regs
MOV PC, LR ; return
; R0=p, R4=r
F2
PUSH {R4} ; save regs
ADD R4, R0, 5 ; r = p+5
ADD R0, R4, R0 ; return r+p
POP {R4} ; restore regs
MOV PC, LR ; return

## Slide 114
Stack during Nonleaf Function
At beginning of f1
Just before calling f2
After calling f2

## Slide 115
C Code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}
Recursive Function Call

## Slide 116
ARM Assembly Code
0x94 FACTORIAL STR R0, [SP, #-4]! ;store R0 on stack
0x98 STR LR, [SP, #-4]! ;store LR on stack
0x9C CMP R0, #2 ;set flags with R0-2
0xA0 BHS ELSE ;if (r0>=2) branch to else
0xA4 MOV R0, #1 ; otherwise return 1
0xA8 ADD SP, SP, #8 ; restore SP 1
0xAC MOV PC, LR ; return
0xB0 ELSE SUB R0, R0, #1 ; n = n - 1
0xB4 BL FACTORIAL ; recursive call
0xB8 LDR LR, [SP], #4 ; restore LR
0xBC LDR R1, [SP], #4 ; restore R0 (n) into R1
0xC0 MUL R0, R1, R0 ; R0 = n*factorial(n-1)
0xC4 MOV PC, LR ; return
Recursive Function Call

## Slide 117
ARM Assembly Code
0x94 FACTORIAL STR R0, [SP, #-4]!
0x98 STR LR, [SP, #-4]!
0x9C CMP R0, #2
0xA0 BHS ELSE
0xA4 MOV R0, #1
0xA8 ADD SP, SP, #8
0xAC MOV PC, LR
0xB0 ELSE SUB R0, R0, #1
0xB4 BL FACTORIAL
0xB8 LDR LR, [SP], #4
0xBC LDR R1, [SP], #4
0xC0 MUL R0, R1, R0
0xC4 MOV PC, LR
Recursive Function Call
C Code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}

## Slide 118
Before call
During call
After call
Stack during Recursive Call

## Slide 119
Caller
  Puts arguments in R0-R3
  Saves any needed registers (LR, maybe R0-R3, R8-R12)
  Calls function: BL CALLEE
  Restores registers
  Looks for result in R0
Callee
  Saves registers that might be disturbed (R4-R7)
  Performs function
  Puts result in R0
  Restores registers
  Returns: MOV PC, LR
Function Call Summary

## Slide 120
How to Encode Instructions?

## Slide 121
How to Encode Instructions?
Design Principle 1: Regularity supports design simplicity
  32-bit data, 32-bit instructions
  For design simplicity, would prefer a single instruction format but…

## Slide 122
How to Encode Instructions?
Design Principle 1: Regularity supports design simplicity
  32-bit data, 32-bit instructions
  For design simplicity, would prefer a single instruction format but…
  Instructions have different needs

## Slide 123
Good design demands good compromises
Multiple instruction formats allow flexibility
  ADD, SUB: use 3 register operands
  LDR, STR: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (regularity supports design simplicity and smaller is faster)
Design Principle 4

## Slide 124
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
3 instruction formats:
  Data-processing
  Memory
  Branch
Machine Language

## Slide 125
Data-processing
Memory
Branch
Instruction Formats

## Slide 126
Operands:
  Rn: first source register
  Src2: second source – register or immediate
  Rd: destination register
Control fields:
  cond: specifies conditional execution
  op: the operation code or opcode
  funct: the function/operation to perform
Data-processing Instruction Format

## Slide 127
op = 002 for data-processing (DP) instructions
funct is composed of cmd, I-bit, and S-bit
Data-processing Control Fields

## Slide 128
op = 002 for data-processing (DP) instructions
funct is composed of cmd, I-bit, and S-bit
  cmd: specifies the specific data-processing instruction. For example,
    cmd = 01002 for ADD
    cmd = 00102 for SUB
  I-bit
    I = 0: Src2 is a register
    I = 1: Src2 is an immediate
  S-bit: 1 if sets condition flags
    S = 0: SUB R0, R5, R7
    S = 1: ADDS R8, R2, R4 or CMP R3, #10
Data-processing Control Fields

## Slide 129
Src2 can be:
  Immediate
  Register
  Register-shifted register
Data-processing Src2 Variations

## Slide 130
Src2 can be:
  Immediate
  Register
  Register-shifted register
Data-processing Src2 Variations

## Slide 131
Immediate encoded as:
  imm8: 8-bit unsigned immediate
  rot: 4-bit rotation value
32-bit constant is: imm8 ROR (rot × 2)
Immediate Src2

## Slide 132
Immediate encoded as:
  imm8: 8-bit unsigned immediate
  rot: 4-bit rotation value
32-bit constant is: imm8 ROR (rot × 2)
Example: imm8 = abcdefgh
Immediate Src2
rot | 32-bit constant
0000 | 0000 0000 0000 0000 0000 0000 abcd efgh
0001 | gh00 0000 0000 0000 0000 0000 00ab cdef
… | …
1111 | 0000 0000 0000 0000 0000 00ab cdef gh00

## Slide 133
Immediate encoded as:
  imm8: 8-bit unsigned immediate
  rot: 4-bit rotation value
32-bit constant is: imm8 ROR (rot × 2)
Example: imm8 = abcdefgh
Immediate Src2
rot | 32-bit constant
0000 | 0000 0000 0000 0000 0000 0000 abcd efgh
0001 | gh00 0000 0000 0000 0000 0000 00ab cdef
… | …
1111 | 0000 0000 0000 0000 0000 00ab cdef gh00
ROR by X = ROL by (32-X)
Ex: ROR by 30 = ROL by 2

## Slide 134
  ADD R0, R1, #42
        cond = 11102 (14) for unconditional execution
        op = 002 (0) for data-processing instructions
        cmd = 01002 (4) for ADD
        Src2 is an immediate so I = 1
        Rd = 0, Rn = 1
        imm8 = 42, rot = 0
DP Instruction with Immediate Src2

## Slide 135
  ADD R0, R1, #42
        cond = 11102 (14) for unconditional execution
        op = 002 (0) for data-processing instructions
        cmd = 01002 (4) for ADD
        Src2 is an immediate so I = 1
        Rd = 0, Rn = 1
        imm8 = 42, rot = 0
DP Instruction with Immediate Src2
0xE281002A

## Slide 136
  SUB R2, R3, #0xFF0
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 00102 (2) for SUB
  Src2 is an immediate so I=1
  Rd = 2, Rn = 3
  imm8 = 0xFF
  imm8 must be rotated right by 28 to produce 0xFF0, so rot = 14
DP Instruction with Immediate Src2
0xE2432EFF
ROR by 28 =
ROL by (32-28) = 4

## Slide 137
DP Instruction with Register Src2
Src2 can be:
  Immediate
  Register
  Register-shifted register

## Slide 138
DP Instruction with Register Src2
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift (i.e., >>, <<, >>>, ROR)

## Slide 139
DP Instruction with Register Src2
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift (i.e., >>, <<, >>>, ROR)
  First, consider unshifted versions of Rm (shamt5=0, sh=0)

## Slide 140
  ADD R5, R6, R7
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 01002 (4) for ADD
  Src2 is a register so I=0
  Rd = 5, Rn = 6, Rm = 7
  shamt = 0, sh = 0
DP Instruction with Register Src2
0xE0865007

## Slide 141
DP Instruction with Register Src2
Rm: the second source operand
shamt5: the amount Rm is shifted
sh: the type of shift
Shift Type | sh
LSL | 002
LSR | 012
ASR | 102
ROR | 112
  Now, consider shifted versions.

## Slide 142
DP Instruction with Register Src2
  ORR R9, R5, R3, LSR #2
  Operation: R9 = R5 OR (R3 >> 2)
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11002 (12) for ORR
  Src2 is a register so I=0
  Rd = 9, Rn = 5, Rm = 3
  shamt5 = 2, sh = 012 (LSR)
  1110 00 0 1100 0 0101 1001 00010 01 0 0011
  0xE1859123

## Slide 143
DP with Register-shifted Reg. Src2
Src2 can be:
  Immediate
  Register
  Register-shifted register

## Slide 144
DP with Register-shifted Reg. Src2
  EOR R8, R9, R10, ROR R12
  Operation: R8 = R9 XOR (R10 ROR R12)
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 00012 (1) for EOR
  Src2 is a register so I=0
  Rd = 8, Rn = 9, Rm = 10, Rs = 12
  sh = 112 (ROR)
  1110 00 0 0001 0 1001 1000 1100 0 11 1 1010
  0xE0298C7A

## Slide 145
Shift Instructions Encoding
Shift Type | sh
LSL | 002
LSR | 012
ASR | 102
ROR | 112

## Slide 146
Shift Instructions: Immediate shamt
  ROR R1, R2, #23
  Operation: R1 = R2 ROR 23
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is an immediate-shifted register so I=0
  Rd = 1, Rn = 0, Rm = 2
  shamt5 = 23, sh = 112 (ROR)
  1110 00 0 1101 0 0000 0001 10111 11 0 0010
  0xE1A01BE2

## Slide 147
Shift Instructions: Immediate shamt
  ROR R1, R2, #23
  Operation: R1 = R2 ROR 23
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is an immediate-shifted register so I=0
  Rd = 1, Rn = 0, Rm = 2
  shamt5 = 23, sh = 112 (ROR)
Uses (immediate-shifted) register Src2 encoding
  1110 00 0 1101 0 0000 0001 10111 11 0 0010
  0xE1A01BE2

## Slide 148
Shift Instructions: Register shamt
  ASR R5, R6, R10
  Operation: R5 = R6 >>> R107:0
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is a register so I=0
  Rd = 5, Rn = 0, Rm = 6, Rs = 10
  sh = 102 (ASR)
  1110 00 0 1101 0 0000 0101 1010 0 10 1 0110
  0xE1A05A56

## Slide 149
Shift Instructions: Register shamt
  ASR R5, R6, R10
  Operation: R5 = R6 >>> R107:0
  cond = 11102 (14) for unconditional execution
  op = 002 (0) for data-processing instructions
  cmd = 11012 (13) for all shifts (LSL, LSR, ASR, and ROR)
  Src2 is a register so I=0
  Rd = 5, Rn = 0, Rm = 6, Rs = 10
  sh = 102 (ASR)
  1110 00 0 1101 0 0000 0101 1010 0 10 1 0110
  0xE1A05A56
Uses register-shifted register Src2 encoding

## Slide 150
Src2 can be:
  Immediate
  Register
  Register-shifted register
Review: Data-processing Format

## Slide 151
Data-processing
Memory
Branch
Instruction Formats

## Slide 152
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset
funct = 6 control bits
Memory Instruction Format

## Slide 153
Recall: Address = Base Address + Offset
  Example: LDR R1, [R2, #4]
  Base Address = R2, Offset = 4
  Address = (R2 + 4)
Base address always in a register
The offset can be:
  an immediate
  a register
  or a scaled (shifted) register
Offset Options

## Slide 154
ARM Assembly | Memory Address
LDR R0, [R3, #4] | R3 + 4
LDR R0, [R5, #-16] | R5 – 16
LDR R1, [R6, R7] | R6 + R7
LDR R2, [R8, -R9] | R8 – R9
LDR R3, [R10, R11, LSL #2] | R10 + (R11 << 2)
LDR R4, [R1, -R12, ASR #4] | R1 – (R12 >>> 4)
LDR R0, [R9] | R9
Offset Examples

## Slide 155
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: register (optionally shifted) or immediate
funct = 6 control bits
Memory Instruction Format

## Slide 156
Mode | Address | Base Reg. Update
Offset | Base register ± Offset | No change
Preindex | Base register ± Offset | Base register ± Offset
Postindex | Base register | Base register ± Offset
Examples
Offset: LDR R1, [R2, #4] ; R1 = mem[R2+4]
Preindex: LDR R3, [R5, #16]! ; R3 = mem[R5+16]
; R5 = R5 + 16
Postindex: LDR R8, [R1], #8 ; R8 = mem[R1]
    ; R1 = R1 + 8
Indexing Modes

## Slide 157
funct:
  I: Immediate bar
  P: Preindex
  U: Add
  B: Byte
  W: Writeback
  L: Load
Memory Instruction Format

## Slide 158
Memory Format funct Encodings
Type of Operation
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 159
P | W | Indexing Mode
0 | 1 | Not supported
0 | 0 | Postindex
1 | 0 | Offset
1 | 1 | Preindex
Memory Format funct Encodings
Type of Operation
Indexing Mode
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 160
P | W | Indexing Mode
0 | 1 | Not supported
0 | 0 | Postindex
1 | 0 | Offset
1 | 1 | Preindex
Memory Format funct Encodings
Type of Operation
Value | I | U
0 | Immediate offset in Src2 | Subtract offset from base
1 | Register offset in Src2 | Add offset to base
Add/Subtract Immediate/Register Offset
Indexing Mode
L | B | Instruction
0 | 0 | STR
0 | 1 | STRB
1 | 0 | LDR
1 | 1 | LDRB

## Slide 161
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: immediate or register (optionally shifted)
funct = I (immediate bar), P (preindex), U (add),
B (byte), W (writeback), L (load)
Memory Instruction Format

## Slide 162
Memory Instr. with Immediate Src2
  STR R11, [R5], #-26
  Operation: mem[R5] <= R11; R5 = R5 - 26
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 00000002 (0)
  I = 0 (immediate offset), P = 0 (postindex),
  U = 0 (subtract), B = 0 (store word), W = 0 (postindex),
  L = 0 (store)
  Rd = 11, Rn = 5, imm12 = 26

## Slide 163
Memory Instr. with Register Src2
  LDR R3, [R4, R5]
  Operation: R3 <= mem[R4 + R5]
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 1110012 (57)
  I = 1 (register offset), P = 1 (offset indexing),
  U = 1 (add), B = 0 (load word), W = 0 (offset indexing),
  L = 1 (load)
  Rd = 3, Rn = 4, Rm = 5 (shamt5 = 0, sh = 0)
  1110 01 111001 0100 0011 00000 00 0 0101 = 0xE7943005

## Slide 164
Memory Instr. with Scaled Reg. Src2
  STR R9, [R1, R3, LSL #2]
  Operation: mem[R1 + (R3 << 2)] <= R9
  cond = 11102 (14) for unconditional execution
  op = 012 (1) for memory instruction
  funct = 1110002 (0)
  I = 1 (register offset), P = 1 (offset indexing),
  U = 1 (add), B = 0 (store word), W = 0 (offset indexing),
  L = 0 (store)
  Rd = 9, Rn = 1, Rm = 3, shamt = 2, sh = 002 (LSL)
  1110 01 111000 0001 1001 00010 00 0 0011 = 0xE7819103

## Slide 165
Encodes: LDR, STR, LDRB, STRB
op = 012
Rn = base register
Rd = destination (load), source (store)
Src2 = offset: register (optionally shifted) or immediate
funct = I (immediate bar), P (preindex), U (add),
B (byte), W (writeback), L (load)
Review: Memory Instruction Format

## Slide 166
Data-processing
Memory
Branch
Instruction Formats

## Slide 167
Encodes B and BL
op = 102
imm24: 24-bit immediate
funct = 1L2: L = 1 for BL, L = 0 for B
Branch Instruction Format

## Slide 168
Branch Target Address (BTA): Next PC when branch taken
BTA is relative to current PC + 8
imm24 encodes BTA
imm24 = # of words BTA is away from PC+8
Encoding Branch Target Address

## Slide 169
ARM assembly code
0xA0 BLT THERE
0xA4 ADD R0, R1, R2
0xA8 SUB R0, R0, R9
0xAC ADD SP, SP, #8
0xB0 MOV PC, LR
0xB4 THERE SUB R0, R0, #1
0xB8 BL TEST
PC = 0xA0
PC + 8 = 0xA8
THERE label is 3 instructions past PC+8
So, imm24 = 3
PC
PC+8
BTA
Branch Instruction: Example 1
0xBA000003

## Slide 170
ARM assembly code
0x8040 TEST LDRB R5, [R0, R3]
0x8044 STRB R5, [R1, R3]
0x8048 ADD R3, R3, #1
0x8044 MOV PC, LR
0x8050 BL TEST
0x8054 LDR R3, [R1], #4
0x8058 SUB R4, R3, #9
PC = 0x8050
PC + 8 = 0x8058
TEST label is 6 instructions before PC+8
So, imm24 = -6
Branch Instruction: Example 2
PC
PC+8
BTA

## Slide 171
ARM assembly code
0x8040 TEST LDRB R5, [R0, R3]
0x8044 STRB R5, [R1, R3]
0x8048 ADD R3, R3, #1
0x8044 MOV PC, LR
0x8050 BL TEST
0x8054 LDR R3, [R1], #4
0x8058 SUB R4, R3, #9
PC = 0x8050
PC + 8 = 0x8058
TEST label is 6 instructions before PC+8
So, imm24 = -6
Branch Instruction: Example 2
PC
PC+8
BTA

## Slide 172
ARM assembly code
0x8040 TEST LDRB R5, [R0, R3]
0x8044 STRB R5, [R1, R3]
0x8048 ADD R3, R3, #1
0x8044 MOV PC, LR
0x8050 BL TEST
0x8054 LDR R3, [R1], #4
0x8058 SUB R4, R3, #9
PC = 0x8050
PC + 8 = 0x8058
TEST label is 6 instructions before PC+8
So, imm24 = -6
Branch Instruction: Example 2
PC
PC+8
BTA
0xEBFFFFFA

## Slide 173
Review: Instruction Formats

## Slide 174
Encode in cond bits of machine instruction
  For example,
  ANDEQ R1, R2, R3 (cond = 0000)
  ORRMI R4, R5, #0xF (cond = 0100)
  SUBLT R9, R3, R8 (cond = 1011)
Conditional Execution

## Slide 175
Review: Condition Mnemonics

## Slide 176
Conditional Execution: Machine Code

## Slide 177
Start with op: tells how to parse rest
    op = 00 (Data-processing)
    op = 01 (Memory)
    op = 10 (Branch)
I-bit: tells how to parse Src2
Data-processing instructions:
    If I-bit is 0, bit 4 determines if Src2 is a register (bit 4 = 0) or a register-shifted register (bit 4 = 1)
Memory instructions:
    Examine funct bits for indexing mode, instruction, and add or subtract offset
Interpreting Machine Code

## Slide 178
0xE0475001
Interpreting Machine Code: Example 1

## Slide 179
0xE0475001
  Start with op: 002, so data-processing instruction
Interpreting Machine Code: Example 1

## Slide 180
0xE0475001
  Start with op: 002, so data-processing instruction
  I-bit: 0, so Src2 is a register
  bit 4: 0, so Src2 is a register (optionally shifted by shamt5)
Interpreting Machine Code: Example 1

## Slide 181
0xE0475001
  Start with op: 002, so data-processing instruction
  I-bit: 0, so Src2 is a register
  bit 4: 0, so Src2 is a register (optionally shifted by shamt5)
  cmd: 00102 (2), so SUB
  Rn=7, Rd=5, Rm=1, shamt5 = 0, sh = 0
  So, instruction is: SUB R5,R7,R1
Interpreting Machine Code: Example 1

## Slide 182
0xE5949010
Interpreting Machine Code: Example 2

## Slide 183
0xE5949010
  Start with op: 012, so memory instruction
  funct: B=0, L=1, so LDR; P=1, W=0, so offset indexing;
  I=0, so immediate offset, U=1, so add offset
  Rn=4, Rd=9, imm12 = 16
  So, instruction is: LDR R9,[R4,#16]
Interpreting Machine Code: Example 2

## Slide 184
How do we address operands?
Register
Immediate
Base
PC-Relative
Addressing Modes

## Slide 185
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 186
Source and destination operands found in registers
Used by data-processing instructions
Three submodes:
  Register-only
  Immediate-shifted register
  Register-shifted register
Register Addressing

## Slide 187
Register-only
  Example: ADD R0, R2, R7
Immediate-shifted register
  Example: ORR R5, R1, R3, LSL #1
Register-shifted register
  Example: SUB R12, R9, R0, ASR R1
Register Addressing Examples

## Slide 188
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 189
Operands found in registers and immediates
  Example: ADD R9, R1, #14
Uses data-processing format with I=1
  Immediate is encoded as
    8-bit immediate (imm8)
    4-bit rotation (rot)
  32-bit immediate = imm8 ROR (rot x 2)
Immediate Addressing

## Slide 190
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 191
Address of operand is:
base register + offset
Offset can be a:
  12-bit Immediate
  Register
  Immediate-shifted Register
Base Addressing

## Slide 192
Immediate offset
  Example: LDR R0, [R8, #-11]
  (R0 = mem[R8 - 11] )
Register offset
  Example: LDR R1, [R7, R9]
  (R1 = mem[R7 + R9] )
Immediate-shifted register offset
  Example: STR R5, [R3, R2, LSL #4]
  (R5 = mem[R3 + (R2 << 4)] )
Base Addressing Examples

## Slide 193
How do we address operands?
Register Only
Immediate
Base
PC-Relative
Addressing Modes

## Slide 194
Used for branches
Branch instruction format:
  Operands are PC and a signed 24-bit immediate (imm24)
  Changes the PC
  New PC is relative to the old PC
  imm24 indicates the number of words away from PC+8
PC = (PC+8) + (SignExtended(imm24) x 4)
PC-Relative Addressing

## Slide 195
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation
Power of the Stored Program

## Slide 196
Program Counter (PC): keeps track of current instruction
The Stored Program

## Slide 197
How to implement the ARM Instruction Set
Architecture in Hardware
  Microarchitecture
Up Next